## Slide 1
Quantum sensor networks with high efficiency transduction
Silvia Zorzetti
Superconducting Quantum Materials and Systems (SQMS) Center, Fermi National Accelerator Laboratory

## Slide 2: Introduction to Quantum Transduction
Optical
Microwave
~200 THz
∼GHz
Cryogenic temperature
Superconducting
qubits/sensors
Room temperature
Transducer
Optical
communication

## Slide 3: Quantum transduction in computing and sensing
Single microwave
photon counter
Enable sensor networks and
coherent postprocessing
Remote entanglement
generation
Optical
Microwave
~200 THz
∼GHz
Cryogenic temperature
Superconducting
qubits/sensors
Room temperature
Transducer
Optical
communication

## Slide 4: Introduction to Quantum Transduction
Quantum transduction
  Mediates microwave/optical frequencies.
  Electro-optic transduction provides a direct conversion
Electro-optic nonlinearity for transduction
  Nonlinear crystal: LiNbO3, AlN
  High electro-optic coefficient and low losses at both microwave and telecom frequencies
  Pump light three wave mixing:
  Bidirectional conversion:
Optical
Microwave
~200 THz
∼GHz
Cryogenic temperature
Superconducting
qubits/sensors
Room temperature
Transducer
Optical
communication

## Slide 5: Electro-optic direct frequency conversion
2D Thin-film lithium niobate cavity
@19.95mW
Nature communications 12, 1 (2021)
Limiting factors
Single-photon microwave-optic coupling coefficient (g). Determined by field overlap.
Q factor of the microwave cavity
  Q optical cavity up to 107
  Q microwave <
Limited pump power. High pump power leads to overheating of the device and noise.
2D Thin-film lithium niobate cavity
@0.32 mW
Optica 7, 1714 (2020)
Bulk LN in 3D microwave cavity
@1.48 mW
PRX QUANTUM 1,020315 (2020)

## Slide 6: Electro-optic direct frequency conversion
2D Thin-film lithium niobate cavity
@19.95mW
Nature communications 12, 1 (2021)
2D Thin-film lithium niobate cavity
@0.32 mW
Optica 7, 1714 (2020)
Bulk LN in 3D microwave cavity
@1.48 mW
PRX QUANTUM 1,020315 (2020)
M-O coupling

## Slide 7: 3D electro-optical quantum transduction
3D electro-optical design for transduction
High-Q cavities to boost microwave-optic conversion efficiency in quantum transduction
Estimated conversion efficiency up to 50% at 140
Characterization of Electro-optic materials
First precise measurements of loss tangent and permittivity of lithium niobate (LN) at millikelvin temperatures
Fermilab’s 3D Bulk Niobium superconducting cavity ()
Physical Review Applied, 13, 034032 (2020).
Applications
Sensing: photon-counting in the optical regime
Communication: increase entanglement rate
Phys. Rev. B 107, L220302 (2022)
Npj Quantum Information, 8 149 (2023)
ArXiv in preparation – with Prof. Zhuang
IEEE QCE23 – with Prof. Cacciapuoti
Notes: Mension anisotropic

## Slide 8: 3D electro-optical quantum transduction
3D electro-optical design for transduction
High-Q cavities to boost microwave-optic conversion efficiency in quantum transduction
Estimated conversion efficiency up to 50% at 140
Characterization of Electro-optic materials
First precise measurements of loss tangent and permittivity of lithium niobate (LN) at millikelvin temperatures
Fermilab’s 3D Bulk Niobium superconducting cavity ()
Physical Review Applied, 13, 034032 (2020).
Applications
Sensing: photon-counting in the optical regime
Communication: increase entanglement rate
Phys. Rev. B 107, L220302 (2022)
Npj Quantum Information, 8 149 (2023)
ArXiv in preparation – with Prof. Zhuang
IEEE QCE23 – with Prof. Cacciapuoti
This talk
This talk
Notes: Mension anisotropic

## Slide 9: 3D electro-optical quantum transduction
3D electro-optical design for transduction
High-Q cavities to boost microwave-optic conversion efficiency in quantum transduction
Estimated conversion efficiency up to 50% at 140
Characterization of Electro-optic materials
First precise measurements of loss tangent and permittivity of lithium niobate (LN) at millikelvin temperatures
Fermilab’s 3D Bulk Niobium superconducting cavity ()
Physical Review Applied, 13, 034032 (2020).
Applications
Sensing: photon-counting in the optical regime
Communication: increase entanglement rate
Phys. Rev. B 107, L220302 (2022)
Npj Quantum Information, 8 149 (2023)
ArXiv in preparation – with Prof. Zhuang
IEEE QCE23 – with Prof. Cacciapuoti
Notes: Mension anisotropic

## Slide 10: 3D cavity Electro-Optic Design
Key points of the design
Match optical free spectral range to microwave frequency
Optimal field overlap between microwave and optical modes
High microwave quality factor (~105)
Estimated conversion efficiency
  50% at 140
Hybrid resonant cavity
Emax on the rim of the optical resonator
Optical whispering gallery mode (WGM)
Optical coupler

## Slide 11: Hardware challenges
Typical WGM optical coupling setup with 8 piezo stages for 20mK *
Our transduction microwave cavity
Optical coupling
Laser
Microwave tuning
Draft cryogenic transduction setup
Laser
Optical coupling
Microwave tuning
Alignment
Optical components in system needing positioning capabilities for alignment
Total 6 critical dimensions of control for coupling problem (including dynamic polarization control)
Optical coupling
Optical coupling maintained during cooldown through monitoring waveform
Thermal quasiparticle
The laser pump will induce thermal quasiparticle and increase the system temperature
* Sahu R. Cavity quantum electrooptics – Fink Group IST

## Slide 12: Positioning/Alignment System
Custom holders for crystal and prism
LiNbO3 crystal and coupling prism on brackets
Mechanical System Block Diagram
Optical Table Setup for visible laser alignment
with two digital microscopes
Achieving optimal optical coupling to resonator requires precise positioning control
Piezo and motor translation and rotation stages
Manual kinematic mounts for lenses (2 DOF)
Digital microscopes for top and side views

## Slide 13: Evaluation
Figures of merit | 
Single-photon microwave-optical coupling rate () | Hz
Microwave quality factor () | 
Cooperativity () | 0.58
Conversion efficiency | 50%
Operating bandwidth | 100kHz
Pump power () | 140
Tunability | 700MHz
Figures of merit | 
 | 0.58
Conversion efficiency | 50%
Operating bandwidth | 100kHz
Tunability | 700MHz
High microwave quality factor leads to high conversion efficiency
Low pump power —> low thermal quasiparticle poisoning
Trade-off between MO coupling and efficiency. High efficiency and low pump power leads to entanglement without need of further purification
Operating bandwidth is within acceptable values for superconducting qubits
Quantum Sensing
Quantum Communication
Quantum Computing
** Wang et al. Npj Quantum Information, 8 149
Increase the operating range
Notes: Sample the TM110 mode

## Slide 14: Evaluation
Optical mode
Figures of merit | 
Single-photon microwave-optical coupling rate () | Hz
Microwave quality factor () | 
Cooperativity () | 0.58
Conversion efficiency | 50%
Operating bandwidth | 100kHz
Pump power () | 140
Tunability | 700MHz
Figures of merit | 
 | 0.58
Conversion efficiency | 50%
Operating bandwidth | 100kHz
Tunability | 700MHz
Operation under very different environmental conditions and close to the sensing cavity with a high magnetic field.
Ref. | Material | Notes |  | 
npj Quantum Inf. 8, 149 (2023) | Niobium | SRF |  | 
npj Quantum Inf. 8, 149 (2023) (Supp.) | Copper | Normal conducting |  | 
arXiv:2203.12714, 2022 | Nb3Sn | Magnetic field Ba=6T |  | 
Ref. | Material | Notes |  | 
npj Quantum Inf. 8, 149 (2023) | Niobium | SRF |  | 
npj Quantum Inf. 8, 149 (2023) (Supp.) | Copper | Normal conducting |  | 
arXiv:2203.12714, 2022 | Nb3Sn | Magnetic field Ba=6T |  | 
Notes: Sample the TM110 mode

## Slide 15: 3D electro-optical quantum transduction
3D electro-optical design for transduction
High-Q cavities to boost microwave-optic conversion efficiency in quantum transduction
Estimated conversion efficiency up to 50% at 140
Characterization of Electro-optic materials
First precise measurements of loss tangent and permittivity of lithium niobate (LN) at millikelvin temperatures
Fermilab’s 3D Bulk Niobium superconducting cavity ()
Physical Review Applied, 13, 034032 (2020).
Applications
Sensing: photon-counting in the optical regime
Communication: increase entanglement rate
Phys. Rev. B 107, L220302 (2022)
Npj Quantum Information, 8 149 (2023)
ArXiv in preparation – with Prof. Zhuang
IEEE QCE23 – with Prof. Cacciapuoti
Notes: Mension anisotropic

## Slide 16: Haloscope using transduction - motivation
Optical single photon counter
M-O transducer as a parametric amplifier
Haloscope with homodyne detection is commonly used but not optimal
Need of microwave single photon counters
Dissipation due to long RF cables
Use microwave-optical transducers for ultra-low noise parametric amplification
Low dark photon count  system temperature ~ cavity temperature  SNR and scan-rate improvement

## Slide 17: HALOscope using Teleportation-based Transduction And Photon-counting (HALO-TTAP)
ArXiv in preparation – SQMS/Fermilab and A. Brady (U. Arizona) , Zhuang, (USC)
The transducer’s temperature can be higher than 10mK
The transducer can be integrated with the sensing cavity in high magnetic field ()
Low loss signal conditioning over fiber optics

## Slide 18: HALO-TTAP advantage
Sensing advantage: enhancement of power SNR and axion scan-rate
Evaluate the scan-rate for ideal homodyne over the scan-rate achieved with transduction ()
Parameters: microwave loss, optical coupling and pump power

## Slide 19: HALO-TTAP advantage
Achieve over double the scan rate with pump power below 1 mW
This level of pump power is compatible with the cooling power of most commercial dilution refrigerators
> 5 at Pp
High microwave to achieve a higher advantage

## Slide 20: HALO-TTAP advantage
Scan rate improvement is possible over a wide range 2—20 GHz
Achieve over double the scan rate with pump power below 1 mW
This level of pump power is compatible with the cooling power of most commercial dilution refrigerators
> 5 at Pp

## Slide 21: Other applications in quantum computing and sensing
Entangled microwave-optical photons
Sensor network with joint post-processing
Remote entanglement generation
IEEE QCE23 – with Prof. Cacciapuoti, UniNa
Gravitational waves
Coherent post-processing of dark matter
Quantum networks
Interconnecting superconducting qubits

## Slide 22: Thank you!

## Slide 23: 3D cavity Electro-Optic
 Pump power limit
Figures of merit
 Pump power limit
Maximum efficiency 
Maximum efficiency 

## Slide 24: 3D cavity Electro-Optic
Figures of merit
50% at 150
 Pump power limit
 Pump power limit
 Maximum efficiency
 Maximum efficiency

## Slide 25: 3D cavity Electro-Optic
Figures of merit
50% at 150
Transduction in a superconducting QED system with a qubit
 Pump power limit
 Pump power limit
 Maximum efficiency
 Maximum efficiency

## Slide 26: Optical coupling
Microwave Q

## Slide 27: Haloscope using transduction
Evaluate the scan-rate using a Fisher information approach
Ideal homodyne:
Transduction based photon-counting:
NT, NTrans: Thermal noise of the sensing cavity and the transduction cavity
: to evaluate the advantage of this approach
arXiv in preparation in collaboration with Prof. Quntao Zhuang at USC and Dr. Brady at University of Arizona

## Slide 28: 3D electro-optical quantum transduction
3D electro-optical design for transduction
High-Q cavities to boost microwave-optic conversion efficiency in quantum transduction
Estimated conversion efficiency up to 50% at 140
Characterization of Electro-optic materials
First precise measurements of loss tangent and permittivity of lithium niobate (LN) at millikelvin temperatures
Fermilab’s 3D Bulk Niobium superconducting cavity ()
Physical Review Applied, 13, 034032 (2020).
Applications
Sensing: photon-counting in the optical regime
Communication: increase entanglement rate
Phys. Rev. B 107, L220302 (2022)
Npj Quantum Information, 8 149 (2023)
ArXiv in preparation – with Prof. Zhuang
IEEE QCE23 – with Prof. Cacciapuoti
Notes: Mension anisotropic

## Slide 29: Measurement of LiNbO3’s permittivity and loss tangent at mK
Aluminum cavity
Experimental Setup
Frequency shift:
Loaded Q factor:
TE mode
TM mode
Approach
The principal axis of LN is aligned with the z axis
LN sample

## Slide 30: Measurement of LiNbO3’s permittivity and loss tangent at mK
LiNbO3 property at 50mK
arXiv:2302.12916
,