## Slide 1: WP1 status and RF design
Alexej Grudiev on behalf of WP1
20/04/2023
FCC-ee Pre-Injector: CHART Collaboration Meeting
INFN Frascati, April 20-21, 2023

## Slide 2: Joint WP1 meetings since last collaboration meeting

## Slide 3: Some details on Who is doing What
Task 1.1: electron source and Pre-Pre-injector design
  Steffen, Zdenek (Master student, till 1/09/2023 ) (CERN)
Task 1.2: RF design of linacs
  Alexej, Adnan (Fellow, from 1/06/2023) (CERN)
Task 1.3: Beam dynamic design of the linacs
  Simona, Mattia (PSI)
Task 1.4: RF module design and cost
  Jean-Yves (PSI)
Great Support from
  Riccardo and Paolo (PSI), Andrea and Yongke (CERN), Iryna (IJCLab)

## Slide 4
Baseline layout
t [ms]
Vrf
0
5
10
40
200 Hz electron
200 Hz
positron
Common linac at 400 Hz
200Hz + 200 Hz
pLinac
Common Linac
DR
SPS (PBR)
eLinac
EC
BC
1.54 GeV
6 GeV
1.54 GeV
Positron source
Electron source
HE Linac
BR
20 GeV
2.8 GHz
200 Hz
2.8 GHz
2 x 200 Hz
2.8 – 5.6 GHz
200 Hz
2.0 GHz
200 Hz

## Slide 5: Parameters at BR injection
parameter | Baseline | Alternative | Comments
Ring for injection | BR | SPS or PBR | Destination
Injection energy [GeV] | 20 | 6 | Fixed
Bunch population [1e10] | 2.5 |  | 4 nC
Number of bunches | 2 | 2 | 
Repetition rate [Hz] | 200 | 200 | 
Bunch spacing [ns] | 25 |  | Sub-harmonics of 400 MHz, 2.5ns
Normalized transverse emittances (RMS): γε_x,y [um] | <10, <10 |  | 
Energy spread (RMS) [%] | ~0.1 |  | Can be adjusted by energy compressor
Bunch length (RMS) [mm] | ~1 |  | 
Stability at injection in BR for bunch length ~ 1 mm will be studied by BR team.
If longer bunches are required, TL will be adapted to stretch them.

## Slide 6: Nominal beam parameter evolution
parameter | e-source | eLinac | Common | HE linac | TL | comments
Injection energy [GeV] |  | ~0.2 | 1.54 | 6 | 20 | 
Energy gain [GeV] | ~0.2 | ~1.52 | 4.46 | 14 | 0 | 
Extraction Bunch population, (charge) [1e10, (nC)] | 4.13, (5.0) | 3.0, (4.8) | 2.88, (4.6) | 2.75, (4.4) | 2.5, (4.0) | 5% margin on each step. 10% for TL+BR
Extraction Normalized transverse emittances (RMS): γε_x,y [um] | <4.0 | <5.1 | <6.4 | <8 | <10 | 20% margin on each step. 20% for TL+BR
Energy spread (RMS) [%] |  |  |  |  | 0.1 – 0.5 | Can be adjusted by energy compressor
Bunch length (RMS) [mm] |  |  |  |  | 1 -- 10 | 
Bunch length and energy spread specification are given at 20 GeV.
At lower energy stages they can be different depending on what is better for linacs or e-source.
Positrons from DR

## Slide 7
Electron source and pre-pre-injector
Baseline Layout provide required parameters
It is being updated for 2.8 GHz and 3m long accelerating structure with A/lambda=0.15
More details in talk by Zdenek

## Slide 8: RF design status
2.0 GHz RF structure for p-linac is designed (Hermann, LINAC22)
  3m long, constant aperture radius = 30mm,
  2D-field map of full-length structure is calculated and used in BD
2.8 GHz RF structure for e- and c-linacs is designed (Hermann, LINAC22)
  3m long, <a/lambda> = 0.15
  Also, to be used in pre-pre-injector
C-band, 5.6 GHz RF structure is a viable option for high energy linac (still to be designed based on the required aperture from the BD)
  ~3m long, <a/lambda> ~ 0.25 (?)

## Slide 9: Beam dynamics in e- and c-linacs
Final emittance is < 6.4 mm mrad
Final emittance is < 5.1 mm mrad
More details in the talk by Simona

## Slide 10: HE-linac beam dynamics design (work in progress)
Option 1(S-band): 2.8 GHz, a/lambda=0.15, 30 MV/m
  It is essentially e-linac (200 Hz) RF modules for the energy gain from 6 to 20 GeV
Option 2(C-band): 5.6 GHz, a/lambda=0.25(under evaluation, TBC), 40 MV/m
  This is work in progress
More details in the talk by Simona

## Slide 11: Preliminary Linac parameter summary
 | e- linac | Common linac | HE linac | HE linac
Repetition Frequency (Hz) | 200 | 400 | 200 | 200
RF Frequency (GHz) | 2.8 | 2.8 | 2.8 | 5.6
Gradient (MV/m) | 28 | 25 | 30 | 40
a (mm) (a/l) | 16.1 (0.15) | 16.1 (0.15) | 16.1 (0.15) | 13.4 (0.25)
Length structures (m) | 3 | 3 | 3 | 3
Phase (deg) | 90 | 90 | 90 | 90
N. Structures | 16 | 60 | 156 | 118
N. correctors | 16 | 60 | 156 | 118
Max. strength correctors | << 20 T.mm | << 20 T.mm | < 20 T.mm | < 20 T.mm
N. BPM | 16 | 60 | 156 | 118
N. Quadrupoles | 16 | 60 | 156 | 118
K1 (1/m2) = 1/(B*rho)*G | 1.51 | 1.51 | 1.51 | 1.51
Length quads (m) | 0.25 | 0.25 | 0.25 | 0.25
Total length (m) | 60 | 225 | 585 | 442.5
C-band linac is 142.5 m shorter (30%)

## Slide 12: Positron linac beam dynamics design
Positron linac baseline
Electron separation chicane at ~200 MeV
Solenoidal focusing up to ~700 MeV
Quadrupolar focusing till 1.54GeV
More details in the talk by Mattia

## Slide 13: Preliminary layout of the positron linac
14 RF modules
#1
T
#1
#1
#1
#1
#1
#1
#1
#2
#2
#2
#2
#2
#2
Capture linac: ~15m
Solenoid focusing: ~40m
quad focusing: ~53m
e-/e+ separation
Matching
Energy compression
2m
15m
?m
125m

## Slide 14: Layout of electron and common linacs
30 RF modules
8 RF modules
1.5 E
G
e- source: ~10m
Electron linac: 60m
Common linac: 225m
Positron injection
6 GeV
?m
?m
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
…

## Slide 15
Baseline layout with length estimates
pLinac
Common Linac
DR
SPS (PBR)
eLinac
EC
BC
1.54 GeV
6 GeV
1.54 GeV
Positron source
Electron source
HE Linac
BR
20 GeV
2.8 GHz
200 Hz
2.8 GHz
2 x 200 Hz
2.8 – 5.6 GHz
200 Hz
2.0 GHz
200 Hz
70 m
225 m
585 – 442.5 m
125 m
X + Y + (880 or 737.5) m, overall length < ~1 km
X m
Y m
More details about cost and power in the linacs in the talk by Jean-Yves

## Slide 16: Summary and milestones
Done
Done
In progress
Started

## Slide 17: Back up

## Slide 18: Energy compressor after HE linac
Required R56
Question to the transfer line designers
for the moment we assume it is possible to do energy compression after the HE linac so we do not need to minimize energy spread in HE linac design