## Slide 1: Flux concentrator from SuperKEKB to ILC
2023/4/21
KEK iCASA positron group
Y. Enomoto

## Slide 2: Recent topics
2022/9 New group to develop positron source for ILC launched in KEK iCASA (Innovation Center for Applied Superconducting Accelerators)
2023/4 5 years budget for selected time-critical work packages* was approved
  *Source, SRF, nano-beam
International
Development
Team under ICFA
Pre-lab organized
by MoU’S among
the relevant labs.
IDT
ILC construction
by ILC Lab.
Aug. 2020
Experiment
at ILC
IDT phase
Pre-lab phase
Construction phase
Physics experiment
ILC lab. based on
the Governmental
agreement
Pre-lab
IDT
Joint R&D
(ILC technology network)
Int. Expert Panel
+ governmental
discussions

## Slide 3
WPP | 1 | Cavity production
WPP | 2 | CM design
WPP | 3 | Crab cavity
WPP | 4 | E- source
WPP | 6 | Undulator target
WPP | 7 | Undulator focusing
WPP | 8 | E-driven target
WPP | 9 | E-driven focusing
WPP | 10 | E-driven capture
WPP | 11 | Target replacement
WPP | 12 | System design
WPP | 14 | Injection/extraction
WPP | 15 | Final focus
WPP | 16 | Final doublet
WPP | 17 | Main dump
ILC Technology Network
WP-prime 1
Cavity production
WP-prime 2
Cryomodule design
WP-prime 3
Crab cavity
WP-prime 4
Electron source
WP-5
Undulator
Undulator positron scheme
E-driven positron scheme
WP-prime 6
Rotating target
WP-prime 7
Magnetic focusing
WP-prime 8
Rotating target
WP-prime 9
Magnetic focusing
WP-prime 10
Capture cavity
WP-prime 12
System design
WP-13
Collective effect
WP-prime 14
Injection/extraction
WP-prime 15
Final focus
WP-prime 17
Main dump
WP-18
Photon dump
WP-prime 11
Target replacement
WP-prime 16
Final doublet
ML&SRF
(Main linac &
Superconducting RF)
Sources
DR
(Damping ring)
BDS
(Beam Delivery System)
Dump
Time-critical WPs
KEK’s main WPs
SRF
Sources
Nanobeam
with Americas and Europe
ATF collaboration
H. Hayano support us mainly on capture cavity design
KEK members in charge
WP-8 : Y. Morikawa
WP-9 : Y. Enomoto
WP-10 : M. Fukuda
WP-11 : Y. Enomoto

## Slide 4: Main mission of positron source group
Goals of ILC positron group in KEK till 2027 is demonstrate our design
  Prepare
    engineering design report (EDR)
    3D CAD model
    Drawings for manufacturing
  Arrange test environment
  Construct prototype and test it
3D model and test bench of positron source for SuperKEKB
We are going to prepare similar ones for ILC

## Slide 5: five years development plan for positron source
FY |  | 2022 |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  | 
year |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 
Quarter |  | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1
Test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
High power test bench |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
W-Cu connection |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Target unit | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 3rd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC base | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
magnet | Solenoid + ST |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Chamber, vacuum, support |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Acc. Structure | Dummy |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 1st unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2nd unit |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FC power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RF power supply |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design
Manufacuring
test
5 years budget start from FY2023

## Slide 7: Comparison SKEKB and ILC
Make use of past experiences in the SuperKEKB
  Total system design, building up test bench, temperature measurement of FC
  Magnetic, thermal, tracking simulation using CST
Present parameter is not realistic from the viewpoint of ohmic loss and huge power requirement for the pulsed power supply
  20 times of the SuperKEKB (FC@100Hz)
  50 times of the SuperKEKB (PS@300Hz)
  Optimization of the parameter is necessary
Is Shorter pulse length possible?
  Need higher voltage
  Discharge risk
  Flat top control of PS
  PS, load, transmission line are not independent
Present model is very rough model
  Need realistic simulation
 | ILC | SKEKB | BINP design | BINP operation*
Primary Current |  | 12 kA |  | 
Secondary current | 25 kA | 12 kA | 120 kA | 0.73 x 120kA
Peak Bz | 5 T | 3.5 T (+1 T from DC magnet) | 10 T | 7.3 T
Pulse width | 25 us | 5 us | 26 us | 26 us
repetition | 300 Hz** 100 Hz | 50 Hz | 50 Hz | 12.5 Hz
Ohmic loss | (41 kW) 14 kW | 0.7～0.8 kW (measured) | 4 kW | 0.5 kW
Beam loss | 4 kW | Small | Small | Small
Total loss＠Load | (45 kW) 18 kW | 0.7～0.8 kW (measured) | 4 kW | 0.5 kW
Power for power supply | 630 kW 210 kW | 12 kW |  | 
Energy recovery power supply is necessary
Pulsed power supply for the FC in SuperKEKB W1800 x D1500
*Reference for BINP operation
・RuPAC2016 WEXMH01
・IPAC2016 THPOR018
・RuPAC2021 TUA02
**assume half sine

## Slide 8: Bunch structure
Create positron for 66 ms
Store them in the DR for 199.3 ms
Extract them to main linac for 0.7 ms
20 pulse / train
66 bunch / pulse
1320 bunch / train
Repetition 5 Hz
FC must keep field variation below the requirement to keep bunch-by-bunch charge variation
Minimum current pulse width is about 500 ns
Flat top control is necessary to satisfy short pulse length to reduce ohmic loss and flat field
ILC
M. Kuriki, OHO seminar 2021
…….
3.3 ms✕20 = 66 ms
66
train
pulse

## Slide 9: Pulse width dependence
Magnetic field shape is determined by skin depth
It is important to use realistic current waveform for simulation.
Half sine pulse width
Exp
500 us
100 us
12.5 us
6 us
0.5 us
Present design value of pulse width is 25 us for ILC
SuperKEKB

## Slide 10: Transient Magnetic field simulation for FC
~ 2014
Now
Simulation using realistic model and measured current shape was established
Excitation current
SuperKEKB

## Slide 11: From conceptual model to engineering model
☑Mechanical design
□Electric feedthrough
experiences in SuperKEKB
□Cooling water pass
completely new issue
Conceptual design and its simulation looks work
Before going to detailed simulation, prepare “realistic” model ←（now）
Once the model design finished, it will be imported to CST and ansys
Detail design will be modified taking into account simulation results
Iterate several times…
P. Martyshkin
ILC

## Slide 12: Simulation flow of positron source
FC mag. field(CST)
Solenoid mag. Field.(CST)
Acc. Structure (SuperFish, CST)
Tracking (CST)
Target ~ entrance of 1st ACC
Tracking (CST)
1st ACC entrance ~ exit
FC structure (ansys)
Target thermal(ansys)
Target structure(ansys)
Target particle generation (Gambet, Fluka)
FC mag. field(ansys maxwell)
Ohmic loss
Loretz force
Thermal exp.
Energy deposit
Magnetic field
Magnetic field
Particle dist.
Particle dist.
EM field
FC thermal(CST)
FC thermal (ansys)
Ohmic loss
Transient
Transient
Transient
Transient
Static
Transient
Static, transient
Transient
Single, PIC
Single particle
Frequency domain
Tracking (GPT)
1st ACC exit ~ chicane
Single, PIC
Particle dist.
Magnetic field

## Slide 13: Particle tracking from targe to the entrance of 1st acc structure

## Slide 14: FC temperature change by ohmic loss measurement (left) and simulation (right)

## Slide 15
Simulation method have already established through the experiences of SuperKEKB positron source development
Apply the same method for new FC design for ILC

## Slide 16: Energy recovery pulse driver for Q magnet
Turn on both IGBTs and current flow from both of capacitors.
Turn off IGBT 1 and control gate voltage of IGBT 2 to keep constant current
Turn off both IGBTs and stored energy is recovered to the capacitor (C_HV).
Operation principle of the circuit
Parameters are very different from those for FC power supply.
But the same circuit is considered as one of a possible solution.

## Slide 17: Energy consumption balance
Chart: 
| Pjoule-mag | Pjoule-cable | PL | Ptotal | Pmeasured
Q (50 Hz, 300 A) x 1 | 76 | 302.6 | 2250 | 2628.6 | 827
Stored energy in inductance
Loss in cable
Loss in coils
Total energy
Consumed energy (measured)
Recovered energy
Total energy recovery efficiency = 100 x (1 - Pmeasured / Ptotal ) = 68.5%
L energy recovery efficiency = 100 x (1- Pmeasured / PL ) = 80.1%
Measured consumed energy includes loss in puled driver circuit and DC power supplies to charge capacitors
  True energy recovery efficiency (ratio of recovered energy and stored energy in inductance is better than 80.1%
Power (W)

## Slide 18: Magnetic field measurement
Pick up coil is mounted on FRP rod.
XYZ stage with motor drive
Rotary stage with motor drive
XYZ positions are monitored by linear gauge by 10um precision

## Slide 19: Looking from downstream side with the measurement system attached

## Slide 20: Comparison between simulation and measurement
Chart: z (mm)
| 100 | 94.999999999999901 | 89.999999999999901 | 84.999999999999901 | 79.999999999999901 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 5 | 4.7999999999999901 | 4.5999999999999899 | 4.4000000000000004 | 4.2 | 4 | 3.7999999999999901 | 3.5999999999999899 | 3.3999999999999901 | 3.2 | 3 | 2.7999999999999901 | 2.5999999999999899 | 2.3999999999999901 | 2.19999999999999 | 2 | 1.7999999999999901 | 1.5999999999999901 | 1.3999999999999899 | 1.19999999999999 | 1
exp x2 | 0.15497 | 0.1959 | 0.21521 | 0.24804 | 0.26996 | 0.29178 | 0.31555 | 0.32743 | 0.35086 | 0.36473 | 0.38128 | 0.452 | 0.47391 | 0.49298 | 0.51528 | 0.55739 | 0.58844 | 0.58884 | 0.59933 | 0.60532 | 0.61396 | 0.6219 | 0.62485 | 0.63785 | 0.65382 | 0.67115 | 0.71149 | 0.75099 | 0.77719 | 0.81174 | 0.88055 | 0.93879 | 0.97571 | 0.97477 | 0.98448 | 0.99453 | 0.99017 | 0.99451 | 0.99777 | 1 | 0.99334 | 0.98329 | 0.97316 | 0.95992 | 0.93789 | 0.91412 | 0.88005 | 0.83813 | 0.81469 | 0.76529 | 0.67364 | 0.62621 | 0.53194 | 0.46263
Vertical axis is normalized at peak value to 100%
Target exit surface is z = 0
Distance between FC and target is 2 mm
Solid line shows simulation using CST

## Slide 21: Summary
Simulation method for designing FC is ready
Magnetic field measurement is ready
Requirement for ILC is very high
  Present parameter is not realistic
parameter optimization to reduce power is necessary
  Max. voltage of power supply, pulse width, load inductance and resistance, peak current, magnetic field profile and peak value are not independent
  Total design consideration including power supply is important
To reduce power for both FC and power supply,
  Need flat-top control
  Reduce pulse width
  Need Higher voltage
    Reduce load inductance
    Counter measure for discharge
  Need energy recovery power supply
Our plan
  FY2023 design and simulation
  FY2024 prototype manufacturing
  FY2025~ full power pulsed power supply (300 Hz compatible)

## Slide 22: Outlook and Collaboration
Many common point and method between FCC and ILC, SuperKEKB
  Not only FC but target, acc. Structure….
Similar development phase
  From conceptual design to engineering design
New group launched and new budget approved
Now it’s time to start new collaborative work!

## Slide 23: Back up

## Slide 24
In the case of 7T operation, ohmic loss is ½ of 10T operation
As is usual with accelerator operation, design and real parameters are different
BINP FCのdesign parameter
us

## Slide 26
2016～2021
12.5 Hz, 7.3 T
Compared with 50 Hz, 10 T
(12.5/50) x (7.3/10)2 ～ 1/8

## Slide 27: Circuit diagram of power supply for FC
T. Natsui
1 pulse energy stored in the capacitor = ½CV2 = ½ x 1.4 uF x 18.5 kV2 = 240 J
In the case of 50 Hz, average power = 240 J x 50 Hz = 12 kW
Power in the inductance of FC： ohmic loss = 11.2 kW : 0.8 kW = 93.3 : 6.6
Suppose the same ratio for the ILC case, 12 kW * (14 kW / 0.8 kW) = 210 kW
Including charging efficiency, control, cooling etc., roughly speaking, 5% of the total power is consumed in the FC, in the case of ILC, total power requride = 14 kW x 20 = 280 kW
Need the same amount of cooling water to dump whole neregy