## Slide 1
◦ Estimates extrapolated from BaBar for a detector with
BaBar-like acceptance
◦ Bunch crossing instantaneous rate: 476MHz
 At 1036 the average rate about half that (only half the RF buckets
are filled)
◦ Level-1 trigger rates (scaled from BaBar)
 At 1036: 50kHz Bhabhas, 25kHz beam backgrounds, 25kHz
“irreducible” (physics + backgrounds)
  75kHz with a Bhabha veto at L1 rejecting 50%
  100kHz without Bhabha veto
 50% headroom desirable (from BaBar experience)
◦  baseline: 150kHz rate capability
◦ HLT output rate
 Expect do be able to achieve 25nb logging cross section with a
safe real-time HLT
 Could be improved by maybe 5-10nb with a more aggressive
filter (storage & processing cost vs. risk)
◦  Have to log 25kHz of 75kByte events
Luitz 2010
Estimated trigger rates

## Slide 2
Technical choices for the TDR : trigger
Baseline:
  re-implement BaBar L1 trigger with some improvements
    Shorter latency (~6us instead of 12us)
    Higher sampling frequencies (DCH and EMC)
    2-d map for calorimeter
Possible additions
  SVT trigger
  What about the TOF ? (in DELPHI we used it in the trigger)
  Do we need to identify the bunch at the trigger
  level?
  Bhabha Veto
  Do we need an absolute time stamp at the trigger level?
Challenge
  To keep the event loss due to dead time below 1% => a maximum of ~70ns “per-event dead time” is allowed in trigger and FCTS
Other considerations
  What goes in L1, what in L3, what’s the optimum?
150kHz
Exponential Inter-arrival time pdf.
Luitz 2010

## Slide 3
 Drift Chamber Trigger (DCT)
◦ Track Segment Finder (TSF) performs lookup table driven hit
pattern recognition inoverlapping 8-wire supercells
◦ Binary Link Tracker (BLT) combines track segments in 5 to 10
superlayers to short / long tracks (B and A tracks)
◦ PT Discriminator (PTD) applies mininum transverse momentum
requirement using
◦ track segments (A’tracks)
 Calorimeter Trigger (EMT)
◦ Combines EMC crystals to towers in 40 phi bins
◦ Applies three different energy thresholds (M, G, E clusters)
 IFR (instrumented flux return) Trigger
◦ Encodes hit topologies of penetrating particles
 Global Level 1 Trigger (GLT)
◦ Combines, matches and counts inputs from the above objects to
Level 1 primitives

## Slide 4
BaBar IR
B1 at 21 cm from IP

## Slide 5
Zed coordinate Track ditribution before upgrade
Chai 2004

## Slide 6
Superb IR
15 cm far from IP

## Slide 7
DC Trigger flow
No
search
Search for patterns
Compute zed@beam axis
IP compatible? yes
No
Compute Pt
Pt > 200 MeV? yes
Deliver info to GLT
EMC Trigger flow
Search for clusters
Deliver info to GLT
GLT
Correlate info and assert trigger
Receive info from DC
Receive info from EMC
Receive info from DC
Receive info from EMC
Trigger FLOW
IFR

## Slide 8
The BaBar trigger/DAQ layout

## Slide 9
Babar DC trigger system: a detail
Chai 2004

## Slide 10
DC track finder algorithm
Faster sampling means better precision
(if the gas mixture is the same) do we need it?
Chai 2004

## Slide 11
Zed@IP track finder algorithm

## Slide 13
B into K D* from SuperB fast simulation
Real space
Conformal space
We have only linearized the problem in such a way that we could use
the very same algorithm we use for the zed coordinate in the DC.

## Slide 14
This transformation is necessary for pattern recognition. In the conformal
space we look for clusters rather than linear dependencies so we could
use the same algorithm we use for the EMC.

## Slide 15
Hough transformation
We would do the same thing to look for energy deposit in the calorimeter

## Slide 16
What we get in the B-> D* K sample
Zed resolution RMS=6.5 cm
R resolution RMS = 2.4 cm
Hypothesis: error on x coordinate = error on y coordinate : gaussian, sigma 0.8 mm
error on z coordinate : gaussian, sigma = 1.5 cm

## Slide 17
t sample
Red: fast reconstruction , green MC

## Slide 18
What we get in the t sample
Zed resolution RMS=1.4 cm
R resolution RMS = 1.2 cm

## Slide 19
DC trigger geometry

## Slide 20
Babar DC trigger
G. Felici

## Slide 23
A standard approach
If we immagine the trigger system as an independent sub-detector optically coupled
with the f.e. electronics, we can use the same trigger processor hw for EMC and DC,
In such a way that we could minimize the effort to develop it.
The debug process could benefit from such a decision.
This could be done by defining the same interface with the fe and a common
bus to exchange the information with the GLT. The firmware running on the
board can make the difference in between the 2 detectors.
Since from front end optical links are the standard we could use for instance
VME protocol to initialize local trigger boards and the GLT to debug and monitor.
In this case we have also «spare» links on the backplane which could be used
to get faster links in between GLTs and LTMs.

## Slide 24
TP0_FEMC
TP0_EMC0
TP0_EMC1
TP0_EMC2
TP0_DC0
TP0_DC0
Central
Trigger
Processor
CTP
A sketch of the trigger Crate
The central trigger processor gets the informations from the TP0 units
and create the trigger.
The edge of DC chamber has the same addr structure of the EMC.
VMEbus

## Slide 25: Spare slides

## Slide 26
Involved groups:
LNF (DC fe primitives and architecture definition)
Napoli (links and architecture definition)
Roma1 (EMC Fe primitives architecture defintion)
Roma3 (trigger architecture and algorithm development)

## Slide 27
B to D*K sample
Secondary tracks from b meson are more curling than the ones coming from t decays

## Slide 28
The GLT receives input signals from DCT, EMT and IFT
as 9 different trigger objects.
◦ DCT objects
 A track (a long track passing all 10 superlayers)
 B track (a short track reaching superlayer 5)
 A’track (an A track satisfying a mininum pt > 800 MeV)
◦ EMT objects (with different energy thresholds)
 M cluster (minimum ionizing cluster > 100 MeV)
 G cluster (intermediate energy cluster > 300 MeV)
 E cluster (high energy electron/gamma > 800 MeV)
 X cluster (MIP in the forward endcap > 100 MeV)
 Y cluster (electron in the backward barrel > 1 GeV)
◦ IFT objects (3-bit pattern)
 U (e.g. U=3 encoding two back-to-back sextants in either the
barrel or the endcap)

## Slide 29
The GLT delays and combines these objects into a total of 17 object counts:
◦ Back-to-back objects
 A*, B* (back-to-back short/long tracks)
 M*, G* (back-to-back M/G clusters)
 EM (E vs M clusters back-to-back)
◦ DCT + EMT match object
 AM (A track and M cluster phi match < 72 deg)
 BM (B track and M cluster phi match < 72 deg)
 A’M(A’trackandMclusterphimatch<36deg)
 BMX (M cluster object vetoed by X without BX phi match)
 Outputs
 GLT outputs 24 trigger lines to the Fast Control and Timing system (FCT)
 Each line is specified by one or more cuts in terms of the 17 object
counts
 A cut is defined by an operation code (>=, = , <) and a cut value (0-7),
e.g., ( nB >= 2 and nA >= 1 )

## Slide 30
Track segment finder block diagram
Chai 2004

## Slide 31
Fitting details

## Slide 32
The physics objectives of an experiment at a Super B Factory revolve around the search for New Physics. The specific approaches fall into several distinct categories
  Improvements in the classic unitarity triangle-related measurements to the “ultimate” precision
    UT angles
      measure asymmetries with minimum systematic error
        lepton tag has smallest systematics
      Measure branching ratios of rare modes for g
    UT sides
      use the recoil method to reduce backgrounds and theoretical uncertainties
      Maximum sensitivity for very rare decays – B, D, t, exotica
    Branching fractions
    ACP, AFB
    Kinematic distributions
Hitlin 2004