## Slide 2
Image credit: Fermi LAT/NASA
Gamma ray all-sky map

## Slide 3
In 1963 the «Vela» satellites, were realized to monitor the application of the Nuclear Test Ban Treaty…
…and recorded 73 gamma-ray bursts (GRBs)!
Image credit: NASA

## Slide 4: Overview
Silicon drift detectors (SDD) for x/gamma-ray science in astrophysics
  High energy resolution in the 0.1 - 20 keV range
  Excellent scaling with respect to the area
  Capable of room-temperature operation
  Suitable for imaging applications
Application Specific Integrated Circuits:
  Hybrid detectors: RIGEL for the ADAM project
  Linear detectors: VEGA for wide-field monitor applications
  SiSwich detectors: LYRA and ORION for the HERMES and THESEUS mission concepts

## Slide 5: Charge pulse processing schemes
Highly flexible and configurable
Best pile-up rejection algorithms
Early digitalization (the earlier, the better!)
High-frequency clock and digitally intensive
High power consumption per channel
Low-power consumption is possible
Lower risk of Mixed/Signal design issues
Scales well with the number of channels
Complex pile-up strategies are harder to implement
More sensitive to PVT (process/voltage/temperature) variations

## Slide 6: Hybrid detectors - The PixDD detector and the RIGEL ASIC
Part of the Advanced Detector for x-ray Astronomy Missions (ADAM) project.
Development of redout system to be placed at the focal plane of X-ray optics.
Science drivers:
  Study matter under extreme conditions, low flux compact cosmic sources.
Key features:
  Hybrid detector architecture (PixDD + Rigel ASIC)
  References: Y. Evangelista (2018), M. Gandola (2022)

## Slide 7: The Pixel Silicon Drift Detector
300 μm
300 μm

## Slide 8: RIGEL Architecture
300 μm
300 μm
Readout Pixel Cell (RPC)
Specification | Requirements
Energy range | 8400 el. (30 keV)
ENC (intrinsinc) | ≃10 e- rms
Shaping time | 0.5–5.0 μs
FWHM @5.9 keV | < 150 eV @ 0°C
Energy threshold | 0.5-3 keV
ADC resolution (Wilkinson) | 10 bit
Power consumption | < 1 mW/channel

## Slide 9: The hybrid RIGEL/PixDD detector
16x16 RPC
16 A/D Converters
Configuration
9510 µm
7365 µm
Trigger
Logic
I/O Interface
Technology:
AustriaMicroSystem CMOS 0.35 µm
RIGEL full 16x16 ASIC micrograph
Assembled RIGEL/PixDD detector
Sensor (PixDD)
47 µm
Readout chip (Rigel)
23 µm
PixDD cross-section
Bump-bonding connection

## Slide 10: Main RIGEL experimental results
Mean ENC @ 20°C:
  11.6 el. r.m.s. (RIGEL intrinsic)
  19.2 el. r.ms. (PixDD/RIGEL)
Channel gain dispersion: 13%
Low sensitivitiy to small TID levels
ASIC samples

## Slide 11: Main experimental results
Summed Spectrum
All pixels with FWHM (5.9 keV) < 300 eV
T = 0°C
FWHM=162± 0.2 eV
Mean ENC @ 20°C:
  11.6 el. r.m.s. (RIGEL stand-alone)
  19.2 el. r.ms. (PixDD/RIGEL)
Channel gain dispersion: 13%
Low sensitivity to small TID levels
Mean FWHM @ 0°C:
  162 eV on 55Fe 5.9 keV line
Power consumption 640 µW/channel
Low-leakage, high-resolution detector
Simple readout/postprocessing architecture
SDD operates with relatively low-voltages (<100 V)
Larger area require 4-sides buttable ASIC/SDD
ASIC cost rise 1-to-1 with detector area (independent from the n. of channels)

## Slide 12: Imaging with linear silicon drift detectors
  References: E. Gatti (1987)
  Wide Field Monitor (WFM)

## Slide 13: Readout of a linear SDD - the VEGA ASIC
  References: R. Campana (2014), M. Ahangarianabhari (2015)
  Must be capable of triggering also small charge fractions (for better charge cloud shape reconstruction)
  Synchronized readout between channels and adjacent chips

## Slide 14: Main VEGA experimental results
Intrinsic ENC @ 27°C: 13.0 el. r.m.s.
Opt. FWHM @ -30°C: 185 eV on 55Fe 5.9 keV line (hexagonal det.)
Power consumption 0.4 mW/channel
Reduced number of channels
Reduced constraints in terms of area occupation
Sensitivity to production defects in the detector is increased
Requires large drift voltages (1300V)
High channel occupancy for each event
… how can we increase the energy range?

## Slide 15: SiSwich detectors and distributed readout with LYRA and ORION ASICs
Science drivers:
  Detection and localization of Gamma-Ray Burst, triggering observation by other ground/spaceborne instruments (THESEUS/HERMES)
HERMES key features:
  Based on large constellation of nano-satellites
  Inexpansive, fast and modular approach
THESEUS key features:
  Medium class satellite, with several onboard instruments for GRB follow-up
  X-Gamma/Ray Spectrometer (XGIS) with large detection plane (50x50 cm2)
Common key features
  SiSwich detector (SDDs are illuminated from both sides)
  THESEUS References : L. Amati (2017), G. Stratta (2017)
  HERMES References: F. Fiore (2020), Y. Evangelista (2020)

## Slide 16: THESEUS and the X-Gamma Imaging Spectrometer - Overview
Coded Aperture Mask (60x60 cm2)
1-150 keV
energy range
Collimator Assembly
Field of View ≈ 77°
Detection Plane (50x50 cm2)
XGIS (80 kg per camera):
Wide Energy Range: 2 keV – 20 MeV
Imaging capability
Spectroscopy grade energy resolution
Matrix of 10x10 Detection Modules

## Slide 17: X-Gamma Imaging Spectrometer - Detection module
8x8 monolithic top-SDD matrix
8x8 monolithic
bot-SDD matrix
64x CsI(Tl) scintillators
Top Front-End (FE) PCB
Bottom FE-PCB
64x ORION-FE
X-Ray detection (2-20 keV)
Rigiflex connectors
Back-End (BE) PCB
8x ORION-BE
per module
Gamma-Ray detection (20 keV – 5 MeV)
128x per module
12 800x FE per camera
800x ORION-BE per camera
Scintillation light readout for energy and position reconstruction
~4.5 cm

## Slide 18: The ORION chipset - Pixel readout: double detection architecture (SiSwich)
SDD-Bottom pixel
Scintillator
SDD-Top pixel
X-Ray
ORION Front-End (Top)
ORION Front-End (Bot)
ORION Back-End
X-Event!

## Slide 19: The ORION chipset - Pixel readout: double detection architecture (SiSwich)
ORION Front-End (Top)
ORION Front-End (Bot)
ORION Back-End
Gamma-Ray
SDD-Bottom pixel
Scintillator
SDD-Top pixel
The energy and the position of interaction within the crystal can be inferred by comparing the top and bottom signals!
Gamma-Event!

## Slide 20: The HERMES cubesat
GAGG Scintillator
SDD pixel-1
X-ray
SDD pixel-2
γ-ray
10 cm
10 cm
We can reconstruct the gamma event when both SDD trigger, but can’t reconstruct the depth of interaction

## Slide 21: Distributed readout electronics: the ASIC “constellation”
990 µm
ORION-FE micrograph
FE-2
FE-1
490 µm
3 mm

## Slide 22: LYRA ASIC architecture
LYRA-FEs closely connected to the SDDs
LYRA-BE placed on the BE PCB

## Slide 23: LYRA Current mode transimssion

## Slide 24: The ORION ASIC architecture
ORION-FEs closely connected to the SDDs
ORION-BE placed on the BE PCB

## Slide 25: The ORION ASIC architecture
Current mode transmission minimizes the charge injection
High risk of charge injection toward anode bond-wires!

## Slide 26: The ORION ASIC - X ray processing
High gain output
1 us peaking time
X-Ray
No trigger on the Gamma processor

## Slide 27: The ORION ASIC - Gamma ray processing
Low Gain output
3 us shaping time (meet collection time of scintillation light)
Gamma-Ray
Trigger on the X-Processor is discarded

## Slide 28: Test PCB for analog characterization
Design and manufacturing by
25 mm2 per pixel ~80 pA/cm2 anode current
2x2 SDD (Backside)
SDD
ORION-FE (dual channel)
ORION-BE
(analog only)

## Slide 29: Experimental Equivalent Noise Charge vs. Temperature
24.3 el. rms
(212 eV FWHM on Si)
39.6 el. rms
(3.7 keV FWHM on CsI(Tl))

## Slide 30: XGIS Demonstration Model
XGIS module Frame + bottom SDD (8x8)
XGIS module «deploied»
XGIS module assembled!
Courtesy of OHB Italy s.p.a.
Top FE-PCB
Bot FE-PCB
Back End-PCB

## Slide 31: Acknowledgments
Technological Aims:
  Development of large area Silicon Drift Detectors
  Development of dedicated readout electronics
Target Applications:
  High-energy resolution & high-rate for soft X-ray detectors in advanced light sources
  Low-power & high-energy resolution detectors for X-/Gamma-ray astrophysics

## Slide 32: Other ASIC collaborations going on at SDIC-Lab
Fast, room temperature X-ray inspection systems for food safety, material recycling and control with CZT/CdTe detectors
2D high repetition-rate x-ray cameras for Linac Coherent Light Source (LCLS-II) at the Stanford Linear Accelerator Center (SLAC)
…and always open for more! Thank you!