## Slide 1: The EuAPS betatron photon beam: ultra-bright light pulses for imaging and spectroscopy
Francesco Stellato
University of Rome «Tor Vergata» & INFN
on behalf of the EuPRAXIA collaboration
High Precision X-ray Measurements 2023
June 22nd, 2023

## Slide 2: Summary
The EuAPS project
  EuPRAXIA & EuAPS
Plasma acceleration & Betatron emission @ EuPRAXIA
Betatron X-ray source figures
Photon science plan:
  Imaging
  Spectroscopy
  … and beyond
Outlook

## Slide 3: The EuPRAXIA project
Facility with very high field plasma accelerators, driven by lasers or beams
1 – 100 GV/m accelerating field
Shrink down the facility size
1
Producing particle and photon pulses to support several urgent and timely science cases
Enable frontier science in new regions and parameter regimes
2
https://www.eupraxia-facility.org/
Courtesy M. Ferrario

## Slide 4: The EuPRAXIA project
Courtesy M. Ferrario

## Slide 5: The EuPRAXIA project
Courtesy M. Ferrario

## Slide 6: The EuPRAXIA project
European Distributed Facility
5 excellence centers
2 construction sites
2
2
2
4
2
3
5
1
6
2
Beam-driven plasma user facility EuPRAXIA Headquarter
Laser-driven plasma user facility: candidates
Excellence Center
Horizon Europe
Beam-driven plasma user facility EuPRAXIA Headquarter
Technology Incubator (CZ - ELI)
User Data Center (H)
Theory & simulations (P)
Advanced Applications Beamlines (UK)
Laser-Plasma Acc. & 1 GeV FEL (F)
Plasma Acc. & High Rep. Rate Dev. (D)
Courtesy M. Ferrario

## Slide 7
In order to produce compact accelerators, new schemes are being developed
EuPRAXIA is the first ever design of a plasma accelerator facility
Assman et al. Eur. Phys. J. (2020)
The EuPRAXIA project

## Slide 8: The EuPRAXIA project
Electrons (0.1-5 GeV, 30 pC)
Positrons (0.5-10 MeV, 106)
Positrons (GeV source)
Lasers (100 J, 50 fs, 10-100 Hz)
X-band RF Linac (60 MV/m , up to 400 Hz)
Plasma Targets
Betatron X rays (1-10 keV, 1010)
FEL light (0.2-36  200 nm, 109-1013)
Courtesy M. Ferrario

## Slide 9: EuPRAXIA@SPARC_LAB
SITE 1: LNF-INFN
> 108 M€ invest funding
Beam-driven plasma accelerator
Europe`s most compact and most southern FEL
The world`s most compact RF accelerator (X band with CERN)
Courtesy A. Cianchi

## Slide 10: EuAPS – EuPRAXIA advanced photon sources
Scientific Quality: 50/50;
Impact: 47/50;
Implementation: 94/100
Courtesy A. Cianchi
Next Generation EU
Research Infrastructures

## Slide 11: Plasma acceleration @ EuPRAXIA
Particle accelerators produce photons by making electrons bunches move on curved trajectories.
In plasma acceleration, a driver pulse (laser or electron) creates a wakefield in a plasma
The plasma wakefield accelerates a witness electron bunch injected behind the driver pulse. The electrons wiggle in the plasma wakefield and get accelerated

## Slide 12: Betatron radiation @ EuPRAXIA  EuAPS
The accelerated electron can be used to run a Free Electron Laser  EuPRAXIA
Albert et al. PPCF 56 (2014)
At the same time, the electrons, as a «byproduct» of their movement on a curved trajectory, emit photons in the X-ray region.
This phenomenon is referred to as betatron emission.

## Slide 13: Betatron radiation @ EuPRAXIA  EuAPS
Betatron X-ray radiation with a certain degree of coherence is emitted with a synchrotron-like (wiggler) process within a narrow cone.
Paroli & Potenza Adv Phys X 2017
Curcio et al. Phys. Rev. Accel. Beams 2017; Curcio et al. NIM 2017
Betatron radiation has been measured and characterized at the FLAME laser facility of the INFN-LNF

## Slide 14: Betatron radiation @ EuPRAXIA  EuAPS
Betatron radiation covers the hard X-rays region and has a good spatial coherence. The brightness can be comparable with that of third-generation synchrotrons.
Curcio et al. NIM 2017
Paroli et al. NIM 2015
Preliminary simulations of the EuPRAXIA betatron spectrum (for maximized brilliance exploiting high plasma density)
Stellato et al. Cond. Matt. 2022

## Slide 15: Betatron radiation @ EuPRAXIA  EuAPS
Parameter | Value
Photon energy | 2-10 keV
Photons/pulse | 107 - 109
Pulse duration | 10-50 fs
Repetition rate | 1 Hz
Expected parameters of the EuAPS betatron radiation source
Photon science case

## Slide 16: Betatron radiation @ EuPRAXIA  EuAPS
What are betatron pulses good for?
Betatron radiation covers a broad energy range
Spectroscopic techniques
Betatron pulses are short (femtoseconds)
Pump-probe, time-resolved experiments
Betatron radiation is partially (spatially) coherent
Phase-contrast imaging

## Slide 17: Photon Science @ EuAPS in a nutshell
Ultra-fast, pump-probe
time-resolved X-ray Spectroscopy
Imaging
at a small-scale source
Tissues
Plants
Cultural Heritage
Physics of warm-dense matter
Femtochemistry of organometallic complexes

## Slide 18: Photon Science @ EuAPS
1- Static imaging ​
  2- Static X-ray absorption (and emission) spectroscopy​
    3- Time-resolved pump-probe absorption (and emission) spectroscopy
      4- Time resolved imaging (ultrafast dynamics)
        … and beyond (wide-angle X-ray scattering, diffraction, …)
Ultra-fast, (partially) coherent photon pulses

## Slide 19: Photon Science @ EuAPS- Timeline
Imaging of biological (and cultural heritage) samples
  Exploits the brilliance and coherence of betatron radiation,
  requires small divergence and good focusing
Static X-ray Spectroscopy
  Relatively easy, but does not exploit the radiation time structure
Ultra-fast X-ray spectroscopies exploiting ultra-short betatron pulses
  More complicated, requires timing between pump and probe pulses, but fully exploits the fs pulse duration
Time-resolved diffraction
  Depending on the samples, requires monochromatic beams with high flux

## Slide 20: Photon Science @ EuAPS - Timeline
The betatron X-ray source will be developed @ FLAME (200 TW, 35 fs) to optimize:
  Laser parameters
  Plasma source devices
  Electron diagnostics
  X-ray spectrum
  Photon flux
In early 2024  moved to the SPARC bunker, installation of a new compressor and refurbishing of the old one.
The advanced photon diagnostics and the user end station will be tested and installed during/after the commissioning of the source

## Slide 21: Where are we?
Betatron science has already allowed performing X-ray measurements
We are not aiming at reinventing the wheel, but we can build up and improve moving from the wheels that have already been invented.

## Slide 22: Biological imaging
Betatron sources can fill the gap between synchrotrons and X-ray tubes for imaging and Computer Tomography (CT)
Pulsed X-ray source (duration <30 fs)
>1010 photons/pulse
Small diameter <1 m
Critical energy of some keV
Low repetition rate: 0.05 Hz
 Total acquisition time: 2 h
Guo et al. Scientific Reports 2019

## Slide 23: Computer Tomography (CT)
Cole et al. PNAS 2018

## Slide 24: Phase-contrast imaging
Betatron sources have a spatial coherence that allows performing Phase Contrast Imaging (PCI).
In PCI, one measures the difference in wavefront, while in “traditional” imaging one measures the difference in the X-ray absorption coefficient between different “objects”
PCI provides better contrast than radiography, especially when dealing with biological samples.
PCI has been shown to work pretty well for thin samples exploiting a betatron source
Wenz et al. Nature communications 2015

## Slide 25: Imaging – Experimental setup
Variable sample-detector distance
Accurate sample positioning and rotation
Small pixel, 2D X-ray detector
CCD or CMOS
Courtesy A. Balerna

## Slide 26: Imaging – The pilot experiment
Green science
X-ray imaging of leaves (and wood)
aiming at the (tens of) microns resolution
Experiments performed with the broad radiation spectrum filtered by different materials to obtain difference maps emphasizing the presence of heavy metal contaminants  pollution control
Reale et al. - MIDIX Soft X-rays microradiography

## Slide 27: Imaging – Cultural Heritage
Imaging of ancient paper documents
with Dr. Giulia Festa, Centro Studi e Ricerche Enrico Fermi
Characterization of inks
(chemical sensitivity thanks to filters)

## Slide 28: Time-resolved imaging
Nanoparticles dynamics
                Shock-waves in materials
Liquid jet explosion
under X-ray beams

## Slide 29: Absorption Spectroscopy
X-ray Absorption Spectroscopy
Measures the X-ray absorption coefficient and acts as a local probe (5 Å) around metals
Metal ions
Proteins
Like synchrotron wigglers, betatron sources have a broad energy spectrum (1-10 keV)
Unlike synchrotrons, betatron emit very short pulses (10-50 fs)
They are therefore ideal sources to perform time-resolved spectroscopic experiments

## Slide 30: Absorption Spectroscopy
Interaction of biomolecules (at high concentration) with transition metal ions.
Time-resolved studies of metallic materials and warm-dense matter.

## Slide 31: Absorption Spectroscopy
Single-shot XANES spectrum at the Ti K-edge
Kettle et al. Phys. Rev. Lett. 2021
Cylindrical crystal
Mosaic crystal analyzer
Single-shot EXAFS spectrum at the Cu K-edge
Kettle et al. arxiv 2023

## Slide 32: Absorption Spectroscopy – Experimental setup
X-ray Absorption Spectroscopy
in dispersive mode
Curved or mosaic crystal analyzers
+
Position sensitive detector
+
High-power femtosecond laser for pump-probe measurements
No monochromator to maximize the photon flux on the sample

## Slide 33: Ultra-fast Spectroscopies
Optical laser pump / betatron probe experiments can follow the non-equilibrium dynamics of the copper heating process via XAS on fs timescale
Mahieu et al. Nature Comm 2015
Measurements of Ionization States in Warm Dense Aluminum with Betatron Radiation
Mo et al. 2017

## Slide 34: Emission Spectroscopy
Courtesy A. Balerna
Design and performance of a compact x-ray emission spectrometer having a dispersive refocusing Rowland (DRR) circle geometry  high energy resolution even for UNFOCUSED x-ray sources

## Slide 35: Outlook
Imaging
  A source itself, but contributing to technology development of betatron sources to obtain synchrotron-level images at small-scale facilities
X-ray spectroscopy
Ultra-fast experiments exploiting ultra-short betatron pulses
Synergy with the EuPRAXIA@SPARC_LAB Free Electron Laser beamlines
(same location, same pulse-length, although different wavelength and brilliance)
EuPRAXIA’s goal: novel technologies for (science at) compact accelerators

## Slide 36: Acknowledgements
@
You all for the kind attention
People
Balerna
L. Brombal
F. Brun
A. Cianchi
A. Curcio
M. Coreno
S. Donato
Z. Ebrahimpour
F. Galdenzi
M. Galletti
M. Ferrario
A. Marcelli
V. Minicozzi
S. Morante
R. Pompili
V. Shpakov
F. Villa