## Slide 1
A Computer Vision-based system for virtual dosimetry of workers in Nuclear Medicine Therapy
Giorgia Stendardo,
ISS grant-holder
ML@INFN | SAPIENZA UNIVERSITA’ DI ROMA| 6 MARZO 2023

## Slide 2
CONTEXT
Incidents and “near misses” in NMT may lead to unintended exposure of workers.
spill from a syringe
vomiting patient
fall of a radioiodine pill
PROBLEM
Personal passive dosimeters
only time-integrated dose!
Active dosimeters
uncomfortable and might be forgotten!

## Slide 3
SOLUTION
Real-time tracking
of the body pose of workers with Computer Vision algorithms.
Virtual dosimetry
by integrating tracking and
ambient dosimeters data within
computed radiation field maps.

## Slide 4
HOW DOES IT WORK?
Video capture from
2 RGB cameras
Detection of the human pose in each frame (2D)
Reconstruction of the 3D coordinates of the pose in the real world

## Slide 5
HOW DOES IT WORK?
High-resolution webcam (1080p)
At least 2 cameras for stereo vision!
Video capture from
2 RGB cameras
Detection of the human pose in each frame (2D)
Reconstruction of the 3D coordinates of the pose in the real world
NMT testing room (350x350)

## Slide 6
HOW DOES IT WORK?
Video capture from
2 RGB cameras
Detection of the human pose in each frame (2D)
Reconstruction of the 3D coordinates of the pose in the real world
Camera Calibration &
Stereo Calibration
Relative orientation
World coordinates
Camera coordinates

## Slide 7
Video capture from
2 RGB cameras
Detection of the human pose in each frame (2D)
HOW DOES IT WORK?
Reconstruction of the 3D coordinates of the pose in the real world
0 nose
1 left eye
2 right eye
3 left ear
4 right ear
5 left shoulder
6 right shoulder
7 left elbow
8 right elbow
9 left wrist
10 right wrist
11 left hip
12 right hip
13 left knee
14 right knee
15 left ankle
16 right ankle
Human Pose Estimation Algorithm
Google’s pre-trained convolutional neural network model: MoveNet.MultiPose.
Up to 6 people per frame and 17 keypoints per person detected.
Confidence score for each keypoint location (>70% for shoulders and eyes).

## Slide 8
Video capture from
2 RGB cameras
Detection of the human pose in each frame (2D)
HOW DOES IT WORK?
Reconstruction of the 3D coordinates of the pose in the real world
Mean position error 5%
Triangulation
using calibration parameters and left camera as world origin

## Slide 9
CHALLENGES
Camera position
Occlusions &
Background objects
Multiple people
MoveNet is optimized for:
distances between 2-4 mt from camera.
camera positioned at eye-level and parallel to the floor.
White coats: 10% error and confidence scores < 20% for wrists and knees.
Furniture (e.g. infusion pole) may be confused with a person.
Accuracy of MoveNet in scenes with more than 1 person is under evaluation.
Use of multiple cameras
Fine tuning the model with a training dataset of medical staff images

## Slide 10
TAKE HOME MESSAGE
Tracking operators helps to better reconstruct abnormal events dynamics, by filling the gaps in incident reports of eyewitnesses.
Tracking the pose will enable a non-physical dosimetry, by means of ambient radiation detectors and Monte Carlo simulations of routine and incident scenarios.

## Slide 11
Thank you!
giorgia.stendardo@iss.it
This system is being developed within the “SIREN” project funded by INAIL (grant BRIC 2019) and is under testing at IFO and Policlinico di Milano.