## Slide 1: Status of PRIN 2017: Imaging in Liquid Argon
Bologna
01 Marzo 2023

## Slide 2: Research Units

## Slide 3: Milestones

## Slide 4: Work Packages (1)

## Slide 5: Work Packages (2)

## Slide 6: Agenda

## Slide 7: Connection with Near Detector of DUNE

## Slide 8: GRAIN cryostat

## Slide 9: Light Sensor
Matrices of Silicon PhotoMultipliers
  From Hamamatsu different models and sizes
  Choose to work now with 16x16 matrices of 1x1 mm2 or 3x3 mm2 SiPM
  256 is the maximum channel count we can afford with presently available electronics (ASIC)
~ 5 cm
~ 2 cm
TSV = Through Silicon Vias
HWB = Hole Wire Bond
2800 Euro

## Slide 10: Lenses
Need to focus on 6x6 cm2 sensitive area
2x2 mm2 SiPM size
Light is focused: ~5 photons per SiPM
32x32 matrix SiPM TSV
~ 7 cm

## Slide 11: Coded Aperture Masks
Light is distributed over the full sensor area
3x3 mm2 SiPM size
Light is focused: ~2-3 photons per SiPM
32x32 matrix SiPM HWB
~ 10 cm

## Slide 12: Example of reconstruction: cosmic muon

## Slide 13: Charged current event

## Slide 14: Event reconstruction with lenses

## Slide 15: Simulation suite

## Slide 16: Demonstrator
Matrix of SiPMs mounted on a mezzanine board
Motherboard contains 8 ASIC (256 ch in total)
DAQ with FPGA on demo board

## Slide 17: Test with ARTIC (1)
1.3 m
Lens cameras
Movable system
of the light source
along a rail
Build a first simple working set up
  (readout, reflections, cryogenics)
Tune simulation parameters
Check current simulation results
Evaluate:
  the Point Spread Function by point source light
  the reconstruction capability by using two faced detectors

## Slide 18: Test with ARTIC (2)
1.3 m
Lens cameras
Movable system
of the light source
along a rail
Test with cosmics
with more detectors (3 or more?)
…many things to be done…
-- NOT BEFORE SUMMER 2023 --

## Slide 19: Requirements for GRAIN
  Cryogenic SiPM readout
  Time and Amplitude information
  Sensors from 1x1 up to 4x4 mm2
    50 to 900 pF/channel
  Power budget < ~1000 W for 50-70k channels
    Includes all components and heat load from cables
  As few data/control lines as possible (1024 ch /ASIC ??)
    To minimize thermal bridges
    Less cables

## Slide 20: Requirements for GRAIN
  < 1ns time resolution
  Coarse peak amplitude measurement
    Time-over-Threshold or “fast” integrator
    Typical signal range 1 to ~10 p.e., up to several 1000s
  Multi-hit capable with no deadtime during spill
    Expect a few (1-10) hits/channel/spill (9.6 us)
    Very long interspill O(700 ms) with minimal activity
  [optional] per channel bias trimming

## Slide 21: Roadmap for new ASIC development
INFN-Torino interested to develop an upgraded ALCOR
1024 channel / ASIC seems feasible -> huge simplification on feedthrough and mechanics
Need to write a document with requirements:
  Simulation of time distribution of photons for a full spill on a sensor area (same edepsim file but using lens or masks optics) –(Lea, Alessandra,Valerio, Valentina)
  Simulation of present Alcor architecture by using time distribution of photons (INFN-To)
  Evaluation of simulated performance and definition of optimal architecture (Alessio, Lea, Alessandro, Nicolo’, Manuel)
  Definition of maximum power for cryogenic operation (Ruggero, Claudio, Lea, Alessandro)
  Definition of maximum power for camera assuming power gating on Analog FE and Digital sector (Nicolo, Manuel….)

## Slide 22: Roadmap for new ASIC development
  Estimation data Throughput from each camera (vedi simulation)
  Definition of data output lines (one LVDS?) (Nicolo’, Manuel, Alessio, Lea, Alessandro..)
  Definition of input lines (ASIC configuration SPI, clock, power, test…..) (Nicolo’, Manuel, Alessio, Lea, Alessandro..)
  Definition of clock requirements and implementation and integration with SAND (Michele, Nicolo’, Alessio,….)
  Design of feedthrough and flanges (Alessandro, Nicolo’)
  Study DAQ for GRAIN (FPGA) and integration with SAND (Michele, Nico, Sergio Di Domizio, Alessio,…)
  Design of Slow Control system (Michele, Nico, Sergio Di Domizio, Alessio,…)

## Slide 23: TEST in LAr

## Slide 24: Men At Work

## Slide 25: ALCOR tests
Focused only on analog front end (so far)
  Many iterations of power and reference V values
  Now: AVDD = DVDD = ~1.35 V
  Vref: 650 mV (tested 600 to 750 range)
  Playing with preamp CG, boost currents, most optimal value is always lowest possible (0, 0)
  Second highest gain (1) looks best at cryo T
Nicolò Tosi, Ignazio Lax, A. Badiali, F. Chiapponi, Manuel Roca Rolo, Fabio Cossio

## Slide 26: Waveforms at Room Temperature

## Slide 27: Amplitude histograms

## Slide 28: ToT histograms

## Slide 29: ToT histograms

## Slide 30: ToT histograms

## Slide 31: Waveform at 77k
GAIN = 1, one active channel

## Slide 32
GAIN = 0, one active channel

## Slide 33: Further observations
Performance with 1x1 sensors is best
  Unfortunately we will most likely use 3x3
Single channel waveform looks worse when more than one channel is enabled at a time
  Regardless of presence/absence of SiPM
Zero reliability issues observed so far at cryo T
  Out of ~20 cold cycles performed
Test of DAQ part still in progress