## Slide 1: SiPM Based UV Cameras
Report on WP2 and WP3
Nicolò Tosi – INFN Bologna – 01/03/2023

## Slide 2: Work Packages related to this activity
  WP2 UV Camera
    2.1 Search for commercial SiPM devices for warm-cold demonstrator
    2.2 Design and build SIPM and Front-End electronics Printed Circuit Board(s)
    2.3 Design and build PCB for a FPGA-based board for the control of Front-End electronics
    2.4 Development of the DAQ chain from Front End electronics up to storage disk
  WP3 Warm Demonstrator
    3.1 Design of the WD
    3.2 Construction of the WD
    3.3 Interface between WD and UV camera
    3.4 Development of a simulation software of the WD
    3.5 Development of reconstruction software of the WD

## Slide 3: Activities that were carried out
What this talk covers
  A 64 ch SiPM camera prototype (warm TRIROC)
  A 256 ch SiPM camera demonstrator (cryo ALCOR)
What it does not cover
  Warm measurements in GE using a non-SiPM camera in water
  Jointly developed simulation and reconstruction

## Slide 4: Warm electronics "camera"
TRIROC, 64ch warm readout ASIC (EASYROC family)
Hamamatsu 64 ch 1x1 mm
Mosaic Coded aperture, rank 7
Kapton flex interconnect

## Slide 5: Warm camera
Several Limitations:
The commercial TRIROC board never worked well
The number of pixels was too small for real imaging
The analog signal flex connection was very effective, but not really scalable
Small but significant success:
We reconstructed individual point sources (LED) with deconvolution
Not quite successful with 2 LEDs

## Slide 6: Valuable insights from the Warm Demo
  We cannot realistically extract analog signals for >> 1k channels
    => We decided to risk switching to the yet unproven ALCOR
  The DCR from a SiPM at room temperature is a problem
    => It would not be useful to continue to develop for warm tests
  We needed a lot more than 64 pixels
    => Demonstrator unfortunately limited to 256

## Slide 7: Cold demo requirements and design
  Cryo-compatible SiPM ASIC
    ALCOR, developed by INFN-TO
    32 channel SiPM front end
  Support both 1x1 and 3x3 mm sensors
  Have enough pixels for imaging

## Slide 8: ASIC Board

## Slide 9: Current Status
  All the circuit boards are built and OK
    All the SiPM boards (4 1x1 and 4 3x3) are assembled
    Two SiPM boards of each time have been coated with PTB
    One ASIC board has one ASIC wirebonded
    A second one will soon have all ASICs wirebonded
  The analog part of the ASIC has been tested extensively
  FPGA Firmware can configure the ASICs and dump raw data
    Very Basic DAQ software exists to read raw data
    Real DAQ Software with GUI, automatic scans, etc... is being written

## Slide 10: An example waveform with scope ToT

## Slide 11: What still needs to be done: software
  Complete the DAQ software and documentation
    Basic features, configuration file parsing, raw data readout, ... ~75% done
      May still need to modify the firmware somewhat
    Automatic parameter scan (with fitting, etc...) < 50% done
    Data analysis features (ToT to amplitude, ...) 0% done
    GUI ~50% done:

## Slide 12: What still needs to be done: hardware
  Characterize SiPM matrices at cryo T (IV curve)
    All tools are available in principle, but the setup needs to be built and used.
    Opportunity to measure some properties of PTB coating
    Only test that does not require DAQ
  Calibrate ToT with pulsed source
  Investigate ToT with "weird" signals
    Study optimal thresholds for this type
    of event

## Slide 13: Future work plan
  March:
    IV curves
    Get software to at least usable state
  April:
    ToT calibration and studies
    Multiple board integration and synchronization
  May: contingency