## Slide 1
Ionizing Radiation from Laser Target Interactions:
High Irradiance for SLAC MEC-U Project and
Low Irradiance for Laser Material Processing
J. Bauer, P. Connolly, J. Liu, S. Rokni, A. Rosenstrom, H. Tran, P. Tsai, M. Woods
SLAC National Accelerator Center, Menlo Park, CA USA
SATIF-16, May 28–May 31, 2024
1Also at Georgia Institute of Technology

## Slide 2: Outline
Introduction
Characterization of Source Term
High Irradiance: SLAC MEC-U
  Radiation Source Terms
  Prompt and Residual Radiation Hazards
Low Irradiance: Laser Material Processing Applications
Conclusion

## Slide 3: High-Intensity Laser-Matter Experiments
Study of matter in extreme conditions
Laser inertial confinement fusion
High pressure and shock physics
Generation of betatron X-ray beam
Source of proton, and ion beams
Study of astrophysical processes
Basic Plasma Science
Extreme Conditions
Basic Plasma Science
Notes: The rapid development of ultra-short, intense lasers technology led to the emergence of numerous cutting-edge disciplines and important breakthrough including:
Predict material behavior relevant to fusion and extreme technological environments

## Slide 4: MEC Instrument: Ti:sapphire short-pulse laser with wavelength of 800 nm
  4 TW 150 mJ in 40 fs
  25 TW 1 J in 40 fs
  100 TW 4 J in 40 fs
1 J, 40 fs, 10 Hz, 25 TW
Notes: Originally designed for 1.6 mm Pb walls originally designed for keV X-rays from LCLS and low intensity (1016 W/cm2) laser experiments.
CD1 is conceptual design or proposal submitted to Department of Energy
Focusing to few μm spot size yields laser intensities up to 1020 W/cm2 (current) and more.
Originally designed for 1.6 mm Pb walls originally designed for keV X-rays from LCLS and low intensity (1016 W/cm2) laser experiments.
CD1 is conceptual design or proposal submitted to Department of Energy
Focusing to few μm spot size 𝑟 yields laser intensities up to 1020 W/cm2 (current) and more. 𝐼=2𝑃/(𝜋𝑟^2 )

## Slide 5: Ionizing Radiation from Laser-Target Interactions
Laser-solid interactions create plasma layer on the surface of the target
Further laser interactions with the plasma accelerates electrons in the plasma up to MeV energies, which can then be ejected from the plasma
These “hot” electrons interact with the target material and target chamber and generate bremsstrahlung photons
Mixed field of electrons and photons (and neutrons)
Different acceleration mechanisms depending on laser wavelength, intensity, targets
H. Daido et al.,
Rep. Prog. Phys. 75 (2012) 056401
Notes:   metals (mainly acceleration of electrons)
  carbohydrates (protons/ions)
  liquid/frozen targets (protons, target easily replenished)

## Slide 6: Characterization of Hot Electron Source Term
Particle-in-cell (PIC) method code EPOCH:
    Study high energy density physics and laser-plasma interactions
    Suitable for fs time-scale and micron size-scale simulations
    Hot electron source function of laser-optics parameters:
      Energy distribution, Angular distribution, Laser conversion efficiency
T. D. Arber et al., “Contemporary particle-in-cell approach to laser-plasma modelling”, Plasma Phys. Control. Fusion 57, 113001 (2015).
Notes: Thank Rohini Mishra for her help in learning how to use PIC codes.
Between the two solvers the full collision-less behavior of a kinetic plasma can be simulated. The core algorithm is standard for PIC codes.
EPOCH code will give the same results as all codes based on this algorithm set and is chosen here simply as it was freely available, frequently updated to expand processing output data, and supported an online questions/answer forum.

## Slide 7: Hot Electron Source Term:
7
Cold e-
Hot e-
Spectrum best fitted with Maxwellian distribution:
Th scales with laser intensity I between 1017 to 1022 W/cm2:
T. Liang, et al., RPD (2017), Vol. 175, No. 3, pp. 304–312
Notes: EPOCH code will give the same results as all codes based on this algorithm set and is chosen here simply as it was freely available, frequently updated to expand processing output data, and supported an online questions/answer forum.
Particle-in-cell (PIC) method code EPOCH:
    Study high energy density physics and laser-plasma interactions
    Suitable for fs time-scale and micron size-scale simulations
    Hot electron source function of laser-optics parameters:
      Energy distribution, Angular distribution, Laser conversion efficiency
      Lambda= 0.8 um
      2D EPOCH
Anna Ferrari uses Maxwellian with ponderomotive scaling given by Kluge et al. (2011) with hot electron temperature Th consistent with Wilks’ papers.
Wilks1997 “found that the distribution of electrons is roughly a Maxwellian ‘tail’ of hot electrons, superimposed on the initial background temperature.

## Slide 8: Hot Electron Source Term: Summary between 1017 to 1022 W/cm2
Energy distribution:
  Maxwellian characterized by temperature Th
  Th scales with laser intensity
Angular distribution:
  Gaussian characterized by σ ~ 45o
  Ratio of forward-to-backward hot electron energy flux scales with intensity and becomes more forward-peaked
Laser absorption:
  Conversion efficiency scales with laser intensity up to 60%
simulate interaction  obtain hot electron spectrum
Spectrum  source term for FLUKA  confirmed w/radiation measurements
T. Liang, et al., Health Phys. 2018 Dec;115(6):687-697

## Slide 9: Comparison of Bremsstrahlung Dose Yield, H*(10) in mSv/J at 1 m
0 deg, simple Cu target, no target chamber
comparison to measurement data
Uncertainties removed to reduce visual clutter
Agreement between measured data and calculated dose yield curves (EPOCH + FLUKA)
T. Liang, et al.,
RPD (2017), Vol. 175, No. 3, pp. 304–312
T. Liang, et al.,
Health Phys. 2018 Dec;115(6):687-697
Notes: What is shown is 0o dose yield models with 2.54 cm Al shielding (target chamber).
Measurements at Titan were taken parasitically to another experiment, so data is subject to error.
At 1020 W/cm2, dose yield is about 10-2 mSv/J (1 mrem/J). For a 1 J laser, with 2000 shots in 1 h…2000 mrem (2 rem) in 1 h at 1 meter
Not uncommon for 10k shots per experiment…10 rem per experiment at 1 meter
Instantaneous dose rate can also be VERY high due to multiple shots in 1 second (5, 10 Hz operation)

## Slide 10: MEC-U and LCLS
Underground cavern downstream LCLS Hutch 6
High-Rep-Rated Short Pulse (RR-SP): 1054 nm, 150 J, 150 fs, 1 PW, 10 Hz with 1um focusing: 3 x 1021 W/cm2
High-Energy Long Pulse (HE-LP): 1 kJ, 20 ns, 2 shots/hour
High-Rep-Rated Long Pulse: 200 J, 20 ns, 10 Hz

## Slide 11: MEC-U Layout in 80-m-long Underground Cavern
11
  FEL beam
  existing FEL hutches
  laser-only hutch
  laser + FEL hutch
  laser hall: Petawatt laser
  laser hall: kJ laser
  access tunnel
  shield wall with maze
  equipment / personnel access tunnel
  support building
Notes: HE-LP ~ 10E16 w/cm2;
Scale = Cavern

## Slide 12: MEC-U Source Term for Protons
Spectrum based on PIC Simulation for LMJ-PETAL at CEA/Cesta
Similar laser parameters: 150 J, 1 PW, 2x1021 W/cm2
Input to FLUKA
  5% conversion of laser energy to accelerated protons for liquid targets
  Energy spectrum up to 115 MeV (average 23 MeV)
  Forward-backward yield ratio 1:1 (confirmed with SLAC PIC simulation)
  ± 20° opening angle
B. Martinez Matter Radiat. Extremes 7, 024401 (2022)
Proton Spectrum from B. Martinez Matter Radiat. Extremes (2022)
Implementation in FLUKA
P. Connolly, et al., MEC-U Radiation Source Term Definitions, SLAC RADIATION PHYSICS NOTE-22-09, 10/25/2022
Notes: Solid target is assumed to have same yield as liquid targets

## Slide 13: Laser Shot Operations
Laser Shot Estimates for Prompt Radiation |  | 
Target | Number of Shots | 
 | 1 year | 1 hour
Solid (high Z) | 4,000,000 | 24,000
Liquid (low Z) | 50,000,000 | 36,000
  Average Power over 6000 h/y
Target | Prompt Radiation Analysis | 
 | Electron (W) | Proton (W)
Solid (Copper) | 16.7 | 1.4
Liquid (H/He/Ar) | 20.8 | 17.4
Total | 37.5 | 18.8
  Proton source terms assume liquid hydrogen and solid targets with hydrogenous surface contamination.
  Shielding design limits: Protons dominate the prompt and induced radiation hazards
Notes: 4Mx 0.6 solids x 150j
50Mx 0.06x150J f
17.4 = 50Mx 150 jx 0.05/6000/3600 or liquid

## Slide 14: Bulk Shield Walls
Shielding criterion:
6 mSv for all shots in 1 year (6000 h)
Proton source term dominates shielding design due to high energy neutron production
 1.6 m heavy concrete (4.0 g/cm3)
Dose inside TAX dominated by electron source term, outside by proton source term
(6000h)
Large Laser Pipe (1.2 m OD) serves as an exclusion boundary.
Dose rate 30 cm from the shield wall at beam height
A. Rosenstrom, et al.,
MEC-U Shield Wall Study,
SLAC RADIATION PHYSICS NOTE-22-11-R1,
3/8/2023

## Slide 15: Residual Dose Rates around the Target Chamber
Use 10% of the annual shots for prompt radiation analysis
only activation from steel platform
3D view inside the target chamber
@ 1 hour cool down
Optical Laser
FEL
Ion source term dominates the generation of residual radiation due to reactions.
Na-22 () dominates long-term in the aluminum target chamber
mrem/h
Estimated Total Dose from Chamber Entry to Target Chamber During Downtime [uSv] |  |  |  | 
Time Inside the Target Chamber [h] | Cooldown Times [h] |  |  | 
 | 1 | 8 | 24 | 48
1 | 140 | 50 | 35 | 30
4 | 420 | 180 | 135 | 120
Initial dose estimates have been produced for the anticipated operation model
P. Conolly, et al.,
MEC-U Movable Component Residual Radiation Studies,
SLAC RADIATION PHYSICS NOTE-23-13,
4/2/2024
Notes: How long is each experiment ?
What is the delay time?
User< staff, tech? time?
How Many experiments per year?

## Slide 16: Radiation Hazard for Laser Material Processing Applications Using a Short-Pulse Laser (Low Irradiance)
5

## Slide 17: Laser Material Processing Using a Short-Pulse Laser (Low Irradiances)
Precise material machining using an ultrashort pulsed (1013 W/cm20) laser with high repetition rate has many industrial and commercial applications.
A laser-induced plasma with a “hot” electron temperature of up to a few keV forms at the target surface and emits Bremsstrahlung x-rays.
Ionizing radiation hazard from these low-energy x-rays could be significant, due to high laser rep rates (tens of kHz; equivalent to tens of watt laser beam)
Legall et al., J. Laser Appl. 32, 022004 (2020 )
Legall et al., Appl. Phys. A 124, 407 (2018)
Notes: Electron temperature Te scales with peak intensity as I1/3 (Ref. Legall et al, Feb 2020)
The spectra of x-rays from a laser-induced plasma can be described by a Maxwellian distribution with the dependence on the hot electron temperature Te of the plasma:
Two examples of Bremsstrahlung x-ray spectra plotted using the above equation with Te of 0.9 keV and 3.1 keV, which correspond to laser intensities at and W/cm2.
The higher the laser intensity, the higher the electron temperature, and hence the harder the photon spectrum is.
Electron temperature Te scales with peak intensity as I1/3 (Ref. Legall et al, Feb 2020)
The spectra of x-rays from a laser-induced plasma can be described by a Maxwellian distribution with the dependence on the hot electron temperature Te of the plasma:
𝑓(𝐸) ~ (𝐸〖𝑇_𝑒〗^(−3) )^0.5 𝑒^((−𝐸/𝑇_𝑒 ) )
Two examples of Bremsstrahlung x-ray spectra plotted using the above equation with Te of 0.9 keV and 3.1 keV, which correspond to laser intensities at 6.6×10^13 and 2.8×10^15 W/cm2.
The higher the laser intensity, the higher the electron temperature, and hence the harder the photon spectrum is.

## Slide 18: SLAC and Coherent Inc. Radiation Experiments
SLAC collaboration with the Coherent Inc., a laser machine manufacturer.
Radiation dose measurements for laser intensities (7x1013 – 2.8 x 1015 ) W/cm2 on thin tungsten foil targets
Laser Parameters
  1035 nm
  350 fs FWHM
  Max. 2.1 mJ
  10 - 25 kHz
  ~10 um spot
Instruments:
    Ion chamber survey meters (Victoreen 451B with open-window for H’(0.07) and closed-window for H*(10)
    Personnel dosimeters (Landauer InLight 4-element dosimeters for shallow doses and deep doses)
Notes: ICRU
H’(0.07) Directional for instruments corresponding to shallow
H*(10) Ambient to deep dose

## Slide 19: Victoreen 451B Survey Meter Dose Rate Results
Corrections for survey meter signals to H’(0.07) and H*(10) :
  Energy-dependent response from PNNL calibration to low-energy ISO x-rays (down to 14 keV for M-20)
    At 5 keV, the H*(10) has large uncertainty (may be overestimated by x10)
  Distance from the target to the instrument
  Air attenuation
  Detector volume effect
Maximum H’(0.07) at 28 cm:
~10 mSv/h/W (0.15 Sv/h at 15 W)
H*(10) is order of magnitudes lower
Notes: M-20
X-ray beam filters
Moderated filter, 20 kV
Ambient dose equivalent

## Slide 20: Dosimeter Dose Results (with SLAC-developed dose algorithm)
Intensity (x1014 W/cm2) |  | Shallow Dose (mSv/h/W) | H’(0.07) from Fluke 451B survey meter with open window (mSv/h/W) |  | 
 | Exposure Time (s), Laser Power (W) | 12 cm, 45o | 12 cm front face, 45o | 28 cm front face scaled to 12 cm, 45o | 28 cm front face, 45o
1.3 | 180, 0.72 | Undetermined* | 11.6 | 11.3 | 0.7
5.2 | 135, 7.2 | Undetermined* | 30.7 | 26.6 | 1.9
13 | 180, 7.2 | 49.0 | 87.5 | 104.8 | 9.1
28 | 225, 15 | 61.8 | 76.5 | 87.9 | 10.0
*Due to low energy of the x-ray (< 4 keV)
Notes: Inlight dosimeter

## Slide 21: Conclusion
Generation of ionizing radiation in ultra-intense laser-matter interactions is widely recognized.
Increasingly rapid pace of development of high irradiance lasers is making facilities using high-intensity lasers into large sources of radiation, requiring effective shielding, comparable to medium size accelerator facilities.
Coupling of results from particle-in-cell (PIC) simulations to model the source terms, with particle transport codes provides a powerful tool to design the required shielding, and plan for evaluating and planning for radiation protection aspects of such facilities.
X-ray radiation hazards are also present when ultrashort pulsed lasers with high repetition rate are used in industrial and commercial material processing.
Benchmarking of results from the simulations with measured data is essential to provide effective solutions
Notes: The rapid development of ultra-short, intense lasers technology led to the emergence of numerous cutting-edge

## Slide 22: Thank You

## Slide 23: Aluminum Alloy
5000- and 6000-series comparable activation
7000-series about x2 higher (no plans to use 7000-series)
no significant difference after ~1 day cool-down
up to 0.15% cobalt  no significant change
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023
Dominant proton source term only

## Slide 24: Hot Electron Source Term: Laser conversion efficiency scales with laser intensity
Conversion of laser’s pulse energy to hot electron energy scales with laser intensity up to 60%
Notes: J. Fuchs et al., Nat. Phys. 2, 48-54 (2006) uses the scaling factor from textbook by McKenna.
Laser-Plasma Interactions and Applications by P. McKenna, D. Neely, and Robert Bingham (2013) .
  At >1021 W/cm2, η can reach up to 60%

## Slide 25: HVAC etc. Penetrations through Shield Wall
Large HVAC penetrations to TAX and Laser Hall
Worked with engineers for good solution
Maze-style shielding meets requirements
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023
Laser Hall
TAX hutch
TAO hutch
< 6 mSv outside
from 1-year shots
Dominant proton source term only

## Slide 26: HVAC / Exhaust / Ground Water
Ground Water
Water in activated soil and concrete
Main activation from laser light going east, colinear with FEL
Tritium o.k., Na-22 requires more detailed analysis
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023
Exhaust
Possibility for activated target material pumped out  require HEPA filters
Air Activation
Dose to personnel low enough: With 1 hour cool-down, DAC < 1
Dose to public low enough: With < 0.1 mrem/year for maximum exposed individual no need for continuous air monitoring

## Slide 27: Upcoming Experiment in Collaboration with Accelerator Test Facility at Brookhaven National Laboratory
Goal: Benchmark electron source term model when accounting for scaling with wavelength
SLAC model is based on 800 nm and recent work in collaboration with BNL has applied it to a 9300 nm laser/
Analysis has been performed accounting for the scaling to generate equivalent 800 nm laser intensity for the generation of important parameters used in our model.
An experimental benchmarking effort will aim to demonstrate the validity of our model for radiation protection analysis with the operation of lasers with very different wavelengths
Aluminum Shielding
Dosimeter
Stacked Dosimeters
Active Detector
Shielded/Moderated Dosimeter
Experimental Configuration

## Slide 28: Access Control, Laser Control, Radiation Monitors
Access Control
Hutch access only with
  X-ray FEL stopped
  and laser hazards off
Laser Hazard Control: prompt radiation hazards off during access
Options:
  attenuate laser light (like at MEC)
  turn off amplification during access
  only use small alignment laser
Radiation Monitors
Interlocked Prompt Radiation Monitors outside
Interlocked Residual Radiation Monitors inside hutch
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023

## Slide 29: MEC-U Source Term for Protons [RP-22-09]
Spectrum based on PIC Simulation for LMJ-PETAL at CEA/Cesta
Similar laser parameters: 150 J, 1 PW, 2x1021 W/cm2
Input to FLUKA
  5% conversion of laser energy to accelerated protons for liquid
    Solid target is assumed to have same yield as liquid targets
  Spectrum up to 115 MeV (average 23 MeV)
  Forward-backward yield ratio 1:1 (confirmed with SLAC PIC simulation)
  ± 20° opening angle
  Proton beam hitting Al target chamber
B. Martinez Matter Radiat. Extremes 7, 024401 (2022)
Proton Spectrum from B. Martinez Matter Radiat. Extremes (2022)
Implementation in FLUKA
Notes: Solid target is assumed to have same yield as liquid targets

## Slide 30: Activation Hazard
Operation at up to 6 W (= 10% of shots)
If MEC-U operates as designed, significant activation created
Unlike accelerators
Frequent access needed to area of activation
Challenging to implement shielding
Analysis to understand hazard, to guide engineers
Assumptions for FLUKA irradiation profile:
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023
sketch of irradiation profile for proton source term
5,400,000 shots = 10% of yearly max (solid + liquid targets)
200,000 shots in 3 days = 10% of max (liquid targets)
36,000 shots (liquid target)
time
shot rate

## Slide 31: Dose to Personnel (2)
Working with project to estimate
  Where personnel works
  How long they work there
  How long after beam stopped
 determine pattern for experiment for instrument scientists, users, instrument technicians
Still working out details
Caveats
Estimated pattern only
Assuming 10% of maximum number of shots
Need to cover work on activated detector, optics, targets
Need to cover work inside target chamber
vertical axis indicates:
beam operation
cool-down
location of work in hutch
J. Bauer et al., RadSynch23, May 30 to Jun 2, 2023
Prep Time (5 days)
Laser Testing (2 days)
Experimental Time (7 days)