## Slide 1: Challenges and strategies in planning Long Shutdown 3 for the HL-LHC Upgrades of the LHC experiments at CERN
R. Froeschl, D. Bozzato, T. Lorenzon
30/05/2024 SATIF-16 workshop
EDMS 3092765

## Slide 4: Radiation Protection Aspects of LHC Experiments in LS3
Radiation sources
Multiple and prolonged interventions in radiation areas
Radiological characterization of detector components and infrastructure
Planning for re-start

## Slide 5: Radiation Sources
Main radiation source: Collisions at the interaction point
Collision rate (luminosity) predictions for future operation
Process to update collision profiles annually with measured data from the last operational year
https://op-webtools.web.cern.ch/vistar/?usr=LHC1

## Slide 6: Interventions in the LHC Experiments
LS3 will last 3 years
  Many and long interventions in the experimental caverns (radiation areas)
CERN ALARA rules require establishment of Work-Dose-plannings
  guide optimization process
  define appropriate approval process
  Ensure dose limits and constraints are respected
Estimates of residual dose rates at workplaces for several detector configurations for a multitude of cool-down times needed as input for Work-Dose-plannings

## Slide 7: Residual dose rates assessments – ATLAS
ATLAS:
  General-purpose detector at the LHC
  46 m long, 25 m high and 25 m wide, ~7000 tons weight
  Opening procedure is in steps
Long shutdown 3:
  Upgrades and new installations in view of HL-LHC
  Multiple and prolonged interventions in residual radiation environments
  Monte Carlo simulations to provide input for the Work Dose Planning

## Slide 8: Residual dose rates
Opening
TAS removal and
substitution
ATLAS Detector configurations: 16 scenarios defined with ATLAS Technical Coordination to reach sufficient level of detail
FLUKA-SESAME1 two-step simulations
Full irradiation history up to the end of Run 3
Cool-down times: Grid of 25 cool-down times (from days to 30 years)
A few hundreds of CPU-days of simulation time
1 See T. Lorenzon at SATIF-15
Inner Detector removed on one side

## Slide 9: Residual dose rates
Considerable auxiliary code production
  FLUKA geometry modifications for all scenarios
  Scripting
  Plotting
  Visualization tool for ATLAS technical coordination
Assessments for individual components (dismantling, transport and storage purposes)
Inner detectors removal

## Slide 10: Radiological characterization of detector components and infrastructure
Zoning
Characterization for transport classification
Characterization for storage requirements definition
Refurbishment of detector components
Pre-characterization for clearance and waste

## Slide 11: Zoning concept for clearance
Partitioning of experimental cavern in 2 zones
  Global control zone: Activation levels a priori expected to be below clearance limit
  Individual control zone: Activation levels not excluded to exceed clearance limit
Different measurement procedures for these zone (verification / clearance measurements)
Definition of zones based on simulations + verification with samples
Simulations assessment performed in most cases with dedicated methodology -> Fluence Conversion coefficients method
Material composition
Time dependent irradiation profile
Cool-down time
Python code
Pre-computed particle and energy dependent coefficients
Apply coefficients during transport calculations
Direct estimation of the desired radiological hazard factor
R. Froeschl. http://dx.doi.org/10.1088/1742-6596/1046/1/012006
D. Bozzato, R. Froeschl, V. Kouskoura. https://doi.org/10.1093/rpd/ncad126

## Slide 12: Zoning – ATLAS in LS3
Multiple of Swiss clearance limit (LL) for Steel 304L after 4 month of cool-down
Individual control
Global control

## Slide 13: Characterization for transport classification
Radionuclide inventories needed to ensure ADR compliant classification of transports
  Very large objects for which certified containers are difficult to obtain
FLUKA Monte Carlo simulations to compute radionuclide inventories
  Standard FLUKA simulations with RESNUCLE scoring
  Post-processing of SESAME data
  Spectra-based
These results are passed to radioactive transport service for proper transport classification
Example: CMS Endcap (YE1) noses
  6 meters diameter, ~150 tons

## Slide 14: Characterization for transport classification
Mass-speciﬁc radionuclide inventory in one CMS YE1 nose after 90 days of cool-down (top contributors only)

## Slide 15: Planning for re-start
Restart period might require assessments of detector configurations and beam conditions different from nominal operation
  Pilot beam in 2021
    Prompt radiation for modified shielding configuration
    Dedicated clearance zoning in the experiments (scaffoldings, structural supports, …)
    RP input needed to define beam parameters
The actual start-up configurations will depend on the progress of LS3
Importance of knowledge conservation
D. Bozzato, R. Froeschl. https://doi.org/10.1080/00295639.2023.2211191 (ICRS14/RPSD-2022)
CMS during 2021 pilot beam
ATLAS during 2021 pilot beam

## Slide 16: Conclusions
Long Shutdown 3 will be very complex in terms of radiation protection for the LHC Experiments
Residual dose rate estimates for Work-Dose-plannings
Radiological characterization of big and complex environments and detector components
Dedicated tools coupled to FLUKA code developed to perform required assessments
Need to plan for the re-start after LS3

## Slide 18: Backup

## Slide 19: ALARA levels at CERN for the classification of interventions
Group 1 Criteria: ‘hard’ limits used to determine the minimum ALARA Level
Group 2 Criteria: base of a radiological risk assessment

## Slide 20: Fluence conversion coefficients method
Let’s consider a compound material constituted by a certain number of elements having mass fractions . The material is irradiated, and residual activity is left. The specific activity of a radionuclide in the material can be expressed as
Production cross section of radionuclide r from element e due to particle evaluated at the average energy for the considered bin
Production term : production of radionuclide r from element e due to particles ,…
Specific activity of radionuclide b
Time evolution matrix : build up of radionuclide r and full decay chain to isotope b depending on time dependent irradiation time/profile and cooling time (Bateman coefficients).
Fluence energy spectrum integrated over the energy bin of width dE centered around energy
Weighting coefficient that can be applied for particle and for the energy bin that is centered around