## Slide 1
Monte Carlo calculation code applications for the shielding design of a transportable positron generator
Inès DUARTE – Nicolas MARY – Cédric DOSSAT – Nathalie CHATRY (TRAD Tests & Radiations)
Jean-Michel REY (POSITHÔT)
May 29th 2024
SATIF-16 – Frascati, Italy

## Slide 2
Who are we ?
The positron generator
The objectives
The radiation assessments
Conclusion

## Slide 3
1
Who are we ?

## Slide 4
RADIATION RESISTANCE TESTS
ELECTRONIC COMPONENTS
For more information :
rayxpert.com
trad.fr
r2cots.com
fastrad.net
SOFTWARES EDITORS
& ENGINEERING
TRAD Tests & Radiations
Company founded in 1994 and based in France
TRAD
Notes: -Parler du bunker avec source de Co60 + préciser que les composants électriques qu’on vend ont été qualifiés en dose
-Préciser les applications des autres codes de calcul

## Slide 5
RayXpert v1.9.3
Figure 1: RayXpert® interface
Notes: Monte Carlo calculation code launched in 2013
CAD modeling tools and import step file + beam /decay source + volume mapping / sensitive elements

## Slide 6
Table 1: Description of the Physics simulated in the last version of RayXpert®
*depending on the isotope
Particles | Interaction process | Energy ranges |  | Nuclear Decay Database | Cross section
Electron | Bremsstrahlung, Ionisation, Multiple diffusion, Lewis theory | 1 keV | 1 TeV | JEFF 3.1.1 & EAF2010 | Based on GEANT4
Positron | Bremsstrahlung, Ionisation, Multiple diffusion, Lewis theory | 1 keV | 1 TeV |  | 
 | Annihilation | 1.022 MeV | 100 GeV |  | 
Photon | Compton diffusion, Photoelectric Effect | 1 keV | 100 GeV |  | 
 | Pair production | 1.022 MeV | 100 GeV |  | 
Neutron | Elastic and Inelastic scattering, Radiative capture, Induced fission | MeV* | 20 MeV* | - | ENDF/B-VII.1
Particles | Interaction process | Energy ranges |  | Nuclear Decay Database | Cross section
Electron | Bremsstrahlung, Ionisation, Multiple diffusion, Lewis theory | 1 keV | 1 TeV | JEFF 3.1.1 & EAF2010 | Based on GEANT4
Positron | Bremsstrahlung, Ionisation, Multiple diffusion, Lewis theory | 1 keV | 1 TeV |  | 
 | Annihilation | 1.022 MeV | 100 GeV |  | 
Photon | Compton diffusion, Photoelectric Effect | 1 keV | 100 GeV |  | 
 | Pair production | 1.022 MeV | 100 GeV |  | 
Neutron | Elastic and Inelastic scattering, Radiative capture, Induced fission |  | 20 MeV* | - | ENDF/B-VII.1
They trust us :
RayXpert v1.9.3
Notes: - French Atomic Energy and Alternative Energies Commission
French company Specialised in nuclear fuel cycle
International atomic energy agency
French Radioprotection and nuclear safety institute

## Slide 7
POSITHÔT
Founded in 2015 by Jean-Michel REY and issued from the fundamental physics institute of the CEA
First transportable positron generator created in 2018
For more information :
posithot.com
Figure 2: https://www.posithot.com/about/
Offers materials analysis using positron annihilation spectrometry
Allows to detect the defects in the matter without generating radioactive waste

## Slide 8
2
The positron generator

## Slide 9
The positron generator
Target
Figure 4: Visualization of the photon secondaries created from the target in RayXpert®
Figure 3: Image of the POSITHÔT generator
Notes: Pas le droit de parler de la techno par soucis de confidentialité
Problématique de rayonnements photoniques de la cible + du beam dump

## Slide 10
3
The objectives

## Slide 11
The objectives
→ Sizing of the positron generator shielding complying with the regulations on ionizing radiation sources and transportable limitations
I. Dose rate outside the generator ≤ 7.5 μSv/h = 1.25 mSv/month
II. A total weight < 45 tons for the equipment portability
Public area < 80 μSv/month
Supervised area < 1.25 mSv/month
Monitored area < 4 mSv/month
Monitored area < 2 mSv/h
Monitored area < 100 mSv/h
Monitored area > 100 mSv/h
Figure 5: French Nuclear Safety Authority (ASN) equivalences for radiation zoning
Areas accepted

## Slide 12
4
The radiation assessments

## Slide 13
The radiation assessments
The initial radiation zoning
Quantity calculated:
Photon H*(10)
Virtual mesh resolution:
25 x 25 x 25 cm³
Figure 6: Dose mapping definition in RayXpert®
Public area < 80 μSv/month
Supervised area < 1.25 mSv/month
Monitored area < 4 mSv/month
Monitored area < 2 mSv/h
Monitored area < 100 mSv/h
Monitored area > 100 mSv/h
Figure 5: French Nuclear Safety Authority (ASN) equivalences for radiation zoning
Figure 7: Initial zoning assessment in RayXpert®, errors < 30%
Maximum about 20 mSv/h
Notes: - Import step
- Définition de cartographie

## Slide 14
The radiation assessments
The shielding definition
Public area < 80 μSv/month
Supervised area < 1.25 mSv/month
Monitored area < 4 mSv/month
Monitored area < 2 mSv/h
Monitored area < 100 mSv/h
Monitored area > 100 mSv/h
Figure 5: French Nuclear Safety Authority (ASN) equivalences for radiation zoning
Addition of 5.5 tons
 41 tons in total
Figure 9: Additional shielding in RayXpert®
Figure 8: Identification of the leakage areas in RayXpert®, errors < 30%

## Slide 15
Figure 10: Lead shot shielding in RayXpert®
Lead shot for:
Limiting the weight (ρ = 7 g.cm-³)
Providing a simple access for maintenance
The radiation assessments
The shielding definition
Public area < 80 μSv/month
Supervised area < 1.25 mSv/month
Monitored area < 4 mSv/month
Monitored area < 2 mSv/h
Monitored area < 100 mSv/h
Monitored area > 100 mSv/h
Figure 5: French Nuclear Safety Authority (ASN) equivalences for radiation zoning
Figure 9: Additional shielding in RayXpert®

## Slide 16
The radiation assessments
The final radiation zoning
Public area < 80 μSv/month
Supervised area < 1.25 mSv/month
Monitored area < 4 mSv/month
Monitored area < 2 mSv/h
Monitored area < 100 mSv/h
Monitored area > 100 mSv/h
Figure 5: French Nuclear Safety Authority (ASN) equivalences for radiation zoning
Figure 11: Final zoning assessment in RayXpert®, view from the top, errors < 30%
100 cm
80 cm
60 cm
Maximum about 2 μSv/h
Reducing the dose rate outside the generator by a factor of 11,000 and by a factor of 25,000 for the most problematic direction
Figure 12: Final zoning assessment in RayXpert®, view from the side, errors < 30%
100 cm
110 cm

## Slide 17
5
Conclusion

## Slide 18
Conclusion
Import of STEP files for complex infrastructure geometry
Monte Carlo calculation for shielding design
CAD interface and dose mapping for shielding optimization
Figure 13: Zoning assessments in RayXpert® for a healthcare facility
Figure 14: Determination of the origin of dose contribution thanks to the gradient mode of the dose mapping display feature in RayXpert®

## Slide 19
Thank you
For your attention
www.rayxpert.com
ines.duarte@trad.fr
907 voie l’Occitane
31670 Labège