## Slide 1: Radiation Shielding Analysis for Synchrotron Radiation Beamlines of 4th Generation Storage Ring in Korea
Mahdi Bakhtiari, Nam-Suk Jung, Hee Seock Lee
Pohang Accelerator Laboratory (PAL), POSTECH
2024.05.29
The 16th workshop on Shielding aspects of Accelerators, Targets and Irradiation Facilities (SATIF-16)-INFN-LNF-Italy

## Slide 2: Contents
Introduction
4thGSR (4th Generation Storage Ring) construction project in Korea
Radiation safety control policy
Shielding design to determine tunnel structure
Beamlines radiation safety issues
  Front-end safety magnet design
  Safety shutter
  Optics hutch
  Experimental hutch
  Ray tracing
Monte Carlo calculation results
Safety magnet design using FLUKA 4-4.0 and PHITS-3.34.1 codes
Dose calculations from gas Bremsstrahlung (GB) using FLUKA 4-4.0
Safety shutter design using semi-empirical formula and FLUKA 4-4.0
Dose calculations from synchrotron radiation (SR) using FLUKA 4-4.0
Summary and conclusions

## Slide 3: Introduction: 4thGSR project in Korea
History
2019. 10 : Start a Conceptual Design of 4thGSR by PAL/KBSI/KAERI collaboration
2020. 5 : Determine a construction site as ‘Cheongju’
2020. 6 : Publish a Conceptual Design Report (CDR)[1]
2021. 7 : Determine a institution to conduct construction project
as KBSI (Korea Basic Science Institute)
2021. 7 (~ 2027. 6) : Start a construction project, ‘Multipurpose Synchrotron
Radiation Construction Project’
Counterpart in the construction project
KBSI : Building & Infrastructure
PAL : Accelerator & Beamline
(+ Radiation Shielding, Radiation Protection System)
4th GSR
PAL-XFEL
PLS-II
[1] Pohang Accelerator Laboratory, “Conceptual Design Report of 4GSR”, PAL-PUB-2000-004, 2000.

## Slide 4: Introduction: Specification and layout of 4thGSR in Korea
 | Parameter | Value in TDR [1]
Storage Ring (SR) | Beam Energy | 4 GeV
 | Stored Current | 400 mA
 | Ring Circumference | 799.297 m
 | Symmetry | 28
 | Straight Section No. | 28
 | Straight Section length | 6.06 m
 | Emittance | 62 pm rad
Booster | Energy | 0.2 GeV to 4 GeV
 | Circumference | 772.893 m
Linac | Energy | 200 MeV
 | Reputation rate | 2 Hz
 | Pulse charge | 1 to 3 nC (Multi-bunch) 0.01 to 1 nC (Single-bunch)
 | Pulse length | ≈128 ns (Multi-bunch) 6~8 ps FWHM (Single-bunch)
4
Linac: 200 MeV
Linac to Booster Injection
Booster to SR Injection
Booster: 0.2 to 4 GeV
SR: 4 GeV, 400 mA
Booster ring & storage ring in the same tunnel
10 beamlines will be constructed at the end of the first construction phase.
Beam direction: Counter-clockwise
Plan view
[1] Multipurpose synchrotron radiation accelerator (Korea-4GSR) detailed design report (2023)-In Korean
e beam

## Slide 5: Radiation safety control policy
SR
Booster
Beamline, User Accessible, 1 mSv/y
Infield, RW Accessible, 10 mSv/y
Same safety control policy to PAL
Dose criteria
Area (Zone) Classification | Dose
Restricted Area | 0.25 mSv/y ≤ Dose < 1 mSv/y
Generally-Controlled Area | 1 mSv/y ≤ Dose < 20 mSv/y
Radiologically-Controlled Area | 20 mSv/y ≤ Dose < 1 mSv/h
High Radiation Area | Dose ≥ 1 mSv/h (No Access)
Dose Limit (based on Korean Regulation) | Dose
Radiation Workers (RW) | 20 mSv/y
Frequent Visitors | 6 mSv/y
Public (including User) | 1 mSv/y
Site Boundary | 0.25 mSv/y
Shielding Criteria | Dose | Note
RW accessible area | 10 mSv/y, (5 µSv/h) ½ of dose limit based on ALARA | Normal operation
User accessible area | 1 mSv/y (0.5 µSv/h) | Normal operation
(In Accident) | 1 mSv within 1 h for single event | 

## Slide 6: Shielding design to determine tunnel structure
According to the radiation safety control policy:
  The required walls thickness were calculated using SHIELD 11 [1] (1st step).
  The required shielding thickness were more precisely determined using FLUKA 4-4.0 (CERN branch) [2,3] Monte Carlo code calculations [next slide].
Position | Wall thickness (cm)
Outer Sidewall | Non injection area: 80 cm concrete
 | Injection area: 100 cm concrete
Inner Sidewall | Non injection area: 50 cm concrete
 | Injection area: 70 cm concrete
End wall | ID* beamline: 130 cm concrete + 4 cm Pb with 2.5 cm Fe
 | BM** beamline: 180 cm concrete
Ceiling | 50 cm
Injection area
Non Injection area
[1] W.R. Nelson and T.M. Jenkins, SLAC-R-737, 2005
[2] C. Ahdida et al, Frontiers in Physics 9, 788253 (2022).
[3] G. Battistoni et al, Annals of Nuclear Energy 82, 10-18 (2015).
Outer sidewall
ID*: Insertion device (undulator or wiggler)
BM**: Bending magnet
Inner sidewall

## Slide 7: Shielding design to determine tunnel structure
  Normal operation with a uniformly distributed beam loss was assumed in FLUKA simulations for determining the tunnel structure.
  5 beam loss positions were considered each one cell.
Beam loss
Total dose distribution (µSv/h), 5.88E10 e/s
White areas < 0.2 µSv/h
LGBM1U
LGBM1D
Combined magnets
Beam loss positions at one cell of the storage ring.
Center magnet
LGBM: Longitudinal Gradient Magnet
Optics hutch
ID
beamline
BM
beamline
beam loss position

## Slide 8: Shielding design to determine tunnel structure
ID
beamline
BM
beamline
180 cm
BM beamline top view
Geometry
150 cm
60 cm
120 cm
40 cm
Fe: 2.5 cm thick
Pb: 4 cm thick
Fe: 2.5 cm thick
264 cm
32.5 cm
Gap size: 0.5 cm
130 cm
Pb: 15 cm thick
Fe: 2.5 cm thick
130 cm
Pb: 4 cm thick
Top view
Vertical view
Beampipe size:
Outer D: 3.4 cm
Inner D: 2.76 cm
Shielding door:
1 cm Fe+ 5 cm Pb + 15 cm PE +1 cm Fe
  Monte Carlo calculations were performed to precisely determine the tunnel structure.
Beam
Infield
Tunnel
Optics hutch

## Slide 9: Radiation sources considered for beamline shielding design
  Normal operation:
      Gas Bremsstrahlung (GB) is produced by stored electrons interacting with residual gas in a vacuum chamber.
      Synchrotron radiation (SR) is generated when electrons travel through a bending magnet, wiggler, or an undulator.
      High energy Bremsstrahlung as a result of stored electron interaction with the storage ring components.
      Accidental case:
        Electron beam accidentally strikes the storage ring components, intense Bremsstrahlung radiation is generated, passing through the beamline.
      These radiations needs to be suitably shielded.
Source of radiation:

## Slide 10: Beamlines radiation safety issues
Important components and regions in beamline shielding design:
Front-end components
  Safety magnet
  Collimators
  Safety shutters
Optics hutch
  Mirrors
  Stopper
  Collimators
Photon transport line (PTL)
Experimental hutch
Ray tracing
Front end
Optics hutch
PTL to experimental hutch
Stopper, Pb: 20 cm thick
Optics components
Collimators
Pb: 25 cm thick
Safety shutter
Safety magnet
400 cm
140 cm
180 cm
1320 cm
Pb (2 mm)
Fe (6 mm)
Optics hutch
Top view
Vertical view
Collimator
Pb: 2 cm thick
Beam
Beam

## Slide 11: Considered beamlines radiation safety issues
In PLS-II, The Bending Magnets (BM) are powered in series  No need for safety magnet
In 4thGSR, each BM is equipped with its own dedicated power supply
   A permanent magnet is considered for 4thGSR beamlines to remove the primary electron beam in case of magnet power loss (Accident case)  Called a safety magnet
The safety magnet specifications:
  Length: 50 cm
  Magnetic field: 0.5 T
  Gap size: 4 cm
  Simulations were performed using:
    FLUKA 4-4.0 with the JEFF-3.3 [1] neutron library.
    PHITS-3.34.1 [2] with EGS5 mode and the JENDL-4.0 [3] neutron library.
    Same materials, geometries, mesh size, threshold energies were used in both codes.
Safety shutter
Front-end safety magnet design
Safety shutters provide protection in the forward direction from gas Bremsstrahlung, white beam, and radiation from beam losses in the storage ring.
  Optics hutch (OH)
Optics hutch shields the secondary radiations generated from Bremsstrahlung radiation interaction with optics components.
[1] A.J.M. Plompen, et al, European Physical Journal A, 56, 181 (2020).
[2] T. Sato et al, J. Nucl. Sci. Technol. 61, 127-135 (2024)
[3] K. Shibata et al, J. Nucl. Sci. Technol. 48, 1-3 (2011).

## Slide 12: Shielding calculations results: Safety magnet design
ID
beamline
BM
beamline
Top view
Vertical view
Safety magnet
Beam
Safety shutter
Collimators
FLUKA geometry
PHITS geometry
Safety magnet
Safety shutter
Collimators
Vertical view
Top view
Beam
ID
beamline
BM
beamline
172 cm
Detailed geometry of the front end was modeled in FLUKA
Soil
The FLUKA geometry was converted into PHITS geometry to compare the results.
Geometry
172 cm

## Slide 13: Shielding calculations results: Safety magnet design
FLUKA 4-4.0
PHITS-3.34.1
Electron beam hits the collimator
Safety magnet
The distance between the collimator and the safety magnet is important to suppress the radiation. In this case, it is 172 cm.
Except for the current components, no other components should be added between the safety magnet and the downstream collimator.
FLUKA and PHITS show the same electron beam track after passing in the magnetic field.
Electron beam hits the collimator
Vertical view
Safety magnet
No interaction
Magnet region
0.5 T
PHITS-3.32
An error of electron transport in the magnetic field simulation in the old version of PHITS-3.32 was found and reported.  Fixed in the new version PHITS-3.34.1.
Electron beam track

## Slide 14: Shielding calculations results: Safety magnet design
FLUKA 4-4.0
PHITS-3.34.1
Photon
Neutron
Radiation distributions (Top view)
Deflection of the electron beam by the safety magnet onto the collimator produces significant radiation.
Electron beam hits the collimator
Electron beam hits the collimator

## Slide 15: Shielding calculations results: Safety magnet design
Cut-2
Shielding door:
1 cm Fe+ 5 cm Pb + 15 cm PE +1 cm Fe
Cut-2
Dose distribution
Cut-1
Dose is far below 1 mSv (1000 µSv) after the wall and optical hutch for this accident case.
Beam
Cut-1
Cut-2
Cut-1
FLUKA 4-4.0
PHITS-3.34.1
Beamline hole
Beamline hole
ICRP 116 (anterior–posterior) was used in FLUKA and PHITS for comparison.
  PHITS and FLUKA are consistent at Cut-1.
ID beamline
ID beamline
  PHITS shows a lower dose than FLUKA at Cut-2.
  Further study is ongoing to compare FLUKA and PHITS in more details.

## Slide 16: Shielding calculations results: Gas Bremsstrahlung
Electron Beam killed
Beam
GB target at 1 atm
6.01 m
Residual gas [2] | Partial Pressure ratio
H₂ | 90%
H₂O | 1%
CH₄ | 3%
CO | 5%
CO₂ | 1%
Beam: Electron 4 GeV
Target: Residual gas inside a 6.01 m length straight section (Shown in table)
Average pressure in the straight section: 1.0 × 10-9 mbar. Calculations performed at atmospheric pressure (1 atm) and then scaled at design value
Multiple scattering of electrons is suppressed [1]: Multiple scattering broadens the bremsstrahlung beam, thus making it less forward peaked scored dose is lower if MS is turned on.
Moller scattering is suppressed: Delta rays are generated in the air target and can deflect the primary electron beam Scored dose is lower if Moller scattering is on
The primary beam should be killed at the end of the target Using cut-offs
[1] Ipe et al, NIMA, 351 (1994).
[2] J. Y. PARK et al. J. Korean Phys. Soc. 47, 5, 788 (2005).
GB spectrum
Parameters setting

## Slide 17: Shielding calculations results: Gas Bremsstrahlung
Dose distribution (ID beamline): Top view
The dose rate is below 0.5 µSv/h outside of OH with 6 mm Fe + 2 mm Pb .
The dimension and position of the collimator will be reconsidered by ray tracing.
The stopper dimension can also be adjusted instead of using a collimator.
Cut
Stopper
Optics hutch
Collimator

## Slide 18: Shielding calculations results: Gas Bremsstrahlung
Dose distribution (ID beamline): Vertical view
The dose rate is below 0.5 µSv/h outside of OH with 6 mm Fe + 2 mm Pb .
The neutron dose rate is significantly lower than that of photon.
Cut
Optics hutch

## Slide 19: Shielding calculations results: Safety shutter
Safety shutter thickness:
The thickness of safety shutter was calculated using semi-empirical formula [1.2] and confirmed by Monte Carlo calculations.
 | Straight section (Undulator)
Length of air path, L [m] | 6.01
Distance from dose point to air path, d [m] | 20.9
Bremsstrahlung dose rate [Sv/h] | 0.62 (Tromba’s Eq.) 1.23 (Ferrari’s Eq.)
Required lead* thickness to reach 0.5 [µSv/h] | 32.4 (Ferrari’s Eq.)
* 20 cm-thick Tungsten has the same shielding effect.
[1] G. Tromba and A. Rindi, Nucl. Instrum. Meth. A 292, 700 (1990)
[2] A. Ferrari et al., Nucl. Instrum. Meth. B 83, 518 (1993)
The safety shutter should block:
  The gas Bremsstrahlung.
  All secondary radiation generated from electron loss in storage ring.
Safety Shutter closed
Radiation

## Slide 20: Shielding calculations results: Safety shutter
Safety Shutter: 20 cm-thick tungsten is sufficient to block the GB.
Optics hutch
Optics hutch
ID beamline
Safety shutter closed:
Stored electron beam loss positions
Optics hutch
Optics hutch
Top view
ID beamline
Dose from Gas Bremsstrahlung
A uniform beam loss is assumed in the storage ring (2 mA/min) and injection efficiency of 90%.
20 cm-thick tungsten effectively blocks the forward-peaking bremsstrahlung photons generated from from electron loss in storage ring.
Dose from Bremsstrahlung photons generated from stored electrons
Vertical view
A'
A
A'
A

## Slide 21: Shielding calculations results: Synchrotron radiation (SR)
Synchrotron radiation (SR) source
  In Korea 4thGSR, there will be 9 ID beamlines and one BM beamline at the end of the first phase.
  In this work, the synchrotron radiation shielding results are preliminarily presented for only one ID beamline with In-Vacuum Undulator (IVU24).

## Slide 22: Shielding calculations results: Synchrotron radiation (SR)
SR from an In-Vacuum Undulator (IVU24) was calculated using SPECTRA 11.1.2 code [1].
[1] T. Tanaka, J. Synchrotron Radiation 28, 1267 (2021).
The SR spectrum was used as a photon source in FLUKA with biased sampling.
The input source spectrum is sampled correctly in FLUKA.
SR spectrum:
To FLUKA

## Slide 23: Shielding calculations results: Synchrotron radiation (SR)
Top view
Vertical view
Optics hutch
Optics hutch
The dose rate outside of the optics hutch is less than 0.1 µSv/h which is far below the dose limit of 0.5 µSv/h.
The optics hutch with 6 mm Fe +2 mm Pb is adequate to block the SR radiation generated from IVU24 (ID beamline).
Dose distribution (ID beamline):
ID beamline

## Slide 24: Summary and conclusions
Beamline radiation shielding analysis of 4th generation storage ring in Korea were performed to design the safety magnet, the safety shutter and the optics hutch.
The position of the safety magnet and downstream collimator were carefully selected to ensure the dose level remains below 1mSv in the beamline.
The safety shutter made of tungsten and 20 cm thickness would be adequate to block GB and other Bremsstrahlung radiations.
The OH with 6 mm Fe + 2 mm Pb properly shielded the GB and all other secondary radiations.
The synchrotron radiation from the In-Vacuum Undulator (IVU24) was shielded properly by designed OH.
A comparison between FLUKA and PHITS calculated dose (for the safety magnet) showed discrepancies between them.
More comparisons between FLUKA and PHITS codes is ongoing to study the reason of discrepancy.
STAC8 [1] code will be also used determined the optics hutch and experimental hutch for each beamline and compare with FLUKA.
[1] Y.Asano and N.Sasamoto, Radia. Phys. Chem. Vol.44 p133 (1994)

## Slide 25
Thank You for Your Attention
bakhtiari@postech.ac.kr