## Slide 1: the idea vertex detector and its integration inthe fcc-ee interaction region
Fabrizio Palla1
Manuela Boscolo 2, Filippo Bosi 1, Francesco Fransesini 2, Stefano Lauciani 2
1INFN Sezione di Pisa, Italy
2INFN Laboratori Nazionali di Frascati (RM), Italy
Second ECFA workshop on e+e- Higgs/EW/Top Factories,
Paestum (Italy)
12 October 2023
Fabrizio Palla

## Slide 2: The IDEA Concept

## Slide 3: Requirements
Interaction region detectors must be integrated with the beam pipe
  The vertex detector innermost radius should profit of the reduced beam pipe diameter (2 cm) and should cover
  Must not interefere with the Luminosity Calorimeter (clearance of ~120 mrad)
  The mounting of the vertex tracker must be done inside the support tube
  Minimize the radiation lengths

## Slide 4
Inner Vertex detector:
Modules of pixel size
3 barrel layers at
13.7, 22.7 and 33 mm radius
Outer vertex tracker:
Modules of pixel size
Intermediate barrel at 13 cm radius (improved reconstruction for)
Outer barrel at 31.5 cm radius
3 disks per side
DRIFT CHAMBER
EXSTERNAL CILINDER
OUTER TRACKER
MEDIUM TRACKER
INNER TRACKER
DISK 3
DISK 3
DISK 1
DISK 1
DISK 2
DISK 2

## Slide 5: Inner vertex detector modules
Based on ARCADIA INFN R&D
  Depleted Monolithic Active Pixel Detectors (DMAPS)
  Technology: LF11is 110 nm CMOS node, high-resistivity bulk
  Pixel size 25x25 µm2 , 50 µm thick
  Active area 640 pixel (16 mm) in z and 256 pixels (6.4 mm) in
  Chip periphery plus an inactive zone: total of 2 mm in
  Chips are side-abuttable in z
Modules composed of 2 sensors: total of 8.4 mm 32 mm (z)
  Power budget: assume - including power and readout buses
Chip 1
Chip 2
32 mm
8.4 mm
Readout
z 640 pixel
R-phi 256 pixel
"Fully Depleted MAPS in 110-nm CMOS Process With 100–300-μm Active Substrate," in IEEE Transactions on Electron Devices, June 2020, doi: 10.1109/TED.2020.2985639.
See talk by A. Andreazza
High rate capability (100 MHz/cm2) architecture on a scalable 512x512 pixel matrix (25µm pitch) MD3 Main Demonstrator chip: measured 30 mW/cm2 at full-speed

## Slide 6
Layer 1
15 overlapping staves of 6 modules each
Overlap to allow alignment ~500 µm
Pinwheel geometry: all modules at the same (smallest) radius
Power budget ~12 W
Total weight ~22 grams
Total thickness 0.25% X0
Silicon: 0.053% X0
Power and readout bus: 0.056% X0

## Slide 7: Layer 1 stave detail
Reticular lightweight support to provide stiffness
Thin carbon fiber walls interleaved with Rohacell
2 buses (data and power) 1.8 mm wide and 250 µm thick (50 µm Al, 200 µm kapton) per side
  Inspired to low mass hybrid R&D
Sensors facing interaction point w/o any other material in front
Readout chips either sides
Air cooled

## Slide 8
Layer 2
24 overlapping staves of 10 modules each
Pinwheel geometry
Counter-rotated wrt layer 1 to mitigate charge-asymmetry effects in track reconstruction
Power budget
~32 W
Total weight ~63 grams
Total thickness 0.25% X0

## Slide 9
Layer 3
36 staves of 16 modules each
Lampshade geometry.
Charge symmetric track reconstruction
Total weight ~150 grams
Total thickness 0.25% X0
Power budget
~77 W
NEW

## Slide 10: Overall Inner Vertex layout
Total power ~120 W
Total weight ~230 grams
NEW

## Slide 11
Inner vertex detector supporting conical structures on elliptical chamber
~450 grams
Engineered for air ducts and thermal isolation from the beam pipe during bakeout
Cooling Third layer
Cooling Second Layer
Cooling First Layer
Cooling Pipe

## Slide 12: Thermal simulation in progress
Full model
Extraction of a radial sector for layer 3
Start from a radial sector of layer 3 (relying on periodic symmetry) and import in ANSYS FEA. Then move to all other layers
Layer 3 is the toughest in power dissipation and length
INFN Perugia
G. Baldinelli, F. Bianchi, C. Turrioni
Optimisation of the system ongoing: (speed and T of air, direction of the inlet flow, connection with the other layers, etc…)
A mechanical vibrational analysis will be performed
Experimental validation of the simulations foreseen

## Slide 13: Outer vertex layers modules
Based on ATLASPIX3 R&D
  DMAPS
  50 x 150 µm2
  Up to 1.28 Gb/s downlink
  TSI 180 nm process
  132 columns of 372 pixels
  Active (total) length (r-phi x z)
    18.6 (21) mm x 19.8 (20.2) mm
  Module is made of 2x2 chips – total length:
    size 42.2 mm x 40.6 mm
  Power budget not established yet:
    assume
Power
Data IN/OUT
HV
For details see A. Andreazza talk

## Slide 14
Middle Vertex Barrel
At 13 cm radius
22 staves of 8 modules each.
Lightweight reticular support structure (ALICE/Belle-II like)
Readout chips either side
Power budget
~342 W
Total weight ~1 kg
Water cooled (2 pipes of 2 mm diameter)

## Slide 15: MIDDLE TRACKER

## Slide 16: Stave detail

## Slide 17: Prototypes built for Belle II upgrade in Pisa

## Slide 18
Outer Vertex Tracker Barrel
At 31.5 cm radius
51 staves of 16 modules each
Lightweight reticular support structure (ALICE/Belle-II like)
Total weight ~3.7 kg
Readout chips either side
Power budget
~1400 W
Water cooled (2 pipes of 2 mm diameter)
Notes: NB. Qui la struttura reticolare deve stare giù perché sennò non si riesce ad ottenere il raggio esterno più grande e vicino alla DCH.

## Slide 19
Outer Vertex Tracker Disk 1
2 sides (front and back) each with 4 petals.
One petal is made of different staves of overlapping modules
Total modules per disk: 196
Total weight ~850 grams
Power budget ~ 336 W
Cooling using 1 water pipe (2 mm diameter)
Similar geometry for the other two disks

## Slide 20: Overall layout and dimensions

## Slide 21: Simulated material budget
Armin Ilg
In agreement with CAD estimates
Smaller X/X0 wrt IDEA CDR estimates
even including power and readout
cables in the sensitive region
Silicon only ~15% of the total

## Slide 22: Support cylinder
All elements in the interaction region (Vertex and LumiCal) are mounted rigidly on a support cylinder that guarantees mechanical stability and alignment
  Once the structure is assembled it is slided inside the rest of the detector
  Studies on-going where to anchor it (most likely to the Calorimeter)
Aluminium ribs
Aluminium endcaps
1mm CF + 4mm HC + 1mm CF

## Slide 23: Assembly procedure – I
1) Outer vertx tracker, middle vertex tracker and disks 1 are installed as a rigid structure inside the support tube
2) Disks 2 and 3 are installed inside the support tube

## Slide 24: Assembly procedure – II
3) LumiCal is installed in centered position, then beam pipe with inner vertex detector is inserted with a dedicated tool inside disks and outer vertex tracker, then fixed to both endcaps
4) LumiCal can be aligned in the correct position on the outgoing beams
5) Support tube can be closed

## Slide 25: General integration
    M. Boscolo, F. Palla, F. Fransesini, F. Bosi and S. Lauciani, Mechanical model for the FCC-ee MDI, EPJ Techn Instrum 10, 16 (2023). https://doi.org/10.1140/epjti/s40485-023-00103-7

## Slide 26: Conclusions
A layout of the interaction region with LumiCal and vertex trackers of the IDEA detector has been engineered
  Feasibility studies of integration successfully done including mounting sequence
  Documented in
    M. Boscolo, F. Palla, F. Fransesini, F. Bosi and S. Lauciani, Mechanical model for the FCC-ee MDI, EPJ Techn Instrum 10, 16 (2023). https://doi.org/10.1140/epjti/s40485-023-00103-7
Next/ongoing steps:
  Inner Vertex detector
    Study thermal isolation from the beampipe bakeout in progress
    Study the routing of the services (readout and power cables) in progress
  Outer Vertex Tracker
    Study the routing of the services (readout and power cables, cooling manifolds) in progress

## Slide 27: Thank you for your attention.
27
Space for additional logos
Name of the speaker/author
Date / Name of the event

## Slide 28: Backup

## Slide 29: Half-ladder layout – layer 1
z=0
Chip 1
Chip 2
Chip 1
Chip 2
96.5 mm
0.2 mm
Chip 1
Chip 2
8.4 mm
0.1 mm
Layer 1 ladders are placed at 13.7 mm radius

## Slide 30: Static Simulation old Layer 3
Asimmetric structure
Torsion deformation

## Slide 31
Cooling Fluid Temperature = 14 °C

## Slide 33: OUTER TRACKER

## Slide 34: Typical disk module stave
Cooling pipes
Lower modules
Upper modules
Front
Carbon fibre spacer
Carbon fibre pacers
Back
Electrical bus

## Slide 35: DISK 2

## Slide 36: DISK 3

## Slide 37
All Vertex

## Slide 38: Inner vertex (all 3 layers)
A. Ilg

## Slide 39: Middle and Outer vertex
Middle
Outer
A. Ilg

## Slide 40: Inner Tracking System 3 (ALICE)
  Wafer-scale sensor ASICs
  Fabricated with stitching
  All electrical signals and power routed on-chip
  Ultra-thin and bendable: 50 µm
  266 mm (Z) x variable width* (rφ)
  CMOS MAPS
    65 nm technology
  Open-cell carbon foam spacers
Key benefits
  Extremely lightweight
    Material budget: 0.35% X0 => 0.05% X0
  Uniformly distributed material
  Closer to interaction point
    Beam pipe radius: 18.2 mm => 16 mm
    Radial position: 24 mm => 18 mm
Detector Overview
* The sensor width (rφ) varies with layer
266 mm
open-cell carbon foam spacers
5.6 cm
7.5 cm
9.4 cm
rφ
18 mm