## Slide 1
Stefano Zucca, Lodovico Ratti
INFN
Sezione di Pavia
Università di Pavia
Dipartimento di Elettronica
  11th March 2010 – Pavia
INMAPS 0.18 um CMOS technology:
front-end design status report

## Slide 2
CHANNEL READOUT CHAIN
A preliminary design and layout of each block in the figure above has been carried out.
All the simulations have been performed keeping CD=40 fF.
Use of a mirror feedback configuration for C2 discharge instead of the transconductor in order to reduce the overall noise and threshold dispersion.
Vbl=750 mV
Imir=20 nA
Cfb=5 fF
C1=160 fF
C2=25 fF
Notes: 2

## Slide 3
PERFORMANCE
15um
P=18 uW per pixel
Tp=235 ns
ENC=29 electrons (CD=40 fF)
Threshold dispersion=13e (at the shaper output)
Threshold dispersion=23e (including discriminator contribution)
NLI=1%
Charge sensitivity = 900 mV/fC

## Slide 4
TEMPERATURE VARIATION
The channel readout has been simulated in the temperature range between 0°C and 80°C.
Gain temperature coefficient = 70 uV/(°C fC)

## Slide 5
DEPLETION REGION WIDTH (ISE)
ISETCAD simulations have been performed in order to find out the depletion region width W as a function of the applied voltage.

## Slide 6
DEPLETION REGION WIDTH (ISE)
As expected, the depletion region width W is weakly dependent on the nwell diode voltage biasing (7 um @ Vnwell=0.5 V)

## Slide 7
OPEN ISSUES AND FUTURE ACTIVITIES
PSRR simulations.
Pixel structure (shielding between analog and digital part?).
Almost ready for the analog channel layout (some preliminary block layout have been already performed).
Parallel run with standard resistivity epitaxial layer (strongly recommended by Renato Turchetta): useful to compare the two solutions.
Further ISE TCAD simulations.

## Slide 8
BACKUP SLIDES

## Slide 9
Analog
Digital
Collecting
electrodes
35
35
50
50

## Slide 10
TEMPERATURE VARIATION
This good result has been obtained by exploiting the change in the temperature coefficient in both p and nMOS Id-Vgs characteristics.
MP1 operates in Vgs<0.65 V, while MN1 and MN2 in Vgs>0.65 V. The reduction of MP1 │Vth│ is compensated by Va increasing (in case of increasing temperature, and vice versa), keeping Imir almost constant.