## Slide 1: Performance of the ALICE Inner Tracking System and studies for the upgrade
Giacomo Contin
Universita’ degli Studi di Trieste & INFN Sezione di Trieste
On behalf of the ITS collaboration in the ALICE experiment at LHC

## Slide 2: Summary
System overview and tasks
Hardware features
Physics performance in p-p and Pb-Pb
Outlook on the ITS upgrade plans

## Slide 3: The ALICE experiment
Dedicated heavy ion experiment at LHC
Study of the behavior of strongly interacting matter under extreme conditions of high energy density and temperature
Proton-proton collision program
    Reference data for heavy-ion program
    Genuine physics (momentum cut-off < 100 MeV/c, excellent PID, efficient minimum bias trigger)
Barrel Tracking requirements
Pseudo-rapidity coverage |η| < 0.9
Robust tracking for heavy ion environment
  Mainly 3D hits and up to 150 points along the tracks
Wide transverse momentum range (100 MeV/c – 100 GeV/c)
  Low material budget (13% X0 for ITS+TPC)
  Large lever arm to guarantee good tracking resolution at high pt
PID over a wide momentum range
Combined PID based on several techniques: dE/dx, TOF, transition and Cherenkov radiation

## Slide 4
4
Detector:
Size: 16 x 26 meters
Weight: 10,000 tons
Collaboration:
> 1000 Members > 100 Institutes > 30 countries
ALICE
Central Barrel
2 p tracking & PID
Dh ≈ ± 1

## Slide 5: The ALICE Inner Tracking System
The ITS tasks in ALICE
Secondary vertex reconstruction (c, b decays) with high resolution
  Good track impact parameter resolution < 60 µm (rφ) for pt > 1 GeV/c in Pb-Pb
Improve primary vertex reconstruction, momentum and angle resolution of tracks from outer detectors
Tracking and PID of low pt particles, also in stand-alone
Prompt L0 trigger capability <800 ns (Pixel)
Measurements of charged particle pseudo-rapidity distribution
  First Physics measurement both in p-p and Pb-Pb
Detector requirements
Capability to handle high particle density
Good spatial precision
High efficiency
High granularity (≈ few % occupancy)
Minimize distance of innermost layer from beam axis (mean radius ≈ 3.9 cm)
Limited material budget
Analogue information in 4 layers (Drift and Strip) for particle identification in 1/β2 region via dE/dx
ITS: 3 different silicon detector technologies
Strip Drift Pixel

## Slide 6: The ITS parameters
Accurate description of the material in MC
v
v
v
v

## Slide 7
Half-stave
2 layers of pixels grouped in 2 half barrels mounted face to face around the beam pipe
Half-barrel: outer surface
beam pipe
≈ 1200 wire-bonds
Total surface: ~0.24m2
Power consumption ~1.4kW
Evaporative cooling C4F10
Operating at room temperature
Fast two-dimensional readout (256µs)
High efficiency (> 99%)
L0 trigger capability
Material budget per layer ~1% X0
SPD - Silicon Pixel Detector

## Slide 8: SDD - Silicon Drift Detector
Carbon fiber support
Cables to power supplies and DAQ
Cooling (H2O) tubes
SDD Barrel
HV supply
 LV supply
Commands
Trigger
 Data
Front-end electronics (4 pairs of ASICs)
Amplifier, shaper, 10-bit ADC, 40 MHz sampling
Four-buffer analog memory

## Slide 9: SSD - Silicon Strip Detector
Sensor:
double sided strip:
768 strips 95 um pitch
P-side orientation 7.5 mrad
N-side orientation 27.5 mrad
Hybrid:identical for P- and N-side
Al on polyimide connections
6 front-end chips HAL25
water cooled
carbon fibre support
module pitch: 39.1 mm
Al on polyimide laddercables
End ladder electronics

## Slide 10: Tracking strategy and performance
“Global”
Seeds in outer part of TPC @lowest track density
Inward tracking from the outer to the inner TPC wall
Matching the outer SSD layer and tracking in the ITS
Outward tracking from ITS to outer detectors  PID ok
Inward refitting to ITS  Track parameters OK
“ITS stand-alone”
Recovers not-used hits in the ITS layers
Aim: track and identify particles missed by TPC due to pt cut-off, dead zones between sectors, decays
  pt resolution <≈ 6% for a pion in pt range 200-800 MeV/c
  pt acceptance extended down to 80-100 MeV/c (for )
pt resolution
TPC-ITS prolongation efficiency

## Slide 11: Vertex reconstruction
Vertex from SPD tracklets
Procedure:
“SPD Vertex” from all possible pairs of 2 aligned hits, in a fiducial window (in φ, η)
“SPD tracklet” defined by a pair of hits aligned with the reconstructed vertex
Used to:
Monitor the interaction diamond position quasi-online
Initiate barrel and muon arm tracking
Measure charged particle multiplicity
High efficiency & poorer resolution
Vertex from reconstructed tracks
Procedure:
More accurate second reconstruction of interaction vertex from tracks in the barrel
Used to:
Reconstruct secondary vertices
Estimate the vertex resolution
Poorer efficiency & high resolution
Vertex spread distribution in p-p: comparison of the two methods
The asymptotic limit estimates the size of the luminous region, seen for the vertices reconstructed with tracks.
Notes: Selection of charged particles with pt > 50 MeV/c
The asymptotic limit estimates the size of the luminous
region, seen for the vertices reconstructed with tracks
(filled markers).
The resolution is extrapolated
for most central (5%) Pb-Pb
collisions (orange box).

## Slide 12: Vertex reconstruction: Resolution
Vertex resolution estimation in Pb-Pb
Method to evaluate resolution on the vertex position:
The track sample is randomly divided into two
A primary vertex is reconstructed for each of the sub-sample
The resolution is extracted from the  of the distribution of the residual between the two vertices
The resolution is extrapolated for most central (5%) Pb-Pb collisions
Vertex resolution in Pb-Pb collisions at √s = 2.76 TeV as a function of half of the tracklets multiplicity of the event
Notes: The asymptotic limit estimates the size of the luminous
region, seen for the vertices reconstructed with tracks
(filled markers).
The resolution is extrapolated
for most central (5%) Pb-Pb
collisions (orange box).

## Slide 13
Primary
Vertex
B
e
X
d0
rec. track
ITS Performance: Impact parameter resolution
The transverse impact parameter in the bending plane: d0(rφ) is the reference variable to look for secondary tracks from strange, charm and beauty decay vertices
Impact parameter resolution is crucial to reconstruct secondary vertices : below 75 µm for pt > 1 GeV/c
Good agreement data-MC (~10%)
The material budget mainly affect the performance at low pt (multiple scattering)
The point resolution of each layers drives the asymptotic performance
ITS standalone enables the tracking for very low momentum particles (80-100 MeV/c pions)
Pb-Pb
Notes: in the bending plane: d0(rφ)

## Slide 14
Impact parameter in p-p, global and ITS standalone
p-p
p-p
p-p
< 100 MeV/c
< 100 MeV/c
p-p

## Slide 15: ITS Performance: Particle Identification
The dE/dx measurement:
Analogue read-out of four deposited charge measurements in SDD & SSD
Charge samples corrected for the path length
Truncated mean method applied to account for the long tails in the Landau distribution
The PID performance:
PID combined with stand-alone tracking allows to identify charged particles below 100 MeV/c
p-K separation up to 1 GeV/c
K- separation up to 450 MeV/c
A resolution of about 10-15% is achieved
p-p
p-p
Pb-Pb

## Slide 16
ITS Upgrade Physics Motivations and Simulations Studies
The main physics goals for the ITS upgrade:
    improve the charmed baryonic sector studies
    access the exclusive measurement of beauty hadrons
They can be achieved by:
    improving the impact parameter resolution by factor 2-3 to identify short displaced secondary vertices
    implementing a topological trigger functionality
    exploiting PID in the trigger down to lower pt
Upgrade simulation
Current ITS
No signal
Simulations with different ITS parametrizations

## Slide 17
Reduce beam-pipe radius from 30 mm to ~20 mm
Add a Layer 0 at ~20-22 mm radius (now SPD1 at 39 mm)
Reduce material budget in the first layers from 1.1 to 0.5% X0
    Reducing mass of silicon, power and signals bus, cooling, mechanics
    Using Monolithic Pixels
Reduce the pixel size to the order of 50 x 50 µm2 (425 x 50 µm2 at present)
    Main improvement in z
    Main impact on medium / high pt particles
Reduce the number of detector technologies
    3 pixel layers followed by 3-4 pixel/strip layers
    homogeneous output data format/read-out system
Trigger capability (L2 ~ 100us): topological trigger, fast-OR and fast-SUM
ITS Upgrade - Technical goals

## Slide 18
Considered detector technologies:
Hybrid pixels
    100 µm sensor + 50 µm ASIC
    30 µm x 100 µm pixels
Monolithic pixels
    50 µm ASIC
    20 µm x 20 µm pixels
Silicon strips
    half-length strips
    ADC on-chip
… to be implemented in view of the 2017-2018 LHC shutdown!
ITS Upgrade - Technology Implementation
New design advantages:
occupancy ~ 50%  lower radii
better ambiguity resolution
increased S/N ratio  better PID
digital output and faster read-out
Requirements:
increased spatial resolution
readout time < 50 µs
radiation tolerant (2 Mrad, 2x1013 neq)
low power design (250 mW/cm2)
minimized material budget

## Slide 19: Conclusions
The ALICE Inner Tracking System performance is well in agreement with the design requirements
Track and vertex reconstruction is in good agreement with Monte Carlo simulations
The achieved impact parameter resolution allows to reconstruct the charmed decay secondary vertices
Standalone capability allows to track and identify charged particles with momenta down to 100 MeV/c
The studies for a possible upgrade to improve the physics performance of the ITS are in an advanced stage

## Slide 20: Thanks for your attention

## Slide 21: Backup slides

## Slide 22: SDD calibration
SDD at nominal resolution

## Slide 23
Calibration
The measured intrinsic noise of the 2.6 million SSD channels is used to:
assess the detector efficiency
guarantee the required signal-to-noise ratio
monitor the SSD stability
Cluster charge distribution measured from collision data with all the SSD modules
the gain can be calibrated at the module level
Bad Channel Map
Intrinsic noise: time evolution
Online Calibration
Gain map tuning: after the calibration, the MPVs are stable within a few %
SSD calibration

## Slide 24: Centrality
2.8<h<5.1
-3.7<h<-1.7