Overview
Performance of the ATLAS Liquid Argon Endcap Calorimeter in Beam Tests
Pavol Strizenec (IEP SAS Kosice)
on behalf of ATLAS LAr Endcap Group
Outline:
  - Setup description and data measured
  - MC description
  - Basic performance for electrons
  - Basic performance for pions
  - Noise cuts study
  - Conclusions
Tested part position
P. Strizenec
Calor 2008, Simulation Session, 29.5.2008

---
Setup:
  - Combined test of three LAr detectors in ATLAS forward region
  - Quite complicated area – crack between EM/HAD endcap and forward detector
on 2D view of calorimeters the tested region is marked by red line
one Module0 of EMEC Inner Wheel (lead, accordion shape), readout segmentation 0.1 x 0.1 ( x )
one quadrant in phi of HEC (parallel flat copper plates), readout segmentation 0.1 x 0.1 in outer and 0.2 x 0.2 in inner wheel
one quadrant in phi of FCAL (EM part copper, HAD part tungsten alloy with cylindrical electrodes, parallel to beam), readout segmentation not projective, ~ 0.2 x 0.2
dead materials between calorimeters and in front of FCAL close to the ATLAS case (no beam pipe...), trying to be as close as possible to “nominal” situation
setup placed in H1 cryostat in CERN North Hall, using the H6 beam line
slanting a setup to be “projective” at  ~ 2.8
Tile barrel
Extended Tile
EM barrel
HEC
FCAL
EMEC

---
Limited acceptance, because of space constraint in H1 cryostat
Warm and Cold Tail Catchers are TB specific devices to help identify a longitudinal leakage
HEC 1,2
EMEC Inner
Warm TC: Iron+Scintillator
Cold TC: Copper plates+ LAr
Beam
FCAL ColdCone
FCAL 1,2
Cold TC
Warm TC
Cryostat

---
Cold electronics
HEC 1,2
Excluder
EMEC Inner
Beam
Excluder
FCAL ColdCone

---
Data:
  - Readout was done with various prototypes and versions -1 of final ATLAS electronics, therefore parameters not directly transferable to a data taking
  - Various scans were performed (e-, pi, position (x- and y-), energies 6-200GeV in fixed points)
  - Electronics calibration in a similar way as envisaged for ATLAS
Noise:
  - Some problem with prototype of HEC Power supply found, source of coherent noise, but it was possible partially to correct it
  - noise is measured from empty calo cells, or using estimate from first reading sample x suppression factor (taking into account suppression done by filtering used for signal amplitude reconstruction)
  - also typical cluster noise shown for EM and had. clusters
Cell noise [MeV]
Estimate [MeV]
Noise [MeV]
Cluster EM
EMEC2
80
80
80
EMEC, 0.15
  550
1300
EMEC3
60
60
EMEC, 0.25
HEC0
200
190
FCAL, 0.25
1100
HEC1
280
250
Noise [MeV]
Cluster HAD
EMEC/HEC
HEC2
460
420
EM/HEC, 0.3
4200
FCAL
240
240
EM/HEC, 0.5
7100
FCAL1
180
FCAL2
FCAL, 0.3
3100
370
315
FCAL, 0.5
6700

---
MC:
  - Most simulation done so far with G4 7.1p01, only recently switched to a newer versions (coupled to a ATLAS releases used for analysis), not final results yet
  - Physics list used QGSP_GN and QGSP_BERT, the second one used for comparison with data – better description, specially of shower shape
  - to check the MC geometry – vertical scan with electrons
  - open symbols are MC on all following plots
known weak channel in FCAL readout

---
Basic performance for electrons:
Electron linearity in standard impact points
cone clusters - clear visible that R<0.15 does not collect enough signal
cone 0.25 cluster very close to MC expectation, 0.15 shows difference at low energies
“topo 633” topological cluster (more about topological clustering in a talk of G. Pospelov) expected behaviour – comparable with cone+3 cut
3x3 and 5x5 are standard towers used in EM calo for e/ reconstruction
EMEC/HEC
FCAL

---
Basic performance for electrons:
Electron resolution for standard points
cone and 3x3 clusters - easy to subtract noise
topo 633 cluster - average noise subtracted
EM 3x3 cluster with a "standard" EM corrections – gives the best result
FCAL MC is worse than data – but it's much closer to data with newer G4 (new multiple scattering ?) and ATLAS sw. release
EMEC/HEC
FCAL

---
Basic performance for pions:
Total
Y-scan of 200 GeV pions over a crack
reasonably well described
position of standard impact points showed
MC is QGSP_GN, e.m. scale is fixed with electrons
hint, that early showering in MC is present here
EM layers
HAD layers

---
Basic performance for pions:
Linearity of pions in two standard impact points (e.m. scale, MC is QGSP_BERT)
cone clusters R<0.4, 0.5
topo cluster 420 and R=0.5 with 2 cell cut
reasonably well described for higher energies and larger cluster
discrepancy seen for lower energies
EMEC/HEC
FCAL

---
Basic performance for pions:
Energy resolution of pions in two standard impact points (MC is QGSP_BERT)
cone clusters R<0.3, 0.5
noise subtracted in data - event-by-event estimated for cone, no noise in MC
one calibration constant per layer in cone
MC is close for constant term and too optimistic for sampling term - different to HEC TB, there were a good description with G4. (Both QGSP_GN and QGSP_BERT physics lists shows this difference.)
EMEC/HEC
FCAL

---
Lateral shower profile:
Total
X-scan of 60 GeV pions over a EMEC/HEC region (data are full, MC open symbols)
each profile is energy summed in one phi-bin
reasonably well described, small difference on far tails
MC is QGSP_BERT, still some hint on early showering (EM part slightly more energy on tails, HAD slightly less)
EMEC
HEC

---
Noise cuts analysis
scale and resolution for electrons, , -3 means no cut at all:
resolution optimal ~ 3  cell cut
EMEC/HEC
193.08 GeV
120.0 GeV
 60.0 GeV
 30.0 GeV
 10.0 GeV
 6.0 GeV
beam energies

---
Noise cuts analysis
scale and resolution for pions (e.m. scale):
above 0  resolution only worser
EMEC/HEC
 200.0 GeV
 150.0 GeV
 120.0 GeV
  60.0 GeV
  40.0 GeV
beam energies

---
Conclusions:
  - Performance of ATLAS LAr Endcap calorimeters in the crack region (2.5 < |  | < 4.0 was studied in beam test, and is basically understood
  - This test closes the extensive program of beam-testing the ATLAS LAr endcap calorimeters modules, started already at 1996
  - Standard parameters of noise, response and resolution extracted
  - Expected parameters for electrons seen, well compared with MC
  - For pions MC does not describe data perfectly (larger response and better resolution) at low energies, quite good description at higher energy
  - Limited acceptance makes results very sensitive to a proper shower description in MC, here QGSP_BERTINI physics list gives better results (not all possible physics list tested yet)
  - First paper accepted for publication in NIM A (describing in more details what was presented here)
  - Next paper will follow, containing the results presented by next speakers