## Slide 1: Diagnostics for Laser-Wakefield Accelerators
Malte C. Kaluza
Institute of Optics and Quantum Electronics, FSU Jena, Germany
Helmholtz-Institute Jena

## Slide 2: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook

## Slide 3: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook

## Slide 4: Laser Wakefield Acceleration of Electrons: Principle
Acceleration of electrons in a (laser-driven) plasma wave
Injection of background electrons into accelerating phase of the plasma wave
A. Pukhov et al., APB 74, 355 (2002)

## Slide 5: Laser Wakefield Acceleration of Electrons @ JETI: Setup
Setup of a LWFA experiment @ JETI:
Target
Magnet
Lanex
Camera
Few-cycle probe
M. Schnell, MCK et al., PRL 108, 075001 (2012) S. Kuschel, MCK et al., PRL 121, 154801 (2018)
Gas-Jet
Gas-Cell
M. Schwab, MCK et al., APL 103, 191118 (2013) D. Adolph, MCK et al., APL 110, 081105 (2017) I. Tamer, MCK et al., Opt. Expr. 28, 19034 (2020)
B. Landgraf, MCK et al., RSI 82, 083106 (2011) A. Adelmann, MCK et al., Appl. Sci. 8, 443 (2018)

## Slide 6: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
energy spectrum:
  energy of (mono-energetic?) peak
  background?
charge
pulse duration
source size
divergence
pointing (stability)
…

## Slide 7: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 8: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 9: Laser Wakefield Acceleration of Electrons: Optical probing
transverse optical probing
gas-jet
main pulse
electrons
X-rays,…

## Slide 10: Laser Wakefield Acceleration of Electrons: Optical probing
imaging lens
probe pulse
transverse optical probing
gas-jet
main pulse
electrons
X-rays,…

## Slide 11: Laser Wakefield Acceleration of Electrons: Optical probing
 Rotation of probe polarization:
 measure frot to deduce B-field distribution!
Transverse probing of B-fields in under dense plasma with linearly polarized probe pulse:
when  different h for circularly polarized probe-components (“Faraday-effect”)
J. A. Stamper et al., PRL (1975)

## Slide 12: Laser Wakefield Acceleration of Electrons: Optical probing
MCK et al., PRL 105 115002 (2010)

## Slide 13: Laser Wakefield Acceleration of Electrons: Optical probing
polarogram 2
polarogram 1
Electron bunch length: z = 4 µm
FWHM= (62) fs, RMS= (2.50.9) fs
A. Buck, MCK et al., Nature Physics 7, 543 (2011)
first experiment @ LWS10 (MPQ Garching): 5-fs main- and probe pulses

## Slide 14: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 15: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 16: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Self focussing
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 17: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Self focussing
Injection
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 18: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Injection
Self focussing
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 19: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Injection
Self focussing
Acceleration
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 20: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Injection
Self focussing
Acceleration
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 21: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Injection
Self focussing
Acceleration
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 22: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 23: Laser Wakefield Acceleration of Electrons: Betatron Radiation
Acceleration of electrons in plasma wave
Fresnel-diffraction pattern at wire edges: rx-ray = (1.8  0.3) µm
electron source size: relectron bunch = (1.6  0.3) µm
M. Schnell, MCK et al. Phys. Rev. Lett. 108, 075001 (2012)

## Slide 24: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 25: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Non-invasive diagnostic of intensity evolution during interaction based on relativistic electron cyclotron resonance
Probe wave length and main-pulse intensity dependent probe-pulse absorption!
Signature of intensity evolution of main pulse during its passage through the plasma!
M. B. Schwab, MCK et al. Phys. Rev. AB 23, 032801 (2020)

## Slide 26: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
High-resolution images of plasma wave:
  Formation and evolution of e-bunch -> e-pulse duration in the plasma
Visualize evolution of accelerator structure (plasma wave)
  visualize point of injection of e-bunch -> acceleration length -> peak energy
Detection of betatron radiation -> source size of electron pulse
Measure intensity evolution of driving main pulse via RECR
  Indirect measurement of acceleration fields -> peak energy of e-bunch
Visualize transverse scattering of laser pulse -> spatio-temporal couplings in main pulse -> e-beam direction/steering

## Slide 27: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
C. Zepter, MCK et al. Phys. Rev. Research 5, L012023 (2023)
Observation of Stimulated Raman Sidescattering, diagnostic for spatio-temporal couplings of main pulse (PFT) and electron beam steering

## Slide 28: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook
When electron pulse cannot be measured non-invasively
  Deduce/estimate e-beam parameters from other parameters (which can be measured non-invasively)
  Possible, when exact correlations between parameters are known (not yet!)
  Use machine-learning algorithms + Bayesian optimization models to find such correlations

## Slide 29: Motivation and Outline
(One of the) Central goal(s) of EuPRAXIA:
  Realize a free-electron laser based on electron pulses from a LWFA
What are the requirements to reach this goal?
  Provide a stable/reliable/controllable GeV-class LWFA-driven electron source
How does a LWFA work?
Which e-beam parameters are essential?
  How are they correlated with accelerator structure (plasma wakefield)?
  How can they be measured?
Beyond existing (and possible) diagnostics:
  machine-learning algorithms, Bayesian optimization models
Summary and outlook

## Slide 30: Summary and Outlook
LWFA-based FEL as one of the central goals of EuPRAXIA seems within reach
essential for its optimization:
  high-resolution diagnostics for
    driving laser,
    plasma/accelerator structure,
    particle pulses,
  find correlations between different parameters also using machine-learning methods
Feedback loops for stabilization of laser and particle pulses.
Thank you for your attention!

## Slide 31: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Generation of few-cycle probe pulses @ JETI via frequency broadening
probe = 5.9 fs
JETI input pulses: 32 fs, ~1 mJ
(5.90.4) fs @ 300 µJ
JETI input pulses: 32 fs, ~1 mJ
(5.90.4) fs @ 300 µJ, (2.80.4) fs @ 200 µJ
shadowgraphy, Faraday-rotation, interferometry, … possible
M. Schwab, MCK et al., Applied Physics Letters 103, 191118 (2013) D. Adolph, MCK et al., Applied Physics Letters 110, 081105 (2017)

## Slide 32: Laser Wakefield Acceleration of Electrons: Optical probing
Polarimetry: Visualization of e-bunches via B-fields
Variation of delay between pump and probe pulse:  Evolution of e-pulse generation!
First online observation of e-bunch generation!
A. Buck, MCK et al., Nature Physics 7, 543 (2011)

## Slide 33: Laser Wakefield Acceleration of Electrons: Optical probing
Polarimetry: Visualization of e-bunches via B-fields
Variation of delay between pump and probe pulse:  Evolution of e-pulse generation!
First online observation of e-bunch generation!
A. Buck, MCK et al., Nature Physics 7, 543 (2011)
Shadowgraphy: Visualization of the plasma wave

## Slide 34: Laser Wakefield Acceleration of Electrons: Optical probing
Shadowgraphy: Visualization of the plasma wave
Variation of plasma density  change of plasma wave length
A. Buck, MCK et al., Nature Physics 7, 543 (2011)

## Slide 35: Laser Wakefield Acceleration of Electrons: Optical probing
A. Buck, MCK et al., Nature Physics 7, 543 (2011)
Polarimetry + Shadowgraphy:
Measurement of e-bunch position within the plasma wave:
e-pulse is indeed accelerated within the 1st wave period!

## Slide 36: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Elongation of 1st plasma wave period starts before injection of electrons.
no „beam loading“ but main pulse amplification.
λp @ ne=1.6x1019 cm-3
„well behaved“
„beam loading“ dominated
„single bubble“ regime
„multi bubble“ regime
wavebreaking radiation
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)

## Slide 37: Laser Wakefield Acceleration of Electrons @ JETI: Optical probing
Elongation of 1st plasma wave period starts before injection of electrons.
no „beam loading“ but main pulse amplification.
λp @ ne=1.6x1019 cm-3
„well behaved“
„beam loading“ dominated
„single bubble“ regime
„multi bubble“ regime
wavebreaking radiation
A. Sävert, MCK et al. Phys. Rev. Lett. 115, 055002 (2015)