## Slide 1: Using Cold Target Recoil Ion Momentum Spectroscopy for Polarization Characterization of SASE Pulses
Antoine Sarracini :: Postdoc | Maloja | SwissFEL :: Paul Scherrer Institute
EuPRAXIA Electron & Photon Diagnostics
June 13 2023

## Slide 2: The ATHOS Beamline at SwissFEL
Up to 3.4 GeV linac, 16 APPLE X undulators
250 – 1800 eV soft X-ray beamline
80 fs pulse duration @ 100 Hz with special modes (short pulse 20 fs, two color X-ray pump-probe up to 500 fs delay)
Maloja: modular atomic, molecular and nonlinear X-ray physics

## Slide 3: APPLE X Soft X-Ray Undulators
APPLE X
φ1
φ2
φ3
φ4
r1
r2
r3
r4
Symmetric and compact 2m long design
Can arbitrarily tune sinusoidal electron trajectory by independent adjustment of phase and gap of magnet arrays
  4x translation degrees of freedom
  4x radial degrees of freedom
Arbitrary polarization control
M. Calvi et al. J. Synchrotron. Rad. 2017

## Slide 4: Polarization Control with APPLE X
Diagonal magnet arrays shifted to produce different polarizations
Linear Polarizations:
  Horizontal :
  Vertical :
  Other : Shift arrays in opposite direction
Circular Polarizations:
  Fully circular:
  Elliptical:
C. Schmitz-Antoniak. Rep. Prog. Phys. 2015

## Slide 5: Polarization Control with APPLE X
M. Calvi. 2021

## Slide 6: Measuring Polarization at XFEL Facilities
“Cookiebox” e--TOF
  16 TOF spectrometers arranged radially
  Developed at Petra III - P04 beamline
  In use at Eu-XFEL, LCLS, FLASH, FERMI
Silicon channel-cut crystal
  Bragg reflections from crystal select polarization
  Rotatable analyzer
  Photodiodes measures X-rays downstream of analyzer
  Tested at Eu-XFEL
P. Walter et al. J. Synchrotron. Rad. 2021
K. S. Schultze et al. Phys. Rev. Res. 2022

## Slide 7: Measuring SASE Polarization: COLTRIMS
Supersonic Gas Jet
Ionizing Radiation
Electron Detector
Ion Detector
Use XFEL beam of varying polarization to ionize He gas target
Measure angular distribution of photoelectron momentum
  Cold Target Recoil Ion Momentum Spectroscopy (COLTRIMS)
Fit photoelectron momentum distribution to dipole & extract angle
H. Schmidt-Böcking et al. Ann. Phys. 2021

## Slide 8: Cold Target Recoil Ion Spectroscopy Basics
Momentum imaging technique
  Δp < 0.1 a.u. momentum resolution and 4π solid angle collection
Uses time-of-flight and ion / e- position detection to reconstruct momenta in ionization / fragmentation processes
  4π solid angle collection by confining ions and electrons to detector areas
  Ions accelerated to detector using E-field
  Electrons confined to detector area using B-field
Resolution limited by gas velocity spread (temperature)
  Supersonic gas jet into vacuum cools target to < 1K
R. Doerner, Uni. Frankfurt.

## Slide 9: The COLTRIMS Detector at Maloja
Slow ion detection on long side (photoemission)
Fast ion detection on short side (Coulomb explosion)
No direct electron detection (yet)
I. Swiderska MSc Thesis. 2022

## Slide 10: Momentum Reconstruction Process
MCP Signal
Delay Line Signal
L. Fechner PhD Thesis. 2014
K. Schnorr. PhD Thesis. 2014

## Slide 11: The COLTRIMS Detector at Maloja
I. Swiderska MSc Thesis. 2022

## Slide 12: Angular Dependence of Photoelectron Momenta
Angular dependence comes from initial angular momentum of electron in atom
Angular dependence of cross section for single photon ionization:
  Angle between electric field vector and electron momentum
  Asymmetry parameter, depends on photon energy

## Slide 13: Angular Dependence of Photoelectron Momenta
Convert to Polar Coordinates
Integrate &
Fit to Dipole
Angular distribution of emitted photoelectrons described by:
– Partial cross-section
– Asymmetry parameter
– 2nd Order Legendre Polynomial

## Slide 14: Undulator Scan
Model for polarization of beam () vs undulator phase parameter ():

## Slide 15: Circular and Elliptical Polarizations
Ellipticity were also characterized by fitting to perpendicular dipoles:
Ratio of B/A gives degree of ellipticity
  B/A = 0 is purely linear
  B/A = 1 is purely circular
B/A = 0.18

## Slide 16: Summary
Arbitrary linear, elliptical and circular polarization of XFEL beam achieved in Athos by SwissFEL undulator / operations groups
Polarizations characterized at Maloja endstation using COLTRIMS
Excellent agreement with theoretical model
Nice example of collaboration between machine development groups and experimental endstations (more in the future)

## Slide 17: Wir schaffen Wissen – heute für morgen
Many thanks to:
Maloja Group
Undulator Group
Operations Group
Science IT Group
Everyone who contributed!