## Slide 1: Preclinical studies with radioactive ion beams: the BARB project
Tamara Vitacchio*1, Olga Sokol1, Daria Boscolo1, Anggraeini Puspitasari1,2, Julius Oppermann1, Walter Tinganelli1, Marco Durante1,3.
*lead presenter
1st Meeting
18 - 20 October 2023

## Slide 2: Context
Radiobiological validation in a preclinical context
→ From the physics model to the human health application
Physicists´ mouse
Biologists´ mouse
18 October 2023

## Slide 3
The potential application of radioactive ion beams (RIBs) of heavy ions in the field of radiotherapy
Study I:
Tumor margin reduction with RIBs combined with PET
Study II:
RIBs as in vivo tracers for vasculature damage
BARB – Biomedical Application of Radioactive Ion Beams
18 October 2023

## Slide 4: Aims of the project - 1
Produce radioactive (ß+-emitters) ion beams (10C, 11C, 15O) at high intensities
Real-time beam monitoring with a new gamma-PET hybrid detector Improved image-guided treatment
Treat a small tumour in a murine model with sub-millimeter precision
Less damage to healthy tissue, while maintaining the same tumour control
Study I:
Tumor margin reduction with 11C
Model: tumor close to the cervical area of the spinal cord (OAR)
18 October 2023
With range verification
(Reduced tumor margins)
Without range verification
(Normal tumor margins)

## Slide 5: Aims of the project - 2
Method: measure the PET signal washout online, to check eventual changes in the vascular system of the tumor induced by high radiation doses
Study II:
RIBs as in vivo tracers for vasculature damage
Aim: To investigate the correlation between vascular permeability and tumor control
Day -21 Day 0 Day +28
Tumor cells injection RIB irradiation & PET signal monitoring Animal monitoring
18 October 2023

## Slide 6
Experiments timeline
February 2024
11C Beamtime
Irradiation with range verification
Irradiation without range verification
Vasculature damage studies
Aim: demonstrate the potential application of RIBs in radiotherapy
November 2023
X- rays dose escalation study
Doses: 0 Gy (control), 5 Gy, 10, 15, 20 Gy)
Finding the dose leading to tumor control
Finding the dose leading to paralysis
So far…
Tumor model development studies
→ Osteosarcoma tumor in the cervical area of the spinal cord (organ at risk)
Paralysis development and assessment protocols
Post-irradiation follow-up protocol
Vasculature mapping studies
18 October 2023

## Slide 7
Establishment of the osteosarcoma tumor model
Created with BioRender.com
18 October 2023

## Slide 8
Results – Tumour growth rate
Week 1 Week 2 Week 3 Week 4
µCT scans, resolution 100 µm
2 weeks
3 weeks
Slicer reconstructions from µCT
18 October 2023
Chart: Tumor growth curves
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Mouse 1 | 0 | 0.018661 | 0.026522 | 0.038001 | 0.064141
Mouse 2 | 0 | 0 | 0.02441 | 0.031039 | 0.053205
Mouse 3 | 0 | 0.014137 | 0.04557 | 0.057881 | 0.066759
Mouse 4 | 0 | 0.011494 | 0.063499 | 0.066759 | 0.09031
Mouse 5 | 0 | 0.029835 | 0.031039 | 0.031815 | 0.075038
Mouse 6 | 0 | 0.025418 | 0.091923 | 0.099353 | 0.28865
Mouse 7 | 0 | 0.024429 | 0.025108 | 0.032264 | 0.077924
Mouse 8 | 0 | 0.026522 | 0.027239 | 0.028731 | 0.034348

## Slide 9
Tumour
Kidney
Resolution: 10 µm
Results – Vascupaint perfusion: 3D maps of vasculature
7,5 mm
10 mm
18 October 2023
Parameters:
Vessel volume | [mm3]
Density | [%]
Number | [mm-1]
Thickness | [mm]
Separation | [mm]
Connectivity | [mm-3]
Surface area | [mm2]

## Slide 10
Post-irradiation follow-up: paralysis
If the spinal cord is damaged during irradiation, the signal can´t be transmitted from the brain to the limbs
The gait of the animals will be affected (speed, stride length and other parameters)
Paralysis is expected in the forelimbs, with a reduction in the grip strength of the animals
Created with BioRender.com
Adapted from: Paw-Print Analysis of Contrast-Enhanced Recordings (PrAnCER): A Low-Cost, Open-Access Automated Gait Analysis System for Assessing Motor Deficits
18 October 2023

## Slide 11: Preliminary results – Gait analysis
The PrAnCER software (custom version) measures for how long a paw is in contact with the floor and it contours it, distinguishing the four different paws
HL
FL
HR
FR
FL
HL
FR
HR
Legend: HL (hind left), FL (front left), HR (hind right), FR (front right)
An “ink track” is produced
The gait of the animals can be visualized and neatened (e. g. if the tail is present in the field of view)
18 October 2023

## Slide 12: Preliminary results – Gait analysis
Normally behaving mouse
Mouse with stereotypical behaviour
HL
FL
HR
FR
FL
HL
FR
HR
HR
HR
FR
FR
FR
HL
HL
FL
FL
Legend: HL (hind left), FL (front left), HR (hind right), FR (front right)
18 October 2023

## Slide 13: Preliminary results – Gait analysis
Intra-mouse variability
(six runs)
Inter-mouse variability
(between three animals)
Name | Gait parameter
Stride Length | Distance between successive contacts of the same paw
Step Length | Distance between successive contacts of contralateral front or hind paws along the axis of the direction of motion
Stance Duration | The length of time a paw was in contact with the ground
Chart: Stride Length (Mouse 1)
| a | b | c | d | e | f
Stride Length | 6.2802 | 4.7363 | 5.3066 | 6.0702 | 6.1914 | 5.7812
Chart: Step Length (Mouse 1)
| a | b | c | d | e | f
Step Length | 2.8904 | 2.5342 | 2.7143 | 2.8617 | 3.1851 | 2.8453
Chart: Stance Duration (Mouse 1)
| a | b | c | d | e | f
Stance Duration | 0.021494 | 0.046058 | 0.064481 | 0.027635 | 0.036846 | 0.046058
Chart: Stride Length
| Mouse 1 | Mouse 2 | Mouse 3
Stride Length | 5.7277 | 5.3721 | 5.2547
Chart: Step Length
| Mouse 1 | Mouse 2 | Mouse 3
Step Length | 2.8385 | 2.9264 | 2.9829
Chart: Stance Duration
| Mouse 1 | Mouse 2 | Mouse 3
Stance Duration | 0.040428 | 0.035618 | 0.085974
18 October 2023

## Slide 14: Histology protocols
If the spinal cord is hit during irradiation, there will be damages that can be visualized via histology sampling
This technique can also show the inner structure of the tumor tissue and the presence of metastasis in the lung
18 October 2023

## Slide 15
Tumor histology useful to confirm the presence or abscence of tumor tissue
Animals will be kept for 6 months
  Osteosarcoma is highly metastatic to the lungs
  The presence of metastases will be monitored on the µCT during the health checks
Tumor
Tumor + Vascupaint
Lung + metastasis
Lung + metastasis
Vessels filled with Vascupaint
Metastases in the lung
Results – Histology of tumors and lungs
Slices of 10 µm
Hematoxylin-eosin staining
10x magnification
50 µm
50 µm
50 µm
50 µm
18 October 2023

## Slide 16: Results – Histology of the spinal cord
4x
20x
Healthy mouse spinal cord
Slices of 10 µm
Masson´s Goldner Staining Kit (Merck)
Subcutaneous
muscle tissue
Vertebral body
Spinal cord
Subcutaneous
fat tissue
Supraspinal process
of vertebra
Epidural space
White matter
Grey matter
200 µm
200 µm
25 µm
18 October 2023

## Slide 17: Expected results from histology
Expected results: differences in the dorsal part of the spinal cord and surrounding tissues (e.g., radiation-induced epidural fibrosis, differences inside in the myelin, radiation-induced necrosis of the bones)
(Masson’s trichrome stain; above, magnification ×40; below, magnification ×400 objective). Abbreviations: D, dura mater; ED, epidural space. Section from the thoracolumbar trasition region of the spine. From Yokogawa et al., 2015
Radiation-induced epidural fibrosis
Grade 0
No fibrosis
Grade 1
Minimum fibrosis
Grade 2
Moderate fibrosis
Grade 3
Severe fibrosis
From https://radiologykey.com/spinal-cord-radiobiology/
C
D
Demyelination after 22 Gy
No irradiation = no demyelination
Radiation-induced demyelination
18 October 2023

## Slide 18: Conclusions and future outlook
The murine tumor model in the proximity of the spinal cord was established
The following endpoints and the respective protocols for the post-irradiation follow-up were identified:
  Tumor control and metastases: caliper, µCT, histology
  Spinal cord damage: gait analysis, grip strength test, histology
  Vasculature damage: perfusion and µCT assessment
X-rays irradiation in November
  Animals will be followed-up for six months for tumor growth and paralysis development
Beamtime with C-ions in February 2024
  Irradiation with range verification
  Irradiation without range verification
  Low-dose and high dose irradiation (PET signal washout)
  Same follow-up of the animals
18 October 2023

## Slide 19
Clinical Radiobiology Group
Group leader: Dr. Walter Tinganelli
Post-docs:
  Dr. Olga Sokol
  Dr. MD. Anggraeini Puspitasari
  Dr. Reema Chowdhury
Technical Assistants:
  Julius Oppermann
  Leonie Hartig
PhD student:
  Tamara Vitacchio
Students:
  Katelin Sherman
  Dennis Fritsche
GSI Biophysics Department - Director: Prof. Dr. Marco Durante
Radiation Physics Group
Dr. Daria Boscolo
Dr. Christoph Schuy
Dr. Uli Weber
LMU Group
Prof. Dr. Katia Parodi
Giulio Lovatti
Acknowledgements
18 October 2023

## Slide 20: Thank you for your attention!
1st Meeting
18 October 2023