## Slide 1
Dosimetric study of lung modulation and motion effects in carbon ion therapy for lung cancer
m.c.martire@gsi.de
Maria Chiara Martire1,2, Olga Sokol1, Kilian Baumann3,4, Klemens Zink4,5,Christian Graeff1,2
1Biophysics, GSI Helmholtzzentrum für Schwerionenforschung, Darmstadt, Germany
2Department of Electrical Engineering and Information Technology, Technical University of Darmstadt, Germany
3Department of Radiotherapy and Radiation Oncology, Philipps-University Marburg, Marburg, Germany
4University of Applied Sciences Giessen, Germany
5Institute of Medical Physics and Radiation Protection
Insights Pisa Workshop 18th – 20th October 2023

## Slide 2
Why 12C ions therapy for lung cancer ?
Inoperable
Metastatic
Radioresistant
Non-Small Cell Lung Cancer
(NSCLC):
Insights Pisa Workshop 18th – 20th October 2023
Effective and precise radiotherapy treatment
Chen et al. Radiation Oncology 2019
Bradley et al., Lancet Oncol., 2015
“74 Gy radiation was not better than 60 Gy, and might be potentially harmful. Treatment-related deaths were more common in the high-dose group”
Photon
Carbon
m.c.martire@gsi.de
normal tissue
target
12C6+
300 MeV/u
photons
20 MV

## Slide 3
Investigate the radio-biological effect on normal tissue cells
Investigate and compare the clinical impact through dosimetric studies
Range and motion related uncertainties INTERPLAY effect
Lung tissue heterogeneities  LUNG MODULATION effect
T. Steinsberger et al., Physica Medica 2021
Insights Pisa Workshop 18th – 20th October 2023
Why 12C ions therapy for lung cancer ?
Lower integral dose
Very sharp dose gradients
Increased biological effectiveness
12C Therapy :
m.c.martire@gsi.de

## Slide 4
Motion related uncertainties – Interplay effect
Active scanned beam
Target motion
ACRF Image X Institute
B. Marchand et al., EPAC 2000
Interplay effect
Insights Pisa Workshop 18th – 20th October 2023
4D dose calculation
From the 4DCT and the optimized 3D plan, a 4D plan is created
To each beam spot a motion state is assigned
4D dose calculation:
  Only tumor motion is considered (perfectrescan plan, interplay neglected)
  Tumor and beam motion considered (interplay plan)
m.c.martire@gsi.de

## Slide 5
Lung tissue heterogeneities – Modulation effect
Clinical CT
Micro-CT image of a porcine lung sample
Resolution ~ 10 μm
Resolution ~ mm
Diameter= 1.80 cm
Diameter = 0.4 mm
Not included in treatment plans optimization!
Larsson-Collerfelrt A., Ph.D. thesis 2007
J. Burg et al Phys. Med. Biol. 2021
Insights Pisa Workshop 18th – 20th October 2023
Trachea
m.c.martire@gsi.de

## Slide 6
Broadened Bragg curve
12C ions
Gaussian modulation function
σ
t
D(z)
Dmod (z)
Pristine Bragg curve
D(z)
⊛
Dmod (z)
Voxelised geometry
(sub-mm voxels randomly assigned to air/lung tissue)
Pore size = d
Ringbaek et al., Phys. Med. Biol. 2017.
Lung tissue heterogeneities – Modulation effect
Mathematical model
Insights Pisa Workshop 18th – 20th October 2023
m.c.martire@gsi.de

## Slide 7
σ
t
  Lung modulation in TRiP98:
  Convolve in each voxel the Gaussian kernel to the pristine Bragg curve
  For biological doses, convolve the Gaussian kernel with the dose-averaged α, β and LET distributions of the unperturbed beam (computational demanding)
  Reproduce the dose degradation (dose calculation)
  Optimize for the lung modulation effect (optimization + dose calculation)
Modulation Power
Lung tissue heterogeneities – Modulation effect
Mathematical model
[mmH2O]
Insights Pisa Workshop 18th – 20th October 2023
  Transfer the modulation effect to rougher structures (2mm CT voxels)
  Material-specific quantity (Lung ~ 208 μm)
m.c.martire@gsi.de

## Slide 8
A. Paz et al., Medical Physics, 2021
Broadening of the primary 12C ions spectra
High-LET particles displaced in depth entails the shift in depth of the RBE maximum
Changes in the biological dose distribution (higher toxicity behind the target)
Target distal edge
Lung tissue heterogeneities – Modulation effect
Radiobiological effect
Insights Pisa Workshop 18th – 20th October 2023
Validation of radio-biological effect through cell survival experiments
m.c.martire@gsi.de

## Slide 9
Assess differences between reference and degraded plan comparing absorbed dose, RBE-weighted dose, RBE and survival
Cell plates position to detect differences maximum
12C unperturbed and degraded plans optimized in TRiP98
Pmod = 208 μm
H2O
(200 mm)
TARGET
Porous material
(100 mm)
5 mm between two adjacent cell plates
(minimum phantom resolution)
Materials & Methods
Insights Pisa Workshop 18th – 20th October 2023
Beam
1. Validation of radio-biological effect with cell survival experiments
Experimental setup
Simulations setup
m.c.martire@gsi.de

## Slide 10
Survival
RBE-weighted dose
Max[ref-deg] 196 mm
Difference
Results
Insights Pisa Workshop 18th – 20th October 2023
1. Validation of radio-biological effect with cell survival experiments
 | 194 | 196 | 198
RBE-weighted dose (Gy) | 0.34 | 0.96 | 0.20
RBE | 0.01 | 0.59 | 0.33
Svv (%) (absolute values) | 5% (52 vs 47) | 18% (84 vs 66) | 6% (86 vs 80)
Max difference’s
depth
-2 mm +2 mm
Differences
Depth (mm)
Setup errors
Phantom resolution
The biological error could cover the physical quantities differences
m.c.martire@gsi.de

## Slide 11
2. Clinical impact investigated with dosimetric study
3 NSCLC 4DCTs data from the Cancer Imaging Archive
Different clinical scenarios are investigated
For each patient the Tumor + 3mm isotropic margins and Lung structure are created
For each patient 5 different plans are optimized and compared :
Plan | 3D | 3D + Lungmod | 3D | 3D + Lungmod | 4D + Interplay | 4D + Perfectrescan
OPTIMIZATION | DOSE CALCULATION
Reference | X |  | X |  |  | 
Lungmod dose | X |  |  | X |  | 
Lungmod opt |  | X |  | X |  | 
Interplay | X |  |  |  | X | 
Perfectrescan | X |  |  |  |  | X
Single field plan, with Tumor + 3mm target and a constant Pmod (208 μm) are optimized
Matherials & Methods
Insights Pisa Workshop 18th – 20th October 2023
Asses and compare the clinical impact of lung modulation and motion effects through dosimetric studies
m.c.martire@gsi.de

## Slide 12
Plan quality assessed and compared through dose distributions, dose volume histograms (DVH) and dosimetric metrics
Dose distribution
DVH
Dosimetric metrics
Target coverage:
D95 ≥ 95% (A)
Dmean ~ 100%
Lung dose:
V20 ≤ 20% (B)
A
B
Matherials & Methods
Tumor
Lung
Insights Pisa Workshop 18th – 20th October 2023
2. Clinical impact investigated with dosimetric study
m.c.martire@gsi.de

## Slide 13
Tumor in the middle lobe
Tumor volume = 80 cc
Tumor Δmotion = 3.8 mm
Depth in lung tissue ~ 7cm
Tumor in the upper lobe
Tumor volume = 18 cc
Tumor Δmotion = 0.7 mm
Depth in lung tissue ~ 3cm
P1
P2
P3
Tumor in the lower lobe
Tumor volume = 128 cc
Tumor Δmotion = 8 mm
Depth in lung tissue ~ 10cm
Lung modulation effect depends on:
Distance traversed by particles into the lung
Tumor dimension
Tumor position
Motion effect depends on:
Breathing motion aplitude (Δmotion)
Patient Data
Insights Pisa Workshop 18th – 20th October 2023
Δmotion = MotionEnd-Inhale – MotionEnd-Exhale
2. Clinical impact investigated with dosimetric study
m.c.martire@gsi.de

## Slide 14
Results – Lung modulation uncertainties
Reference plan
Degraded plan
Re-optimized plan
Tumor + 3mm
Tumor +3mm
Tumor + 3mm
Lung
Lung
Lung
Heart
P1 | Ref | Degraded | Re-optimized
Dmean (%) | 99.8 | 98.4 | 99.8
P2 | Ref | Degraded | Re-optimized
Dmean(%) | 100 | 98.8 | 100
P3 | Ref | Degraded | Re-optimized
Dmean(%) | 100 | 98.5 | 100
Insights Pisa Workshop 18th – 20th October 2023
2. Clinical impact investigated with dosimetric study
m.c.martire@gsi.de

## Slide 15
P3
Reference plan
Perfectrescan plan
Interplay plan
Δmotion = 8 mm
Reference
Interplay
Insights Pisa Workshop 18th – 20th October 2023
2. Clinical impact investigated with dosimetric study
Results – Motion uncertanties
Tumor +3mm
Lung
P3 | Ref | Perfectrescan | Interplay
D95 (%) | 97 | 97.3 | 91.9
V20(%) | 28.6 | 28.9 | 28.9
P2 | Ref | Perfectrescan | Interplay
D95 (%) | 99 | 98 | 96
V20(%) | 4 | 3.9 | 3.9
Δmotion = 0.7 mm
m.c.martire@gsi.de

## Slide 16
Discussion
Dosimetric study results 
Insights Pisa Workshop 18th – 20th October 2023
Small dose degradation caused by modulation effect, indipendently on patients characteristics (computational demanding)
Severe dose degradation caused by motion uncertanties (also with small Δmotion)
4D optimization techniques to deliver high conformal target dose in a single fraction
The more motion uncertanties are controlled, the more modulation effect has to be taken into account
The modulation effect is a systematic error (improves with hypo-fractionaction)
The interplay effect is a random error (averaged out in multiple fractions)
Cell survival experiments simulations
Radiobiological effect not negligible for high-LET ions
Derivation of model of relative biological efficiency
m.c.martire@gsi.de

## Slide 17
Thank you for your attention!
Insights Pisa Workshop 18th – 20th October 2023
Acknowledgements
m.c.martire@gsi.de

## Slide 18
    Voxels with -900 ≤ HU ≤ -500 are identified as lung parenchyma.
    Construct the Gaussian modulation function
      Pmod : assumed constant in all voxels
      t(z) : water-equivalent thickness of lung tissues traversed by beam
      Thus,
    Convolve in each voxel the Gaussian kernel to the pristine Bragg curve to obtain the modulated dose
Gaussian modulation function
σ
t
Ringbaek et al., Phys. Med. Biol. 2017.
Lung tissue heterogeneities – Modulation effect
Implementation in TRiP4D
Insights Pisa Workshop 18th – 20th October 2023
Notes: Fro each voxel the depth dose distribution should be convolved with the modulation function. Which means, for all energies, both primary and secondary particles. In TRiP the convolution is perfromed directly with alpha, beta and LET distributions, so only 3 times, instead of 18