## Slide 1
New image reconstruction approach for in-vivo range verification of multiple field carbon ion treatments by means of in-beam PET system
1 st INSIGHTS meeting on new horizons in radiation therapy
D. Bersani1, M.G. Bisogni1, 2, P. Carra1, 2, P. Cerello3, M. Ciocca4, V. Ferrero3, M. Moglioni1, 2, F. Pennazio3, M. Rafecas5, S. Ranjbar3, 6, G. Sportelli 1, 2, V. Vitolo4, J. Werner5, E. Fiorina3
1 Istituto Nazionale di Fisica Nucleare, Sezione di Pisa, Italy 2 Dipartimento di Fisica, University of Pisa, Italy 3 Istituto Nazionale di Fisica Nucleare, Sezione di Torino, Italy 4 Centro Nazionale di Adroterapia Oncologica, Fondazione CNAO, Pavia, Italy 5 Institute of Medical Engineering, Universität zu Lübeck 6 Dipartimento di Fisica, University of Torino, Italy

## Slide 2: in-beam PET for carbon ion treatments
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
2
11C (T1/2≈ 20.3 min)
10C (T1/2 ≈ 19.3 s)
15O (T1/2 ≈ 2.0 min)
13N (T1/2≈ 10.0 min)
Charged particles
𝛄 511 keV
Rotating
treatment couch
PET
scanner
C beam
Dose
profiler
target activation
projectile fragmentation
Bimodal imaging system for in-vivo range monitoring in particle therapy (in-beam PET + Dose profiler)
𝛄 511 keV
12
Irradiation-induced activity inside the patient correlated to the delivered dose distribution
19 head-and-neck and brain patients treated with either protons or carbon ions monitored within a clinical trial (ID NCT03662373)
Ferrero, V. et al. Online proton therapy monitoring: clinical test of a Silicon-photodetector-based in-beam PET. Sci Rep 8, 4100 (2018)
Fischetti, M. et al. Inter-fractional monitoring of 12C ions treatments: results from a clinical trial at the CNAO facility. Sci Rep 10, 20735 (2020)

## Slide 3: in-beam PET for carbon ion treatments
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
2
11C (T1/2≈ 20.3 min)
10C (T1/2 ≈ 19.3 s)
15O (T1/2 ≈ 2.0 min)
13N (T1/2≈ 10.0 min)
Charged particles
𝛄 511 keV
Rotating
treatment couch
PET
scanner
C beam
Dose
profiler
target activation
projectile fragmentation
Bimodal imaging system for in-vivo range monitoring in particle therapy (in-beam PET + Dose profiler)
𝛄 511 keV
12
Irradiation-induced activity inside the patient correlated to the delivered dose distribution
19 head-and-neck and brain patients treated with either protons or carbon ions monitored within a clinical trial (ID NCT03662373)
Improve PET image quality and detection of inter-fractional morphological changes during the treatment
Ferrero, V. et al. Online proton therapy monitoring: clinical test of a Silicon-photodetector-based in-beam PET. Sci Rep 8, 4100 (2018)
Fischetti, M. et al. Inter-fractional monitoring of 12C ions treatments: results from a clinical trial at the CNAO facility. Sci Rep 10, 20735 (2020)

## Slide 4: in-beam PET for carbon ion treatments
Coincidence event rate
1st field
0° IEC
2nd field
290° IEC
3rd field
180° IEC
Multiple fields irradiation
Low statistics of irradiation-induced positron emitters due to the reduced number of primary particles (at least 10x compared to protons)
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
3

## Slide 5: in-beam PET for carbon ion treatments
Coincidence event rate
1st field
0° IEC
2nd field
290° IEC
3rd field
180° IEC
Multiple fields irradiation
Low statistics of irradiation-induced positron emitters due to the reduced number of primary particles (at least 10x compared to protons)
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
3
Recover the signal of 11C (T1/2≈ 20.3 min) of previously irradiated fields and reconstruct only one PET image to increase statistical significance

## Slide 6: in-beam PET for carbon ion treatments
New approach hypotheses
Most of the activation is due to projectile fragmentation into 11C (T1/2≈ 20.3 min)
increasing the acquisition time means increasing statistics​
contributions from different irradiation angles can be summed
Most of activation is located within the Clinical Target Volume (CTV) that is covered by INSIDE in-beam PET for all the irradiation beam fields
target activation
projectile fragmentation
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
4

## Slide 7: in-beam PET for carbon ion treatments
New approach hypotheses
Most of the activation is due to projectile fragmentation into 11C (T1/2≈ 20.3 min)
increasing the acquisition time means increasing statistics​
contributions from different irradiation angles can be summed
virtual detector
patient-tailored response model
Most of activation is located within the Clinical Target Volume (CTV) that is covered by INSIDE in-beam PET for all the irradiation beam fields
The basic idea is:
convert all PET coincidences detected during a multiple field irradiation in a single space
reconstruct only one PET image comprising all the delivered beam fields
target activation
projectile fragmentation
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
4

## Slide 8: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
5
f=1/10 of primary particles simulated
beam line
Beam time-space structure
Patient anatomy provided by the CT
Coincidences
Primaries
Planning CT
Coincidence event rate
Most of the β+ activity is located into the CTV
Monte Carlo simulation of 7 patients
Calculation of the Activity Volume Histogram (AVH) representing the annihilations occurred in any volume

## Slide 9: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
5
f=1/10 of primary particles simulated
beam line
Beam time-space structure
Patient anatomy provided by the CT
Coincidences
Primaries
Planning CT
Coincidence event rate
Most of the β+ activity is located into the CTV
Monte Carlo simulation of 7 patients
Calculation of the Activity Volume Histogram (AVH) representing the annihilations occurred in any volume
Simulation of the emitting isotopes within the PET acquisition time of each beam field + residual activity backgroung from all previously irradiated beam fields (mainly 11C)

## Slide 10: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
6
Annihilation Maps
290°
180°
0°
+
+
1st field 2nd field 3rd field

## Slide 11: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
6
Annihilation Maps
290°
180°
0°
Total
+
+
1st field 2nd field 3rd field

## Slide 12: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
6
Annihilation Maps
CTV
5 cm dilated CTV
290°
180°
0°
Total
+
+
1st field 2nd field 3rd field

## Slide 13: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
6
AVH - Patient 005C
same activity level
2%
95%
Volume fraction
Activity threshold [counts]
Annihilation Maps
CTV
5 cm dilated CTV
290°
180°
0°
Total
+
+
1st field 2nd field 3rd field
Evaluation of the capability to identify the CTV from the background (ROI around CTV within 5 cm = dilated CTV) by setting an activity threshold
Considering the activity threshold corresponding to the 95% of the CTV, the percentage of voxels selected into the dilated CTV is in the range of 2-12%

## Slide 14: Virtual detector approach
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
7
Virtual detector to identify in a single space all the acquired coincidences and thus reconstruct only one PET image
1st FIELD – 0°
beam
x
y
z
DOSE
VIRTUAL DETECTOR
z
y
DOSE
Rotating detector around the patient
Fixed treatment couch
0°
0°
0°
Fixed detector position
Rotating treatment couch
VIRTUAL
REAL

## Slide 15: Virtual detector approach
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
8
VIRTUAL
REAL
2nd FIELD – 290°
VIRTUAL DETECTOR
290°
0°
0°
x
beam
z
y
290°
290°
DOSE
Rotating (real) detector around the patient
Fixed treatment couch
Fixed detector position
Rotating treatment couch
Virtual detector to identify in a single space all the acquired coincidences and thus reconstruct only one PET image

## Slide 16: Virtual detector approach
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
9
VIRTUAL
REAL
3rd FIELD – 180°
VIRTUAL DETECTOR
x
y
z
beam
180°
290°
0°
180°
180°
0°
290°
DOSE
Rotating (real) detector around the patient
Fixed treatment couch
Fixed detector position
Rotating treatment couch
Virtual detector to identify in a single space all the acquired coincidences and thus reconstruct only one PET image

## Slide 17: PET reconstruction algorithm
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
10
5
5
5
3 iterations and median filtering (5 mm kernel) between iterations
5
intensity of the j-th voxel after iteration n
(i,j) element of the system matrix
all possible LORs during field k
sensitivity of the j-th voxel in field k
List-mode Maximum Likelihood Expectation Maximization (MLEM) algorithm

## Slide 18: PET reconstruction algorithm
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
10
5
5
5
j-th voxel
i-th LOR
detector channel
3 iterations and median filtering (5 mm kernel) between iterations
5
intensity of the j-th voxel after iteration n
(i,j) element of the system matrix
all possible LORs during field k
sensitivity of the j-th voxel in field k
List-mode Maximum Likelihood Expectation Maximization (MLEM) algorithm
System matrix implemented with Siddon’s single ray-tracing

## Slide 19: PET reconstruction algorithm
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
10
5
5
5
j-th voxel
i-th LOR
detector channel
3 iterations and median filtering (5 mm kernel) between iterations
SENSITIVITY
0°
180°
290°
3rd field
2nd field
1st field
SENSITIVITY
SENSITIVITY
0°
180°
290°
FOV: 70×96×96, Voxel 3.2 mm
real
detector
virtual
detector
5
intensity of the j-th voxel after iteration n
(i,j) element of the system matrix
all possible LORs during field k
sensitivity of the j-th voxel in field k
Patient-talored sensitivity
List-mode Maximum Likelihood Expectation Maximization (MLEM) algorithm
System matrix implemented with Siddon’s single ray-tracing

## Slide 20: PET image simulation
1st field 2nd field 3rd field
270°
195°
15°
STEP 1:
Beam simulation
Time-tagged
Positron emitter isotopes scoring
1/10 of primary particles
Annihilation Maps
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
11
Fiorina E et al. Monte Carlo simulation tool for online treatment monitoring in hadrontherapy with in-beam PET: A patient study. Phys Med. 2018
time

## Slide 21: PET image simulation
1st field 2nd field 3rd field
270°
195°
15°
Isotope decays are simulated
All positrons are simulated x10
Photons transportation to the detector
STEP 1:
Beam simulation
Time-tagged
Positron emitter isotopes scoring
STEP 2:
PET simulation:
time
1/10 of primary particles
Annihilation Maps
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
11
Fiorina E et al. Monte Carlo simulation tool for online treatment monitoring in hadrontherapy with in-beam PET: A patient study. Phys Med. 2018

## Slide 22: PET image simulation
1st field 2nd field 3rd field
270°
195°
15°
Isotope decays are simulated
All positrons are simulated x10
Photons transportation to the detector
STEP 1:
Beam simulation
Time-tagged
Positron emitter isotopes scoring
STEP 2:
PET simulation:
time
1/10 of primary particles
Annihilation Maps
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
11
Fiorina E et al. Monte Carlo simulation tool for online treatment monitoring in hadrontherapy with in-beam PET: A patient study. Phys Med. 2018
Data analysis and
image reconstruction
Coincidence window = 1 ns
Time resolution = 247 ps
Energy resolution = 15%
Energy window = 0.1 MeV

## Slide 23: PET image simulation
1st field 2nd field 3rd field
270°
195°
15°
Isotope decays are simulated
All positrons are simulated x10
Photons transportation to the detector
STEP 1:
Beam simulation
Time-tagged
Positron emitter isotopes scoring
STEP 2:
PET simulation:
time
1/10 of primary particles
Annihilation Maps
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
11
Fiorina E et al. Monte Carlo simulation tool for online treatment monitoring in hadrontherapy with in-beam PET: A patient study. Phys Med. 2018
Data analysis and
image reconstruction
Coincidence window = 1 ns
Time resolution = 247 ps
Energy resolution = 15%
Energy window = 0.1 MeV
Multiple fields MLEM reconstruction

## Slide 24: Voxel Based Morphometry
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
12
All positrons are simulated x1000 to increase the statistics by a factor 100
Random selection of simulated events (probability 0.01±20%) to get 500 datasets (list-mode coincidences file) with a statistics comparable to experimental data
Reference intensity distributions are obtained for each voxel
Statistical comparison of each voxel value with the reference intensity distribution p-value
Two tailed hypothesis test with significance level α = 0.01
1) N = 500 simulated images on Planning/ Control CT
2) Reference intensity distributions for each voxel i
3) p-value calculation
<Iisim>
Iiobs
ri
ri = number of images in the tail [Iiobs> < Iisim > or Iiobs> < Iisim >]
N = 500
Kraan AC et al. Localization of anatomical changes in patients during proton therapy with in-beam PET monitoring: A voxel-based morphometry approach exploiting Monte Carlo simulations. Med Phys. 2022

## Slide 25: Voxel Based Morphometry
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
13
1) N = 500 simulated images on Planning/ Control CT
2) Reference intensity distributions for each voxel i
3) p-value calculation
ri
Kraan AC et al. Localization of anatomical changes in patients during proton therapy with in-beam PET monitoring: A voxel-based morphometry approach exploiting Monte Carlo simulations. Med Phys. 2022
All positrons are simulated x1000 to increase the statistics by a factor 100
Random selection of simulated events (probability 0.01±20%) to get 500 datasets (list-mode coincidences file) with a statistics comparable to experimental data
Reference intensity distributions are obtained for each voxel
Statistical comparison of each voxel value with the reference intensity distribution p-value
Two tailed hypothesis test with significance level α = 0.01
ri = number of images in the tail [Iiobs> < Iisim > or Iiobs> < Iisim >]
N = 500
<Iisim>
Iiobs

## Slide 26: clinical trial
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
14
The
Planning CT
Control CT
Patient 008C
PZ008
ACC, 16 (64 Gy(RBE)) fractions, 4 Gy(RBE) per fraction
Monitored beam fields: 270° - 320° - 15°
Control CT after 7 fractions no replanning
Planning CT
Control CT
Patient 006C
PZ006
ITAC, 10 (41 Gy(RBE))+6 fractions, 4.1 Gy(RBE) per fraction
Monitored beam fields: 270° - 195° - 15°
Control CT after 7 fractions replanning

## Slide 27: Voxel Based Morphometry results: patient 008C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
15
500 simulated images on the control CT
Measured fraction 7
270°
15°
320°

## Slide 28: Voxel Based Morphometry results: patient 008C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
15
500 simulated images on the control CT
p-value map
significance level α=0.01
Measured fraction 7
Fraction 7 vs Control CT
less activity than expected
more activity than expected
VBM
CTV
270°
15°
320°

## Slide 29: Voxel Based Morphometry results: patient 006C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
16
500 simulated images on the control CT
Measured fraction 7
270°
195°
15°

## Slide 30: Voxel Based Morphometry results: patient 006C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
16
500 simulated images on the control CT
p-value map
significance level α=0.01
Measured fraction 7
Fraction 7 vs Control CT
VBM
CTV
less activity than expected
more activity than expected
270°
195°
15°

## Slide 31: Voxel Based Morphometry results: patient 006C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
17
500 simulated images on the planning CT
Measured fraction 2
270°
195°
15°

## Slide 32: Voxel Based Morphometry results: patient 006C
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
17
500 simulated images on the planning CT
p-value map
significance level α=0.01
Measured fraction 2
Fraction 2 vs Planning CT
VBM
CTV
less activity than expected
more activity than expected
270°
195°
15°

## Slide 33: Conclusions and prespectives
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
18
The proposed image reconstruction approach will be tested on more patient data.
Statistical variability in experimental data will be further investigated (e.g., different irradiation time, biological washout).
This research has received funding from the CNAO, the Tuscany Region under POR FSE 2014-2020 and INFN, project SYNCT CUP I55F21002760008, and the INSIDE project (PRIN 2013)
The new proposed image reconstruction method is based on exploitation of the multiple field irradiation to improve PET image quality and detection of inter-fractional morphological changes during the treatment.
The hypothesis that most of the activity is located into the CTV was verified by using Monte Carlo simulation and Activity Volume Histograms.
A Voxel Based Morphometry method was implemented on patients enrolled into the INSIDE clinical trial (patients 008C and 006C) to locate spot inter-fractional morphological changes.

## Slide 34: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
34
270°
195°
15°
+
+
+
Annihilation Maps
1° beam
acquisition time
2° beam
acquisition time
3° beam
acquisition time
Coincidence event rate

## Slide 35: Hypotesis verification
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
35
AVH- Patient 006C
AVH- Patient 008C
AVH- Patient 009C
AVH- Patient 004C
AVH- Patient 005C
AVH- Patient 001C
AVH- Patient 002C
95 %
CTV volume
7 %
11 %
6 %
7 %
2 %
12 %
2 %

## Slide 36: Biological washout
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
36
Estimation of the washout effect due to metabolic processes in living tissues
Exponential fit 200 s after the end of the first field irradiation
MC Simulation
Patient 008C
Experimental data
τ ≈ 116 s
τ ≈ 80 s

## Slide 37: Statistical analysis
1 st INSIGHTS meeting Hadrontherapy, monitoring and new devices
37
Coincidenze
PET coincidences
Mean value of PET coincidences of each field for each patientca