## Slide 1: Precision of the positron emission activity range during irradiation with radioactive carbon and oxygen beams
Peter Dendooven
PARTREC, Department of Radiation Oncology,
University Medical Center Groningen, the Netherlands
INFN Pisa – 23 January 2023
Pisa, 18-20 October 2023
INnovative Systems In radiation therapy:
breakthrouGHs novel detectors, Treatments and AI techniqueS

## Slide 2: Contents
introduction
  PET imaging of ion beams
  radioactive ion beams for radiotherapy
experiments within the BARB and S533 projects at GSI/FAIR
  setup
  PET imaging of C-10, C-11, O-14 and O-15 radioactive ion beams
conclusions

## Slide 3: Production of positron emitters along the beam path
K. Parodi, PhD Thesis, Dresden, 2004
proton beam
carbon beam
measured positron annihilation activity profile along the beam path in PMMA

## Slide 4: PET activity peak vs. Bragg peak for C-11 and O-15
A. Mohammadi et al., Phys. Med. Biol. 65 (2020) 125006
shift between the Bragg peak and the PET activity peak positions for C-11 and O-15 beams with a momentum acceptance of 0.5%.
radioactive ion beams: PET activity overlaps the Bragg peak 😄
How accurately can the PET activity peak position be measured ?
  (a proxy for the Bragg peak) ?
How quickly can a relevant accuracy be reached ? Real-time verification ?

## Slide 5: Radioactive ion beams to image the range

## Slide 6: Short-lived positron emitter beams at HIMAC

## Slide 7: Short-lived positron emitter beams at HIMAC
Japanese Journal of Medical Physics (Igakubutsuri) Vol. 24 (2004) No. 2 p. 37-48
The examination of optimal positron emitting nuclide in the estimation of attainment depth within the body of RI beams by positron camera
H. Mizuno, Y. Iseki, E. Urakabe, M. Suda, M. Kanazawa, A. Kitagawa, T. Tomitani, Y. Nakamura, T. Kanai, K. Ishii

## Slide 8: The BARB and S533 projects
ERC Advanced Grant
PI: Marco Durante
Co-PI: Katia Parodi
Biomedical Applications of Radioactive ion Beams
www.gsi.de/work/forschung/biophysik/erc_barb
produce high-intensity beams of short-lived isotopes of carbon and oxygen
use these beams for examination of simultaneous treatment and online imaging
GSI Experiment S533
nuclear and atomic interactions for ion-beam therapy with positron emitters of carbon
PI: Sivaji Purushothaman

## Slide 9: Experimental setup for radioactive ion beams
Mid-focal plane
Aluminium disk degrader
SCI
TPC
Target Chamber
Production Traget
9Be ➔8 g/cm2
Primary beam: 12C
380 MeV/u & 290 MeV/u
Experimental focal plane
Symmetric branch
TPC: Time Projection Chamber TPC
MUSIC: Multi-Sampling Ionization Chamber
SCI: Plastic scintillators
IC: Parallel plate Ionization Chamber
TPC
MUSIC
MUSIC
TPC
SCI
SCI
IC
PET imaging
setup
for O-14, O-15 beams:
O-16 primary beam

## Slide 10: Intensity monitoring and PET imaging
parallel-plate
ionization chamber
dual-panel
PET scanner
dual-panel
PET scanner
PMMA phantom
120×250×350 mm3
sensitivity map
D Kostyleva et al, Phys Med Biol 68(2023)015003

## Slide 11: Dual-panel PET scanner
PET scanner
Biograph mCT technology
two 23 × 23 cm2 panels
sensitivity center FoV = 2.2 %
angular coverage close to 50%
each panel:
4×4 block detectors
13×13 scintillators
4×4×20 mm3 LSO
I. Rausch et al, Eur J Nucl Med Mol Imag Phys 2 (2015) 26
setup at UMCG PARTREC (Groningen)

## Slide 12: Number of coincidences vs. time
C-10
beam-on data is useful
C-11
beam-on data is
not useful

## Slide 13: Positron emission images
number of coincidences
X [mm]
Y [mm]
2×2 mm2 pixels
achromatic
Y [mm]
Y [mm]
monoenergetic
achromatic
1D profiles
depth in PMMA [mm]
depth in PMMA [mm]
short range
long range
-o- C-10
-o- C-11
-o- C-12
-o- C-10
-o- C-11
-o- C-12
80% dose range*
80% dose range*
*dose range from D Boscolo et al, NIM A 1043(2022)167464

## Slide 14: Positron activity peak position & uncertanty
peak position = surrogate for the dose range
peak position accuracy is determined by counting statistics

## Slide 15: Positron emission activity peak position
change from C-10 to C-11 domination over time
radioactive beams show a stable peak position

## Slide 16: Oxygen images vs. number of cycles
O-14
O-15
O-16
cycle:
1 s on
1.3/1.5 s off
ions/cycle
O-14: 1.1×106
O-15: 1.1×107
O-16: 6.0×107
O-15 gives the
best images

## Slide 17: Results from carbon ions
Peak position [mm]
C-11
C-11
C-10
C-10

## Slide 18: Results from oxygen ions
Peak position [mm]
O-14
O-14
O-15
O-15

## Slide 19: A figure-of-merit: O-15 “wins"
relative number of decays during the beam off period of the first beam cycle:
= reaction cross section
= decay constant
= cycle time
= beam on time

## Slide 20: Conclusions
range uncertainty is dominated by counting statistics
C-11 shows a limited gain over C-12 for quick information
need to use C-10 for significant gain (much shorter half-life)
considering carbon and oxygen ions from in-flight: O-15 is preferred
  C-10 is not far behind
  biological and cost issues are also relevant in the choice of ion
using the ISOL method (production at low energy + acceleration):
  C-10 might be preferred
  C-9 is very appealing (T1/2 = 0.13 s)
all details of GSI/FAIR experiments in:
D. Kostyleva et al., Phys. Med. Biol. 68 (2023) 015003
S. Purushothaman et al., Sci. Rep. accepted for publication

## Slide 21
ERC Advanced Grant
Thank you