## Slide 1
INSIGHTS 2023
  —
    Estimating the proton stopping power from prompt gamma timing data: algorithms, models, and first experiments
    J. F. Werner1, Veronica Ferrero2, Niklas Schmid3, Elisa Fiorina2, Davide Bersani4, Piergiorgio Cerello2, Jona Kasprzak1, Felix Mas Milan2, Marco Pullia5, Sahar Ranjbar2,6, Roberto Sacchi6, Anna Vignati6, Francesco Pennazio2, Magdalena Rafecas1
    1Institute of Medical Engineering, Universität zu Lübeck 3Automatic Control Laboratory (IfA), ETH Zürich 5National Center of Oncological Hadrontherapy, Fondazione CNAO, Pavia
    2Istituto Nazionale di Fisica Nucleare, Sezione di Torino 4Istituto Nazionale di Fisica Nucleare, Sezione di Pisa 6Department of Physics, University of Turin

## Slide 2: (Charged) particle therapy
A very brief introduction
Irradiation of tumours with protons, carbon ions, ...
Particles gradually lose energy ↔ stopping power
Dose maximum just before particle has lost all kinetic energy
 Stopping power is crucial for treatment planning
Particle beam
Lomax AJ. Br J Radiol 2020.
Bragg peak

## Slide 3: Adaptive treatment and treatment verification
(Re-) planning
Treatment
Indication?
Planning CT
Control CT @ fx 22
Modified from Fiorina E. et al. Frontiers in Physics 2021
Treatment is split into fractions
Changes between fractions can lead to mismatch between planning and execution of treatment
Treatment verification  Need for replanning
We propose:
  Estimate the stopping power from measurements during the treatment
  Compare stopping power used in planning to measurement

## Slide 4: Interaction of charged particles with matter
Inelastic nuclear reactions
Neutrons
Secondary charged particles
emission ( PET)
Prompt Gamma emission
  Within < 10 ps
  Few keV to several MeV
Prompt gamma radiation

## Slide 5
Treatment verification with secondary particles
Charged particle therapy
Deviations along the beam path are mostly detected through (cumulative) changes of range
Time-structure of emission holds additional information
PG Activation
CTV (clinical target volume)
End of activation
Particle range
Patient / Phantom
Young Investigator Forum – DGMP 2023

## Slide 6: Rationale of the method
PG emission in time and space reveals the average speed of the charged particles in the patient.
 From that distribution we should be able to estimate the tissues stopping power during the irradiation.
Red line: expected motion
0
1
PG-Emission in MC-simulation of homogeneous PMMA and 219 MeV p+ proton beam
15
10
5
0
-5
-10
-15
-20
Emission position (cm)

## Slide 7: Prompt Gamma Timing (PGT)
Uncollimated time-sensitive photon counting
Record reference plane time t0
Record detector arrival time td
Time difference consists of
  Proton travel time tp
  Deexcitation time of nucleus
  Photon travel time tγ
  See Golnik et. al. 2014
(ns)

## Slide 8: Prompt Gamma Timing (PGT)
Uncollimated time-sensitive photon counting
Record target entry time t0
Record detector arrival time td
Time difference consists of
  Proton travel time tp
  Photon travel time tγ
Different detector positions  complementary information
Detection time difference (ns)

## Slide 9: Spatiotemporal emission reconstruction
Emission position (cm)
Emisison time (ns)
15
10
5
0
-5
-10
-15
-20
from Prompt Gamma Timing (SER-PGT)
The (unkown) emission dictates the measured PGT data
Reconstruction: solution of inverse problem based on maximizing likelihood of measurement + threshold
Approach first published: Pennazio et. al., PMB 2022
Unknown emission
Measurement
Reconstruction
Reconstructed emission
Emisssion time (ns)
Emisssion position (cm)
15
10
5
0
-5
-10
-15
-20

## Slide 10: Spatiotemporal emission reconstruction
from Prompt Gamma Timing (SER-PGT)
Maximum Likelihood Expectation Maximization (ML-EM)
  : number of detections in temporal bin n of detector d
  : spatiotemporal emission at spatial bin j and temporal bin p
  (system matrix element) is the probability of an emission in spatial bin j emitted in timebin p to be detected in detector d in timebin n  calculated using FLUKA
SER-PGT disentangles complementary information of multiple PGT detectors
First published: Pennazio et. al., PMB 2022
Emisssion time (ns)
Emisssion position (cm)
15
10
5
0
-5
-10
-15
-20

## Slide 11: FLUKA simulation setup
1.18 g/cm3 PMMA block
62-227 MeV proton beams
  Monochromatic, FWHMxy=0
  All emissions at time 0
  50 realizations of 107 p+ per energy
110 LaBr3:Ce crystals for PG detection
  Homogeneous cylindrical crystals, length: 3.81 cm, radius 3.81 cm
  Energy depositions recorded directly in custom user routine

## Slide 12: Reconstructed PG emissions
FLUKA simulations
107 protons
30 cm PMMA cubic phantom
110 PG detectors
 Range estimation errors:
But can we get more?
Expected range
15
10
5
0
-5
-10
-15
-20
15
10
5
0
-5
-10
-15
-20
Emisssion position (cm)
Emisssion position (cm)

## Slide 13: 1D-motion model of charged particles
For homogeneous media
Geiger‘s Range rule:
Kinetic energy must match range at each position  (see Bortfeld 1997)
Numerical integration yields position over time
Numerical integration
Common parameters
Werner, Ferrero et. al., submitted to PMB, under review

## Slide 14: Our Approach
+
=
Reconstruction
Motion model
Stopping power estimation
30
25
20
15
10
5
0
-5
Emisssion position (cm)

## Slide 15: MC-simulation based results
Stopping power
107 protons per run; 50 runs per energy
proton energies from 110 MeV to 220 MeV
30-cm PMMA phantom
110 PG detectors
Reproduced from Ferrero, Werner et al. Frontiers in Physics 2022

## Slide 16: MC-simulation based results
Stopping power
107 protons per run; 50 runs per energy
proton energies from 60 MeV to 220 MeV
30-cm PMMA phantom
110 PG detectors
 Error of stopping power ratio to water: for protons with ≥ 160 MeV

## Slide 17: The MERLINO prototype
Measurement of the EneRgy Loss for IN-vivo Optimization in particle therapy
2 Photon detectors
  LaBr3:Ce monolythic crystals coupled to PMTs, 3.81 cm length, 3.81 cm diameter
In coincidence with Ultra Fast Silicon Detector (UFSD) between beam nozzle and patient
  Challenge: clinical beam rates up to 108 particles per second
Triggered acquisition with digitizer
Coincidence time resolution ~250-300 ps FWHM
LaBr3:Ce
UFSD
PMMA
proton
PI: V. Ferrero, INFN Turin

## Slide 18: Preliminary reconstruction of experimental data
227 MeV proton beam @CNAO, 1E7 pps average rate
LaBr3:Ce
UFSD
PMMA
proton
V. Ferrero and F. Pennazio
PMMA phantom without airgap, multiple measurements with different detector positions
PGT1
PGT2
PGT3
PGT4
PGT5
PGT6
PGT7
PGT8
PGT9
PGT10
PGT11
PGT12
PGT13
PGT14
Experimental data
Simulated data

## Slide 19: Preliminary reconstruction of experimental data
227 MeV proton beam @CNAO , 1E7 pps average rate
Homogeneous PMMA phantom
PMMA phantom with 4 cm gap
a.u.
a.u.
0
1
0
1
Preliminary
LaBr3:Ce
UFSD
PMMA
proton
V. Ferrero and F. Pennazio
PMMA phantom with and without airgap
14 PG detector positions
Triggered acquisition with digitizer
Preliminary
15
10
5
0
-5
-10
-15
-20
Emisison depth (cm)
15
10
5
0
-5
-10
-15
-20
Emisison depth (cm)

## Slide 20: What about inhomogeneous materials?
Outlook
Separate material into homogeneous regions
Independent parameters for each region
Exploit beams of different energy crossing the same material
 Tradeoff between number of regions, size of regions and number of free parameters

## Slide 21: Conclusion & Outlook
Stopping power
PG emission in time and space can be reconstructed via Prompt Gamma Timing data from several detectors.
It reveals the average speed of the charged particles in the patient and by extension the stopping power during the irradiation.
Demonstrated using MC-simulations of homogeneous phantom.
 Experimental validation and extension to inhomogeneous phantoms underway.
Prompt Gamma Timing spectra
PG emission in time and space
Reconstruction
Motion fit
Reproduced from Ferrero, Werner et al. Frontiers in Physics 2022

## Slide 22
Thanks to
Nuclear imaging group – Institute of Medical Engineering, Universität zu Lübeck
Medical Physics group – INFN Torino and Department of Physics, Universitá degli Studi di Torino
Staff of the National Center of Oncological Hadrontherapy, Fondazione CNAO, Pavia Dr. Fernando Hueso-González – Instituto de Física Corpuscular IFIC Valencia

## Slide 23: Motion of relativistic charged particles
Slowing down in electron cloud
Dominated by electronic stopping power
Full description with Bethe-Bloch equation
Dominated by sharp stopping power increase at end of the particle range
https://physics.nist.gov/PhysRefData/Star/Text/PSTAR.html

## Slide 24: Details on the particle motion model
Calculating time and position profiles
Position
Time:
(Bortfeld 1997)

## Slide 25: How do we fit a 1D-function to a 2D distribution?
After reconstruction:
Threshold
Calculate COG of each timebin
Range  last COG with emission over threshold
Fit motion-function to COG-Time pairs

## Slide 26: Interactions of charged particles with matter
Electromagnetic
Inelastic Coulomb interactions with electrons  quasi-continous slowing down
Elastic Coulomb scattering with nuclei  widening of beam
Nuclear
Significant energy loss (or fragmentation)
Induced radioactive decays
Prompt Gamma
β+
δ
Neutrons, …

## Slide 27: Spatiotemporal PG emission
Gamma radiation from nuclear interactions
Emission within 100 ps after interaction
Energies ranging up to 15 MeV
 PG emission is closely linked in time and space with the particles

## Slide 28: System matrix calculation
Via Monte Carlo simulation
Probability of a photon emitted in spatial bin j and temporal bin p to be detected by detector d in temporal bin n
Simulate photon emissions homogeniously distributed along the beam axis
Record number of detected events for each combination of detector, time and spatial bin
Add emission time dimension by shift

## Slide 29: Point spread function
To test the inherent limits of the modelled system, reconstruct data forward projected from an optimal object using the same system matrix.
MC: significant tail in spatial PSF – likely due to 3.5 cm detector size
Analytical SM only considering center detectors face  perfekt PSF
28.09.2023

## Slide 31: Preliminary reconstruction of experimental data
227 MeV proton beam @CNAO, 1E7 pps average rate
LaBr3:Ce
UFSD
PMMA
proton
V. Ferrero and F. Pennazio
PMMA phantom with and without airgap
14 PG detector positions
Triggered acquisition with digitizer