## Slide 1: Introductions to accelerators II: Transverse Dynamics
Dr Tatiana Pieloni (Tatiana.Pieloni@epfl.ch)
Laboratory for Particle Accelerator Physics, EPFL

## Slide 2: Linear Dynamics - continued
practical questions to be answered:
How to ensure bound motion of a particle beam?
What are conditions for stability?
Amplitude and frequency of particle oscillations?
Statistical beam properties like beam width and angular spread?
How to design magnet lattices (arrangements of dipoles and quads in a line)?
Chromaticity
What is the impact of field errors in bending and focusing magnets?

## Slide 3
Statistical Beam Properties
Single particle Phase space ellipse
Courant-Snyder Invariant of motion
Particle Action versus beam emittance
Emittance and distribution function
Liouville theorem
consequences of conservation of emittance

## Slide 4: Phase Space Ellipse
1
4
2
3
x’
x
J = particle action (oscillation amplitude)
observing the coordinates of a particle at one location in a ring for consecutive turns
x, x’ describe an ellipse in phase space when  is varied
example x  0.37×2 phase advance per turn
see also Schmüser/Rossbach sect. 4.3/4.4, Wiedemann chap. 8.1.2

## Slide 5: Courant-Snyder Invariant
E.D. Courant and H.S. Snyder, Theory of the Alternating Synchrotron, Annals of Physics 3 (1958) 1
x’
x
at one location this phase space ellipse is sampled by a particle with action J
when moving along the magnet lattice, the ellipse is changing shape, but it stays an ellipse
the area of the ellipse is invariant (Courant-Snyder Invariant) and equals 2 × action.
the unit is [mrad], or often [mmmrad]
this constant of motion refers to a single particle, emittance is a statistical property

## Slide 6: Action vs. Emittance
x
single particles are associated with a particular ellipse
when observing a beam with a wire scanner a (projected) rms (root mean square) width x is measured; one ellipse corresponds to x
emittance  is the average value of action J

## Slide 7: Beam Emittance
beam emittance as statistical property:
two-dimensional Gaussian distribution:
projected Gaussian distribution:
see Wiedemann sec. 8.1.3

## Slide 8: Fractions of Beam in rms widths
rms width n | beam fraction r
1 | 39%
2 | 86%
3 | 99%
From practical measurements (wire scan, beam screen) the projected rms width of the beam is determined.
What fraction of beam is contained in ?
compute the beam fraction inside an ellipse corresponding to nx:
note: This applies for a two dimensional Gaussian distribution.

## Slide 9: Liouvilles Theorem
the phase space density is conserved
The phase space density behaves like an incompressible liquid.
q
p
see also Wiedemann sec. 8.1.1
Beams subject to conservative forces as in our accelerator (without dissipative forces i.e. synchrotron radiation)  preserve the phase space density over time

## Slide 10: Conservation of Emittance
x
px
x
px
with a given emittance a beam can be made small with large angular spread, or can have small angular spread with a large size

## Slide 11: Phase Space Ellipse in Drift Space
remember:

## Slide 12: Phase Space Ellipse after focusing
x‘
s, x
di
v
e
r
ging
beam
c
o
n
v
e
r
ging
beam
f
ocusing
quadrupole
beam
w
ai
s
t
di
v
e
r
ging
beam
Quad

## Slide 13: Beam Waist (e.g. interaction point collider)
β* = Beta function at waist

## Slide 14: Phase Space Ellipse - Parameters
for upright ellipse:
reminder:
x’
x

## Slide 15: Remarks on Beam Distributions
Protons, Ions
“protons never forget” G.Voss
can have “strange” distributions since those depend on the history of beam generation and acceleration; i.e. no damping mechanism
however: in practice often close to Gaussian distribution
Electrons
in a ring electrons radiate photons which continuously mixes particles in phase space and generates an equilibrium Gaussian distribution
i.e. a large injected beam will shrink to equilibrium while a small beam will grow

## Slide 16
Next: FODO Lattices
FODO parameter space
FODO with bending magnets

## Slide 17: Reminder: Quadrupole Doublet
l
 Mdoublet is always focusing

## Slide 18: FODO Cell
Unit sequence of magnets used to build an accelerator
Alternating gradients  net focusing!

## Slide 19: FODO Cell II
illustration:
particle trajectories of varying phase and amplitude in a FODO cell
Gaussian (projected) profile

## Slide 20: FODO Cell Parameters
we obtain for + in the focusing quad and - in the defocusing:
phase advance per cell:
+
-
see Wiedemann sec. 10.1

## Slide 21: FODO Cell: choice of phase advance
+ reaches minimum at opt=76.3deg
at this point the vacuum chamber needs a minimal size
note scaling per L
Example LEP(CERN) operating modes:
µx/µy [degrees]:
60/60, 90/60, 90/90, 102/90
(stronger foc. = smaller emittance)

## Slide 22: FODO Cell with Bending Magnets
FODO structure with bending magnets to form a ring - the standard scheme for synchrotrons
D/2
F
B
B
B
B
F
D
D/2
example:
2 FODO cells
 = 55m
separated function

## Slide 23
Weak focusing can be neglected for machines with large bending radius

## Slide 24
Dispersion
….for particles with d energy equations of motion change!
Bending in a dipole changes with the particle energy…

## Slide 27
D(s) is a periodic function in FODO cells
Notes: TODO…

## Slide 28: Dispersion Function in a Ring
the dispersion function at position s is calculated by integrating over contributions from bending magnets (1/≠0) around the ring:
D, D’ are periodic functions:

## Slide 29: Beam size with finite momentum spread
besides emittance also momentum spread may contribute to beam size and angular spread, via dispersion function; when the beam momentum spread is d:
d > 0
d < 0
x
x’
quadratic addition of transverse and longitudinal contributions:
at some locations the momentum contribution should be suppressed by designing for D=0, D‘=0
examples:
interaction point in a collider where beams should be as small as possible
undulators/source magnets, where divergence of emitted radiation should be small

## Slide 30: Path Length Change with Momentum
for an off-momentum particle the path length changes; consider a particle on a closed dispersion trajectory, i.e. no betatron oscillation: J=0, but p ≠0
the change in circumference for this particle is:

x
we introduce the momentum compaction factor c:
see Wiedemann sec. 8.4.6

## Slide 31
Next: Chromatic Focusing Error
Focusing Error - What happens?
Chromaticity
Correction using Sextupole Magnets

## Slide 32: Chromatic Errors
a spread of momentum leads to chromatic aberrations, similarly to aberrations of optical lenses:
nominal focal length
p/p > 0
p/p = 0
p/p < 0

## Slide 33: Chromaticity
particles with momentum deviation are focused differently, leading to a shift of the betatron frequency
Chromaticity  = change of tune per relative change of momentum:
integration over gradients around ring, betafunction as “sensitivity factor”:
see Wiedemann sec. 15.4.1

## Slide 34: Sextupol Magnet
[PSI / SLS Sextupol]
Sextupoles are placed in a region of finite dispersion:
sort particles according to their energy deviation

## Slide 35: Chromaticity – Correction using Sextupoles
nominal focal length
quadrupol
sextupol
p/p > 0
p/p = 0
p/p < 0
a sextupol acts like a position dependent quadrupole
positive dispersion
Dx > 0
total chromaticity in a ring:
see Wiedemann sec. 15.4.2

## Slide 36: Caution with Sextupoles
while sextupoles can correct chromatic focusing errors, they are nonlinear elements
nonlinear elements drive resonances and reduce the dynamic aperture of a ring, which must be carefully optimized when designing a ring
phase space portrait with sextupole kick

## Slide 37
Next: Lattice Imperfections
closed orbit distortion
gradient errors

## Slide 38: Closed Orbit
[closed orbit – conceptual sketch]
the oscillating trajectory is not closed
The stable mean value around which the particles oscillate is called the closed orbit. Every particle in the beam oscillates around the closed orbit.
in practice the closed orbit does not exactly follow the design orbit, but deviates due to small errors
the closed orbit represents the beam center, particles with nonzero actions oscillate around it
to assess practical implications and tolerances the effect of orbit distortions must be estimated
see Wiedemann sec. 15.2.3

## Slide 39: The closed orbit
The general expression of the closed orbit Xco(s) in the presence of a deflection q is:
oscillating term
kink at the location of the deflection
divergence for Q = n
amplitude modulated by the envelope b
Xco(s)

## Slide 40: Unintended deflection
The first source is a field error (deflection error) of a dipole magnet.
This can be due to an error in the magnet current or in the calibration table (measurement accuracy etc).
  The imperfect dipole can be expressed as a perfect one + a small error.
=
+
real dipole
ideal dipole
small dipole error
A small rotation (misalignment) of a dipole magnet has the same effect, but in the other plane.
=
+
real dipole
ideal dipole
small dipole error

## Slide 41: Unintended deflection
=
+
real quadrupole
ideal quadrupole
The second source is a misalignment of a quadrupole magnet.
  The misaligned quadrupole can be represented as a perfectly aligned quadrupole plus a small deflection.
small dipole error
No magnetic field on the beam axis
Non-zero magnetic field on the beam axis !

## Slide 42: Effect of a deflection
We set the machine tune to an integer value:
  Q = n N
Turn no 1
Turn no 2
Turn no 3
Turn no 4
Deflection
Beam direction
When the tune is an integer number, the deflections add up on every turn !
  The amplitudes diverge, the particles do not stay within the accelerator vacuum chamber.
Xco(s)

## Slide 43: Effect of a deflection
We set the machine tune to a half integer value:
  Q = n+0.5, n N
Turn no 1
Deflection
For half integer tune values, the deflections compensate on every other turn !
  The amplitudes are stable.
  This looks like a much better working point for Q!
Turn no 2
Turn no 3
Turn no 4
Beam direction
Xco(s)

## Slide 44: Many turns reveal something
Q = n + 0.5
Q = n + 0.4
Q = n + 0.3
Q = n + 0.2
Q = n + 0.05
The particles oscillate around a stable mean value (Q ≠ n)!
The amplitude diverges as we approach Q = n  integer resonance
Q = n + 0.1
Q = n
Let’s plot the 50 first turns on top of each other and change Q.
  All plots are on the same scale
  We just encountered our first resonance – the integer resonance that occurs when Q = n N

## Slide 45: Gradient Error
s
C
K(s)
most simple case: the distortion of the gradient is short and can be treated as a thin lens
we want to know:
the tune shift caused by the error
the modification of the beam width (via computing β(s))

## Slide 46: Gradient Error - Calculation
method: modify 1-turn transport matrix by multiplying thin lens error matrix
resulting tune shift for distributed gradient errors:
see Wiedemann sec. 15.3.1
solution explodes for Q  Integer × 0.5
this error modulates the beam width around the ring
the effect is called „Beta-Beat“
the Beta-Beat propagates at the double frequency of an orbit distortion
note: double frequency

## Slide 47: Gradient Error Example continued
accelerator lattice with 13 regular FODO cells, one quad in center has an error of +2%
when / is plotted against phase advance we see the “error kick” and the double beat frequency

## Slide 48
Next: Lattice Insertions
low Beta insertion

## Slide 49: Low Beta Insertion
concept sketch: using a quadrupole doublet it is possible to focus particles in the horizontal and vertical planes simultaneously through the interaction point
incoming trajectories, parallel to reference orbit, in x,y

## Slide 50: Low Beta Insertion
the most simple IR configuration
doublet focusing
large beta function in doublet  aperture limitation for ring
see also Wiedemann sec. 10.2.4

## Slide 51: Low Beta Insertion – Example of LHC
LHC interaction region
with Low-Beta + D.S.

## Slide 52: Beam Waist (e.g. interaction point collider)
β* = Beta function at waist

## Slide 53: Orbit Correction: Reminder - Closed Orbit Distortion by Kick 
kick  is caused by an unwanted magnetic field, or an off-set quadrupole (errors)
however, kick can be applied also on purpose to correct the orbit
with several kicks j the contributions are added:

## Slide 54: Orbit Correction
given is a set of beam positions representing an orbit
calculate a set of (wanted) corrector strengths to minimize the orbit amplitide
this can be formulated as a problem of linear algebra (Rkj coefficients last slide):
this is solved exactly for , however in practice we need flexible solutions
Singular Value Decomposition (SVD) is one approach:
W = diagonal matrix with singular values, inversion simple
solution:
: exact solution
: minimizes (magnet currents)
: minimizes (rms orbit deviation)
 in practice this is done using computer codes of the accelerator control system
see Wiedemann sec. 15.4.2