## Slide 1: Plasma Accelerators
Enrica Chiadroni (Sapienza Univ. - SBAI Dept. and INFN - LNF )
Overview of different schemes
27 July 2023 - 2 August 2023
Ettore Majorana Center (Sicily, IT)

## Slide 2: Outline
Basic principle of plasma-based acceleration
  Issues contributing to improving acceleration techniques
Current research highlights
Other uses for plasma in the accelerator field
  Plasma lenses
  Plasma wigglers/undulators
Conclusions

## Slide 3: Relativistic Plasma Waves
Courtesy of M. Ferrario

## Slide 4: Relativistic Plasma Waves
Courtesy of M. Ferrario

## Slide 5: Relativistic Plasma Waves
Courtesy of M. Ferrario
Collective behavior !!

## Slide 6: Relativistic Electron Electrostatic Plasma Wave
Plasma angular frequency/regular frequency
The disturbance does not propagate as a wave
  Plasma oscillation is purely an electrostatic oscillation
The oscillations lead to local compression (bunching) and rarefaction in the electron density
  Electron oscillations are fast, ions are regarded as stationary

## Slide 7: Acceleration in Plasma Waves

## Slide 9: Cold Wavebreaking Field
The ionized plasma can sustain accelerating gradient 2-3 orders of magnitude larger than in conventional RF-based accelerators
Maximum accelerating field a plasma can sustain: Cold wave breaking field
Characteristic scale length of the accelerating field, i.e. the plasma wake, is the plasma wavelength λp
Credits: C. Joshi, UCLA

## Slide 10: Plasma Definition
A partially or completely ionized gas, globally neutral, is a plasma if it exhibits a collective behavior
  Coulomb shielding
    Dimensions >> Debye length
  Plasma Oscillations
    Temporal response >> wp-1
The large electric fields a plasma can sustain are supported by collective motion of plasma electrons, forming a space charge disturbance moving at a speed slightly smaller than c

## Slide 11: Collective Fields to Accelerate Charged Particles
1956, G I Budker and V I Veksler of the (then) USSR (Budker G I 1986 Proc. CERN Symp. on High Energy Accelerators vol 1 (Geneva: CERN) pp 68–80)
  Use of the fields generated in a plasma by the passage of a medium-energy electron beam to accelerate ions to high energy
Toshi Tajima and John Dawson of UCLA (Phys. Rev. Lett. 43 267 (1979))
  Use of a relativistically propagating disturbance or a wake created in a plasma by the passage of a short laser pulse to accelerate electrons to ultrahigh energies in a short distance
Pisin Chen at al., (Phys. Rev. Lett. 54 693 (1985))
  instead of a laser pulse, one can use a high-current bunch of electrons to generate very high electric fields in a plasma that can be used to accelerate particles extremely rapidly
Laser Wakefield Accelerator
Plasma Wakefield Accelerator
The plasmas does not only provide high acceleration gradients, ~GV/m, but they also serve to focus accelerated beam to micrometer scale spot size
First Ideas
Credits: C. Joshi and T. Katsouleas, AIP Physics Today 2003

## Slide 12: Basic Assumptions
Upstream from the laser or beam driver, each fluid can be treated as at rest or cold
For underdense plasmas, the phase velocity of the excited wakefields is roughly the speed of light, c
  Compared with this speed, all the initial thermal velocities of plasma particles can be treated as zero
Wavelike assumption
  Fields in the wake depend on the variable ct−z, where the phase velocity of the wave is essentially c
Quasi-static approximation
  The driver evolves on a time scale much longer than the plasma response
    the driver can be consider as non-evolving when calculating the plasma response. Therefore, the wake depends weakly on the distance the driver has moved into the plasma

## Slide 13: Plasma States
In Nature and in Laboratory
Notes: Grafico temperatura-densita’

## Slide 14: Plasma States
In Nature and in Laboratory

## Slide 15: Plasma Source
Gas-filled capillary
H2-filled capillary discharge
PH2 = 10 mbar
Total discharge duration :800 ns
Voltage : 20 kV
Peak current : 200 A
Capacitor : 6 nF
L = 3 cm
H2-filled capillary discharge
Courtesy of A. Biagioni (INFN - LNF)
Notes: Gas-filled capillary: The capillary is filled with hydrogen set at 10mbar (~100mbar outside the chamber).
A valve opens for few ms (~5ms) letting gas flow inside the capillary.
A discharge of ~20kV and 200A ionizes the gas.
L = 600 nH
R = ??
Rp = ??

## Slide 16: Plasma Source
Gas-filled capillary

## Slide 18: Response of a homogeneous plasma to a high frequency field
Let’s consider a charge q in an oscillating electric field with a non-uniform envelope
  Slowly varying envelope approximation (SVEA):
  Non relativistic equation of motion
    but not negligible (II order theory)
  Position of q = “slow” drift + “fast” oscillation
Hypotheses

## Slide 19: Fast Oscillations of Electrons
Let’s first neglect the B field and Taylor expand the E field around

## Slide 20
From III Maxwell equation:
The particle motion equation can be written as
Notes: dr1 =displacement with respect to the equilibrium r0

## Slide 21: Ponderomotive Force
Ponderomotive force
Ponderomotive force per unit volume

## Slide 22: Acceleration Mechanism

## Slide 23: Self-Injection and External Injection of Electrons
The driver, creating the bubble, can be either a dense relativistic particle beam (PWFA) of sub-
ps duration and kA level peak current
ultra-intense laser pulse (LWFA), ~1018 W/cm2, of few 10s fs duration
❖ Rapid acceleration of injected electrons to ultra-relativistic energies, inside the micrometer-sized structured plasma environment
❖ the trapped electron beam remains short, dense, and free of
significant space-charge driven emittance degradation
enrica.chiadroni@uniroma1.it
❖ ❖
❖
❖
The witness can be either self-injected or externally injected

## Slide 24: The Dawn of Compact Accelerators
September 2004
Notes: Malka’s next talk for an insight on LWFA

## Slide 25: The Dawn of Compact Accelerators
September 2004
See Malka’s talk for an insight on Laser Wakefield Acceleration
Notes: Malka’s next talk for an insight on LWFA

## Slide 26: Particle-driven Plasma Wakefield Acceleration
The high-gradient wakefield is driven by an intense, high-energy charged particle beam as it passes through the plasma.
The space-charge of the electron bunch blows out plasma electrons which rush back in and overshoot setting up a plasma oscillation
First demonstration of the excitation of a wakefield by a relativistic beam in the linear regime, i.e. beam density typically less than the plasma density => J. Rosenzweig et al., Phys. Rev. Lett. 61, 98 (1988)
Peak acceleration gradient ~ 1.6 MeV/m, but the experiment clearly showed the wakefield persisting for several plasma wavelengths
Single bunch

## Slide 27: PWFA: Energy doubling in a meter scale
Gaussian electron beam with 42 GeV, 3nC @ 10 Hz, sx = 10µm, 50 fs
85cm Lithium vapour source, 2.7x1017cm-3
  Accelerated electrons from 42 GeV to 85 GeV in 85 cm
  Reached accelerating gradient of 52 GeV/m
    Energy gain of the 3 km-long SLAC linac
Single bunch
  ∆E/E >> 1%
Credits: P. Muggli
Blumenfeld, I. et al. Nature 445, 741–744 (2007)

## Slide 28: Two-bunch Train PWFA
Bunch length of tens of fs down to fs scale
  A second, appropriately phased accelerating beam (witness beam), containing fewer particles than the drive beam, is then accelerated by the wake
    Bunch train (D+W) for bunch acceleration (∆E/E<<1)

## Slide 29: PWFA: High-efficiency acceleration
Injection of two beams into the plasma
  One drives the wake, driver, one samples the wake, witness
Beam loading is key for
  Narrower energy spread, ∆E/E <<1%, and high efficiency
Litos, M. et al. Nature 515, 92–95 (2014)

## Slide 30: Limitation of PWFA
PWFA acting as an energy transformer has the great potential to double beam energy in a single stage
The energy transfer from the drive bunch to the plasma is optimized by maximizing the transformer ratio
Energy gain
Symmetric drive bunch current profile in a single-mode structure: the maximum accelerating field behind the drive bunch cannot exceed 2 times the maximum decelerating field amplitude along the drive bunch
Wakefield theorem*
*V. V. Tsakanov, Nucl. Instrum. Methods Phys. Res., Sect. A 432, 202 (1999)

## Slide 31: Limitation of PWFA
Energy gain
The transformer ratio critically depends on the bunch shape and on the density ratio
<< 1
R ≤ 2
Notes: Semi-analitical model. One dimensional, fluid, relativistic, cold plasma equations have been numerically solved.

## Slide 32: Enhancing Transformer Ratio
By properly tailoring the driver bunch shape, the witness beam energy might be more than doubled when
  The maximum possible transformer ratio for a bunch with given length and total charge corresponds to that charge distribution which causes all particles in the bunch to see the same retarding field*
Tailoring longitudinal current profile such that all longitudinal slices lose energy at the same rate
  Asymmetric drive bunch current profile, i.e. triangular, double triangle, doorstep-like distributions, or multiple ramped bunch trains, overcome this limit (R.Ruth et al., PA 1985; W. Lu et al.,PAC 2009)
*K. Bane, P. Chen, and P. B. Wilson, SLAC-PUB-3662,1985

## Slide 33: PWFA: High-efficiency acceleration
Electric field in plasma wake is loaded by presence of trailing bunch
Allows efficient energy extraction from the plasma wake
Litos, M. et al. Nature 515, 92–95 (2014)

## Slide 34: Resonant PWFA
Bunch spacing depends on the plasma density
Increase in energy of a trailing particle ∆γmec2 ~ eE+,maxLd = Rγbmec2
Preservation of witness emittance and length
Better control of the energy spread
Multi-bunch shaping

## Slide 35: From Linear Regime: nb<<n0
Focusing force is sinusoidal
Lower wakefields
Transverse forces not linear in r
Symmetric for positive and negative witness bunches
Well described by theory
Notes: The plasma response to the perturbation introduced by the electron beam can be expressed by the degree of nonlinearity of the plasma dynamics that defines the plasma wave regime.

## Slide 36: to Quasi-Linear and Non-Linear Regime
The wake structure depends on the driver pulse «intensity»
Ez
Higher wakefields
transverse forces linear in r (emittance preservation)
High charge witness acceleration possible
Requires more intense drivers
Not ideal for positron acceleration

## Slide 37: Quasi-non Linear Regime
Condition for blow-out
  Bubble formation w/o wavebreaking, lp is constant
    Resonant scheme in blowout
  Linear focusing force => emittance preservation
A measure of non-linearity is the normalised charge
Using low emittance, high brightness beams
  Quasi-non Linear Regime
<<1 linear regime
>1 blowout regime
Notes: The figures of merit are the beam charge in the cubic plasma skin-depth, kp^-3, the so-called reduced charge

## Slide 42: High Quality Beams
Notes: Modern accelerators require high quality beams: ==> High Luminosity & High Brightness
==> High Energy & Low Energy Spread

## Slide 43: Towards the Applications
Multi-GeV acceleration of high brightness electron beams in cm-scale plasma structures
Injection and matching to plasma accelerating module
  The beam has to be focused to the matching spot to prevent envelope oscillations that may cause emittance growth
    Blow-out regime
Typical numbers
Matching condition

## Slide 44: Towards the Applications
Extraction from plasma accelerating module
  plasma fields stronger than in conventional accelerators
beams experience huge transverse size variation when propagating from the plasma outer surface to the conventional focusing optics
the particle transverse motion becomes extremely sensitive to energy spread
  the beam angular divergence has to be reduced and the transverse spot size increased to limit the chromatic induced emittance degradation in vacuum
M. Migliorati et al., PRST AB 16, 011302 (2013)
Notes: And recall the high rep rate and low energy spread

## Slide 45: Active Plasma Lenses
Discharge current in gas-filled capillary
Cylindrical symmetry
  purely radial focusing effect
Tunability
Focusing strength k∝γ -1
High focusing gradient ~ kT/m
  short focal length
  weak chromaticity

## Slide 47: Active Plasma Lens
Measurements at SPARC_LAB
Measurements
Beam dynamics and beam -plasma simulation
Focusing gradient
~ 100 T/m

## Slide 48: Plasma lens vs conventional focusing
Single Quadrupole Magnet
Single Plasma Lens

## Slide 49: Extraction Beamline
EuPRAXIA@SPARC_LAB Case
R. Pompili et al., Phys. Rev. AB 22, 121302 (2019)

## Slide 50: Plasma Wigglers
Betatron radiation based radiator
Courtesy of J. Rosenzweig
S. Kiselev et al., PRL 93, 135004 (2004)
Notes: Correggere K

## Slide 51: Radiation properties

## Slide 52: Conclusions
Plasma-based acceleration techniques have demonstrated accelerating gradients up to 3 orders of magnitudes beyond presently used RF technologies
Plasma-based acceleration techniques have provided solid feasibility proofs of FEL lasing paving the way to applications
Successful efforts on improving beam quality
R&D on beam stability, staging and continuous operation, as necessary steps towards the realization of compact plasma-based accelerator facilities
  Challenges in high repetition rate
Plasma-based, ultra-high gradient accelerators therefore open the realistic vision of very compact accelerators for scientific, commercial and medical applications

## Slide 53: References
Plasma lens experiments
  J. van Tilborg et al. PR-AB 20, 032803 (2017)
  S. Kuschel et al., Phys. Rev. Accel. and Beams 19, 071301 (2016)
Other Wakefields schemes
Recent papers