## Slide 1: Beam coupling impedance and collective effects for the Future Circular Lepton Collider
Emanuela Carideo
Special thanks:
M. Migliorati, F. Zimmermann, M. Zobov, D.Quartullo, Y.Zhang, M.Behtouei, B.Spataro
FCCIS – The Future Circular Collider Innovation Study. This INFRADEV Research and Innovation Action project receives funding from the European Union’s H2020 Framework Programme under grant agreement no. 951754. The information herein only reflects the views of its authors and the European Commission is not responsible for any use that may be made of the information.

## Slide 2
FCC-ee main parameters
High luminosity e+e- collider as potential first step to cover a beam energy range from 45.6 GeV to 182.5GeV

## Slide 3: Resistive wall
      The interaction of the beam with the environment can produce wakefields (impedances in the frequency domain) that induce instabilities
      The resistive wall impedance is produced by the finite conductivity of the pipe walls. The presence of the coating affects the RW impedance, increasing its imaginary part. The coating of the copper surface is required to reduce the SEY of the beam pipe walls for EC mitigation. The presence of this film makes the surface resistance of the beam pipe higher than pure copper
      Since the resistive wall impedance is proportional to , its contribution to the total machine impedance increases linearly with the machine length.
      The main difference between FCC-ee and other colliders is its large circumference ≈ km
      By increasing the machine length the contribution of the RW impedance assumes more and more importance with respect to other elements
      In FCC-ee, RW represents the main source of wakefields
35mm

## Slide 4: Main impedance sources: Bellows
They represent the second highest impedance source so far. We have used an upper pessimistic estimate of 20000 bellows
Simulated models of FCC-ee beam vacuum chamber including bellows. On the left there is a simplified model with circular geometry, in the centre a simplified model with winglets, on the right the realistic model
Other models are being considering for example from ESRF.

## Slide 5: Collimation system : Geometrical impedance
Geometric longitudinal wakefield of a 5 mm Gaussian bunch

## Slide 6: Collimation system : Resistive Wall
Table of the collimator settings for the Z machine and for the 4 IPs layout. The table includes both betatron and off-momentum collimators. The synchrotron collimators and masks upstream the IPs are not included in this table.
beam
For the resistive wall contribution we suppose parallel plates with infinite thickness and use IW2D for the impedance and wakefield evaluation.

## Slide 7: Collimation system
dipolar vertical impedance
dipolar horizontal impedance

## Slide 8: Total impedance: Longitudinal

## Slide 9: Total impedance: Transverse Dipolar

## Slide 10: Wake potential of 0.4 mm Gaussian bunch due to the main FCC-ee components, evaluated so far
How did we do these simulations?

## Slide 11
Wake potential for a Bellow of a 3.5 mm Gaussian bunch obtained directly by CST (blue curve) and with the convolution by using the wake potential of 0.4 mm Gaussian bunch (orange dots).
Method to calculate the Wake Potential by software simulation: Comparison of the wake potential of 3.5 mm bunch length between PyHT and CST - Bellows

## Slide 12: Method to calculate the Wake Potential by software simulation: BPMs

## Slide 13: Method to calculate the Wake Potential by software simulation: Tapers

## Slide 14: Method to calculate the Wake Potential by software simulation: RF Cavities

## Slide 15: Wake and impedance repository for FCC-ee: https://gitlab.cern.ch/ecarideo/FCCee_IW_Model
A repository, or Git project, encompasses the entire collection of files and folders associated with a project. Working in repositories keeps development projects organized and organized and protected.
The Repository also provides more opportunities for project transparency and collaboration, working together to build the best possible final product.
In this folder there are some of FCC-ee components and for each machine components the calculated impedance and wake
How is it developed?

## Slide 16
Longitudinal Dynamics: Microwave Instability
Bunch length (bottom) and RMS energy spread (top) as a function of bunch population in the case with (BS) and without (SR) beamstrahlung, which is considered here independent of the longitudinal impedance.
Longitudinal phase space
SR bunch length = 4.37 mm
BS bunch length = 14.5 mm

## Slide 17: Bunch length and energy spread for considered cases
The transverse impedance almost does not affect the longitudinal dynamics

## Slide 18: Longitudinal Dynamics: Beam-Beam interaction
The stable area is represented by the white region, and the colour map close to the figure represents the increase of the horizontal beam size σx with respect to the nominal value.
Without the collective effects there is a stable area in the middle at any simulated intensity up to a bunch. When we include the impedance model shows how this stable region is reduced. We have a narrower stable region at the nominal intensity.
Blow-up of the horizontal beam size σx/σx0 as a function of the bunch population and of the horizontal tune scan without impedance( left) and if including the impedance

## Slide 19: Transverse Dynamics: TMCI - PyHT & Delphi
Real part of the frequency shift of the first coherent oscillation modes as a function of the bunch population without beamstrahlung, by considering only the RW impedance produced by a NEG film with 100 nm thickness given by IW2D.
The TMCI, Transverse Mode Coupling Instability,
occurs when the frequencies of two neighboring coherent oscillation modes merge together. Above the transverse instability threshold the bunch is lost and this makes the TMCI very dangerous for the beam.
In addition to simulations with the tracking code, the TMCI threshold has been also evaluated with the analytic Vlasov solver DELPHI

## Slide 20: TMCI instability
On the top, real part of the frequency shift of the first coherent oscillation modes as a function of the bunch population without beamstrahlung, by considering only the transverse wakefield.
On the right, real part of the coherent tune shift as a function of intensity considering both longitudinal and transverse wakefield, by using PyHEADTAIL.
New parameter SR: Bunch length of 4.37 mm

## Slide 21: TMCI: longitudinal and transverse wake
New parameter BS: Bunch length of 14.5 mm

## Slide 22: Mitigation techniques
Chromaticity
Higher momentum compaction
Higher harmonic cavity
Feedback system and transverse coupled beam instability
Reduction of β function at the interaction point

## Slide 23: Chromaticity
On the left, real part of the frequency shift of the first coherent oscillation modes as a function of the bunch population without beamstrahlung, so considering a bunch length of 4.37mm and a value of Chromaticity of +5
On the right, real part of the frequency shift of the first coherent oscillation modes as a function of the bunch population without beamstrahlung, so considering a bunch length of 4.37mm and a value of Chromaticity of -5

## Slide 24
Strong dependence of the TMCI from the Chromaticity
Real part of the frequency shift of the first coherent oscillation modes as a function of the bunch population considering a bunch length of 4.37mm and a value of Chromaticity of +50 (Unrealistic value)

## Slide 25: Higher momentum compaction: MI
Energy spread and bunch length with the updated impedance model and the parameters of 2.1, with two different momentum compaction factors: 1.48 × 10−3 and 2.5 × 10−3

## Slide 26: Higher momentum compaction: TMCI
Transverse dynamics analysis considering the transverse RW with a momentum compaction of 1.48 e-3 a bunch length of 3.5 mm (left) and of 14.5 mm (rigth) so considering the beamstrahlung effect.
Transverse dynamics analysis considering the transverse RW with a higher momentum compaction and bunch length of 4.5 mm (left) and of 15.2 mm (rigth) so considering colliding bunches, beamstrahlung effect.

## Slide 27: Higher momentum compaction: beamstrahlung and collective effects in collision
Blow-up of the horizontal beam size σx/σx0 as a function of the bunch population and of the horizontal tune scan for arc cell of 45 ◦ /45◦
The safe tune areas are much larger and less current dependent, and the horizontal size blow-up is much lower for the tunes affected by the X-Z instability.
The blow-up of the horizontal beam size as a function of the bunch population

## Slide 28: Higher harmonic cavity
Bunch length, on the left, and energy spread, on the right, as a function of bunch population with and without the higher harmonic cavity system. The results are obtaining by using the code SBSC.

## Slide 29: Feedback system and transverse coupled beam instability
The most dangerous mode is that closest to the origin (with negative frequency)
Rise time of about 6 revolution turns
A robust feedback is required for the instability suppression!
The beam spectrum of some most dangerous coupled bunch modes and the transverse impedance of a 35 mm copper pipe without coating at low frequency
Notes: The transverse impedance is inversely proportional to the square root of the frequency

## Slide 30: ITSR instability: Imaginary Tune Split and Repulsion
[…] However, a resistive transverse damper also destabilizes the single-bunch motion below the transverse mode coupling instability intensity threshold (for zero chromaticity), introducing a new kind of instability, which has been called ITSR instability (for imaginary tune split and repulsion). […]
Introduction
Only Transverse wakefield with resistive feedback at 10 turns damping time

## Slide 31
ITSR instability: Imaginary Tune Split and Repulsion
Longitudinal and Transverse wakefield with a resistive feedback at 10 turns damping time
The spread in the synchrotron tune due to the longitudinal wakefield helps to mitigate the ITSR instability

## Slide 32: ITSR instability: Imaginary Tune Split and Repulsion
Longitudinal and Transverse wakefield with a resistive feedback at 4 turns damping time
Beamstrahlung reduces the effect of the longitudinal wakefield which, on its turn, has a beneficial effect on the TMCI with a resistive transverse damper. What happens if both effects are present?

## Slide 33: Reduction of β function at the interaction point
Normalized horizontal beam size as a function of the horizontal tune for a bunch population of Np = 2.8 x 1011 (on the left) and Np = 1.4 x 1011 (on the right) at different chromaticities with β∗x = 10 cm.
X-Z instability threshold is inversely proportional to the horizontal betatron function at the interaction point
It generates a reduction of the dynamic aperture and of momentum acceptance.

## Slide 34: Conclusions
The collective effects are particular important on the Z resonance due to the low energy and high beam current.
Simulations have been performed for the main elements to characterize and optimize the impedance of important machine components. The RW is the most important source of the machine impedance, followed by bellows and collimators.
Two collective effects codes have been compared, PyHT, tracking simulation code, and Delphi, a Vlasov solver. The comparison results demonstrate a good agreement between the two codes.
Studies of collective effects have been done without beam-beam interaction but with both longitudinal and transverse wakefields simultaneous which reveal a lower threshold for the TMCI due to the strong effect of the longitudinal wakefields.
Since the impedance is expected to increase with the addition of more components the situation could become worst. So we have studied eventual mitigation techniques.

## Slide 35: Challenges and Future Plan
FCC-ee is an ongoing project, every time we analyze new devices, we find a continuous increase of the total machine impedance. For this reason, of course, we want to continue the work for the evaluation, reduction and optimization of the impedances of the main machine elements (e. g. collimators system which is an important source of transverse impedance), and also for implementing the FCC-ee repository.
Collective effects play an important role for the stability of the machine, an important aim will be to continue to investigate on the beam-beam effect, longitudinal and transverse coupling impedance
We need to look to other diversified mitigation techniques: Beam instability thresholds and stability regions can change according to the new impedance sources that will be gradually added.

## Slide 36: Thanks for your kind attention!

## Slide 37: Back up slides

## Slide 38: NEG coating is needed to mitigate the electron cloud build-up in the positron machine and for pumping reasons in both rings.
IW2D results for a circular pipe.
Longitudinal Impedance
Transverse Impedance

## Slide 39: More realistic model: We estimated a factor 1.1 for winglets contribution
The quadrupole wake has been calculated but its contribute can be negligible
Contribution of the winglets: we used CST with a low conductivity material (but still in the good conductor regime). Then we divided the result by its surface impedance and multiplied it by the double-layer surface impedance

## Slide 40: New evaluation of the impedances using different NEG coating : 100 nm 150 nm and 200 nm

## Slide 41
Longitudinal dynamics

## Slide 42: TMCI analyzes using wake with different NEGs : 100nm, 150 nm and 200 nm
On the letf the plot of the TMCI considering a wake with 100nm of NEG and a beam length of 3.5mm
On the right the plot of the TMCI considering a wake with 100nm of NEG and a beam length of 12.1mm

## Slide 43: TMCI analyzes using wake with different NEGs : 100nm, 150 nm and 200 nm
On the letf the plot of the TMCI considering a wake with 150nm of NEG and a beam length of 3.5mm
On the right the plot of the TMCI considering a wake with 150nm of NEG and a beam length of 12.1mm

## Slide 44: TMCI analyzes using wake with different NEGs : 100nm,150 nm and 200 nm
On the letf the plot of the TMCI considering a wake with 200nm of NEG and a beam length of 3.5mm
On the right the plot of the TMCI considering a wake with 200nm of NEG and a beam length of 12.1mm

## Slide 45: Updated FCC-ee impedance model: 20000 Bellows
We initially considered a number of 8000 Bellows
85% of arcs (~ 79 km)
Every arc is 8m long
X2 because we have another bellow before any quadrupole
12000-13000 but to be sure we are performing our calculations considering up to 20000 bellows
BUT

## Slide 46: Longitudinal wake potential and impedance for the three studied models of the bellow

## Slide 47: Beam Position Monitors : #4000
CST perspective view of the four-button BPM
The button has a diameter of 15 mm and a thickness of 3 mm
In order to push the higher order modes trapped in the BPM structure to higher frequencies a BPM design with a conical button, similar to the one used in SIRIUS
BPMs will be installed directly on the beam pipe with a rotation angle of 45°

## Slide 48: Collimation system : Models
CST vertical collimator models for the FCC-ee, proposed by Mauro Migliorati
CST collimator models for the SuperKEKB, thanks to Takuya Ishibashi.

## Slide 49: Collimation system
dipolar vertical impedance
dipolar horizontal impedance

## Slide 50: Total impedance: Transverse Quadrupolar
The oscillations of bellows at high frequency are not physic but they don’t influenced the wake potential of longer bunch. NB the wake of the bellows is still a work in progress.

## Slide 51: New Wakes with new machine parameters : Longitudinal RW with 150nm of coating plus the Bellows without neglected the perturbation introduced by the lateral winglets used to place synchrotron radiation absorbers
https://indico.cern.ch/event/995850/contributions/4401571/attachments/2275135/3864813/FCCweek.pdf

## Slide 52
Longitudinal dynamics: OLD machine parameters
Bunch length (bottom) and RMS energy spread (top) as a function of bunch population in the case with (BS) and without (SR) beamstrahlung, which is considered here independent of the longitudinal impedance.

## Slide 53: TMCI
Without longitudinal resistive wall wakefield
Considering the longitudinal resistive wall wakefield
SR: Bunch length of 3.5 mm

## Slide 54: Transverse RW for a beam length of 12.1mm: TMCI analysis
Transverse wake: PyHT vs Delphi
Longitudinal wake
Without longitudinal wakefield
Considering the longitudinal wakefield

## Slide 55: Interplay between beam-beam and longitudinal impedance
The study of the interplay between beam-beam interaction, beamstrahlung, and longitudinal collective effects has been performed with the simulation code IBB
Comparison between IBB, orange line, and PyHEADTAIL, blue line, of energy spread σp (top) and bunch length σz (bottom) as a function of the bunch population without collision.
IBB simulation results thanks to Yuan Zhang.

## Slide 56
Reduction of β func. at the IP: Luminosity
At high intensity of Np = 2.8 × 1011 and a chromaticity of 5 we lose about 15% of luminosity per IP, but this parameter still remains in a good range, above 180 < 1034/(cm2s)