## Slide 1
6th European Advanced Accelerator Concepts workshop (EAAC2023)
Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy
September 17-23, 2023
Latest algorithmic
advances in the
Exascale Particle-In-Cell
code WarpX
Jean-Luc Vay
Lawrence Berkeley National Laboratory
On behalf of the WarpX team
LBNL, LLNL, SLAC
AM
+ contributors external to ECP from labs,
universities & industry in USA, Europe & Asia

## Slide 2: Outline
US DOE Exascale Computing Project (ECP) & WarpX
  Quick overview of WarpX PIC algorithms
Latest algorithmic advances
  time-averaged PIC
  Hybrid alternating Nodal-Staggered PIC
  Particles in Perfectly Matched Layers
  Mesh refinement
Outlook

## Slide 3: U.S. DOE Exascale Computing Initiative (ECI) – 2016-2023
D. Kothe – April 30, 2019
Delivers 5x performance of 200 petaflop Summit (ORNL)
Software stack for broad spectrum of apps & workloads
Wide range of apps that deliver high-fidelity solutions faster to more complex problems
Exascale Computing Initiative

## Slide 4: WarpX among 21 applications selected to cover broad range of science

## Slide 5
Challenge of the ECP WarpX Project:
Go from modeling 1 or 2 plasma stages
to tens of stages
in 3D from first principles
Particle-In-Cell on fastest/largest supercomputers
with advanced algorithms

## Slide 6: Timeline for Exascale project WarpX From initial code coupling to ensemble of chains of multi GeV-scale stages
Initial coupling of AMReX and Warp/PICSAR
2016
Modeling chain of 5-10 multi-GeV-scale plasma accelerator stages
2020
Modeling a single multi-GeV-scale plasma accelerator stage
2018
Modeling chain of 10-20 multi-GeV-scale plasma accelerator stages
2021
Modeling chain of 20-50 multi-GeV-scale plasma accelerator stages
2022
Modeling of chain of 50-100 multi-GeV-scale plasma accelerator stages
2023
Collider designs
2030 -
Modeling of single plasma accelerator stage with static mesh refinement
2017
Modeling chain of 3 multi-GeV-scale plasma accelerator stages
2019
Original
Notes: Instructions:
Summarize milestone-based plan for next 3 years

## Slide 7: Timeline for Exascale project WarpX From initial code coupling to ensemble of chains of multi GeV-scale stages
Initial coupling of AMReX and Warp/PICSAR
2016
Modeling chain of 5-10 multi-GeV-scale plasma accelerator stages
2020
Modeling a single multi-GeV-scale plasma accelerator stage
2018
Modeling chain of 10-20 multi-GeV-scale plasma accelerator stages
2021
Modeling of novel plasma e- beam injection scheme
2022
Modeling of chain of 15-30 multi-GeV-scale plasma accelerator stages
2023
Collider designs
2030 -
Modeling of single plasma accelerator stage with static mesh refinement
2017
Modeling chain of 3 multi-GeV-scale plasma accelerator stages
2019
Revised
Notes: Instructions:
Summarize milestone-based plan for next 3 years

## Slide 8: Quick overview of WarpX PIC algorithms

## Slide 9: WarpX is an electromagnetic Particle-In-Cell (PIC) code
Δt
Eulerian
electromagnetic fields on structured grid
Lagrangian
charged macroparticles
+
+
+
+
+
+
-
-
-
-
-
-
Push particles
Newton-Lorentz
Deposit sources
w/ shape factor
Gather fields
w/ shape factor
Solve fields
Maxwell*
*Electrostatic+magnetostatic option available at runtime

## Slide 10: WarpX supports many advanced features: some are unique
Geometries
1D3V, 2D3V, 3D3V and RZ (quasi- cylindrical)
Multi-Physics Modules beyond standard PIC
ionization, Coulomb collisions, QED processes, Maxwell’s Eq. in matter, embedded boundaries
Advanced Algorithms
mesh refinement, Maxwell spectral solvers, boosted frame, Galilean frame, …
High-order particle shape |  |  |  |  |  |  | 
Moving window |  |  |  |  |  |  | 
Single source CPU & GPU |  |  |  |  |  |  | 
Dyn. LB for CPU & GPU |  |  |  |  |  |  | 
Mesh refinement |  |  |  |  |  |  | 
Boosted frame |  |  |  |  |  |  | 
Spectral Maxwell solver |  |  |  |  |  |  | 
✓ | ✓ | ✓ | ✓ | ✓ |  | ✓
✓ | ✓ | ✓ | ✓ | ✓ |  | ✓
 |  | ✓ | ✓ |  | ✓ | ✓
 |  |  |  |  |  | ✓
 |  |  |  |  |  | ✓
 | ✓ |  |  |  |  | ✓
 |  |  |  |  |  | ✓
ecp-warpx.github.io
Open source
Code*
Epoch
Osiris
PICADOR
PIConGPU2
Smilei
VPIC1
WarpX3
1 Gordon Bell Finalist 2008
2 Gordon Bell Finalist 2013
3 Gordon Bell Winner 2022

## Slide 11
cΔt/Δx~0.45
Higher order
Kronecker δ pulse
Finite-difference
N→∞ = Pseudo-spectral (FFT)
cΔt/Δx~0.045
Accurate but Expensive
(with leapfrog integrator)
Arbitrary-order Maxwell solver offers flexibility in accuracy

## Slide 12
1I. Haber,R. Lee,H. Klein & J. Boris,Proc. Sixth Conf. on Num. Sim. Plasma, Berkeley, CA, 46-48 (1973)
PSATD cΔt/Δx=50
1 time step
Easy to implement arbitrary-order n with PSATD (k=k⚯  kn).
Pseudo-Spectral Analytical Time-Domain1 (PSATD)
Analytical integration in Fourier space.
No Courant condition

## Slide 13: Galilean PSATD PIC controls the numerical Cherenkov instability (NCI)
Original idea by Manuel Kirchen (U. Hamburg) Concept and applications: Kirchen et al., Phys. Plasmas 23, 100704 (2016)
Grid follows the relativistic plasma.
+ integrate analytically, assuming
is constant over one timestep.
Derivation of the algorithm by Rémi Lehe (Berkeley Lab):
Lehe et al., Phys. Rev. E 94, 053305 (2016)
Standard PSATD PIC
Galilean PSATD PIC
Plasma moves through fixed grid.

## Slide 14: WarpX also implements mesh refinement
Need to avoid spurious:
  self-forces
  wave reflections
  dispersion mismatch

  buffer regions
  multiple grids with PMLs around patches
  subcycling/pseudo-spectral solvers
1J.-L. Vay, J.-C. Adam, A. Héron, Computer Physics Comm. 164, 171-177 (2004).
2J.-L. Vay, D. P. Grote, R. H. Cohen, & A. Friedman, Computational Science & Discovery 5, 014019 (2012).

## Slide 15: Latest algorithmic advances

## Slide 16: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 17: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 18: Simulations in boosted frame can be limited by CFL condition
Dz<<Dx
Lorentz
Transform
Dz>>Dx
Attempting to simulate
with Galilean PSATD-PIC
with cDt=Dz
Unstable
laser
z
x
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 19
Push particles
Field solve in k-space
Gather forces
Deposit currents
FFT: xk
iFFT: kx
O. Shapoval, et al., Phys. Rev. E 104, 055311 (2021) doi.org/10.1103/PhysRevE.104.055311
Instability with large time step comes from time aliases
Standard PSATD PIC: fields are sampled at each time step  aliasing

## Slide 20
Push particles
Field solve in k-space
Gather forces
Deposit currents
FFT: xk
iFFT: kx
O. Shapoval, et al., Phys. Rev. E 104, 055311 (2021) doi.org/10.1103/PhysRevE.104.055311
Solution is to average analytically fields to gather
Standard PSATD PIC: fields are sampled at each time step  aliasing
Average fields to gather over 1 time step*
Solution:
*proposed by R. Lehe
Takes advantage of PSATD solver to average fields analytically
The fields that evolve with Maxwell’s equations are untouched (no field damping over time)

## Slide 21
Standard Galilean PSATD-PIC
Unstable
laser
Averaged field within time step
Averaged Galilean PSATD-PIC
Stable
laser
Example: cΔt=Δz=10Δx
Velocity push:
Sampled fields within time step
Dx
Dz=10Dx
*O. Shapoval, et al., Phys. Rev. E 104, 055311 (2021) doi.org/10.1103/PhysRevE.104.055311
Averaged PSATD PIC stabilizes simulations at large time steps

## Slide 22: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 23
Staggered vs nodal Maxwell solve pros & cons
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal

## Slide 24
Staggered vs nodal Maxwell solve: dispersion relation
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
order 16
nodal
staggered

## Slide 25
Staggered vs nodal Maxwell solve: compactness of stencil support
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
nodal
staggered

## Slide 26
Staggered vs nodal Maxwell solve: stability with domain decomposition
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
nodal
staggered

## Slide 27
Staggered vs nodal Maxwell solve: interpolation errors
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
E + v x B

## Slide 28
Staggered vs nodal Maxwell solve: numerical Cherenkov instability (NCI)
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
laser
Staggered - unstable
Nodal - stable

## Slide 29
Staggered vs nodal Maxwell solve: summary
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
Numerical dispersion
Stencil compactness
Stability w/ domain decomposition
Interpolation errors
NCI
Numerical dispersion
Stencil compactness
Stability w/ domain decomposition
Interpolation errors
NCI
Field
solve
Field
gather

## Slide 30
Staggered vs nodal Maxwell solve: retaining advantages of both
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
E,B,J
Staggered (Yee)
Nodal
Staggered
Nodal

## Slide 31
*E. Zoni, et al., Comput. Phys. Comm. 279, 108457 (2022) doi.org/10.1016/j.cpc.2022.108457
laser
Nodal: stable
Staggered: unstable
Alternating: order 2
Alternating: order 4
Alternating: order 6
Alternating: order 8
~✕2 speedup simulations of laser-plasma accelerator
More guard cells
Less guard cells
Alternating nodal-staggered PIC loop provides significant speedup
~✕10 speedup simulations of high-field physics with QED effects*
Mitigates calculation of (E2-c2B2) from staggered grid.
Alternating
Alternating
Alternating
Alternating

## Slide 32: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 33: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 34: New algorithm to handle particles crossing Perfectly Matched Layers*
Standard Perfectly Matched Layer (PML)
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306
Additional terms are exact solution for absorbing layer for particles crossing PMLs at normal incidence.
Standard PML

## Slide 35: New algorithm to handle particles crossing Perfectly Matched Layers*
Standard Perfectly Matched Layer (PML)
New terms for particles crossing PML
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306
Additional terms are exact solution for absorbing layer for particles crossing PMLs at normal incidence.
Standard PML
PML w/ deposition

## Slide 36: New algorithm to handle particles crossing Perfectly Matched Layers*
Standard Perfectly Matched Layer (PML)
New terms for particles crossing PML
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306
Additional terms are exact solution for absorbing layer for particles crossing PMLs at normal incidence.
Standard PML
PML w/ deposition
PML w/ damped deposition

## Slide 37
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306
Provides efficient absorption of e- ejected transversally in LPA simulations

## Slide 38
Work is ongoing to extend algorithms to wider range of angles.
Absorption is less perfect when particles are ejected at a lower angle.
*R. Lehe, et al., Phys. Rev. E 106, 045306 (2022) doi.org/10.1103/PhysRevE.106.045306

## Slide 39: Advanced algorithms & advances in algorithms are needed
Lower # time steps
Optimal Lorentz boosted frame
Time-averaged PIC
Higher accuracy
Spectral (FFT-based) Maxwell solvers (PSATD)
Particles in Perfectly Matched Layers (PML)
(Adaptive) Mesh Refinement
Preserve scalability
PSATD: FFT on local subdomains
Hybrid alternating nodal-staggered PIC
Higher stability
Galilean PSATD suppresses Numerical Cherenkov Instability (NCI)
Lorentz
Transform
Notes: Instructions:
List any technical, programmatic, or personnel challenges / risks and if / how you plan to manage them

## Slide 40: MR simulation with 4x refinement to simulate LWFA with ion motion
Maxwell Solver : PSATD
Refinement Ratio = 4 4 1

## Slide 41: More than 6x cost saving with 4 4 1 mesh refinement
Transverse lineout of focusing field and ion density at (towards the end of the bubble, where ion motion is prominent)
Without Mesh Refinement
(#Nodes)*(Time)
= 22*0.409 = 9.002
With Mesh Refinement
(#Nodes)*(Time)
= 5*0.269 = 1.345
Computational Cost
Estimates
6.69x less node hours used with MR!
Transverse electric field
Ions charge density

## Slide 42: Outlook

## Slide 43: Can do now simulations of chains of 50 multi-GeV LWFA stages
Work in collaboration with A. Ferran Pousa (DESY)
LWFA lattice:
Length plasma columns: 28cm
Gaps: 3cm
Plasma lens model: linear thick lens (3 mm) w/ “residence correction”
Electron beam:
Charge: -1 fC
Size: 0.75 mm x 0.75 mm x 0.1 mm
Emittance: 1 mm.mrad
Grid size/resolution:
128 x 128 x 17664
2 mm x 2 mm x 0.01 mm
Computer: 256 GPUs for 8h on Perlmutter (NERSC)

## Slide 44
Ez [V/m]
r [C/m3]
Iteration 14800; t = 51.4 ps
Stage 5
Stage 4
Stage 2
Stage 3
e- beam
Or high-resolution simulations of a few multi-GeV LWFA stages
LWFA lattice:
Length plasma columns: 32cm
Gaps: 1cm
Electron beam:
Charge: -0.15 nC
Size: 0.6 mm x 0.6 mm x 3 mm
Emittance: 0.25 mm.mrad
Grid size/resolution:
2304 x 2304 x 19456
0.14 mm x 0.14 mm x 0.008 mm
Computer: 49248 GPUs for 12h on Frontier (OLCF)

## Slide 45: RZ solver w/ novel algorithms for faster/bigger/longer simulations
Geometries
1D3V, 2D3V, 3D3V and RZ (quasi- cylindrical)
Multi-Physics Modules beyond standard PIC
ionization, Coulomb collisions, QED processes, Maxwell’s Eq. in matter, embedded boundaries
Advanced Algorithms
mesh refinement, Maxwell spectral solvers, boosted frame, Galilean frame, …
ecp-warpx.github.io
Open source
Algorithms developed for 3D simulations are also being implemented in axisymmetrical (+ azimuthal Fourier decomposition) for modeling:
faster
at higher resolution
longer chains of plasma accelerator stages

## Slide 46: WarpX: conceived & developed by a multidisciplinary, multi-institution team
Ryan
Sandberg
Andrew
Myers
Weiqun
Zhang
John
Bell
Jean-Luc Vay (ECP PI)
Rémi
Lehe
Olga Shapoval
Ann Almgren (ECP coPI)
Marc Hogan (ECP coPI)
Lixin Ge
Cho
Ng
David Grote (ECP coPI)
Revathi
Jambunathan
Axel Huebl
Yinjian
Zhao
Kevin
Gott
(NESAP)
Edoardo
Zoni
Hannah Klion
Prabhat Kumar
Junmin
Gu
Marco Garten
AM
Arianna Formenti
(France)
a growing list of contributors from labs, universities…
Lorenzo
Giacomel
(Switzerland)
…& private sector
Henri
Vincenti
Luca
Fedeli
Thomas
Clark
Neïl
Zaim
Pierre
Bartoli
(Germany)
Maxence Thévenet
Alexander
Sinn

## Slide 47: Outlook: Ecosystem is growing
WarpX
full PIC, LPA/LPI
AMReX
Containers, Communication, Portability, Utilities
MPI
CUDA, OpenMP, SYCL, HIP
Diagnostics
I/O code coupling
ADIOS2
HDF5
Lin. Alg.
BLAS++ LAPACK++
Ascent
...
Python: Modules, PICMI interface, Workflows
ZFP
VTK-m
openPMD
PICSAR
QED Modules
FFT
on- or multi- device
ABLASTR library: common PIC physics
ARTEMIS
microelectronics
ImpactX
accelerator lattice design
Desktop
to
HPC
HiPACE++ quasi-static, PWFA
Object-Level Python Bindings
extensible, AI/ML
pyAMReX
Notes: lead
data-driven (AI/ML) activities
start-to-end
transform community of compete projects into community ecosystem of interoperable modules
competition/duplication
we need them together

## Slide 48
Thank You!
Questions?

## Slide 49
Funding Support
WarpX: longitudinal electric field in a laser-plasma accelerator
rendered with Ascent & VTK-m
This research was supported by the Exascale Computing Project (17-SC-20-SC), a collaborative effort of two U.S. Department of Energy organizations (Office of Science and the National Nuclear Security Administration) responsible for the planning and preparation of a capable exascale ecosystem, including software, applications, hardware, advanced system engineering and early testbed platforms, in support of the nation’s exascale computing imperative. This work was also performed in part by the Laboratory Directed Research and Development Program of Lawrence Berkeley National Laboratory under U.S. Department of Energy Contract No. DE-AC02-05CH11231, Lawrence Livermore National Laboratory under Contract No. DE-AC52–07NA27344 and SLAC National Accelerator Laboratory under Contract No. AC02–76SF00515. This research used resources of the Oak Ridge Leadership Computing Facility, which is a DOE Office of Science User Facility supported under Contract DE-AC05-00OR22725, the National Energy Research Scientific Computing Center (NERSC), a U.S. Department of Energy Office of Science User Facility located at Lawrence Berkeley National Laboratory, operated under Contract No. DE-AC02-05CH11231, and the supercomputer Fugaku provided by RIKEN.

## Slide 50: Plasma accelerators are challenging to model
Short driver+wake propagates through long plasma
Many time steps.
E.g., for a 10 GeV LPA scale stage:
~1μm wavelength laser propagates into ~1m plasma millions of time steps needed (even with moving window)
Simulations (in 2D) can take days for 1 stage (at insufficient resolution for collider beam quality).
For multi-TeV collider, need for ×10s-1000s stages ×10s-1000s (high res. 3D) ×10s (ensembles)!
Need for advanced algorithms and supercomputing!
Very small features: Many grid cells.
wake
driver
plasma