## Slide 1: EuAPS EuPRAXIA Advanced Photon Source – WP2
Alessandro Cianchi
University of Rome Tor Vergata & INFN
On behalf of SPARC_LAB & Eupraxia collaborations

## Slide 2
INFN-LNF
ENEA
ESA-ESRIN
CNR-ARTOV
ASI
TOR VERGATA
South East Rome, within 10km, several research institutions
Slightly less than 30,000 students
Faculty of Economics.
Faculty of Law.
College of Engineering.
Faculty of Literature and Philosophy.
Faculty of Medicine and Surgery.
Faculty of Mathematical, Physical and Natural Sciences.

## Slide 3: EuPRAXIA Galaxy @ TOR VERGATA
Alessandro Cianchi – PNRR and EuPRAXIA beam instrumentation
Francesco Stellato – PNRR and EuPRAXIA user experiments
Mario Galletti –PNRR and laser
Federico Galdenzi – PNRR users experiments
Federica Stocchi – PNRR
Mauro Sbragaglia – EuPRAXIA Simulations
Daniele Simeoni - EuPRAXIA Simulations
Fabio Guglietta - EuPRAXIA Simulations
Gianmarco Parise –EuPRAXIA Simulations

## Slide 4: Outline
What are we going to do?
  A user facility based on Betatron source
Where?
  In the SPARC tunnel @ LNF
Who?
  INFN-LNF, INFN-Mi, CNR-Montelibretti, CNR-Potenza, Tor Vergata
To do what?
  Applications

## Slide 5
High repetition lasers
L. Labate (CNR)
4.863.150,00
Betatron X rays source
A. Cianchi (Tor Vergata)
7.864.500,00
9.457.088,00
High power lasers
P. Cirrone (INFN)
Principal Investigator
M. Ferrario (INFN-LNF)
22.350.588,00
Management & Financial office
A. Falone (INFN)
Milano
Milano
Pisa
Frascati/Roma Tor Vergata
Potenza
Catania

## Slide 6: Betatron radiation emission
The radiation has its characteristics of both FELs and synchrotrons
  Large bandwidth similar to Synchrotrons
  Short pulse duration like a FEL

## Slide 7: Synchrotrons vs FELs
Patricia Daukantas Synchrotron Light Sources for the 21st Century Optics & Photonics News Settembre 2021
Ph/ (s mm2 mrad2 0.1% of bandwidth)

## Slide 8: Wiggler or undulator?
K>>1
K≤1

## Slide 9: Damped oscillations and acceleration lead to inhomogenous brodening
Differently from a wiggler, the oscillation amplitude and frequency depend upon time.
Furthermore, each electron corresponds to a different initial amplitude (position of injection) : this will bring to an inhomogeneous broadening of the radiation spectrum.
In a magnetic undulator, the strength parameter is approximately the same for all electrons and depends only on physical constants and the magnetic field.
Each electron's strength parameter in a plasma focusing channel differs. It depends on the oscillation amplitude, leading to inhomogeneous broadening of the radiation spectrum and suppression of the spectral-angular correlations.
Another cause for inhomogeneous broadening is undoubtedly the energy spread, common to both a magnetic undulator and a plasma-focusing cannel.

## Slide 10
Betatron Radiation
Synchrotron Radiation
Peak
Mean
Critical frequency
On-axis
Cumbersome expression, where Bessel K functions are integrated upon time.
No appearance of Bessel K5/3.
This enhances low-frequency photons compared to the Synchrotron Radiation spectrum (effect of the acceleration).
Power
Spectral Density
Courtesy A. Curcio

## Slide 11: Ionization injection
Electrons that get accelerated have to travel along the cavity sheath and enter the cavity at the back.
It is found that these electrons originate from a ring-shaped region around the laser axis
In contrast, in the case of ionization-induced injection electrons are ionized inside the cavity, close to the maximum intensity of the laser. Injection can, therefore, occur longitudinally, and the initial position of trapped electrons is very different
It results in a better controlled injection and more beam stability
Döpp, Andreas, et al. "Stable femtosecond X-rays with tunable polarization from a laser-driven accelerator." Light: Science & Applications 6.11 (2017): e17086-e17086.

## Slide 12: Off Axis injection
A high-power laser (red) is focused into a double-peaked “M” shaped gas jet (blue).
The laser evolution during the first density peak leads to off-axis electron injection during the following density downramp.
Subsequent large-amplitude betatron oscillations (yellow) cause intense emission of X-ray radiation (purple).

## Slide 13: Expected Parameters
Parameter | Value | unit
Electron beam Energy | 100-500 | MeV
Plasma Density | 1018-1019 | cm-3
Photon Critical Energy | 1 -10 | keV
Number of Photons/pulse | 106-109 | 
Repetition rate | 1-5 | Hz
Beam divergence | 3-20 | mrad

## Slide 14: Example of gas cell
Götzfried, J., et al. "Research towards high-repetition rate laser-driven X-ray sources for imaging applications." Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 909 (2018): 286-289.
Laser 800 nm, 27 fs, 1.9 ± 0.1 J in a spot size of 30 μm (FWHM intensity), which
corresponds to a peak intensity of 5.5 × 1018 W∕cm2 and a peak power of 70 TW resulting in 𝑎0 ≈ 1.6.
Plasma density of 5×1018 cm−3
length 11 mm
Critical energy at 13.5 keV
About 700 pC, pure H2
(1.6 ± 0.35) × 109 photons/msr/s
Divergence of 12 × 6 mrad2 (s.d.)

## Slide 15: Other gas cell examples
Wenz, Johannes, et al. "Quantitative X-ray phase-contrast microtomography from a compact laser-driven betatron source." Nature communications 6.1 (2015): 1-6.
Döpp, A., et al. "Quick x-ray microtomography using a laser-driven betatron source." Optica 5.2 (2018): 199-203.

## Slide 16: Gas cell (Pallas Collaboration)
J. Kim et Al., RSI 25, 92, 023511 (2021)
Courtesy A. Biagioni
The high brightness beam target developed by PALLAS project in collaboration with LNF could be an interesting opportunity.
No strong modifications to the Interaction chamber
Vacuum pumping system
Rep Rate (10 Hz)
Neutral gas pressure(1 bar)
Laser ablation/sapphire materials
Complicate machining

## Slide 17
Betatron sources have already allowed performing X-ray measurements
EuAPS is not aiming at reinventing the wheel, but we can build up and improve moving from the wheels that have already been invented.

## Slide 18: Photon Science @ EuAPS
Imaging of biological (and cultural heritage) samples
  Exploits the brilliance and coherence of betatron radiation, requires small divergence and good focusing
Static X-ray Spectroscopy
  Relatively easy, but does not exploit the radiation time structure
Ultra-fast X-ray spectroscopies exploiting ultra-short betatron pulses
  More complicated, requires timing between pump and probe pulses, but fully exploits the fs pulse duration
Time-resolved imaging (ultrafast dynamics)
Wide angle scattering, diffraction
  Depending on the samples, requires monochromatic beams with high flux
Courtesy F. Stellato
Condensed Matter 7.1 (2022): 23.

## Slide 19: Imaging – The pilot experiment
Green science
X-ray imaging of leaves (and wood)
aiming at the (tens of) microns resolution
Experiments performed with the broad radiation spectrum filtered by different materials to obtain difference maps emphasizing the presence of heavy metal contaminants  pollution control
Reale et al. - MIDIX Soft X-rays microradiography

## Slide 20: Imaging – CT and Phase Contrast
Betatron sources can fill the gap between synchrotrons and X-ray tubes for imaging and Computer Tomography (CT)
Guo et al. Scientific Reports 2019
Cole et al. PNAS 2018
Betatron sources have a spatial coherence that allows performing Phase Contrast Imaging (PCI). In PCI, one measures the difference in wavefront, while in “traditional” imaging one measures the difference in the X-ray absorption coefficient between different “objects”
PCI provides better contrast than radiography, especially when dealing with biological samples. Wenz et al. Nature communications 2015

## Slide 21
Material Science Applications: Warm Dense Matter (WDM)
Mahieu, B., et al. "Probing warm dense matter using femtosecond X-ray absorption spectroscopy with a laser-produced betatron source." Nature Communications 9.1 (2018): 3276.

## Slide 22: Where?
The source will be hosted at LNF-INFN
Several parts will be realized at CNR (Photon Diagnostics) and at Tor Vergata (User end station)
INFN-Mi will take care of simulation and data analysis
There is now a contribution from Trieste university that focuses on applications
Activity | Where | Target
2.1 | INFN-Mi | Simulation & Data Analysis
2.2 | LNF-INFN | Plasma source
2.3 | LNF-INFN | Synchronization
2.4 | CNR-Potenza | Photon Diagnostics
2.5 | Tor Vergata | End user station
2.6 | CNR- Montelibretti | Photon time diagnostics

## Slide 23
Flame building ground floor
Flame building underground floor
S. Lauciani

## Slide 24: SPARC_LAB bunker
Layout in the SPARC bunker and connection with FLAME building
S. Lauciani

## Slide 25: Interaction point
Main issue is the pumping of 20-30 bar with repetition rate at least 1 Hz
The focusing parabola has to be at least at 10-4 mbar
V. Lollo

## Slide 26
Plasma simulations are performed using FBPIC
Self-injection is exploited
A long gasjet is employed, 5 mm
n0 is in the range 3.5 1018 cm-3 - 2.5 1019 cm-3
Laser energy is varied between 1 J and 3 J
Injected particles are tracked for post processing
Radiation yield is computed with a specifically developed script (A. Frazzitta)
Field is calculated by Liénard-Wickert retarded fields
Spectrum is calculated by Fourier transform
Numerics has been optimized for performances and reliability vs sampling
A. Rossi “Electron yield numerical studies for the EuAPS betatron source” Tuesday Poster ID179

## Slide 27: A. Frazzitta: “Betatron radiation from accelerated electrons: an analytical study”, Wednesday poster ID 268
By generalizing well-known results (I. Kostyukov, S. Kiselev, and A. Pukhov), we derive a comprehensive analytical expression for the emission spectrum in solid angle for single particles subjected to constant longitudinal force and linear transverse force moving in a planar trajectory.
Model's approximations are presented, along with intensity plots on the detector and trends in critical frequency for some plasma wiggler strength and longitudinal force values.
Comparison with numerical calculation are presented too

## Slide 28: Two phases
The betatron X rays source will be developed at FLAME bunker optimizing:
  Laser parameters
  Plasma source devices
  Electron diagnostics
  X rays spectrum
  Photon flux
In the middle of 2024, it will be moved in the SPARC bunker, with the installation of a new compressor and refurbishing the old one.
The main goal is to make a replica of the source developed at FLAME
The advanced photon diagnostics and the user end station will be tested and installed during/after the commissioning of the source

## Slide 29: Conclusions
EuAPS will be the first brick of EuPRAXIA, a user facility based on the radiation emitted by electrons plasma accelerated.
There are several challenges that we have to address to move from a single-shot proof of principle experiment to a user facility
Users will use an utterly innovative source with properties between Synchrotron radiation and FEL radiation paving the way to imagine and realize completely new experiments

## Slide 30: Acknowledgment
ANANIA, Maria Pia; BALERNA, Antonella; BIAGIONI, Angelo; BORTOLIN, Claudio; BROMBAL, Luca; BRUN, Francesco; COSTA, Gemma; CRINCOLI, Lucio; CURCIO, Alessandro; DEL GIORNO, Martina; DI PASQUALE, Enrico; DI PIRRO, Giampiero; DI RADDO, Gianluca; DONATO, Sandro, FALONE, Antonio; FERRARIO, Massimo; FRANCESCONE, Daniele; FRAZZITTA, Andrea; GALDENZI, Federico; GALLETTI, Mario; GHIGO, Andrea; LAUCIANI, Stefano; LIEDL, Andrea; LOLLO, Valerio; ROSCIOLI, Leonardo; ROSSI, Andrea Renato; STELLATO, Francesco; STOCCHI, Federica