## Slide 1: ALBUS – Advanced Laser-driven Beamlines for User-specific Studies
Florian-Emanuel Brack, F. Kroll, E. Beyreuther, M. Reimold, U. Schramm, K. Zeil and J. Metzkes-Ng
6th European Advanced Accelerator Concepts workshop (EAAC 2023) – 20.09.2023 - Isola d'Elba, Italy

## Slide 2: Motivation
Pulsed laser-plasma accelerated particle source paired with pulsed high-field magnets
Medical Sciences
HED Physics
Matter & Materials
Detector Physics

## Slide 3: Why pulsed high-field magnets?
Replacing large infrastructure with compact electromagnets
Electromagnet through which a high current flows for a short time, generating a strong magnetic field.
Gantry 2 @ PSI
Prototype of a pulsed
dipole magnet
Notes: Electromagnet through which a high current flows for a short time, generating a strong magnetic field.

## Slide 4: „Infamous“ application case - Radiotherapy
Beam transport
Cyclotron
13 m × 11 m
Gantry
Universitäts Protonen Therapie Dresden
Solenoid
Dipole
Quadrupole
2.40 m
Height [m]
Radiation safety
Energy [MeV]
Length [m]
Masood et al., Phys. Med. Biol. 62 (2017)
Notes: Spiralförmige Bahn  sehr lang

## Slide 5: ALBUS at HZDR
Pulsed power portfolio @ HZDR for beamline optics
Pulsed B-field:
1 T  10 T
Quadrupole
250 T/m
focal length
N
N
S
S
p+
Solenoid
20 T
focal length
p+
Dipole
10 T
deflection radius
Dipolemagnet
p+
100
10
10

## Slide 6: ALBUS at HZDR
Pulsed power portfolio @ HZDR for beamline optics
Quadrupole
250 T/m
focal length
Solenoid
20 T
focal length
Dipole
10 T
deflection radius
100
10
10
Pulsed B-field:
1 T  10 T

## Slide 7: Pulse Generators
Adapting large scale high-field lab equipment to mobile pulse generators
Eel = 25 – 94 kJ
frep < 5 pulses/minute
Modular & compact

## Slide 8: In vivo radiobiology with LPA protons
Implementing a beamline meeting strict requirements
Brüchner et al., Radiat. Onc., Vol. 9 (2014) Animal study approval DD24-5131/338/35 Kroll et al., Nat. Phys. 18 (2022), 316
human tumour (HNSCC) on mouse ear, spherical (3mm diameter)
endpoint: radiation induced tumor growth delay
Lateral homogeneity
Dose
5 mm
-5 % 4 Gy +5 %
Time
Dose
Precise dose delivery
4 min
4 Gy
± 10%
Depth
Dose
Depth homogeneity
4 Gy
± 5%
4 mm
shots
Dose
Dose per shot
600 mGy
330 – 800 mGy
Talk by J. Metzkes-Ng
Thu, 12:00
Brüchner et al., Radiat. Onc., Vol. 9 (2014) Animal study approval DD24-5131/338/35 Kroll et al., Nat. Phys. 18 (2022), 316

## Slide 9: In vivo radiobiology with LPA protons
r [mm]
Solenoid
0
20
- 20
E1 < E2 < E3
delivered dose
beam transport
LPA source
Using the ALBUS-2S (two solenoids) beamline
Brack et al., Sci. Rep. 10 (2020), 9118
Kroll et al., Nat. Phys. 18 (2022), 316
model-conform dose delivery

## Slide 10: In vivo radiobiology with LPA protons
Using the ALBUS-2S (two solenoids) beamline
Brack et al., Sci. Rep. 10 (2020), 9118
Kroll et al., Nat. Phys. 18 (2022), 316
Talk by J. Metzkes-Ng
Thu, 12:00

## Slide 11: Ultra-high dose rate irradiations at Draco PW
Mouse model study did not meet FLASH criteria (ultra-high peak dose rate, but low mean dose rate)
ns-long single-pulse homogeneous dose irradiation with dose ~ 109 Gy/s
      Maximise the single pulse dose-rate while applying homogeneous (depth) dose
  Possible due to adjustable beamline components of ALBUS-2S Beamline
LPA source to investigate the FLASH mechanism with Zebrafish Embryos (ZFE)
Dose-effect curve within all required limits
Metzkes-Ng et al., Scientific Reports (in review)

## Slide 12: Source-to-sample characterization at ALBUS-2S
Using a beamline as a testbed for new detector developments
Time-of-Flight BMS
M. Reimold et al.,
Sci Rep 12 (2022)
LPA proton dosimetry
Marvin Reimold et al.,
Phys. Med. Biol. 68 (2023)
miniSCIDOM
HPLSE, in review
OCTOPOD
M. Reimold et al.,
HPLSE 1-15 (2023)
I-BEAT detector
D. Haffa et al.,
Sci Rep 9 (2019)

## Slide 13: The LIGHT beamline at GSI Darmstadt
Combining conventional and novel LPA acceleration technologies

## Slide 14: The LIGHT beamline at GSI Darmstadt
Combining conventional and novel LPA acceleration technologies
Generation and investigation highly monoenergetic beams with high flux
Development of suitable detectors
Stopping power measurements of dense, highly ionized plasmas
Potential application as injector into the SIS-18 synchrotron at GSI

## Slide 15: Laboratory astrophysics
Embedding laser-driven plasmas in external high magnetic fields
Probing bores allow for direct plasma observation
2 coils in almost Helmholtz-configuration
  up to <20 Tesla constant for several µs
  longer timescale than plasma processes
Small, vacuum compatible, versatile
Stainless steel version planned for higher B-fields
B-field distribution on axis
Accretion processes
Mabey et al.,
Astrophys. J. 896 (2020)
Magnetized RTI
Manuel et al.,
MRE 6 (2021)
Plasma Jet/shocks
Bohlin et al.,
PPCF 64 (2022)
ns-Laser
Probe 1
Probe 2
ps-Laser
Setup at LULI2000
Laser
Probe
Gas Nozzle
Setup at ELFIE
Setup at PALS
Gas Nozzle
Laser
Probe

## Slide 16: Compact air-cooled solenoid magnet (20 T)
Allow higher rep-rate experiments
Cool-down time: ~min
Compact and light-weight PEEK body and housing
100
95
90
85
80
75
70
65
60
Time [h]
Temperature [°C]
0
2
4
6
8
12
16
10
14
18
0
100
80
40
60
20
Layer 3
Sim
w/o cooling
Time [min]
Temperature [°C]
40
20
10
30
50
20
40
60
0
80
60
Exp
w/ cooling

## Slide 17: Rep-rate optimized current pulse generator
Energy recovery is key!
Charger
Thyristor stack
Pulse generator
Modular pulse generator design (125 – 750 µF) capable of 10-Hz-operation
Concept of energy recuperation fully tested and prototype assembled
1-Hz-charger under commissioning

## Slide 18: ALBUS around Europe
Thank you for your attention

## Slide 19: Research using ALBUS technology
Accelerator Physics
Reimold et al.,Phys. Med. Biol. 68 (2023)
Reimold et al., HPLSE 11 (2023)
Gerlach et al., HPLSE 11 (2023)
Reimold et al., Sci. Rep. 12 (2022)
Metternich et al., PRAB 25 (2022)
Kroll et al., Nat. Phys. 18 (2022)
Brack et al., Sci. Rep. 10 (2020)
Haffa et al., Sci. Rep. 9 (2019)
Jahn et al., PRAB 22 (2019)
Jahn et al., NIM-A 909 (2018)
Jahn et al., RSI 89 (2018)
Masood et al., PMB 62 (2017)
Busold et al., Sci. Rep. 5 (2015)
Masood et al., AP-B 117 (2014)
Busold et al., NIM-A 740 (2014)
Busold et al., PRAB 17 (2014)
Busold et al., PRAB 16 (2013)
Laboratory Astrophysics
Perez-Martin et al., HPLSE 11 (2023)
Bohlin et al., PPCF 64 (2022)
Manuel et al., MRE 6 (2021)
Mabey et al., Astrophys. J. 896 (2020)
Mabey et al., Sci. Rep. 9 (2019)
Albertazzi et al., HPLSE 6 (2018)
Albertazzi et al., Science 346 (2014)
Albertazzi et al., RSI 84 (2013)