## Slide 1
Full Energy Beam Exploitation at CLARA: Opportunities for Advanced Accelerator Experiments
Thomas Pacey
E.W. Snedden D. Angal-Kalinin, A.R. Bainbridge, A.D. Brynes, S.R. Buckley, D.J. Dunning, J.R. Henderson, J.K. Jones, K.J. Middleman, T.J. Overton, A.E. Pollard, Y.M. Saveliev, B.J.A. Shepherd, and P.H. Williams, @ STFC ASTeC
M. Colling, B. Fell, G. Marshall, @ STFC TD.

## Slide 2: Outline
CLARA & Full Energy Beam Exploitation (FEBE) Overview
FEBE Infrastructure supporting plasma acceleration
Instrumentation & Diagnostics
Potential types of experiments

## Slide 3
Overview of CLARA & FEBE

## Slide 4
CLARA & FEBE Overview
PHASE 1: 50 MeV,
250 pC, 10 Hz
User area Beam Area 1 (BA1)
Beam exploitation, inc. novel acceleration
Notes: CLARA is FEL test facility at Daresbury Lab North West England
Full Energy Beam Exploitation

## Slide 5
CLARA & FEBE Overview
FEBE: SHIELDED USER FACILITY
Branch line to shielded hutch
Flexible user exploitation space
100 TW class laser
PHASE 2: 250 MeV ASSEMBLED & INSTALLED OFFLINE
2022/23: Installation
2023/24: Commissioning
Straight-on: FEL technology development
NOT YET FUNDED
Tied to UKXFEL CDR and decision on next stages
PHASE 1: 50 MeV,
250 pC, 10 Hz
User area Beam Area 1 (BA1)
Beam exploitation, inc. novel acceleration
Notes: CLARA is FEL test facility at Daresbury Lab North West England
Full Energy Beam Exploitation

## Slide 6: CLARA Now

## Slide 7: Previous exploitation at CLARA
Exploitation with 35 MeV electrons and with 10 TW class laser
Competitive access periods
  October 2018- April 2019 and October 21 – April 2022
Oversubscribed by factor of 2
Approximately 50 % of shifts ‘21-’22 awarded were for advanced acceleration concepts, including dielectric wakefield acceleration laser wakefield acceleration, THz acceleration, and plasma diagnostics.
See Poster by Ed Snedden (Tuesday Session)

## Slide 8: FEBE Beamline & Hutch
Up to 250 MeV
250 MeV – 2 GeV
250 – 600 MeV
Highly instrumented beamline supports
- Setup & characterisation
- Feedback systems

## Slide 9: FEBE Chambers
CLARA
250 MeV e-
Chamber #1
Primary IP
~1.5m length
Up to
600 MeV
Flexible platform for novel acceleration studies
2 identical chambers: Double IP configuration
Dedicated laser in-out coupling chambers
Accelerated beam up to 2 GeV possible in hutch
Chamber #2
Flexible array of diagnostics
T Pacey – CLARA Opportunities for Advanced Accelerators - EAAC 2023, Elba, Italy
Laser from roof

## Slide 10
Beam parameters – “Day 1”
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5
RMS t [fs] | 100 | 50
σE/E [%] | <5 | <1
RMS x [µm] | 100 | 20
RMS y [µm] | 100 | 20
εN x [µm] | 5 | 2
εN y [µm] | 5 | 2
Important: all parameters to be confirmed through measurement using appropriate diagnostics.
10
T Pacey – CLARA Opportunities for Advanced Accelerators - EAAC 2023, Elba, Italy
Notes: Why 5 and have low charge

## Slide 11
Beam parameters – Future potential
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5 → <5
RMS t [fs] | 100 → 50 | 50 → <50
σE/E [%] | <5 → 1 | <1
RMS x [µm] | 100 → 50 | 20 → ~1
RMS y [µm] | 100 → 50 | 20 → ~1
εN x [µm] | 5 → <5 | 2 → 1
εN y [µm] | 5 → <1 | 2 → <1
  R&D: Meeting these parameters will require upgraded and/or new diagnostics
11
T Pacey – CLARA Opportunities for Advanced Accelerators - EAAC 2023, Elba, Italy
Notes: Shown through simulation and achieving optimal machine performance

## Slide 12
Infrastructure supporting plasma acceleration

## Slide 13: Gas Management
Invested in large volume turbos on experimental chambers & mirror boxes – 6 at ~ 2000l/s
Upstream irises and apertures to reduce gas propagation
Negligible modelled emittance growth for Hydrogen,
  Limited growth for heavier species, e.g. Argon

## Slide 14: Beam driven acceleration
Benefitting from high quality beam designed for FEL R&D
Flexible delivery and fine control of longitudinal phase space:
  Variable R56 in chicane compressor & in FEBE arc
  Dielectric wakefield dechirper
Dielectric dechirper

## Slide 15: Electron beam pulse shaping
Photoinjector Laser longitudinal shaping
  Machine Learning driven
  Large number of possibilities
Tungsten mask in FEBE Arc
  Configurable and changeable
  Drive-witness, pulse trains…all possible

## Slide 16: FEBE Laser
120 TW, 5 Hz laser
(Arco, Amplitude).
The laser is housed immediately on top of the FEBE hutch
Photons to target via a shielded periscope.
Installation scheduled for second half of 2024,
Laser ready for exploitation at the beginning of 2025.
Laser room
FEBE hutch
Laser control room
CLARA
250 MeV e-

## Slide 17: Laser delivery to IP
e- @ 250 MeV
Input from laser room periscope
Deformable mirror
Wavefront
Sensor
OAP
Probe line
IP1
FMBOX1
FEC1
FMBOX2
Dump

## Slide 18
Diagnostics & Instrumentation

## Slide 19
Laser synchronization & TOA jitter measurement
FEBE laser oscillator will be optically synchronized to the CLARA optical clock:
Ultralow noise optical clock (complete)
Stabilized <10 fs over 24 hr (design and testing complete)
Two-colour laser-laser locking ( testing underway, all-fibre upgrade design in progress1)
On track to provide <10fs locking of FEBE laser to optical reference
1 – THPA073 IPAC23
2 – PhysRevSTAB.18.012801
3 – IBIC2021 WEPP19
Beam arrival monitor (BAM) R&D:
Targeting 10fs arrival time measurement @20 pC with cone pick-ups design2
  Installation and commissioning in early 2024
Collaboration with DESY & THM to deliver low charge BAM based on PCB substrate and rod pick-ups3
Push 10 fs @<5pC beam charge with low charge BAM.

## Slide 20: 6D Diagnostics R&D across FEBE beam line
Diagnostics undergoing active R&D
All supplemented by well developed diagnostics, e.g. BPMs, YAGs, ICTs
ML based Virtual diagnostics
CSR
BAM
CTR/CDR
OTR: <5um spot size
Dielectric streaker & EO
PM spectro-meter
OTR based emittance
High dynamic range
charge

## Slide 21: FEBE Chamber options
Dielectric wakefield streaker
Passive, robust, single shot bunch length measurement
RMS estimate or full profile reconstruction
Broadband, <50 fs > 1 ps
Resolution improved using pairs orthogonally orientated plates
Permanent Magnet Spectrometer
Can be deployed in second chamber for commissioning beams with energy > 600 MeV
Energy range 50 MeV - 2 GeV
Upstream quad. doublet + correctors for matching into dipole
Modular design, 200mm blocks, 5 modules for 2 GeV
2 options, more in R&D

## Slide 22
Potential
Experiments:
Putting options
together
Only ideas/examples!
Many potential possibilities!
Suggestive, not prescriptive!

## Slide 23
ASTeC R&D will be guided by challenges to establish a plasma FEL user facility (e.g. those targeted through EuPRAXIA). ASTeC will consider a plasma-booster option for one of the UK XFEL beam lines.
Future areas of interest
R&D challenges
Plasma FEL R&D Challenges | 
Emittance, tolerances and mitigation of instabilities | Hybrid, new or alternative schemes
Efficiency, including drive beam and laser issues | Low emittance beam sources (including positrons)
Energy spread | Plasma stability / repeatability (including targets)
Maximum bunch intensity / charge | Synchronization systems, other support systems
Simulation code development and outreach | Controls systems and optimisation (including machine learning)
ASTeC with our users would be well placed to contribute to many of these areas.

## Slide 24: External injection - LWFA
Witness beam stability & Staging challenges
Ultrashort electron pulse
120 TW laser
Bunch Length & Emittance Diagnostics
Spectrometer up to 600 MeV

## Slide 25: External injection LWFA
High energy gain & energy stability
Ultrashort electron pulse
120 TW laser,
Short focal length
2 GeV spectrometer
& dump

## Slide 26: PWFA staging
Witness beam stability & Staging challenges
Drive-witness CLARA pulse
Spectrometer up to 600 MeV
Emittance diagnostics
PMQ matching triplets
PMQ matching triplets

## Slide 27: Plasma based beam manipulation & instrumentation
Plasma ignition
Bunch Length & Emittance Diagnostics
CLARA beam
250 MeV
Low emittance
Laser based diagnostics

## Slide 28: Summary
FEBE represents a step change in our infrastructure and potential to perform advanced acceleration experiments
Flexibility is at the heart of the design to support & futureproof for our community.
  Have the potential to exploit this for strategically important R&D
FEBE will leverage the full CLARA R&D project
  FEL quality beam, synchronisation, modelling, controls, machine learning optimisation, etc.
Beam commissioning starts in 2024
First exploitation in 2025 – more information to come in 2024
T Pacey – CLARA Opportunities for Advanced Accelerators - EAAC 2023, Elba, Italy
thomas.pacey@stfc.ac.uk edward.snedden@stfc.ac.uk

## Slide 29: Acknowledgements
Special thanks to:
CLARA Team, across ASTeC and STFC Technology Dept.
EAAC’23 Organisers and Scientific Committee