## Slide 1
Evaluation of
the transfer matrix
of a plasma ramp with squared cosine shape
via an approximate solution of Mathieu differential equation
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop
Stefano Romeo stefano.romeo@lnf.infn.it
Evaluation of
the transfer matrix
of a plasma ramp with squared cosine shape
via an approximate solution of Mathieu differential equation

## Slide 2: Outline: Plasma transport line optimization
Courtesy of A. Biagioni
Which plasma ramp?
High sensitivity to transverse instability!
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop
Stefano Romeo stefano.romeo@lnf.infn.it
Evaluation of ramp transfer matrix
Capillary
Electrode
Plasma channel
Vacuum
Guide
At the edge of discharge capillaries, regions with a gradually decreasing plasma density form, connecting the plasma plateau to the vacuum
These regions are commonly referred to as plasma ramps
Emittance preservation inside plasma is difficult, since in order to balance the extreme focusing field inside plasma the beam needs to be focused up to few micrometers/sub micrometer scale
A PLASMA RAMP CAN HELP TO RELAX MATCHING CONDITIONS!!!
Numerical solution:
For any working point perform several simulation scans
Analytical solution:
Find a general rule for a suitable shape

## Slide 3: Theory: Plasma focusing strength
Plasma focusing strength?
Ion column model
(only the particles inside the bubble)
Envelope equation
Stefano Romeo stefano.romeo@lnf.infn.it
Matching conditions on the plateau
Neglecting constants, the focusing force inside a plasma ramp depends only from the plasma density, with the energy taken as a parameter
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 4: Method: Hill’s Equation
Stefano Romeo stefano.romeo@lnf.infn.it
Hill’s Equation
Negligible deceleration
is a continuous and derivable function
The computation is performed over the inverse matrix in order to have simplified matching conditions
Liouville’s Theorem
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 5: Framework: Squared Cosine plasma ramp
Stefano Romeo stefano.romeo@lnf.infn.it
If is even Hill’s equation becomes a symmetric differential equation
Solutions are continuous and derivable
One solution is even, the other is odd
We can normalize the solutions such as
and
Ramps with an even functional form guarantee the possibility to respect matching conditions
THE CHOICE
Realistic ramp
No discontinuity at any derivative order
Partially concave, partially convex
Never adiabatic
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 6: Expansion: Mathieu Equation
Stefano Romeo stefano.romeo@lnf.infn.it
Hill’s Equation
Mathieu Equation
Even and odd normalized Mathieu Functions
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 7: Simplify: Normalized transfer matrix
Normalized transfer matrices
Extraction
Injection
Stefano Romeo stefano.romeo@lnf.infn.it
Normalization
Geometric factor
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 8: Approximation: Behavior of Mathieu functions
Stefano Romeo stefano.romeo@lnf.infn.it
Sinusoidal behavior
Phase delay between Mathieu functions and their first derivative
The product saturates for
Transfer matrix is unimodular (Liouville’s theorem)
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 9: Alignment: Evaluation of the constants
Stefano Romeo stefano.romeo@lnf.infn.it
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 10: Check: Numerical vs. Analytical Approximation
Stefano Romeo stefano.romeo@lnf.infn.it
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 11: Application: Stabilizing effect of the ramp
Stefano Romeo stefano.romeo@lnf.infn.it
Mehrling-Floettmann equation for emittance growth
Transfer matrix
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop
Mehrling, T., et al. "Transverse emittance growth in staged laser-wakefield acceleration." Physical Review Special Topics-Accelerators and Beams 15.11 (2012): 111303.

## Slide 12: Perspective: Experimental ramps
The measured shapes were replied in numerical simulations by means of segmented lines and tested in comparison with analytical squared cosine shape
Stefano Romeo stefano.romeo@lnf.infn.it
Plasma ramps with squared cosine shape were actually realized at the plasma lab of SPARC_LAB facility by means of tapered capillaries
The results are consistent with the expectations
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 13: Conclusion: Summary
Tons of applications on their way!
Stefano Romeo stefano.romeo@lnf.infn.it
  We opted for a purely analytical approach trying to evaluate the transfer matrix of a plasma ramp
  We concluded that a ramp with a symmetric form could simplify the problem
  We opted for a ramp with a squared cosine shape
  We evaluated that this ramp is never adiabatic and its application lead to Mathieu Equation
  We compared the solution of the Mathieu Equation with actual envelope evolution
  We deduced that the ramp transfer matrix can be normalized to a geometric parameter
  We found an analytical approximation that allows to write the transfer matrix in a simple way
  We opted for a purely analytical approach trying to evaluate the transfer matrix of a plasma ramp
  We concluded that a ramp with a symmetric form could simplify the problem
  We opted for a ramp with a squared cosine shape
  We evaluated that this ramp is never adiabatic and its application lead to Mathieu Equation
  We compared the solution of the Mathieu Equation with actual envelope evolution
  We deduced that the ramp transfer matrix can be normalized to a geometric parameter
  We found an analytical approximation that allows to write the transfer matrix in a simple way
Tons of applications on their way!
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 14: Thank you for the attention!
Stefano Romeo stefano.romeo@lnf.infn.it
Thank you for the attention!
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop

## Slide 15
Stefano Romeo stefano.romeo@lnf.infn.it
Island of Elba 2023-09-18
6th European Advanced Accelerator Concepts Workshop
Very special thanks to those who collaborated with me in the realization of this work
Angelo Biagioni
Lucio Crincoli
Alessio Del Dotto
Massimo Ferrario
Anna Giribono
Gianmarco Parise
Andrea Renato Rossi
Gilles Jacopo Silvi
Cristina Vaccarezza
Very special thanks to those who collaborated with me in the realization of this work
Angelo Biagioni
Lucio Crincoli
Alessio Del Dotto
Massimo Ferrario
Anna Giribono
Gianmarco Parise
Andrea Renato Rossi
Gilles Jacopo Silvi
Cristina Vaccarezza