## Slide 1: Rooting out the gremlins - stable LWFA operation at the PW frontier
Stefan Karsch1,2
1 Centre for Advanced Laser Applications, LMU Munich 2 Max-Planck Institute for Quantum Optics

## Slide 2
ATLAS-3000 at CALA: Schematic system layout
ATLAS-300 homebuilt system:
up to 300 TW, 25 fs, 5 Hz Ti:Sa laser
2 frontends:
ps booster, sat. absorber + Amplitude stretcher & regen
double CPA, XPW + fs-OPA + Amplitude stretcher & regen
ATLAS-3000 main amplifier
by THALES LAS
90 J, 1 Hz,
14 x 16J GAIA HP pump lasers
Homebuilt beam expander & compressor
Up to 60 J
25-30 fs
1 Hz
“Apochromatic” lens telescope supplied by Thales

## Slide 3
[mm]
spatial
spectro-
temp.
near field
far field
contrast
real Strehl: > 0.75
Δλ > 65 nm
ns contrast > 1010
ps contrast ~ 108
log(intensity)
geom. Strehl: > 0.93
Imax(f/22) = 4x1019
ATLAS-3000: on-paper performance

## Slide 4
First laser wakefield acceleration results: LWFA by shock-front injection
old laser, 80 TW on target
f/22, 5 mm gas jet
upgraded laser, 250 TW on target
f/22, 5 mm gas jet
Similar experiment
Stability ?

## Slide 5
A few hours after turning on pump lasers…
Optimized spectrum…
Optimized near field…
Optimized energy…
Optimized near field…
Optimized energy…
First step:
f/33
Cheap trick: mixed gas for ionization-assisted shock injection

## Slide 6
Correlations ? … not clear

## Slide 7
Hidden parameters?

## Slide 8
PFT
PFC
PFT
PFC
Chromatic lens causes pulse front curvature (PFC)
Off-center bundle in chromatic lens causes PFC and pulse front tilt (PFT)
“A(po)chromatic lenses are free from PFT/PFC“ ⇒
Triplet lens expander between AMP1 and AMP2 is designed apochromatic within lambda/50
Yet still detect PFT after beam shift ⇒ expander in practice is not free from STCs
Replace “perfect“ lens telescope by reflective expander
Spatio-Temporal Couplings (STCs) by chromatic optics (beam expander telescopes)

## Slide 9
Lens expander, aperture after compressor 8J on target, f/33
no expander, no aperture
8J on target, f/33
Suppression of STCs improves electron performance (pure hydrogen)

## Slide 10
Spectrally resolved Shack-Hartmann-wavefront sensor
Measurement of Spatio-Temporal Couplings by spectral wavefront retrieval
Take 10 images per filter position to average out pointing jitter
Falcon device:

## Slide 11
760 nm
770 nm
780 nm
790 nm
800 nm
810 nm
820 nm
830 nm
840 nm
PtV <0.2 λ
 | 8.5.23 | 11.5.23 | 15.5.23
Pulse front tilt µrad/nm | -2.6e-6 | -2.0e-5 | -7.7e-6
Pulse front tip µrad/nm | -7.7e-6 | -6.2e-5 | -1.1e-4

## Slide 12
Pointing and fluence variations by air turbulence (after eliminating heat sources):
Moving from 100 TW to PW: as beam size and optical path increase, so does susceptibility to air turbulence.
σF = 10.1%
σF = 3.9%
σF = 10.1%
⟹ σF = 2.8%
Recently: more foam walls:
(shot-to-shot energy variation < 1%)

## Slide 13
Target density gradient
w = 15 µm
LR = 1 mm
LR = 1 mm
f/22
Shot-to-shot peak fluence variation
(from focus camera)
Out-of-focus, fluence variations increase:
fluence fluctuates much stronger out-of-focus than at focus
Self-focusing at target gradient is sensitive to intensity fluctuations
Probable cause: air turbulence in laser housing

## Slide 14
Going from 6m focal length, f/33 to 10 m focal length, f/55:

## Slide 15
f = 50 cm → 1 µm = 2mrad
Long term focus drift seems to saturate after several hours after pump laser start
Homemade active stabilization ongoing (A. Döpp)
Shot-to-shot pointing will take a bit longer…

## Slide 16: Better injection control: Hydrodynamic optical field ionized shocks
0 ns
2 ns
-50 µm +50 µm
density
e-
Injector beam
Witness-driver pair
PWFA
LWFA
Background
density
H2
Plasma simulation support from Oxford (A. Ross)
Independent control of:
injection position → final energy
shock height → charge
plateau density → acceleration gradient
M. Foerster

## Slide 17: HOFI shock stability
Supersonic wire shocks
HOFI shocks

## Slide 18
Blade to produce shock
Optical shock inducing laser beam
LWFA drivie laser beam
Monoenergetic GeV beams
20 mm slit nozzle target, f/55

## Slide 19
…
near field,
far field
cams
input pointing
spectrum, near field,
energy
wavefront
Hunting for correlations: Shot-to-shot diagnostics
Laser
Expt.
e-beam: energy, pointing,
charge
energy, spectrum,
phase, duration,
pointing
plasma: interferometry, beam pointing,
shock position

## Slide 20
Hunting for correlations: Analysis ongoing…
Run 13
Run 19
target moved downstream by 400 µm = 1/3 ZR
400 shots each, relying on statistical fluctuations
electron energy vs. wavefront
electron energy vs. pulse duration

## Slide 21
Stefan Karsch, Andreas Döpp, Moritz Foerster, Hao Ding, Max Gilljohann, Johannes Götzfried, Sabine Schindler, Florian Haberstroh, Katinka v. Grafenstein, Faran Irshad, Enes Travac, Albert Schletter
Thank you for your attention!
Hybrid Data

## Slide 22
Thank you for your attention!
Btw: We are hiring, too…
We are hiring :
CALA postdoctoral fellowship (see https://pulse.physik.uni-muenchen.de)
PHD positions

## Slide 23
Optimization parameters
Pareto front vs. single objective optimization
…currently successfully implemented in the experiment... stay tuned!

## Slide 24
Self injection
Blade induced shock injection
Optically induced shock injection
~30 pC over 1 GeV
~90 pC, 600 MeV
~100 pC,
1 GeV

## Slide 25
Centre for Advanced Laser Applications (CALA)…
…is operated by the Ludwig-Maximilians-Universität München (LMU)
… serves three university user groups
… hosts approx. 40 staff members
… houses two laser systems, ATLAS-3000 and PFS-pro
… and five experimental beamlines

## Slide 26
gas inlet
Optical shock driver
LWFA driving laser beam
Multi-GeV beams
25 mm gas cell target, f/55
Optically induced shock injection
Self injection
~10 pC over
2 GeV
~25 pC at
1 GeV
K. v. Grafenstein
f/37

## Slide 27
Hybrid LWFA-PWFA
First experimental clues (ca. 2010):
S. Corde et al., Phys. Rev. Lett. 107 215004 (2011)
SW. Chou et al., Phys. Rev. Lett. 117 144801 (2016)
Hybrid accelerator & plasma photocathode concept
B. Hidding et al., Phys. Rev. Lett. 104 195002 (2010)
B. Hidding et al., Phys. Rev. Lett. 108 035001 (2012)
nC LWFA electron bunches
J. Couperus-Cabadag et al., Nat. Comm. 8, 487 (2017)
J. Götzfried, A. Döpp et al. Phys. Rev. X 10, 041015 (2020)
> 1 nC, ~0.5 J
< 10 fs, ~ 100 kA
2.5 mrad FWHM
Plasma waves driven by LWFA electrons
M. Gilljohann, H. Ding et al. Phys. Rev. X 9, 011046 (2019)
S. Schöbel et al., New J. Phys. 24, 083034 (2022)
Dual bunches from a single LWFA
J. Wenz et al. Nat. Photonics. 13, 263 (2019)
T. Kurz, T. Heinemann et al. Nat. Comms. 12, 2895 (2021)
External injection of witness beam
Internal injection of witness beam (supersonic shock)
J. Couperus et al. Phys.Rev.Research 3, L042005 (2021)
HOFI shocks: High stability and beam quality from hybrid accelerator
M. Foerster et al. Phys.Rev.X 12, 041016 (2022)

## Slide 28
Latest preliminary results:
GeV-scale hybrid
Implementation of Trojan horse scheme (HZDR)

## Slide 29
energy
125 MeV
250 MeV
375 MeV
500 MeV
propagation direction
propagation direction
radius
0 µm
50 µm
50 µm
Simulation: laser wakefield acceleration (LWFA)