## Slide 1
Laser development for LWFA and future plans
Laura Corner
laura.corner@liverpool.ac.uk
Cockcroft Institute, University of Liverpool

## Slide 2
Outline
LWFA requirements
Some promising technologies
Future plans at Liverpool/Cockcroft in LWFA

## Slide 3
3
Applications for particle accelerators
Laser plasma wakefield acceleration is a promising technology for high gradient particle acceleration - source of compact, perhaps cheaper accelerators - 10 GeV/few cm.
But only with high efficiency drive systems – rf klystrons 40 – 50%, prototypes up to 80 or 90%.
What’s a perfect laser driver?
  High peak power
  High average power
  High rep rate
  Short pulse length
  High efficiency
  Excellent beam quality
One that works!!
Wavelength?
800 nm? 1 mm? CO2 @ 10mm?
How high rep rate?
kHz? 100s kHz? MHz?
Luminosity – collider running time
How short?
Multi-pulse? Modulation of ps pulses? External injection? MOPA? Different injection & acceleration stage lasers?
Lasing medium?
What’s out there?

## Slide 4
4
4
Fibre lasers
Fibre lasers:
  Yb – low quantum defect.
  Direct diode pumping nir (@976nm).
  Optical-optical 80%.
  WPE 40%.
  Single mode – efficiency at focus (intensity!)
  Air/water cooled.
Current laser drivers for LWFA:
  High peak power (100s TW/PW systems, J, <100 fs)
  Low repetition rates ~ 1Hz (low average power)
  Inefficient – expensive to run
Fibre lasers:
  High repetition rates (> kHz)
  Low pulse energy (~ mJ)
  Single fibres considered limited to < 10GW peak power (Schimpf et al. J. Opt. Soc. Am. B. 27 20151 (2010))
Can we use this technology to make both high peak and average power lasers?
Make many low energy pulses into one high energy pulse – coherent combination
Yb:glass
quantum
defect

## Slide 5
5
Tiled aperture

## Slide 6
6
Tiled aperture combination
Signal split and amplified in 64 cw fibres with integrated phase modulators.
Light collected in microlens array.
Phase between adjacent fibres analysed in quadriwave lateral shearing interferometer.
34% beam in central lobe (cf 44% theoretical).
Bourderionnet et al.,
Op Exp 19, 17053 (2011)

## Slide 7
7
7
Filled aperture combination
Binary tree example – polarisation combination and locking
Limits of beam splitter based combining:
Müller et al., Opt. Exp. 29, 27900 (2021)

## Slide 8
8
Polarisation combination
Müller et al., Opt. Letts. 41, 3439 (2016)
Seed split and amplified in large pitch photonic crystal fibres.
Polarisation – piezo mirror phase control.
1 MHz, 1.1mJ, 1kW, 8 fibres (2016).
80MHz, >10kW, 254fs, 12 fibres (2020).
100kHz, 10mJ, 1kW, 120fs, 16 fibres (2021).
Does not scale gracefully to > 1000 fibres.
Stark et al.,
Opt. Letts. 46, 969 (2021)
Müller et al., Opt. Letts. 45, 3083 (2020)

## Slide 9
9
9
Commercial systems

## Slide 10
10
10
Spectral combination
Chang et al., Opt. Exp. 21, 3897 (2013)
Seed split spectrally with filters and amplified in different fibre channels.
Amplified pulses combined on spectral filters and compressed.
54fs combined – S. Chen, AAC, 2022.

## Slide 11
11
11
Concept: R. Wilcox, A. Galvanauskas, W. Leemans
https://www2.lbl.gov/LBL-Programs/atap/Report_Workshop_k-BELLA_laser_tech_final.pdf
Do everything! k-BELLA
https://bella.lbl.gov/kbella/
Fibre

## Slide 12
12
12
Multicore fibres
Klenke et al.,
Opt. Letts. 43, 1519 (2018)
Use multicore fibre.
Less phase difference to correct.
Fewer channels.
Klenke et al., Opt. Letts. 47, 345 (2021)
ps pulses – 70W, 40ps.
fs pulses – 500W & 600mJ, 500fs.
Efficiency!

## Slide 13
New FEBE upgrade and laser
PI Laser:
Variable longitudinal pulse shape
Linac 1
Linac 2
Linac 3
Linac 4
Variable Bunch Compressor
Variable R56
Low T566
4th Harmonic
Cavity
Dechirper
FEBE Arc
Variable R56
FEBE Mask
Flexible design
FEBE Hutch
FEC1
FEC2
100 TW Class Laser
Electron energy up to 250MeV.
Funding received for 100TW laser – space to upgrade to 250TW.
New shielded area with 2 vacuum chambers for experiments.
RF Gun:
100 Hz
250 pC
CLARA
Phase 1
CLARA
Phase 2
CLARA
FEBE
Fig. courtesy T. Pacey, ASTeC
See also talk T. Pacey Wed afternoon

## Slide 14
14
Fibre laser driver simulations
What can we do with a different (efficient!) laser?
Fibre laser: 2J, 150fs,
250MeV to 450MeV in 100mm.
Gradient 2 GV/m.
Energy spread: FWHM 2.4% - 3.5%.
Emittance: 1 mm mrad – 1.04 mm mrad.
Simulations not optimised!
Simulations: Jonathan Christie
FEBE high rep rate photocathode @ 400Hz – can we make this laser?
Combined fibres have shown 120fs, 10mJ pulse energy and
20% measured WPE.

## Slide 15
Future plans @ CLARA – H3 beams project
STFC funding call for innovative accelerator projects.
H3 beams – high quality, high brightness beams for high energy physics.
Aim to address of quality and stability of LWFA electron beams.
£4M, 4 yr proposal – only bid put through to full proposal stage after initial outline call.
Exploit CLARA upgrade.
UK wide research synergies – THz acceleration and manipulation, beamline design, LWFA, external injection, guiding, target design, diagnostics.
Proposal: use THz beam manipulation to create phase-locked fs electron bunch injected into laser driven plasma wake.
Fig: T. Pacey

## Slide 16
CLARA, FEBE & H3 Beams Schematic Overview
100 TW FEBE Laser
FEBE Shielded Hutch
FEC2
FEC1
Variable
Bunch
Compressor
Linac 04:
250 MeV
Transverse
Deflecting
Cavity
THz
Modulation
Chamber
FEBE
Arc
Bunch
Shaping
Mask
Laser transfer arm
FEBE → CLARA
Longitudinal
& Timing
Diagnostics
Transverse Matching into FEBE
Permanent
Magnet
Focusing & Capture
Triplets
High Gradient
Plasma
Cell
Suite of
Energy and Emittance Diagnostics:
0.6 - 1 GeV
CLARA
Beam
~150 MeV
≈60 m
Energy Emittance Diagnostics:
250 – 600 MeV
CLARA:
Stable Beam
Phase-Lock
Accelerate
Compress
Characterise
THz
Driven
Streaker
Fig. S. Jamison

## Slide 17
Conclusions
Need to move beyond Ti:sapp for plasma acceleration > 100Hz.
Fibre combination promising (commercialised) technology.
Can accelerate electrons at gradients > 1GeV/m in simulation with realistic fibre laser parameters.
New CLARA facility ideal for advanced acceleration experiments.
H3 beams project to exploit synergies in UK research to produce high quality LWFA beams.

## Slide 18
Back Up

## Slide 19
External Injection Experiments at CLARA:
Motivation
Laser wakefield acceleration (LWFA) has produced extremely high accelerating gradients and energies (10GeV), but issues with stability, energy spread, repeatability, emittance.
CERN Expert Panel Roadmap (https://e-publishing.cern.ch/index.php/CYRM/issue/view/146) identifies both quality and staging as milestones for credible LWFA.
External injection of high quality, low energy electrons into plasma wakefield: high gradient acceleration w/o loss of quality in simulation.
Experiments @ CLARA (Daresbury Laboratory) – test injection & acceleration experimentally (few expts.so far Amiranoff et al. PRL 81, 995, 1998, Wu et al., Nature Physics 17, 801, 2021).
Investigation of staging without problems of capturing low quality beams from LWFA first stage.
CLARA near-unique facility in the world – accelerator, laser, experimental area.

## Slide 20
  Offered parameters to evolve, based on development time
  ‘Day 1’ → Nominal
Beam parameters
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 20
RMS t [fs] | 100 | 50
σE/E [%] | <5 | <1
RMS x [µm] | 100 | 20
RMS y [µm] | 100 | 20
εN x @ 250 MeV [µm] | 5 | 2
εN y @ 250 MeV [µm] | 5 | 2
  Offered parameters to evolve, based on development time
  ‘Day 1’ → Nominal → R&D
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | <20
RMS t [fs] | 50 | ≤50
σE/E [%] | 1 | <1
RMS x [µm] | 50 | 1
RMS y [µm] | 50 | 1
εN x @ 250 MeV [µm] | <5 | 1
εN y @ 250 MeV [µm] | 2 | <1
  R&D: dedicated effort required beyond normal operations, and/or new diagnostic technology required

## Slide 21
External injection experiments at FEBE
250TW | Pre-interaction | Post-interaction
Charge (pC) | 5 | 5
Central energy (MeV) | 250 | 5436
Energy spread (RMS) | 1% | 2.13%
σx (µm) | 5 | 2.27
σz/c (fs) | 5 | 5
εn (mm mrad) | 1.0 | 1.24
100TW: 1GeV in 80mm – 2GeV in 140mm.
250TW: 5GeV in 400mm.
250TW
250TW
100TW