## Slide 1: Pulse characterisation technique for multi-pulse laser plasma wakefield accelerators
Speaker: Wei-Ting Wang
Position: PhD student
Institute: University of Oxford

## Slide 2: Outline
Introduction
  Why PMoPA
  Pulse train generation
How to characterise pulse trains
  From SSA to FROG
  Requirements for the device
  Experimental setup
  Phase retrieval results
Outlook
  PMoPA and pulse characterisation
Summary

## Slide 3: Why P-MoPA?
Wakefields
Laser pulse
Inefficient laser systems ( Hz)
Ti:sa
crystal
Conventional LWFA
~ Hz
~ 10s fs
Efficient laser systems (kHz)
~ 1k Hz
~ 1 ps
P-MoPA
Yb:YAG
disk
Pulse spacing
200 fs
Notes: Problem of Ti:sa, quantum conversion efficiency and heat
Feature of laser pulses

## Slide 4: Pulse train generation for proof of principle experiment
A. J. Ross et al., Observation of resonant excitation of plasma waves in a plasma channel. Internal communication. (To be submitted).
Pulse
Generation
Pulse
Measurement
GDD
control
Delay time
control
high peak power
Grating pair compressor
Single pulse
Michelson interferometer

## Slide 5: From SSA to FROG
Single-shot autocorrelator
Single-shot blind FROG
Spectrum
Delay time
Physical model
Simulated
SSA signal
Experimental
SSA signal
Pulse train
Beam
Splitting
Camera
NLO
Beam
Splitting
Imaging Spectro-meter
NLO
Experimental FROG trace
Phase retrieval algorithm
Pulse train
Spectrum
Spangenberg et al., Time domain ptychography.
PHYSICAL REVIEW A 91, 021803(R) (2015).

## Slide 6: Requirements for characterisation of multi-pulse trains
Pulse train properties
Number of pulses: 10 - 15
Pulse spacing: 100 fs - 200 fs
Pulse duration (FWHM): 1 ps – 3 ps
Required temporal window: 6 ps
Spectral and temporal resolution
Required points to resolve one cycle: 10
Temporal resolution: 10 fs – 20 fs
Spectral resolution: 0.35 nm
Spectral window: 104.5 nm
Nonlinear crystal
Type-1 BBO
Cut angle:
Temporal window: 12 ps
Imaging spectrometer
Grating: 1200 l/mm
Focal length: 100 mm
Detector size: 2/3”
Resolution: 0.03 nm

## Slide 7: Proof of principle experiment
Imaging spectrometer
Self-referenced cross-correlator
Line-array
spectrometer
Michelson
Interferometer
Grating
Compressor
Chirping
Temporal
interference
2 mJ, at 790 nm, at 1 kHz

## Slide 8: Pulse retrieval results
(d) RMS of filtered spectrum: 8 %
(e) RMS of pulse train spectrum:22 %
(a) Measured
(b) Retrieved
(c) Error
FROG : 9
Retrieved spectrum
Retrieved FROG trace

## Slide 9: Pulse retrieval results
Time-bandwidth product (TBP) of (g): 13
Number of pulses in (g): 11
Avg. pulse spacing: 200 fs
Non-uniformity : 10 fs
Retrieved pulse
Pulse structure
Input
Filtered
Reference
280 fs
160 fs

## Slide 10: Outlook: P-MoPA concept
More challenging to measure pulse train since spectrum is discontinuous!
1. Modulation
2. Compression
4. Acceleration
3. Characterisation
Modulated
pulse
Compressed
pulse
O. Jakobsson et al.,
PHYSICAL REVIEW LETTERS 127, 184801 (2021).

## Slide 11: Outlook: P-MoPA pulse train
Input pulse
Smooth pulse
Smooth spectrum
After modulation
Smooth pulse
Spectral sidebands
After compression
Pulse train
Spectral sidebands
Pulse
Spectrum
Phase

## Slide 12: Summary
We have demonstrated a single shot FROG device for MP-LWFA.
11 pulses with avg. pulse spacing of 200 fs were retrieved.
Image quality of the FROG trace is a key limitation.
More challenging pulse characterisation in P-MoPA.
We are investigating reliable pulse diagnostic techniques for P-MoPA.

## Slide 13: Backup slides

## Slide 14: Pulse characterisation for MP-LWFA
 | Self referenced | Cross referenced
Time | Auto-correlation | Cross-correlation
Frequency | SPIDER (Spectral phase interferometry for direct electric-field reconstruction) | Spectral interferometry
Time-frequency joint | FROG (Frequency resolved optical gating) | Cross-correlation FROG
Antoine Monmayrant et al., J. Phys. B: At. Mol. Opt. Phys. 43 (2010) 103001.

## Slide 15: Resolution of imaging system
Calibration
Grating
Spot size: 15 mm
Focal length: 75 mm
Focused spot size: 5
True resolution: 7 at 405 nm
Imaging system
Resolution testing
Temporal calibration
Spectral calibration
16 fs
0.06 nm
Auto-convolution
Manual delay stage