## Slide 1: EuPRAXIA laser requirements and current conceptual design issues
Leonida Antonio GIZZI (CNR, Pisa, Italy)
with
Paul CRUMP, (FBH, Germany)
Luca LABATE, (CNR, Pisa, Italy)
Guido TOCI (CNR, Firenze, Italy)
http://eupraxia-project.eu
ESFRI
6th European Advanced Accelerator Concepts Workshop
17–23 Sept 2023
Hotel Hermitage, La Biodola Bay, Isola d'Elba, Italy

## Slide 2: Outline
EuPRAXIA laser requirements
Overall layout
Thermal management options
Modelling
Pump lasers
Summary

## Slide 3: The EuPRAXIA Project
With the inclusion in ESFRI and the approval of the Preparatory Phase Project, EuPRAXIA must rapidly move from the conceptual design to a viable technical design of the laser driver.
R. W. Assmann, M. K. Weikum, T. Akhter, D. Alesini, A. S. Alexandrova, M. P. Anania, N. E. Andreev, I. Andriyash, M. Artioli, A. Aschikhin, T. Audet, A. Bacci, I. F. Barna, S. Bartocci, A. Bayramian, A. Beaton, A. Beck, M. Bellaveglia, A. Beluze, A. Bernhard, A. Biagioni, S. Bielawski, F. G. Bisesto, A. Bonatto, L. Boulton, F. Brandi, R. Brinkmann, F. Briquez, F. Brottier, E. Bründermann, M. Büscher, B. Buonomo, M. H. Bussmann, G. Bussolino, P. Campana, S. Cantarella, K. Cassou, A. Chancé, M. Chen, E. Chiadroni, A. Cianchi, F. Cioeta, J. A. Clarke, J. M. Cole, G. Costa, M. -E. Couprie, J. Cowley, M. Croia, B. Cros, P. A. Crump, R. D’Arcy, G. Dattoli, A. Del Dotto, N. Delerue, M. Del Franco, P. Delinikolas, S. De Nicola, J. M. Dias, D. Di Giovenale, M. Diomede, E. Di Pasquale, G. Di Pirro, G. Di Raddo, U. Dorda, A. C. Erlandson, K. Ertel, A. Esposito, F. Falcoz, A. Falone, R. Fedele, A. Ferran Pousa, M. Ferrario, F. Filippi, J. Fils, G. Fiore, R. Fiorito, R. A. Fonseca, G. Franzini, M. Galimberti, A. Gallo, T. C. Galvin, A. Ghaith, A. Ghigo, D. Giove, A. Giribono, L. A. Gizzi, F. J. Grüner, A. F. Habib, C. Haefner, T. Heinemann, A. Helm, B. Hidding, B. J. Holzer, S. M. Hooker, T. Hosokai, M. Hübner, M. Ibison, S. Incremona, A. Irman, F. Iungo, F. J. Jafarinia, O. Jakobsson, D. A. Jaroszynski, S. Jaster-Merz, C. Joshi, M. Kaluza, M. Kando, O. S. Karger, S. Karsch, E. Khazanov, D. Khikhlukha, M. Kirchen, G. Kirwan, C. Kitégi, A. Knetsch, D. Kocon, P. Koester, O. S. Kononenko, G. Korn, I. Kostyukov, K. O. Kruchinin, L. Labate, C. Le Blanc, C. Lechner, P. Lee, W. Leemans, A. Lehrach, X. Li, Y. Li, V. Libov, A. Lifschitz, C. A. Lindstrøm, V. Litvinenko, W. Lu, O. Lundh, A. R. Maier, V. Malka, G. G. Manahan, S. P. D. Mangles, A. Marcelli, B. Marchetti, O. Marcouillé, A. Marocchino, F. Marteau, A. Martinez de la Ossa, J. L. Martins, P. D. Mason, F. Massimo, F. Mathieu, G. Maynard, Z. Mazzotta, S. Mironov, A. Y. Molodozhentsev, S. Morante, A. Mosnier, A. Mostacci, A. -S. Müller, C. D. Murphy, Z. Najmudin, P. A. P. Nghiem, F. Nguyen, P. Niknejadi, A. Nutter, J. Osterhoff, D. Oumbarek Espinos, J. -L. Paillard, D. N. Papadopoulos, B. Patrizi, R. Pattathil, L. Pellegrino, A. Petralia, V. Petrillo, L. Piersanti, M. A. Pocsai, K. Poder, R. Pompili, L. Pribyl, D. Pugacheva, B. A. Reagan, J. Resta-Lopez, R. Ricci, S. Romeo, M. Rossetti Conti, A. R. Rossi, R. Rossmanith, U. Rotundo, E. Roussel, L. Sabbatini, P. Santangelo, G. Sarri, L. Schaper, P. Scherkl, U. Schramm, C. B. Schroeder, J. Scifo, L. Serafini, G. Sharma, Z. M. Sheng, V. Shpakov, C. W. Siders, L. O. Silva, T. Silva, C. Simon, C. Simon-Boisson, U. Sinha, E. Sistrunk, A. Specka, T. M. Spinka, A. Stecchi, A. Stella, F. Stellato, M. J. V. Streeter, A. Sutherland, E. N. Svystun, D. Symes, C. Szwaj, G. E. Tauscher, D. Terzani, G. Toci, P. Tomassini, R. Torres, D. Ullmann, C. Vaccarezza, M. Valléau, M. Vannini, A. Vannozzi, S. Vescovi, J. M. Vieira, F. Villa, C. -G. Wahlström, R. Walczak, P. A. Walker, K. Wang, A. Welsch, C. P. Welsch, S. M. Weng, S. M. Wiggins, J. Wolfenden, G. Xia, M. Yabashi, H. Zhang, Y. Zhao, J. Zhu & A. Zigler EuPRAXIA Conceptual Design Report The European Physical Journal Special Topics 229, 3675–4284 (2020); https://doi.org/10.1140/epjst/e2020-000127-8

## Slide 4
The EuPRAXIA project
The EuPRAXIA project aims at the construction of an innovative compact electron accelerator using laser- and electron-beam-driven plasma wakefield acceleration;
EuPRAXIA foresees the implementation of a laser wakefield accelerator (LWFA) at the 1-5 GeV target energy and a repetition rate of 20-100 Hz, requiring the most advanced and robust ultrashort pulse laser technologies available to date;
The Design Study project was carried out initially by 16 laboratories and universities from 5 EU member states within the European Union’s Horizon 2020 programme;
A Conceptual Design Study has addressed the development of a ultrashort pulse laser system (pulse durations in the range of tens of fs) and energies up to 100 joules, yielding a PW scale peak power, targeting a repetition rate of up to 100 Hz, a performance never achieved so far
EuPRAXIA was included in the ESFRI Roadmap (2021) and a Preparatory Phase project is ongoing.

## Slide 5
The EuPRAXIA project: main specs

## Slide 6: RATIONALE OF LASER DRIVER DESIGN STUDY
Three laser systems envisaged, to drive three stages:
Laser Plasma Injector at 150 MeV (LPI 150MeV) - Laser Plasma Injector/Accelerator at 1 GeV (LPI 1GeV) - Laser Plasma Accelerator at 5 GeV (LPA 5GeV)
For each system, two levels of performances considered:
P0: low energy, 20 Hz rep rate
P1: high energy, 100 Hz rep rate
In the EuPRAXIA project, several alternative technological approaches were considered and down-selected, to provide the required laser driver performances.
We based the design on Chirped Pulse Amplification (CPA) in Ti:Sapphire, pumped by all-solid state green lasers (i.e. diode pumped, frequency doubled Yb or Nd lasers)
Thermal management related to the handling of high pump average power was the most complex aspect in the design, requiring out-of-the-box thinking and original solutions
Optimization of energy extraction was also an issue, aimed to reduce pump energy requirements and waste heat production.

## Slide 7: GENERAL ARCHITECTURE
Modularity of amplification stages:
LPI 150 MeV  Laser1
LPI 1 GeV  Laser1 + Laser2
LPA 5 GeV  Laser1 + Laser2 + Laser3
adjustments on pulse duration/bandwidth
Synchronization: common master oscillator
Pulse duration/wavelength tailoring : separate front end
Scalability: possibility to upgrade from P0 to P1 performance levels without a major changes
LPI 150 MeV
LPI 1 GeV
LPA 5 GeV
Laser 1
Laser 1
Laser 1
Laser 2
Laser 2
Laser 3

## Slide 8: Underpinning EuPRAXIA Laser development
THERMAL
MANAGEMENT OF
POWER AMPLIFIERS
WATER/GAS COOLING
COMPRESSOR AND TRANSPORT: THERMAL AND MECHANICAL STABILITY
Gold -> MD, MLD, MMLD
reduction of the thermal load
cooling of residual heat
control of thermal effects
Main challenges: large optics, mechanical stability, beam quality control, pointing stability
DiPOLE 100 (STCF)
DPSSL PUMP
SOURCES
TECHNOLOGY
P-60 technology (Amplitude)
Currently no solution for full system specs (P1): development
Multipass transmission
AMPLIFIER GEOMETRY
TRANSMISSION
VS. REFLECTION
Multipass reflection
Prototyping needed
DIODE LASERS EFFICIENCY,
BRIGHTNESS AND
LIFETIME
Needs development
Prototyping needed
High repetition rate (100 Hz) will speed up R&D of pending issues for Ti:Sa laser TDR

## Slide 9: Transport to target
Main challenges: large optics, mechanical stability, cooling of gratings, beam quality control …

## Slide 10: Compressor: grating technology
Different technologies under evaluation to address main issues with higher repetition rate. Strategy includes reduction of the thermal load at high average power, cooling of residual heat and control of thermal effects on compression quality.

## Slide 11: Beam Pointing Stability
Environmental angular noise of about 30 nano-rad
1 µrad
Laser angular fluctuations footprints at 150 Hz
0,1 µrad
50 nrad
We already detect
<100nrad fluctuations
Z. Mazzotta, F. Mathieu
in collaboration with
S. Cialdi, D. Cipriani, S. Capra
of Università degli studi di Milano.
Spectral analysis of the laser fluctuation.
100
200
300
400
0
500
Frequency (Hz)
Angular fluctuation (nrad)
16
32
48
64
~40nrad
~10nrad
up to the MHz regime and more
Eupraxia requirements for beam pointing stability are extremely demanding. Both passive and active control will be required. Prior to the implementation of control strategies, tools are being developed to measure pointing stability performances at EuPRAXIA facilities and labs.

## Slide 12: AMPLIFICATION CHAIN: REQUIREMENTS
LASER 1 - Injector 150 MeV |  |  | 
Parameter | Label | P0 | P1
Wavelength (nm) | λ1 (nm) | 800 | 800
Maximum energy on target (J) | Etarget | 5 | 7
Maximum output energy (J) | Eout | 8.8 | 12.5
Energy tuning resolution (% of targeted value) | dE | 7 | 5
Total output energy (incl. Diagnostic beams) | Etot | 7 | 10
Pulse length (FWHM) (fs) | τ1 | 30 | 20
Repetition rate (Hz) | f1 | 20 | 100
Requirement on energy stability (RMS) % | σ<E> | 1 | 0.6
LASER 2 - Injector 1 GeV |  |  | 
Parameter | Label | P0 | P1
Wavelength (nm) | λ2 (nm) | 800 | 800
Maximum energy on target (J) | Etarget | 15 | 30
Maximum output energy (J) | Eout | 18.8 | 37.5
Energy tuning resolution (% of targeted value) | dE | 7 | 5
Shortest pulse length (FWHM) (fs) | τ2 | 30 | 20
Repetition rate (Hz) | f2 | 20 | 100
Requirement on energy stability (RMS) % | σ<E> | 1 | 0.6
LASER 3 - Driver 5 GeV |  |  | 
Parameter | Label | P0 | P1
Wavelength (nm) | λ2 (nm) | 800 | 800
Maximum energy on target (J) * | Etarget | 50 | 100
Maximum output energy (J) | Eout | 62.5 | 125
Energy tuning resolution (% of targeted value) | dE | 7 | 5
Shortest pulse length (FWHM) (fs) | τ2 | 60 | 50
Repetition rate (Hz) | f2 | 20 | 100
Requirement on energy stability (RMS) % | σ<E> | 1 | 0.6
Maximum output energy: (Energy on Target)/(Compressor Efficiency)
Compressor efficiency assumed 80%
Seed energy: 1.5 J

## Slide 13: AMPLIFIERS MODULAR ARCHITECTURE
Three main modules: LASER1, LASER2, LASER3
LASER1: stand-alone for LPI 150 MeV
LASER2: output stage for LPI 1 GeV, second stage for LPA 5GeV
LASER3: high energy stage for LPA 5GeV
Two levels of performance : P0 and P1
LPI 150 MeV
From the
front end
LASER1
Eout 8.8 J (P0) / 12.5 J (P1)
To the
compressor
LPI 1GeV
LASER2
Eout 18.8 J (P0) / 37.5 J (P1)
LPA 5GeV
LASER1
Eout 8.8 J (P0) / 12.5 J (P1)
LASER2
Eout 18.8 J (P0) / 37.5 J (P1)
LASER3
Eout 62.5 J (P0) / 125 J (P1)
LASER1
Eout 8.8 J (P0) / 12.5 J (P1
From the
front end
From the
front end
To the
compressor
To the
compressor
Epump: 19.2J (P0)/ 25.7 J (P1)
Epump: 37.2J (P0)/ 65.2 J (P1)
Epump: 105J (P0)/ 197 J (P1)
Foreseen I/O energy and pump requirements

## Slide 14: THERMAL MANAGEMENT
Expanding knowledge base for water cooled with "through" propagation: some examples
Water cooled Ti:Sa amplifier (“Active Mirror” configuration) under development at ELI-HU (After V. Cvhykov et al. , Opt. Lett, 41, 3017, 2016)
Fluid (D2O ) cooled 3 kW Nd:YAG laser, 20 kW CW pump power, D2O (After X. Fu et al. , Opt. Express, 22, 18421 (2014)
Fluid (Siloxane ) cooled Nd:YLF laser, 5 kW CW pump power (After Z. Ye et al. , Opt. Express, 24, 1758 (2016)

## Slide 15: AMPLIFICATION MODULES: CONCEPTUAL LAYOUT
Pump beam
Pump recycling
mirror
Pump
recycling mirror
Ti:Sapphire
crystals
Input beam
Ouput beam
Steering mirror
Steering mirror
Steering mirror
Steering mirror
Water flow
Water flow
Window
Water flow
Window
Two possible solutions envisaged, determined by thermal management considerations
Common features: - gas cooling found to be insufficient at the given power density
- face cooling of gain elements by water flow (longitudinal cooling)
- gain volume split in some sub-elements to increase cooling surface
- multi-step pumping for parasitic laser management
Double side, double pass pumping
Crystal split in 2 elements, face cooled by water flow, to increase cooling surface
Multipass amplification (4 to 6 depending on stages)
Absorption layer on crystal sides for parasitic lasing suppression
1 – Multipass amplification scheme in transmission

## Slide 16: AMPLIFICATION MODULES: CONCEPTUAL LAYOUT
Multi-pass pumping scheme to ensure effective pump absorption
Overall pump energy equally divided among the 4 elements
Overall gain length split in 4 elements, water cooled on the back side
Multiple reflections required to obtain efficient energy extraction
Absorption layer on crystal sides for parasitic lasing suppression
Ouput beam
Reflective coating
(cooled side)
Absorber
Cooling flow
Cooling flow
Input beam
Pump
recycling
mirrors
Pump
beam
Ti:Sapphire
crystal
Ti:Sapphire crystals
Multipass mirrors
Two possible solutions envisaged, determined by thermal management considerations
Common features: - face cooling of gain elements by water flow (longitudinal coling)
- gain volume split in some sub-elements to increase cooling surface
- multi-step pumping for parasitic laser management
2 – Multipass amplification scheme in reflection (“Active mirror”)

## Slide 17: CRITICAL DESIGN CROSSROAD
Pump beam
Pump recycling
mirror
Pump
recycling mirror
Ti:Sapphire
crystals
Input beam
Ouput beam
Steering mirror
Steering mirror
Steering mirror
Steering mirror
Water flow
Water flow
Window
Water flow
Window
Which geometry is better?
Multipass transmission
Ouput beam
Reflective coating
(cooled side)
Absorber
Cooling flow
Cooling flow
Input beam
Pump
recycling
mirrors
Pump
beam
Ti:Sapphire
crystal
Multipass reflection
Pro’s
Simpler scheme (up to 2 sub-crystals, single pump path)
Broader cooling surface available
Less sensitive to mechanical vibrations
Less sensitive to parasitic reflections (contrast issues)
Con’s
Aberrations from fluid turbulences
Very critical design of the fluid ducts
Pro’s
No aberration from cooling fluid
Modularity
Con’s
Less cooling capability
More complex set-up (up to 3 units required , pump splitting)
More sensitive to mechanical vibrations
Possible issues from parasitic reflections (pulse contrast)
Both schemes equally studied in the preliminary design: equivalent perfomances from simulations
Critical aspects (i.e. optical aberrations from cooling fluid) beyond numerical simulations capabilities
Dedicated experimental development (i.e. realization and testing of small scale pilot devices) is required to address this design choice

## Slide 18: EXAMPLE OF LAYOUT FOR TRANSMISSION AMPLIFIERS
6 passes configuration, bow-tie geometry
Angle between passes ~ n x 1.2° (n=1,2,3)
Footprint length: ~ 4 mt (Laser 1)
~ 5 mt (Laser 2)
~ 8 mt (Laser 3)
(to avoid beam superimposition)
Amplification path
Pumping path (single pump source, split in 2 pulses)
First pulse
Second pulse (from a delay line)
Each pump pulses passes twice through the crystals
Pumping from both sides to reduce peak fluence and parasitic lasing
Extraction During Puming (EDP) implementation
The pump pulse must be split before of the injection; one of the pulses goes through a delay line to implement the EDP
x
y
z
x
y
z
Ti:Sa
Ti:Sa
x
z
y
Off-plane angular multiplexing of the pump beams to have more pump “gates” available
Pump angular multiplexing: 2 pumping “gates” required for each pump laser

## Slide 19: PUMP TIMING AND EDP ENERGY RIPARTITION
t
First pump
pulse
0
tr
2tr
3tr
4tr
5tr
Second pump pulse (after delay line)
Pump pulse absorption time ~10 ns
tr: pulse round trip time between passes
(12 ns, 15 ns, 18 ns respectively for Laser 1, Laser2 and Laser3
The delay line of the second pump pulse has to to provide the proper delay between the two pulses.
Amplified pulse
Seed pulse (at t=0)
Seed pulse
1° Pump pulse
Stored energy
2° Pump pulse

## Slide 20: EXAMPLE OF LAYOUT FOR REFLECTION AMPLIFIERS
3 disks, 2 double passes configuration
Half angle between passes ~ 1.2°-2.4 °
Footprint length: ~ 3 mt (Laser 1)
~ 5 mt (Laser 2)
~ 8 mt (Laser 3)
(to avoid beam superimposition)
Footprint width < 1.5 m
Straightforward extension to 4 disks
Amplification path
Pumping path (single pump source)
x
y
z
x
z
y
Off-plane pump injection to avoid beam path occlusions
One injection “gate“ for each pump source
Delay line
Mirror
Delay line
Delay line
Beamsplitter
Beamsplitter
Pump pulse energy is distributed among the disks by beamsplitters (or waveplates+polarizers)
Each pump pulse passes twice through the crystals
EDP implementation
The arrival of the pump pulse is synchronized with the arrival of the amplified pulse by means of fixed delay lines (equal path length) . Energy repartition between the passes is achieved by fine tuning of the delay
x
y
z
Ti:Sa
Ti:Sa
Ti:Sa

## Slide 21: PUMP TIMING AND EDP ENERGY RIPARTITION
tr: pulse round trip time between passes
(12 ns, 15 ns, 18 ns respectively for Laser 1, Laser2 and Laser3
The delay lines of the pump between the disk ensures synchronization of pump arrival with the seed pulse. Fraction f1 of pump pulse energy is available for 1° pass amplification, fraction f2 for the 2° pass.
The ratio f1/f2 can be adjusted by finely tuning the delay between the pump and the seed pulse
Seed pulse (at t=0)
Seed pulse
Pump pulse
Stored energy
t
0
Disk 1
f1
f2
t
0
tr
5tr
Disk 2
6tr
f1
f2
t
0
2tr
4tr
Disk 3
f1
f2

## Slide 22: NUMERICAL SIMULATION OF AMPLIFICATION MODULES
The different amplification stages were extensively analyzed in the different architectures (transmission vs reflection scheme)
Simulations for the two architectures implemented:
same overall gain length, number of passes
same doping level
same overall pump energy
same beam cross section
We obtained:
- Very similar energy extraction performance for the two schemes
- Very similar sensitivity of output energy vs seed, pump energy
Results are summarized in the following slides
The amplification stages were numerically simulated (MIRO - CEA)
The code allows for the simulation of amplification of ultrashort pulses, accounting for GVD, nonlinear effects, spectral narrowing effects and so on
vs.

## Slide 23: AMPLIFICATION MODULES: AMP 1
Crystal clear aperture  (cm) | 6 cm | Crystal thickness (cm, overall) | 1.2
Doping level (%Wt.) | 0.075 | Absorption coefficient (cm-1) | 1.2
Pump energy (J) | 19.2 | Pump beam diameter (cm, FWHM) | 5.0
Pump fluence at crystal surfaces (J/cm2) | 0.76 | Absorbed pump energy (%) | 94%
Seed pulse energy (J) | 1.5 | Seed beam diameter (cm, FWHM) | 4.7
Output energy | 8.9 | Extraction efficiency | 38.7%
Output beam diameter (cm FWHM) | 4.5 | Output beam peak fluence (J/cm2) | 0.55
EDP scheme | 65% 1st pass, 35% 4th pass | Max GT |  15 (before the 4th pass)
Spump (ΔEout/ΔEpump) | 0.53 | Sseed (ΔEout/ΔEseed) | 2.4
Performance level P0
Pump energy (J) | 25.7 | Pump beam diameter (cm, FWHM) | 5.0
Pump fluence at crystal surfaces (J/cm2) | 1.01 | Absorbed pump energy (%) | 94%
Seed pulse energy (J) | 1.5 | Seed beam diameter (cm, FWHM) | 4.7
Output energy (J) | 12.7 | Extraction efficiency | 43.6%
Output beam diameter (cm FWHM) | 4.6 | Output beam peak fluence (J/cm2) | 0.765
EDP scheme | 65% 1st pass, 35% 4th pass | Max GT |  30 (before the 4th pass)
Spump (ΔEout/ΔEpump) | 0.58 | Sseed (ΔEout/ΔEseed) | 2.67
Performance level P1
6 passes amplification scheme

## Slide 24: AMPLIFICATION MODULES: AMP 2
Performance level P0
Performance level P1
6 passes amplification scheme
Crystal clear aperture  (cm) | 10 | Crystal thickness (cm, overall) | 2.0
Doping level (%Wt.) | 0.05 | Absorption coefficient (cm-1) | 0.79
Pump energy (J) | 37.2 | Pump beam diameter (cm, FWHM) | 9.0
Pump fluence at crystal surfaces (J/cm2) | 0.425 | Absorbed pump energy (%) | 96%
Seed pulse energy (J) | 6.25 | Seed beam diameter (cm, FWHM) | 8.0
Output energy (J) | 19.1 | Extraction efficiency | 35.0%
Output beam diameter (cm FWHM) | 8.0 | Output beam peak fluence (J/cm2) | 0.38
EDP scheme | 60% 1st pass, 40% 3rd pass | Max GT |  6 (before the 3rd pass)
Spump (ΔEout/ΔEpump) | 0.45 | Sseed (ΔEout/ΔEseed) | 1.8
Pump energy (J) | 65.2 | Pump beam diameter (cm, FWHM) | 9.0
Pump fluence at crystal surfaces (J/cm2) | 0.75 | Absorbed pump energy (%) | 96%
Seed pulse energy (J) | 8.75 | Seed beam diameter (cm, FWHM) | 8.0
Output energy (J) | 37.5 | Extraction efficiency | 44.1%
Output beam diameter (cm FWHM) | 8.3 | Output beam peak fluence (J/cm2) | 0.72
EDP scheme | 60% 1st pass, 40% 3rd pass | Max GT |  14 (before the 3rd pass)
Spump (ΔEout/ΔEpump) | 0.53 | Sseed (ΔEout/ΔEseed) | 1.49

## Slide 25: AMPLIFICATION MODULES: AMP 3
Performance level P0 (6 passes)
Performance level P1 (4 passes)
Crystal clear aperture  (cm) | 16 cm | Crystal thickness (cm, overall) | 3.2
Doping level (%Wt.) | 0.03 | Absorption coefficient (cm-1) | 0.47
Pump energy (J) | 105 | Pump beam diameter (cm, FWHM) | 14.0
Pump fluence at crystal surfaces (J/cm2) | 0.51 | Absorbed pump energy (%) | 96%
Seed pulse energy (J) | 18.8 | Seed beam diameter (cm, FWHM) | 12.8
Output energy (J) | 62.4 | Extraction efficiency | 41.5%
Output beam diameter (cm FWHM) | 12.8 | Output beam peak fluence (J/cm2) | 0.49
EDP scheme | 65% 1st pass, 35% 3rd pass | Max GT |  18 (before the 1st pass)
Spump (ΔEout/ΔEpump) | 0.53 | Sseed (ΔEout/ΔEseed) | 1.64
Pump energy (J) | 197 | Pump beam diameter (cm, FWHM) | 14.0
Pump fluence at crystal surfaces (J/cm2) | 0.95 | Absorbed pump energy | 96%
Seed pulse energy (J) | 37.5 | Seed beam diameter (cm, FWHM) | 12.8
Output energy (J) | 126.0 | Extraction efficiency | 44.9%
Output beam diameter (cm FWHM) | 13.0 | Output beam peak fluence (J/cm2) | 1.08
EDP scheme | 65% 1st pass, 35% 3rd pass | Max GT |  20 (before the 3rd pass)
Spump (ΔEout/ΔEpump) | 0.54 | Sseed (ΔEout/ΔEseed) | 1.4

## Slide 26: EXAMPLES OF SIMULATION RESULTS
Input/output spectrum (AMP3, P1)
Input/output beam profile (AMP3, P1)
Output energy vs. number of passes (AMP3, P1, transmission / reflection schemes)
Output energy vs. pump pulse energy (AMP1, P0)

## Slide 27: FLUID-DYNAMICS SIMULATIONS
Water cooling of disk amplifiers: modelling physics
Simulation software: COMSOL multiphysics (ver. 4.2 and 5.2)
Finite Element Analysis approach
Numerical solution of the Navier-Stokes equations for mass and energy transport
Low Reynolds k-ε solution method
Thermal coupling with boundary layer at the channel walls (heated Ti:Sa crystal)
Time-averaged simulation (i.e. time-dependent turbulences not modelled)
Temperature distribution
Velocity magnitude distribution
Water flow direction
292
291
290
289
288
Example:
channel thickness 5 mm, flat channel walls
inlet flow speed 6 m/sec,
heat input 25 W/cm2 (AMP3 at P1 performance level)
heated length 160 mm (AMP3 pump beam );
temperature dependence of water properties
water input temperature 15 °C
mesh  128000 elements
Temperature of Ti:Sa surface at different inlet flow speed
Water inlet temperature 15°C (288.15 K)
Heat input 25 W/cm2, Channel heigth 5 mm
Effective film coefficient (heat exchange coefficient between water and heated wall for different flow speed and heat input levels

## Slide 28: THERMOMECHANICAL SIMULATIONS
Modelling: Finite Element Analysis (FEA)
Temperature distribution
Temperature distribution for AMP3 transmission disk (left, 1.6 cm thickness) and AMP3 reflection disk (right 1.3 cm thickness) at P1 pump level
Deformation distribution
Axial displacement distribution (mm) for AMP3 transmission disk (left, 1.6 cm thickness) and AMP3 reflection disk (right 0.8 cm thickness) at P1 pump level
Optical path difference (OPD)
OPD in microns resulting from thermal expansion and thermooptic effect. Parabolic fit and higher order aberrations also shown. Left: AMP3 transmission disk; right AMP3 reflection disk at P1 pump level
Peak T: 40.8 °C
Peak T: 89.5 °C
Phase modification requires Adaptive Optics compensation

## Slide 29: PUMP SOURCES TECHNOLOGIES
Cryogenically operated Yb:YAG, diode pumped
100J @1030 nm , 10 Hz demonstrated
Energy stabilty 1% RMS (few hours of operation)
60 J SHG @ 515 nm, 10 Hz expected
DiPOLE 100 (STCF)
Possible upgrades include:
IR Output energy 150 J
SHG output > 100 J
PRF 100 Hz @ 10 J
Nd:YAG Disk Amplifier Heads (DAH), liquid cooled.
Current design: flashlamp pumping
Scalable design (n. of DAH units): P20, P30…
Design specificatons (6 DAH):
~80 J @ 1064 nm, 10 Hz
60 J @ 532 nm, 10 Hz
Possible developments
- Diode pumping
- 50 Hz rep rate
P-60 technology (Amplitude)

## Slide 30: DIMENSIONING OF PUMP SOURCES ARRAYS
P0 performance level
Issue: P0 operation regime has a pulse repetition rate of 20 Hz.
The two available pump sources have a repetition rate of only 10 Hz.
To circumvent this problem (until higher rep rate devices are developed) we considered to use two (or two sets) of pump sources and shot them interleaved, so that repetition rate of the pump pulses arriving to the amplifiers id effectively doubled.
Issue: Pump energies higher than about 60 J (as needed by the AMP3 module) require more than a single pump source.
This calls for specific arrangements to multiplex the input from several pump units to the amplification crystals.
P1 performance level
Issue: P1 operation regime considers a pulse repetition rate of 100 Hz, along with higher energies than P0. Currently no solutions for pump sources are available to meet these requirements.
Speculatively, we have considered the availability of a system similar to Amplitude P60 but operating at 50 Hz (conversion to diode laser pumping of the flashlamp pumped P60) with the same output energy of 60 J/pulse in the green.
Again, reaching 100 Hz requires the time interleaving of a pair of twin sources. This analysis did not include the DiPOLE 100 system, as no developments are currently planned toward a high energy, high rep rate system.

## Slide 31: Diode laser developments

## Slide 32: MAIN OUTPUTS OF THE EUPRAXIA DESIGN STUDY
Requirements on energy, pulse duration, stability etc set by the LPA working point
Design based on CPA in Ti:Sapphire, dictated by requirements vs. time scale
Thermal management issues addressed by means of liquid cooling
Main developments required:
Prototyping of Ti:Sa amplifiers: fluid cooling (choice between reflection/transmission amplifier): possibly by means of pilot devices
Addressing 100 Hz pump lasers developments
Thermal management of compressor gratings
Stability (pointing & more) and active control
Driver pulse temporal shaping and synchronization
Construction
Integration Issues

## Slide 33: The end
Thank you!