## Slide 1
3D structure of microbunched plasma-wakefield-accelerated electron beams inferred by coherent optical transition radiation
Helmholtz-Zentrum Dresden-Rossendorf
M. LaBerge, A. Debus, O. Zarini, A. Willmann, R. Pausch, Y. Y. Chang,
J. Couperus Cabadağ, S. Schöbel, P. Ufer, U. Schramm, A. Irman
University of Texas – Austin
A. Hannasch, B. Bowers, R. Zgadzaj, M. C. Downer
Fermilab
A. H. Lumpkin

## Slide 2
We have produced consistent FEL quality electron beams at HZDR
Marie Labat et al., „Seeded free-electron laser driven
by a compact laser plasma accelerator“, Nat. Photon. 17, 150 (2022). https://doi.org/10.1038/s41566-022-01104-w
Comprehensive in-situ diagnostics are important to improve the LPA performance
High spectral-charge density LPA beams + COXINEL line enable free-electron lasing in a seed configuration.

## Slide 3: What would we like to know about our electron beams
Size (micron scale resolution)
Emittance
Structures
  Correlations
  Microbunching
Observe the beam evolution
Ideally observed in a single shot
Dependence of these parameters on the injection process
  Pre-bunched beams

## Slide 4: Longitudinal beam structure is encoded in the coherent transition radiation spectrum
Currents on the foil surface are driven by the electron beam
These radial currents give way to broadband transition radiation
Longitudinal structures in the electron beam are encoded in the transition radiation spectrum
Sim: 200 MeV, 20pC, 10 fs bunch length, 20 µm diameter

## Slide 5: Coherent transition radiation has been a valuable tool for observing electron beam structures
CTR has been used to diagnose microbunching
Determine the displacement between two LPA beams
Characterize slice energy spread of LPA beams
Reconstruct LPA longitudinal beam profile
Tremaine, A., et al.: Observation of self-amplified spontaneous-emission-induced electron-beam microbunching using coherent transition radiation. Phys. Rev. Lett. 81(26), 5816–581 (1998).
Glinec, et al.: Observation of fine structures in laser-driven electron beams using coherent transition radiation. Phys. Rev. Lett. 98(19), 98–101 (2007).
Bajlekov, S. I., et al. "Longitudinal electron bunch profile reconstruction by performing phase retrieval on coherent transition radiation spectra." Physical Review Special Topics-Accelerators and Beams 16.4 (2013): 040701.
See also:
Lundh, O. et al. Few femtosecond, few kiloampere electron bunch produced by a laser–plasma accelerator. Nature Phys 7, 219–222 (2011).
Heigoldt, M. et al.: Temporal evolution of longitudinal bunch profile in a laser wakefield
accelerator. Phys. Rev. ST Accel. Beams 18, 121302 (2015).
Bakkali Taheri, F. et al.: Electron bunch profile reconstruction based on phase-constrained iterative algorithm. Phys. Rev. Accel. Beams 19(3), 032801 (2016).
See also:
Lumpkin, A.H. et al.: Evidence for Microbunching “Sidebands” in a Saturated Free-Electron Laser Using Coherent Optical Transition Radiation. Phys. Rev. Lett. 88(23), 234801 (2002).
Glinec, et al.: Observation of fine structures in laser-driven electron beams using coherent transition radiation. Phys. Rev. Lett. 98(19), 98–101 (2007).
Lin, C. et al.: Long-range persistence of femtosecond modulations on laser-plasma-accelerated electron beams. Phys. Rev. Lett. 108, 094801 (2012).
Lin, C. et al.: Long-range persistence of femtosecond modulations on laser-plasma-accelerated electron beams. Phys. Rev. Lett. 108, 094801 (2012).

## Slide 6
Coherent transition radiation based longitudinal reconstructions at HZDR

## Slide 7: We use a multi-octave spectrometer to measure coherent transition radiation from LPA electron bunches
Single shot capability
5.4 octave frequency range (250 nm – 11.35 µm)
High dynamic range ()
Absolutely and relatively calibrated
Detection limit ~ 50 fC
Time resolution of ~0.5 fs

## Slide 8: Using the radiation spectrum and an iterative phase reconstruction algorithm, we determine the longitudinal beam profile
O. Zarini et al., “Multioctave high-dynamic range optical spectrometer for single-pulse, longitudinal characterization of ultrashort electron bunches,” Phys. Rev. Accel. Beams 25, 012801, 2021.
O. Zarini et al., "Advanced Methods for Temporal Reconstruction of Modulated Electron Bunches," Breckenridge, CO, USA, 2018, pp. 1-5, doi: 10.1109/AAC.2018.8659388.
Measured
Measured
Reconstructed
Notes: Hybrid-input-output and Gerchberg-Saxton reconstruction algorithms sequentially used

## Slide 9: Injection mechanisms have a critical effect on the structure of the electron bunch
Down-ramp injection
K. Schmid et al., "Density-transition based electron injector for laser driven wakefield accelerators", Phys. Rev. ST Accel. Beams, Vol. 13 pp. 091301, 2010
Pak et al., “Injection and Trapping of Tunnel-Ionized Electrons into Laser-Produced Wakes”, Phys. Rev. Lett., vol 104, no. 2 pp. 025003, 2010.
Lu et al., “Generating multi-GeV electron bunches using single stage laser wakefield acceleration in a 3D nonlinear regime”, Phys. Rev. ST Accel. Beams, vol. 10, no. 6, pp. 061301, 2007.
Self injection
Ionization injection
Ionization injection: Inner shell electrons from nitrogen are ionized inside the bubble
Down-ramp: Plasma density gradient changes the shape of the bubble
Self injection: Laser evolution changes the shape of the bubble

## Slide 10: Observed longitudinal bunch structure is injection regime dependent
Injection regime affects both bunch duration and substructure
Discussed in depth yesterday by Alexander Debus, WG 7
Down-ramp injection
Self-injection
Ionization injection (STII)
Measured
Reconstructed

## Slide 11
Transverse information encoded in coherent optical transition radiation

## Slide 12: Near field optical transition radiation encodes electron bunch spatial information
Single electron point spread function (PSF)
Signal after a horizontal linear polarizer
Lens
Radiation from a single electron is annular and radially polarized
When the foil is imaged (near field), a point spread function intensity pattern occurs around the electron location

## Slide 13: Coherent OTR is the result of sums of fields as opposed to intensities
Incoherent OTR
Coherent OTR
Radius (µm)
Radius (µm)
-5
5
0
1 µm
FWHM
2 µm
FWHM
4 µm
FWHM
Intensity (arb.)
Intensity (arb.)
Intensity (arb.)
Charge/ µm
Charge/ µm
Charge/ µm
-5
5
0
OTR
e- bunch
Point spread function (PSF)
Single particle
field (SPF)
Electric field (arb)
-1
1
0
-10
10
0
Radius (µm)
-10
10
0
Radius (µm)
Intensity (arb.)
Incoherent
Coherent

## Slide 14
OTR radiation
Foil
e-
θ Radians
Interference Function
Intensity (arb.)
A. H. Lumpkin et al. “Evidence for Microbunching “Sidebands” in a Saturated Free-Electron Laser Using Coherent Optical Transition Radiation“, Phys. Rev. Let., vol. 88, pp. 234801, 2002.
OTR
COTRI
Far field OTR
COTR interferometry fringes are due to interference between two COTR sources
Two COTR sources close enough together will interfere, resulting in COTR interferometry (COTRI)
In the far field intensity pattern, this manifests as the single source pattern scaled by an interference function

## Slide 15
A. Lumpkin, M. LaBerge et al., “Coherent Optical Signatures of Electron Microbunching in Laser-Driven Plasma Accelerators”, Phys. Rev. Lett., vol 88, pp. 234801, 2020.
We measure the far field and near field COTR simultaneously on a single shot
Blocking foil reflects ~2.5 J Draco pulse
Aluminized Kapton foil is first COTR source
Si wafer is second COTR source
Linearly polarized near field COTR imaged with microscope objective
  Only sees COTR from first source
  600 nm image
Focus of objective imaged using second lens to create far field image on camera
  Sees interference from both COTR sources
Measured
Measured

## Slide 16
COTR from various
microbunched sizes
COTRI from various
microbunched divergences
A. Lumpkin, M. LaBerge et al., “Coherent Optical Signatures of Electron Microbunching in Laser-Driven Plasma Accelerators”, Phys. Rev. Lett., vol 88, pp. 234801, 2020.
Near field and far field COTR can constrain the microbunched emittance
Microbunching fraction
Microbunched size measured to be µm
COTRI outer fringe visibility is most sensitive to microbunched divergence
Microbunched divergence measured to be mrad
Microbunched normalized emittance of mm mrad

## Slide 17
Multi-spectral imaging of coherent optical transition radiation

## Slide 18: Different wavelength COTR patterns exhibit unique aspects of the beam structure
Longer bunches suppress the shorter wavelength COTR
Multiple beamlets will constructively and destructively interfere at different locations at different wavelengths
Multispectral COTR imaging is sensitive to correlations in transverse-longitudinal beam structure

## Slide 19
Ionization
Coherent optical transition radiation patterns correlate with injection regime
Down-ramp:
Small (~5 µm size)
Shape does not dramatically change across wavelengths
Self injection:
Largest (~15 µm size) and most complex
Ionization injection:
Larger (~10 µm size)
Two annular patterns visible at longer wavelengths

## Slide 20
Radiation size scales roughly linearly with coherent bunch size
For lower densities, down-ramp generates slightly smaller radiation patterns
Self injected electron bunches consistently produced the largest radiation patterns
Radiation size across different regimes
The effective radius () of COTR patterns is also very sensitive to injection regime

## Slide 21: Particle in cell simulations show structures that are corroborated by COTR images
Observed COTR patterns show evidence of laser-induced transverse-longitudinal modulation
Isolating the contribution of such a modulation qualitatively reproduces observed long wavelength COTR
High spatial frequency features from the ionization injection process could be responsible for the COTR patterns at shorter wavelengths

## Slide 22
The geometry of down-ramp induces injection leads to a chirp in the bunch
With a reasonable chirp estimate, we back out the beam profile
Using the COTR images and beam profile as inputs to a differential evolution reconstruction algorithm, we can make a 3D bunch reconstruction
Using independent information about the beam’s longitudinal profile and COTR images, we reconstruct a 3D bunch
Measured
Reconstructed

## Slide 23: We use clustering to determine the uniqueness of our reconstructions solutions
Normalized
These reconstructions are not necessary unique
Principle component analysis allows us to identify the number of clusters of reconstructions
When the average of reconstructions in a cluster reproduce the data, we have a compact family of solution
With COTR imaged at more wavelengths, we could further constrain these reconstruction solutions
Principle component analysis of 120 reconstructions

## Slide 24: Outlook and challenges
Combining CTR spectra and images
Pre/post undulator CTR
CTR from a beam driven geometry
Coherent x-ray transition radiation
Non-intercepting diagnostics
Konoplev, I. V., et al. "Single shot, nondestructive monitor for longitudinal subpicosecond bunch profile measurements with femtosecond resolution." Physical Review Accelerators and Beams 24.2 (2021): 022801.
+
Lumpkin, A.H. et al.: Evidence for Microbunching “Sidebands” in a Saturated Free-Electron Laser Using Coherent Optical Transition Radiation. Phys. Rev. Lett. 88(23), 234801 (2002).
Bajlekov, S. I., et al. "Longitudinal electron bunch profile reconstruction by performing phase retrieval on coherent transition radiation spectra." Physical Review Special Topics-Accelerators and Beams 16.4 (2013): 040701.
Lumpkin, Alex H., William M. Fawley, and Donald W. Rule. "A Concept for Z-dependent Microbunching Measurements with Coherent X-ray Transition Radiation in a SASE FEL." (2004).
Diffraction radiation

## Slide 25: Conclusion
Characterizing high peak current, micron-scale beams requires the development and adaptation of various diagnostics
High resolution longitudinal beam information is spectrally encoded in coherent transition radiation
Combined with multi-spectral transverse information, 3D beam structure can be gleaned
Microbunched structures present in LPA accelerated electron beams are injection regime dependent

## Slide 26
Thank you for your attention