## Slide 1: New methods to produce polarized 3He ion beams
Markus Büscher
6th European Advanced Accelerator Concepts Workshop | Isola d'Elba | 20 September 2023
Polarized Fusion: The time has come!
Notes: 15 + 5 minutes

## Slide 2: Polarized Fusion: The basic idea
Physics Today, August 1982
D
T or 3He
(A=5)*

## Slide 3: Polarized Fusion: in The beginnings of nuclear physics
First ideas date back to the 1930s
Mathematical Proceedings of the Cambridge Philosophical Society, 30, 561 (1934). doi:10.1017/S0305004100012810
Maurice Goldhaber, 1911 – 2011
Notes: In 1934, with James Chadwick from the Cavendish Laboratory at Cambridge, he was the first to measure accurately the mass of the neutron
“I don’t have time to age.”

## Slide 4: Enhanced Fusion cross sections
Typical increase of fusion cross sections by factor 1.5
L. Baylor et al., Nucl. Fusion 63 076009 (2023). doi.org/10.1088/1741-4326/acc3ae
M. Temporal et al., Nucl. Fusion 52 103011 (2012). doi:10.1088/0029-5515/52/10/103011
Tokamaks:
Increase in fusion power by factor 1.8 (estimate for ITER)
Laser-induced:
Gain increases by ~45% while the required laser power decreases by about 20%
Notes: Hupin et al.: „operational temperature decreased by as much as 45%“

## Slide 5: Anisotropic Angular distributions
„The anisotropy of the angular differential cross section ... can be used to force the emitted neutrons and α to be two to five times more focused towards the reactor blanket.“
(2019)
See also: The status of “polarized fusion”, H. Paetz gen. Schieck, Eur. Phys. J. A 44, 321 (2010)
Nuclear Fusion with polarized fuel, Springer Proceedings in Physics 187 (2016)
Notes: Hierfür reicht es, wenn nur das Deuteron polarisiert ist.

## Slide 6: Are there show-stoppers?
Does polarization survive (in the fusion plasma) long enough?
How to produce enough polarized fuel (e.g. neutral beams, pellets)?

## Slide 7: Episode 1: Polarization in Fusion plasmas
“The typical association of nuclear spin alignments is with low temperatures, making it counter-intuitive that they could endure in a 108 Kelvin plasma long enough to have practical applications.”
🤯

## Slide 8: The first experimental approach (2010)
Accelerated protons
foil
target
☞ „Are the accelerated (MeV) protons polarized?“
µm-sized relativistic plasma
200 TW laser beam
Notes: µm sized laser-plasmas = test bed for fusion plasmas

## Slide 9: Interactions in plasmas involving Spins
A theoretical study for particle acceleration in plasmas
Relevant processes for e−, p, ions:
T-BMT (Thomas precession)
Sokolov-Ternov effect
Stern-Gerlach force
Radiation reaction (only for ultra-relativistic particles)
Notes: Thomas-Bargmann-Michel-Telegdi
Since then approx. 20-30 theoretical paper on pol. Beam production

## Slide 10: Modelling of Spins in laser-induced plasmas
Implementation of particle spins into a simulation code (in collaboration with A. Pukhov & P. Gibbon …)
PIC Code (VLPL, EPOCH)
Description of spin motion in arbitrary electric and magnetic fields in the semi-classical approach
Thomas-BMT equation
Rotation frequency in cgs units
with
Notes: Paul Ehrenfest: under certain conditions the classical equations of motion apply to the mean values of quantum mechanics; classical mechanics is thus to a certain extent contained in quantum mechanics (principle of correspondence).

## Slide 11: Modelling of Spins in laser-induced plasmas
Implementation of particle spins into a simulation code (in collaboration with A. Pukhov & P. Gibbon …)
PIC Code (VLPL, EPOCH)
Description of spin motion in arbitrary electric and magnetic fields in the semi-classical approach
Thomas-BMT equation
➔ Talk by Lars Reichwein on Thursday: „Acceleration of polarized protons from laser-plasmas“
Notes: Paul Ehrenfest: under certain conditions the classical equations of motion apply to the mean values of quantum mechanics; classical mechanics is thus to a certain extent contained in quantum mechanics (principle of correspondence).

## Slide 12: The (updated) experimental approach
Accelerated Ions
polar.
3He*)
target
Fusion reactions
☞ „Does the (fusion) rate depend on the target polarization?“
☞ „Are the accelerated (MeV) ions polarized?“
☞ „Angular dependence of fusion products?“
µm- to mm-sized relativistic plasma
Petawatt laser beam
*) Isospin partner of tritium (non-radioactive)
Notes: µm sized laser-plasmas = test bed for fusion plasmas

## Slide 13: The Target material: Polarized 3He gas
Metastability-Exchange Optical Pumping (polarizer borrowed from Univ. Mainz)
Photos: Ilhan Engin
C. Mrozik et al., Construction of a compact 3He polarizing facility, J. Phys. Conf. Ser. 2011, 294, 012007
Max. 3He polarization: ~75%
Relaxation times: hundreds of hours (up to 3 bar in transport vessels)
Notes: MEOP rapidly produces nuclear polarization in metastable 3He atoms at mbar-scale pressures by a combination of optical pumping and hyperfine mixing. The metastable nuclear spin polarization is then rapidly transferred to the ground state population via metastability exchange collisions. Typically the gas is then compressed for use in applications.

## Slide 14: The Laser: PHELIX @ GSI Darmstadt
Petawatt High-Energy Laser for Heavy Ion EXperiments
Flashlamp-pumped Nd:glass system
 | Short pulse | Long pulse
Pulse duration | 0.4 – 20 ps | 0.7 – 20 ns
Pulse energy | up to 250 J | 300 – 1000 J
Max. intensity | 2 ∙ 1021 W/cm2 | 1016 W/cm2
Pulse duration 2.2 ps
Shot # per day

## Slide 15: Experimental setup @Phelix (Aug. 2021)
Phelix laser beam
Polarimeter
Pressure booster
3He jet
gas

## Slide 16: Polarimetry for 3He ions
Employ analyzing power of the reaction
Transverse polarization () of the ions
↕︎
Measurable left/right rate asymmetry of 𝛼 particles
Helmholtz coils
off
on
− on
CD2 foil

## Slide 17: After 2 years of data analysis …
expected signal for unpol. ions
Asymmetry
3He-ion polarization conserved after acceleration
2x increased 3He-ion flux from pol. plasma (reason unclear)
Our concept (polarized target @ PW laser) works
Plasma acceleration of polarized beams (e–*), p, ions) feasible
Models/simulation codes incomplete (topic for the coffee breaks)
… shown for the first time!
Preliminary
*) Talk by K.Poder

## Slide 18: Towards polarized 3He beams
PHELIX Experiment 2021:
Target: gas-jet width 1 mm
Max. 3He ion flux ⊥ to laser propagation (→ polarimeters)
EPOCH & VLPL simulations: predicted degree of polarization ≈99%
P. Gibbon, talk at 48th European Conference on Plasma Physics (2022)
Next PHELIX Experiment:
Target jet width 0.5 mm
Max. 3He ion flux ∥ to laser propagation

## Slide 19: Episode 2: How to produce polarized fuel

## Slide 20: Top news: it‘s so simple!
Particle beam

## Slide 21: Breit-Rabi diagram of metastable hydrogen atoms
The typical energy difference (=photon energy) is very small (neV)
😮
e–
p
e–
p
Notes: Das Magnetfeld, das das Proton durch den Elektronenspin sieht, ist 2.08 T für metastabile Atome (16.6 T für den Grundzustand).
Alpha 1 hat ein abstoßendes mag. Moment durch m_J=+1/2 und ein anziehendes durch m_I=+1/2.
Die gemischten Zustände haben zwei anziehende Anteile durch m_J=-1/2 und m_I=+1/2 und zwei abstoßende durch m_J=-1/2 und m_I=+1/2.
Ist B noch relativ klein, dann ist „a“ zwar klein, aber der anziehende Teil von m_J=-1/2 Ist immer noch größer als der abstoßende von m_I=-1/2.
Bei 2.08 T kippt das gerade: Der Einfluß von m_J=-1/2 ist dann kleiner als der von m_I=-1/2.

## Slide 22: Solving the Schrödinger Equation
Metastable Hydrogen atoms traversing the Sona unit
Bmax = 7 mT
Chr. Kannis, PhD thesis, RWTH Aachen (Dez. 2022)

## Slide 23: First experimental results (2021)

## Slide 24: Different starting conditions
Metastable Hydrogen
Start:
|cα1|2 = 1
| cαi|2 = 0.5
| ci|2 = 0.25
Nα1
This also works for ground states ➜ everything with a (known) hyperfine structure can be polarized!
😮
Notes: Grün und blau gemessen, blau veröffentlicht (EPJA)
Koordinatensystem hinter Sona-Einheit

## Slide 25: Possible Applications
Polarized (ground-state) ion sources: Many ion beams can be polarized → Oct. 2023 @COSY: 3He+ (polarized neutron beams!)
Polarized fuel for nuclear fusion → collaboration with US (Univ. California, DIII-D San Diego, JLab und Oak Ridge) UK (Tokamak Energy)
Precision physics / Spectroscopy of anti-matter?
Hyperpolarized samples / New type of MRI?
Deutsche Patentanmeldung 102022213860.0 (19.12.2022): „Eine universelle Methode zur Polarisationserzeugung durch einen kohärenten Radiowellen-Puls“

## Slide 26: Simulations for a polarized 3He1+ BEAM source
E = 10 keV, 𝜆 = 10 cm, 𝜎 = 2/3 cm
Breit-Rabi diagram of 3He+ (very similar to hydrogen)
A. Schneider et al., Direct measurement of the 3He+magnetic moments,
Nature 606, 878 (2022)

## Slide 27: Acceleration of 3He ion beams @COSY
Beam time scheduled for Oct. 2023 / acceleration to 100 MeV

## Slide 28: A first test at a tokamak
First test are planned for fall 2023
➔ Use deuterium diagnostic neutral beam to demonstrate that our method produces highly polarized, high-current-density, ~40 keV neutral beams

## Slide 29: Back to the “show-stoppers”
Does polarization survive (in the fusion plasma) long enough?
How to produce enough polarized fuel (e.g. neutral beams, pellets)?
2023 has been a great year for polarized fusion!
Let‘s finally implement it at fusion facilities!

## Slide 31: 50 years later ... Back on the agenda

## Slide 32: Use D-3He as a proxy for D-T
L. Baylor et al., Nucl. Fusion 63 (2023) 076009

## Slide 33: Further reading …
Deuterium
Tritium
2016
Notes: the prospects are bright

## Slide 34: Anisotropic Angular distributions
Measurements in Basel 1971
The status of “polarized fusion”, H. Paetz gen. Schieck, Eur. Phys. J. A 44, 321 (2010)
Spin-correlation of the reaction at Ed = 430 keV
Polarized fuel
Increases the total cross section
Enhances the differential cross section for ϑ = 0°/180° (decrease for 90°)

## Slide 35: Polarization in plasmas??? What???
Typical energy of (proton) spin states:
Typical temperature of the plasma:
108 K 10 keV
occupation probability of both spin states (almost) equal in thermal equilibrium
no polarization (in thermal equilibrium)
Boltzmann factor as a function of temperature for several energy differences DE (taken from Wikipedia)

## Slide 36: Possible (De-)Polarization effects
Polarization time ~ 5 ms for a 100 GeV proton beam in a 1000 T field
Time scale too long
Separation distances are in the nm-range for e– & sub pm-range for protons
 Spatial separation too small
Conservation of polarization for times < 1 ps in a 103 T field
 Dominant effect
Notes: Thomas-Bargmann-Michel-Telegdi

## Slide 37: Spin dynamics in PIC simulation codes
Spin precession described by the Thomas-BMT equation
t
Implementation into already existing code
Notes: If only T-BMT: no influence of spins on trajectories

## Slide 38: Modelling of Spins in laser-induced plasmas
An example: Laser-plasma acceleration of polarized electrons from a pre-polarized target
accelerating plasma cavities („bubble“)
accelerated polarized electrons

## Slide 39: 3He acceleration from unpolarized gas-jet
Pilot study (Oct. 2015)
Data
Simulation

## Slide 40: Transport of polarized 3He Gas
Every morning: Transfer of 3 bar-liter 3He from FZJ to GSI (250 km)

## Slide 41: polarized 3He gas: Pressure booster
Transport vessel: ≲3 bar
Required pressure: ≈30 bar
Polarized 3He gas jet

## Slide 42: polarized 3He gas: Holding fields
Spins need a magnetic field to hold on
Notes: Halbach-type magnetization pattern

## Slide 43: Experimental setup @Phelix
Installation in the Phelix vacuum chamber (Aug. 2021)

## Slide 44: Polarimetry for 3He ions
CR-39 stack
3He beam
CD2 foil:
Test beam time at Jülich Tandetron
with unpolarized 3He beam
Analysis by: C. Zheng
Notes: Fusionsreaktion mit Deuterium with unpolarized 3He
We employ this fusion reation with transplates the degree of polarization into a measuble angluar asymmetry
The degree of polariztion is tranferred into a spatical asymmetry, the so-called analysing power
Ersatz für pol. Neutronenstrahlen, da hier die Polarisation sitzt
Of course 3He is a bit special, in generall proton acceleration would be adventageous

## Slide 45: “front“ detectors (direct 3He Detection)
Unpolarized gas vs. polarized / Helmholtz coils off
Polarized gas: ~2 times higher count rate
Possible reason: Higher 3He-ion energy (3He1+ vs. 3He2+)
Polarized 3He gas
Unpolarized 3He gas
😮
x
z

## Slide 46: Measured (a-)symmetry
Unpolarized gas vs. polarized / Helmholtz coils off
Long. polarized 3He gas
Unpolarized 3He gas
Change of 𝛼-distribution: modified kinematics for polarized 3He gas
In both cases no left/right (up/down) asymmetry ➔ polarimeter works as expected
😮
😀
x
z

## Slide 47: Measured (a-)symmetry
Polarized gas / Helmholtz coils on ➔ Transversal 3He polarization expected
Asymmetry changes sign ➔ clear indication of 3He-ion polarization
😀
expected signal for unpol. ions

## Slide 48: Polarized Hydrogen target
Method described in:
T. P. Rakitzis, Chem.Phys.Chem. 5, 1489 (2004)
Lamb-Shift polarimeter
For measurement of nuclear polarization
R. Engels et al., Rev.Sci.Instrum. 74, 4607 (2003)
Nozzle
For HCl gas jet
IR/UV Laser
For photo-dissociation & polarization of H atoms,
100 mJ @ 1064 nm,
20 mJ @ 213 nm, 5 Hz, 170 ps

## Slide 49: Polarized Hydrogen target @ FZJ
Circularly polarized 213 nm beam
Linearly polarized 1064 nm beam
Glavish ionizer
Wien filter
Cs cell
Spin filter

## Slide 50: The Sona Transition
P.G. Sona: “A new method proposed to increase polarization in polarized ion sources of H– and D–” Energia Nucleare 14, 295 (1967).
➔ efficient method to exchange the occupation numbers of the ‘pure‘ hyperfine substates α1 and β3 (|F=+1, mF=+1> and |F=1, mF= –1>)
Idea: Flip the quantization axis (Bz) faster than the Larmor precession (non-adiabatic transition)

## Slide 51: The Sona Transition (original idea)
B
B
B
Before: α1
After: β3
μ
μ
ωB
ωLarmor
Sona coil 1
Sona coil 2
Zero-Crossing Point

## Slide 52: Solving the Schrödinger Equation
Metastable Deuterium
“This also works for ground states”
😮
1 keV, 3𝜎=1.5 cm

## Slide 53: Another (even bigger) surprise!!
Oscillations also visible without initial polarization
Simulation
Data
“If magnetic field amplitude (Blong ) and frequency (Brad ) match, everything with a (known) hyperfine structure can be polarized!”
😮
B [a.u.]

## Slide 54: Source for polarized 3He ion beams

## Slide 55: Polarimetry
elastic scattering has high sensitivity
Optimum 3He+ beam energy: ~80 MeV
➔ Acceleration at JULIC cyclotron

## Slide 56: 3He Polarimeter
Measurements: Sept. 2023
3He+ beam
Target-Ladder
holds 5 different targets
12 Detectors
Scintillator and Photomultiplier
exchangeable aperture
8 motorized carts
automated angle-selection

## Slide 57: Polarized fuel for fusion reactors
Option 1: Neutralized kA beams (use ‚standard‘ Sona units)
Option 2: Pellet injection into Tokamaks / Fuel pellets for Laser fusion ➔ Sona coils maybe not useful (velocity to small, magnetic stray fields, ...) ➔ Galileo-Transformation: Sample at rest
1 W = 1 J/s ~ 1019 eV/s ~ 1028 Photons/s
😯
t
Bz
Br
t
RF generator 1
RF generator 2

## Slide 58: A versatile method to produce hyperpolarized samples
This method should work for any (liquid, solid) material with a (simple, known) hyperfine structure
    ➔ e.g. H2O, 11B10H14 and many more!
How to measure the nuclear polarizations? How does the BR-diagram look like?
t
Bz
Br
t
RF generator 1
RF generator 2

## Slide 59: Dealing with Polarized Particles …
.... is relevant, interesting … and fun!*)
*) Not only for fusion research!
Notes: Kreisel = spinning top