## Slide 1: Status of the ERL at HZB
How can bERLinPro contribute to the Accelerator Roadmap?
07/12/23, A. Neumann for the Sealab/bERLinPro Team
Community Report on Accelerators Roadmap
INFN Frascati, Roma, Italia
INFN Frascati National Laboratories

## Slide 2: THE ERL Principle: The Promise
The promise
TM010-p mode at 1.3 GHz
On-crest acceleration
Maury Tigner, A possible apparatus for electron clashing-beam experiments, Nuovo Cim.,
37:1228–1231, 1965, http://doi.org/10.1007/BF02773204.
High average current with Linac like beam emittance/phase space: No net beam power transfer in Linac!
Recirculated beam deceleration
with p phase shift to RF
Beam dumped at
Injection energy
6.5 MeV
Recirculated beam: frep= 1.3 GHz
Merger for low energy injection and high energy recirculated beam
50 MeV
6.5 MeV
High average brilliance Linac quality beam
Injector
Recirculator

## Slide 3: All perfect, can we start right away?
The promise?
No net power transfer between cavity and beam: tens to 100 mA beam current possible  Higher order mode issues* Note: SRF based machine record 10 mA (JLab)
Only RF power required to sustain field in SRF cavity (+over-coupling for stability reasons, detuning control)
Main power invest in the injector, which is also transferred to the beam dump  High power RF couplers, 100 kW class
Beam losses in the recirculator need to be controlled to a low level  Beam halo formation, precise synchronization, beam loss diagnostics
*We roughly know from thermodynamics, nothing is for free in physics: The limits
or, why do we need demonstrator facilities like PERLE and bERLinPro?

## Slide 4: The limit: Beam Break-Up in ERLs
The limit
1st
2nd
Multi-pass transverse beam breakup (BBU):
An injected beam receives an initial kick by a given dipole higher-oder mode (HOM) or excites in first pass a dipole mode by its initial injection caused offset
Kickoffset by optics, beam couples to HOM dipole electric field
Following beam is deflected by the dipole mode and receives more offset  stronger excitation of HOM if phase advance by optics allows positive feedback
Single mode BBU can be mitigated by proper setting of optics phase advance (while preserving recovery) or by RF feedback techniques within cavity or transverse optics manipulations
Multi-mode problem usually tackled by proper HOM damping techniques
This is an intensity effect!
Sum and product of transport matrix, HOM polarization
Recirculation time
Single cavity, single HOM case!
TM110 magnetic field
TM110 electric field
Cavity figure of merits: R/Q, w determined by shape
HOM damping
Beam-breakup instability theory for energy recovery linacs Georg H. Hoffstaetter and Ivan V. Bazarov, PRST-AB, Vol. 7, 054401 (2004)

## Slide 5: How did bERLinPro tackle this?
introduction
beam dump
6.5 MeV, 100 mA
= 650 kW
linac module
3 x 7 cell SRF cavities
44 MeV
modified Cornell booster
3 x 2 cell SRF cavities
4.5 MeV
srf-gun
1.4 cell SRF cavities
1.5-2.3 MeV, single SC solenoid,
merger
dogleg
test and diagnostic line
Recirculator
bERLinPro: A demonstration facility for ERL science and technology
New developments:
Beam dynamics and manipulation (merger, recirculator, study beam break-up)
SRF systems: Photo-injector, high power booster, HOM damped Linac
Electron source: High repetition laser system high QE cathode development
Control of beam losses and radiation protection
High power beam dump
High power CW RF
  Few 100 kW class klystrons  Power couplers!
  Some 10 kW solid state amplifier
Diagnostics, synchronization machine protection, beam loss monitoring, LLRF and detuning control
A stable, efficient Cryoplant
Parameter | bERLinPro
Beam energy recirculator (MeV) | 50
Beam current ERL mode (mA) | 100
Frequency RF and Laser (GHz) | 1.3
Normalized emittance (mm mrad) | 1 (< 0.6 in simulations)
Bunch length (ps) | < 2 (ERL mode), 100 fs @ 10 mA
Beam losses | << 10-5 @ 100 mA
A fully funded 42 M€ project (including completely new building!)

## Slide 6: Where is bERLinPro?
introduction
TH2, TH1: Cleanrooms, SRF Teststands
SLH
BESSY II
bERLinPro
Fala-FEL Place
N
bERLinPro in Berlin Adlershof
SEALAB
BESSY II

## Slide 7: bERLinPro: A quick orientation
introduction
Technical Hall
Basement
Accelerator Hall
Radiation protection cover
bERLinPro is located in a subterraneous radiation protection shelter prepared for maximum beam loss (30 kW in theory)
All technical infrastructure, besides the klystron and some cryogenic installations are above ground in a technical hall
bERLinPro
HoBiCaT, sVTS
LVTs,mVTS
Klystron gallery
60t

## Slide 8: Beam optics studies
Achievements
Parameters at LINAC exit | 
Energy / MeV | 50.1
Bunch length / ps | 4.65
Emittance x,y / µm | 0.58/0.41
Energy spread / keV | 254
Injector and recirculator optics design, magnet layout, collimators
Start to end simulations (Astra+ Elegant), full 3D studies (OPAL), genetic optimization algorithms (MOGA), first look into ML
Wanted vs. unwanted beam studies, dark current, halo formation,
Beam break-up studies and countermeasures, wake analysis and component opt.
Orientation of injector cavities optimized to:
  Reduce coupler kick effects
  Limit back travelling dark current towards cathode
  Short pulse and low emittance modes
M. Abo-Bakr, M. McAteer, J. Völker
B. Kuske, M. Matveenko, E. Panofski, S. Wesch, J. Knedel et al.
Dark current losses along
injector

## Slide 9: Beam vacuum system, magnets, cold boxes
Achievements
Vacuum system complete, realigned with coordinate system adjusted to building (moved over the years) Cabling of diagnostics well advanced
Linac section with coldbox for cryogenics
supplies
Rail system at ceiling to allow ISO5 flow- boxes everywhere at the machine to avoid particulates

## Slide 10: A glance at diagnostics and vacuum system
Achievements
Beamloss
diagnostics
Vacuum sectors
Beam
diagnostics
+ Control system EPICS, visualization and data archiving
Jupyter Notebooks for
Python based data analysis and measurement programs
18x screen stations
24x Striplines, of which 8 with Ion clearing
2x button ion clearing
6x current monitors (ICT)
5x collimators
2x Faraday cups
3x Beam dumps
2 segmented Faraday cups
1 transverse defl. Cavity
Option: 6x THz/Sync. Rad.

## Slide 11: Optimizing the recipe for Na-K-Sb growth by QE and XPS measurements
Investigations into Na-K-Sb as more temperature robust alternative to Cs-K-Sb (baseline cathode)
Time after deposition | Na-K-Sb (WH09) QE @ 515 nm | Cs-K-Sb (P18) QE @ 515 nm
0 days | 2.0% | 3.4 %
8 days | 2.4% | 1.5 %
14 days | 2.2% | 0.3 %
22 days | 2.0% | -
Photocathode Preparation & Analysis System
Sepctral Response Na-K-Sb (WH09)
Spectral response Cs-K-Sb (P18)
High QE photocathodes for SEALAB photoinjector:
Explore multi-alkali Cs- and Na-K-Sb systems, from theoretical modeling (DFG fund), growth and characterization, towards operation in a SRF gun.
Complete infrastructure: growth and characterization system, UHV transport vessels, access to materials science lab EMIL at HZB, collaboration with theory.
J. Kühn, S. Mistry, C. Wang, J. Dube, C. Cocchi, R. Schier, H. Sassnick, et al.
Remember:
Best so far 16.8% at 515 nm (specs 1%)
Cathodes
High QE, sensitive
Lower QE, robust

## Slide 12
Drive laser ready for operation, laser beamline on-going (90% complete)
Two oscillators (50 MHz and 1.3 GHz), many pulse schemes, high average power (up to ~40 Watt) at 515 nm output
last section of 20 m long vacuum pipeline for laser beam transport
laser window
laser spot in accelerator hall
photoinjector module
Water cooled fiber
power amplifier:
mode-locked (NIR) 1.3 GHz oscillator
G. Klemz, I. Will, et al
Bunch spacing and current options:
50 MHz Laser:
  1-100 Hz macro-pulse:  Iavg = 77 pA – 7.7 µA
  CW 3.8 mA
1.3 GHz Laser:
  1 Hz – 1 kHz macro-pulse:  Iavg = 77 pA – 20 µA
  CW 100 mA
All this with 77 pC bunch charge, laser power set up for QE of 1 %

## Slide 13: RF and cryogenics installation status
Achievements
1.3 GHz CW 270 kW Klystron Second test in dummy load
600 kW FuG power supply
Made by CPI
3 Klystrons in house, 1 tested in SLH and at bERLinPro up to 270kW, currently in use for coupler conditioning
2 Klystrons will power Booster, 1 an high-power gun at some point
15 kW solid state amplifiers for Linac Tcav and 1st Booster (zero-crossing)
N2 to cool L700
Pics
courtesy
W. Anders
Booster+Gun coldbox

## Slide 14: Challenges for the SRF+vacuum systems
SRF systems
SRF Gun:
Low emittance high brightness beam
Insertion of a thermally isolated high QE Cs-K-Sn cathode (particulate free)
Control of field emission to avoid dark current based losses and halo formation
High current, high beam power operation (HOM, FPCs)
High emission RF field  beam dynamics optimized shape
Avoid coupler kick-based emittance dilution
Synchronization Laser  RF, precise RF control
2.3 MeV, 100 mA
High beam power
High beam current
Intermediate field levels 10 MV/m
Low coupler kicks
Zero-crossing operation
SRF booster cavity (Cornell)
+4.5 MeV (100mA)
Low beam power
High beam current
Strong higher order mode damping
Higher field levels: 19 MV/m
Multi-pass beam
Precise field control and tuning
Main linac cavity
+45 MeV (2x 100 mA, recovered)
Compact machine: All vacuum parts need to be treated within ISO 4-5 environment
Complete machine analyzed and optimized by wake/impedance studies
Movable local cleanrooms ISO 5, rail system on the ceiling for proper placement

## Slide 15: Evolution of the SRF Gun at HZB
SRF photo-injector: From cradle to grave and resurrection
Time
2013
VTA
Manufacture
2014-2016
HZB
VTA/HTA
Test/Assembly
HTA
String test
HZB
Module assembly
Gunlab
String/Cold mass
2016
2017/2018
Commissioning
Cathode transfer
1st Beam
2018-2021
2011-2012
HZB
Design
PC
Fully in-house developed SRF photoinjector with strong partners
SRF gun history
1.1
1.0
Damage and Recovery
2022
Reassembly

## Slide 16: The SRF Injector 1.0
Status
Booster cavity + couplers
Cathode
transfer
system
SRF gun
SRF booster
1st diagnostic
Laser window
Recirculator
Merger section
Straight diagnostic
line
Exchangeable
Photocathode
Beam dynamics
+SRF optimized 1.4 l/2 cell cavity
SC solenoid for beam emittance
SiC HOM absorber
Transverse steerer magnets
Twin power coupler: Modified TTF-III type 20 kW power

## Slide 17: Short to Midterm plans
What next?
There is light at the end of the tunnel……

## Slide 18: When will we have first beam?
First beam?
“Banana line”
MESA
Gun
Booster
TCav
Cathode transfer system
30 kW dump
Injector line
Focus on commissioning injector with SRF gun and transverse deflecting cavity + diagnostic line
Next stage installation of the Booster module, possible beam transfer into the high power dump
Recirculation, when Linac funding is secured or an interim arrangement can be found
650 kW dump
SRF gun module fully assembled, ready for cooldown and RF test, cathode transfer system on standby
First beam planned for Christmas this year, but unclear because of attack on HZB’s computing system
Use the time to finalize all assemblies
Will we have first beam?

## Slide 19: First studies with bERLinPro (injector)
Topics to study
Even with the medium-power gun (20kW) cavity we can study:
Up to 6-10 mA with the full injection energy  Explore the full parameter space of the SRF injector
100 mA can be potentially studied in macro-pulse regime (large power overhead by klystrons)
Bunch charges up to 0.5 nC are in reach with a high QE cathode
Proof of cathode exchange concept
Studies of beam loss scenarios by dark current or beam halo formation by bunch tails
Propagation of beam and unwanted beam from injector to dump
Beam loss and machine protection concepts
Diagnostic concepts from low-current start-up to mid-power operation (sub µA to some mA)
Beam arrival time and jitter studies
Advanced control concepts, digital twins of the machine, ML+AI assisted control methods
This comes all with the given budget and project status.
A Linac and a high power gun version still need new resources to be
realized, though designs exist
“in the drawer”

## Slide 20: Ultra-fast scattering experiments with the SRF photoinjector
Many ARD aspects: SRF, beam dynamics, instrumentation, controls, …
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
SRF Gun
SRF Booster
Sample Area B
Detector Area
16
Aperture
Sample Area A
Dogleg option
Capabilities of the photoinjector:
1 to 3.5 MeV beam energy with variable bunch charge (1 fC to 100 pC), pulse length (10 fs to 6 ps) and spot size (10 to 100s μm), high stability at MHz repetition rate.
Very flexible longitudinal accelerator/lens system: one gun cavity and three booster cavities, done optimization for bunching scheme, see B. Alberdi et al. [1].
[1] B. Alberdi, et al, Sci. Rep. 12, 13365 (2022)
TOF jitter at position A in units of initial jitter
vs number of cavities in the photoinjector
Ultrafast science drivers:
Diffraction camera for molecular movies with MHz repetition rate (UED).
Imaging of macromolecular structures in liquid phase (UEI).
Complementary to SR and FEL light sources. Enabling multi-modal capabilities for Bessy II/III.
T. Kamps, B. Alberdi Esuain, J. Völker, T. Spohr, E. Ergenlik, A. Neumann, J.-G. Hwang, S. Barg, et al.
Demonstrator phase within funds!

## Slide 21: Realize a Linac for SEALab/bERLinPro
Linac for sealab
New baseline:
Cut down to a simplified more cost saving, less complicated design
A bERLinPro Linac was developed
Full three-cavity string HOM analysed, coupler kick studies, manufacturing study etc….
For a BBU threshold of 2x 100 mA
+ margin this design is an overkill threshold current in the Ampère regime!
Cornell shape cells
No waveguides, TTF coupler + Fast reactive tuner port
Beamtube HOM absorber like Booster/Gun
Simplified module concept, Cornell like, no room temperature parts
Cryo allows to potentially operate one cavity at 4 K as new material demonstrator
Contributes to European ERL roadmap
HORIZON-INFRA-2023-TECH-01-01 iSAS funded!
Funding
Limit

## Slide 22: Acknowledgements
Fin
Many thanks to:
J. Teichert, A. Arnold, P. Murcek, R. Rimmer, A. Burrill, F. Marhauser, S. Belomestnykh, E. Zaplatin, E. Kako, N. Shipman R. Eichhorn, J. Sekutowicz, P. Kneisel, G. Ciovati, A. Matheisen, B. van-der-Horst, M. Schmökel, W.A. Clemens, C. Dreyfuss, D. Forehand, T. Harris, R.B. Overton, L. Turlington, M. Schalwat, S. Lederer, V. Volkov, I. Will, MAC members
+many more
HZB bERLinPro Team & friends
former colleagues
Team Sealab
Thanks for your attention!
Funding: Bundesministerium für Bildung & Forschung Bundesland Berlin, Helmholtz Gemeinschaft