## Slide 1: RF Achievements and Plans
Giovanni Bisoffi-INFN, Peter McIntosh-STFC and the RF Implementation Panel
Community Report on Accelerators Roadmap
12–13 Jul 2023
INFN Frascati National Laboratories

## Slide 2: RF = increase beam energy efficiently and reliably
Per year: 10 M€, 90 FTE (nominal, ~30% higher than actual - ref. Accelerator R&D strategy)
Notes: Including: 3 M€ and 18 FTE in 5 years for MC test stand (obsolete)

## Slide 3: Progress/plan of the LDG RF Implementation Panel
From the RF Roadmap (Nov22 – Mar23):
update future accelerator needs and RF goals, special attention to sustainability (Nov22 – Mar23)
Consult national teams (Apr23 – Oct23):
through ad-hoc surveys, at workshops, town meetings etc
Follow-up technical progress
Pinpoint weak areas, duplications, needed infrastructures, funds, personnel
Demonstrate RF improvements and impact on regular basis (from Apr23):
to LDG and accelerator community
at conferences, workshops, reviews;
at forums, town meetings; to CERN SPC and Council
on websites, social media, brochure, through impact studies, through slide decks.
Strengthen or develop existing, new communities (from Nov23):
to address specific performance requirements
Explore funding routes:
National, EU (e.g follow-up of I.FAST); project-related, R&D-activities
Coordinate with ERL and MC panel and international efforts (from Apr23):
ERL - Integrated into the Horizon Europe - Innovative Sustainable Accelerator Systems (iSAS) proposal.
MC - Focus on infrastructure for RF breakdown studies under strong magnetic field (WG4, WG5)
Snowmass-P5, EIC
Notes: MC: this infrastructure (Graeme is comparing the test stands, as an exercise with proponents), plus related cavity design and RF Power Source items

## Slide 4: Outline
Review of the R&D effort from each working group
Blue board
Needs of future colliders in terms of RF performance
White
Status and technical progress
Yellow board
Hints for the funding agencies – what to invest on...
the take-home message
WG1
WG2
WG4
WG3
WG5
WG6

## Slide 5: WG1-2: RF Cavities: reduce operational cost (Q0 ↑) and capital cost (Eacc ↑)
Higher Eacc
ILC – higher Eacc  smaller linac (= lower capital cost)
MC – quick acceleration (vs m-lifetime)
FCC – fewer cavities  smaller RF installation
Higher Q0
FCC, ERL, ILC – lower RF losses, cryogenic power minimised.
Others: Reproducibility, cost, industrial manufacturing
Niobium (Tc=9.2K, Tcryo= 2K is mandatory)
Eacc > 40 MV/m, Q0 > 1010 - 35% saving in Pele,cryo;
Theoretical limits close? ≤ 57 MV/m s.h. ….
Thin films (higher-TC materials)
Eacc x 2 higher than Nb (≤100 MV/m); Q0>1010 at Tcryo=4.2K (66% saving in Pele,cryo) – 40% cryo-plant cost saving (cryocoolers?))
Cavity types – mostly elliptical: 1.3 GHz (3.9 GHz), 802 MHz (401 MHz), 704 MHz (352 MHz), 650 MHz (325 MHz).
NEEDS:
vs. Eacc
Pdiss, ref
(R&D goal)
(mature)
Notes: cryogenic power reduced by factor > 2 with high measured Q0
Grassellino: we discover that the addition during the mild bake of a step at 75deg for few hours, before the 120deg, increases systematically the quench fields up to unprecedented values of 49 MV/m.

## Slide 6: WG1: Niobium cavity R&D progress
R&D DIRECTIONS:
1.`Further increase Q and Eacc: in the last years surface polishing (HPR, BCP, EP), surface treatment (N doping), heat treatments (low/mid/2-step baking, H degas).
2. Improve reproducibility of high-Eacc fields: Reduce contamination during assembly (Eacc , field emission-FE) via robots in clean room, in-situ plasma processing.
3. Reduce the cost
From-Fine-to-Medium Grain: material 35% cheaper, full cavity 5% cheaper.
4. Risk of losing manufacturing capability?
Few Nb suppliers (1 in China, perhaps 2 in Japan/USA).
Few cavity suppliers (2 in Europe, 2-3 in China, 1 in Japan) – for future machines, must maintain SRF technology skills in both labs & industry.
Need to invest in industrial processes (Eu-XFEL - 800 cavities  FCC – ~1000 cavities, ILC - 8000 cavities).
Labs involved - CERN (CH), CEA and IJCLab (F), DESY, HZB, Hamburg-Uni (D), INFN (LASA, LNF, LNL), STFC (UK)
Notes: medium grain : grain size < 1 mm; large grain : grain size >> 1 cm

## Slide 7: WG1: Niobium cavity R&D goals & direction
  1. More funding & HR for treatments:
  FE studies, cost optimisation, industrial manufacture.
  2. Contributions from other disciplines:
  Robotics - cavity prep. in cleanrooms.
  Chemistry - Plasma proc. for FE recovery.
  3. Maintain/improve infrastructures:
    ISO4 cleanrooms for preparation & assembly.
    Vertical low power test stand
HINTS FOR THE FUNDING AGENCIES
Most R&D benefits several future PP
colliders (FCC, MC, ILC, ERLC)
Notes:   Cost of a single SRF cavity test : 20 k€ (w/fluids, manpower …)
  Cost to implement a new, reproducible, industrialised R&D recipe: 2.5 M€, 4 years, 3 FTE (+ technical support)

## Slide 8: WG2: Thin-film cavities
  Goals: high Q0 @ 4.2K operation; and much higher Eacc.
  → higher TC material allows Tcryo = 4.2K instead of 2K, which reduces Pplug by a factor 3.
  NOTABLE R&D DIRECTIONS:
  A15 materials: So far Nb3Sn-on-Nb (only in USA so far).
    A15-on-Cu: planar samples - Nb3Sn-on-Cu (IFAST EU project, on going); tunability, field trapping to be evaluated.
    Other materials: NbN or NbTiN (lower field, easier synthesis), MgB2 (higher Tcryo possible).
  SIS (multi-layer): higher performance, less defect-sensitive (1.3 GHz cavity test at CEA) – currently in the sample-to-cavity transition phase.
  Cu cavity base production R&D: e.g. by spinning (CERN, INFN), setup industrialized/cheap production process (3D-printing tests in progress); Cu-surface preparation.
Q0 (Nb3Sn) @ 4.2 K ~ Q0 (full-Nb) @ 2 K; Eacc ~25 MV/m; more sensitive to trapped flux; brittle (f0 tuning by mechanical deformation possible?)
Nb3Sn/Nb
Notes: Nb3Sn/Cu, Uni-Hamburg, CERN, INFN, ... On top of I-FAST

## Slide 9: WG2: Thin-film cavities
To facilitate expedited multi-cell coated cavity verification, 1.3 GHz and lower
Intensify R&D:
more SC materials to explore, various techniques, targets
surface/material characterization and SC property measurements.
Cu-cavity production and their polishing.
laser and flash-lamp annealing on Cu samples/cavities.
More funds-people/higher priority for:
facilities (people, liq-He, electricity, …); for many cells, various frequencies
furnace + new ALD coating set-up.
access to clean rooms.
Have more test installations available (so far some at CERN, HZB and DESY, INFN; in preparation at STFC).
Have more sample characterization stations available.
HINTS FOR THE FUNDING AGENCIES
Same EP set-up
Different regime
Plasma Electrlytic Polishing
Flash Lamp Annealing
SIS multilayer coating (Nb/AlN/Nb3Sn) on Ta
Labs: CEA-Saclay, CERN, HZB, HZDR, INFN, STFC, USI, Hamburg U. (DESY), (I.FAST-WP) JLAB, KeK and FNAL
Tightly-knit network, very well connected worldwide.
Small teams, limited budgets, technical support and access to RF tests.
Notes: https://www.hzdr.de/db/Cms?pOid=56060&pNid=3240 on laser and flash lamp annealing

## Slide 10: Progress is constant, from multi-faceted R&D programmes
Metallographic polishing, reducing Nb surface resistance by a factor 5
(collaboration between the Nb and thin film communities)
Latest news!

## Slide 11: WG3: Fundamental power couplers (FPC)
Transmitting hundreds of kW (W’s in the cold mass) reliably through thin ceramic windows (diameter ~ 5÷ 50 cm) into SRF cavities.
Risk: window breach can spoil a complete cryostat with multiple cavities within seconds.
FCCee (Z→W,H → ttb modes): 112→864 couplers, CW, 400-800 MHz, P = 165 - 900 kW
MC (SC driver, NC RF, SC RCS): 250, 7000, 4500 couplers, dc 0.05% → 4%, 325-1300 MHz, P = 100 - 4000 kW
The ceramic window!
Ensures vacuum tightness of FPC vs. the cavity and the entire machine - no leaks allowed!
Mostly Al2O3, metal-brazed, should:
have low losses at operating f and T.
be brazed, with low RF losses (→ high purity).
have a low T-gradient (ensures a known thermal conductivity).
Top-priority R&D topic for high power couplers.
Test box for LHC couplers (400 MHz)
400MHz, LHC,
500 kW CW
NEEDS:
(for ILC and CLIC: FP
specs achieved)
HOMs couplers (see iSAS proposal): R&D on 800, 1300 MHz multicell; ~ kW RF power out of the cold mass
Notes: (usually, high purity difficult to braze, but low losses, low purity vice-versa)
MC 4 MW is an engineering issue which is not for now…

## Slide 12: WG3: Present evolution, labs involved
Development done for specific machines:
Generic R&D on couplers does not exist (except some at EIC, USA)
Coupler modelling capacity is reasonably wide (e.g. Uni-Rostock)
EXPERIMENTAL-FABRICATION CAPABILITIES
CERN: developments for future colliders, can guarantee long-term expertise; couplers for Soleil, ESRF, PERLE, …; has test stands.
CEA: couplers on request for XFEL, ESS - has test stands.
DESY: 1.3 GHz CW couplers – has test capabilities.
RI company: fabricates (and tests) couplers on specs.
EIC (USA): couplers with challenging specs, developments will benefit next colliders.
The coordination event for international experts: (almost) yearly world-wide FPC workshop (WWFPC) brings together international experts.

## Slide 13: WG3: Couplers: what to work on
Suggested directions to improve or speed up R&D:
(mostly at CERN, FCC-driven):
  Water cooled ceramics.
  Highly adjustable couplers using 2 windows.
  New methods of mounting couplers with high cleanliness.
  Resonant ring for efficient testing & conditioning (5 ÷ 10 smaller power sources) .
  Enable smaller labs to build-up test capacity at a moderate cost (~ 300-400 k€).
  Develop Fast Reactive Tuners (a broad-scope promise for colliders and many other applications)
Tuning at room-T (outside the cryomodule), without mechanical deformation. Proof-of-principle at CERN.
Tuning speed > 600 ns (limited by the HV circuit), delivers power savings and improved stability.
Huge potential for all SRF accelerators, not only colliders.
Short coaxial structure, with FE element: RF power goes in and reflected back. FE permittivity changed by an applied voltage → change of Prefl → change of f0.
Applicable to transient detuning: R&D CERN + Lancaster U
Interest shown by: HZB, PERLE, JLAB (also engaged)
Collaboration - bridge gap between R&D & operation.
FE material studies desired.
Potential game changer:
tuning; transient beam loading; microphonics
CERN SPS resonant ring proposal: (~ 20 dB amplification at device under test)
400MHz, LHC 2 1 MW CW expected
HINTS FOR THE FUNDING AGENCIES
Fast Reactive Tuners
Good for small labs!
Notes: Jlab is Jefferson?
PolFEL, NVBJ, Poland may be interested
Industrial capabilities not needed now, for a machine starting operation in 2040 and construction in 2028, at the earliest
A resonant ring is a closed loop of a waveguide system that can amplify power, and it is widely used for the breakdown test of the RF components under high power

## Slide 14: WG4: High-Gradient (HG) Normal-Conducting (NC) RF
CLIC
HG (70 to 100 MV/m), X-Band with very low breakdown rate, key performance parameters for cost (linac length) and efficiency (optimized beam dynamics).
Very strong interplay between HG and beam dynamics for wakefields – precision alignment mitigates.
Muon Collider
HG important for muon capture, fundamentally with high external magnetic field.
FCC
For 20 GeV NC injector in FCC-ee and electrostatic separators in FCC-hh in S and C-Band.
Applications outside HEP require gradients up to 60 - 70 MV/m (synergies)
NEEDS/GOALS:
CLIC
MC
FCC Injector
Notes: Funding for CLIC from 4 to 2 nowadays

## Slide 15: WG4: Current R&D activities to achieve these goals
CLIC
Achieved: Gradient specs attained & deep understanding of fundamental physics (with multi-decade HG development and funding); great stimulus for industrial supply of NC RF components/systems; synergies with applications (XFEL, Eupraxia, ICS, medical, plasma accelerator, RFQ, …)
Generated: new directions - dielectric structures, short pulse acceleration and HT superconductors.
Required: systems engineering and integration, dedicated manufacturing R&D & mech. design with m-level alignment required (applications can bring these aspects further).
Muon Collider
To be urgently planned: HG required in high magnetic fields, with significant need for dedicated test infrastructure.
Fundamental mechanisms of breakdown
Electrodynamics and material science, plasma physics, surface physics (often at University scale), with wide applicability.
POLARIX
deflector, DESY
Notes: FCChh design: «The injected beam will be captured, accelerated and stored using a 400 MHz superconducting cavity system, which is also used to damp the longitudinal injection errors. A system of electrostatic deflectors will be used to damp the transverse injection instabilities/errors and thus ensure transverse stability. “
HG for FCC is S-band, some L-band, some positron capture
CLIC nest step? CLIC-0 , a larger scale development facility, nonsense if CLIC is NOT approved

## Slide 16: WG4: HG NC: priority R&D and investments
Operational HG test infrastructures in Europe (crucial!): CERN (n.3, 50 MW, 12 GHz), Trieste (45 MW, 3 GHz), Valencia (7.5 MW, 3 GHz), Frascati (50 MW, 12 GHz), Uppsala (cryo pulsed DC sys)
Active on X-band linearizers and deflectors: PSI, DESY, STFC-Daresbury Lab
High performance linacs (design÷operation): INFN-Roma, STFC-Daresbury Lab, CERN, PSI, Eindhoven, INFN-LNF, Elettra, Medical (VHEE FLASH)
Top priority: to maintain multiple EU RF test stations (and staff).
Explore HG designs - precision mechanics.
New materials, procedures, care to minimise costs.
Test NC structures in high magnetic fields: paramount for Muon Collider R&D (major requirement):
Fund new and upgrades of existing infrastructures (test stands will open important new areas in HG studies and will stimulate important scientific understanding).
HINTS FOR THE FUNDING AGENCIES
POLARIX deflector, DESY
S-band testing, IFIC Valencia
X-band testing, Tsinghua University, Beijing
Notes: For the MC:
Small scale tests: 5 M€
Full test stand: 100 M€
ANL developments, MICE developmens

## Slide 17: WG5: High Efficiency Amplifiers
Choice driven by: tunnel integration, spatial power density, cost/W, efficiency.
Facilities driven by a vast diversity of RF power sources.
Support/promote development of high efficiency RF power sources for future large-scale particle accelerators.
Intensify collaboration with industry to ensure long-term industrial support for decades to come.
LHC and FCCee are first/primary objectives for such development.
Support various community needs for high efficiency RF sources (either/or):
development synergy
specialised activity
(for novel/customized requirements).
NEEDS/GOALS:
DEVELOPMENT SYNERGY:
Notes: Efficiency imply reducing klystron current, say by 15%
Higher efficiency means having 15% fewer klystrons, with impact on capital and maintenance costs

## Slide 18: WG5: Power amplifier developments
High Efficiency klystrons project at CERN: targeted to improve efficiency and performance for various applications.
FCC klystron efficiency gain from 65% to 80% can save > 1 TWh in 10-years (~ 84 MCHF)
Notes: Klystrons still dominating the scene, in the P vs f plot
M. Jen

## Slide 19: WG5: RF Amplifier R&D status and directions
Klystrons: R&D is (i) costly and (ii) only done with industry, unless significant investment in klystron production infrastructure at Lab level (i.e as done at SLAC). Only 3 qualified vendors worldwide. Large cost increase, 50-100% over ~5 yrs. (CERN, Uni-Lancaster and ESS, CEA)
SSPA: progress (incl. h-increase) rely on industry transistor development; labs contribute with combination/matching techniques (CERN, Uppsala, CEA Saclay, INFN-Legnaro, NCBJ (Swierk), CIEMAT)
Only large projects can afford R&D costs and risks, which benefit many applications; for small labs energy savings are not worth the investment.
105 MW
3.0 TeV CLICe+e- ; pulsed, 1.0 GHz, PRF total = 180 MW
from 380 klystrons and 600 SSPAs
HINTS FOR THE FUNDING AGENCIES
Klystrons: labs taking partial responsibility in the fabrication process would help reduce cost, risks & delivery time.
SSPA: a coordinated lab effort is mandatory. Most promising technology must be selected (e.g. GaN), which should last for decades, and most efficient power combiner (cavity/distributed, considering cost & size). h=70% goal. FCC aims at a prototype SSPA tower in 2026.
Notes: Efficiency of interest for small labs only if it reduces the size of the modulator.
Efficiency is a 3-4 years investment of industry, not interesting for few klystrons!
Klystrons like diamnds are for ever (for 20 years...!)

## Slide 20: WG6: RF Control - LLRF and Artificial Intelligence
Multiple accelerator sections with different beam patterns and RF frequencies → high-level intelligent automation and optimisation.
Reduction of electrical energy consumption → optimal RF control strategies and operational procedures.
Long construction and operation cycles → sustainable RF control systems, with long-term standardised HW/SW, optimal architecture and framework suited for system integration/upgrades.
ILC/FCC/MC superconducting RF cavities → RF field control vs. strong mechanical vibrations and heavy beam loading (with critical electrical/mechanical characteristics of the cavity).
A comprehensive, intelligent, highly automated, and standardised LLRF system is essential for the success of the RF systems of future colliders.
NEEDS:
FCCee
ILC

## Slide 21: WG6: Current R&D effort
RF stability figures achieved! (0.01 % amplitude and 0.01° phase) of FEL machines is more demanding, sufficient for future colliders (e.g. ILC requires 0.07 % and 0.24°).
Real-time cavity field stabilisation, with advanced automation and optimisation algorithm: high-res fast ADCs and high-performance DSPs from telecom industry,.
Standardise LLRF system design: gain long-term industry support (HW/SW platforms like VME, ATCA to MicroTCA, System-on-Chip) and broaden scientific collaboration labs/industry, facilitating large scale projects with in-kind contributions (e.g. HL-LHC, ESS and PIP-II).
Improving availability, reliability and operability (FCC, ILC, MC, …) with many RF stations & cavities (e.g., ILC main Linac has > 560 RF stations and 14500 cavities), → automation and optimisation for RF system operation, e.g. ML algorithms will decrease operation/maintenance costs.
Notes: - some applications of machine learning (e.g., SC cavity quench detection, RF faults classification) already demonstrated.
Chips get obsolete, but a good framework architecture, a modular design with interfaces is flexible to chip update. It should be as modular as possible, to exchange whatever is on the market at the appropriate moment. NO to customized solutions

## Slide 22: WG6: Future priority investment
Stabilising cavity field and minimizing electricity power consumption: optimization of RF system configurations, control strategies and operational procedures (especially for SRF cavities).
Standardise to streamline: to unify R&D activities on various subsystems, to avoid duplications, to attract active involvement from industry:
Simplify system integration, faster prototyping, modular design, promoting better integration with industrial R&D: standardised hardware/software architecture & platforms (e.g. the Eu-XFEL TCA.4 as standard platform).
Standardised software/firmware libraries for sharing knowledge for worldwide LLRF community, avoid duplicated development, enabling fast prototyping and encourage collaboration.
Continuous development of automation & optimization algorithms (e.g. machine learning) to successfully operate RF systems of future colliders.
Most developments are also beneficial to accelerators beyond colliders; therefore a world-wide collaboration is encouraged.
HINTS FOR THE FUNDING AGENCIES
Notes: Standardisations among labs and with industry are opportunities coming from big machines, as XFEL was and a colldier will be
In-kind big projects impose a standardization
Companies in this field tend to cooperate in joint framewrks, good tradition

## Slide 23: In summary
Priority routes in all areas of RF development are clearly identified, as presented here.
European R&D communities are being coordinated to make the R&D progress more effective.
The outcome shall be analysed and then translated into suggested strategic actions and deliverables (Fall 2023).
The process shall be updated at regular intervals and reported to LDG, up until the next ESPP update exercise.
Notes: Per year 10 M€, 90 FTE. Nominal, which is 30% higher than present