## Slide 1: The Future of Solid-State Detectors (from the DRD3 point of view)
Disclaimer:
Solid-state detectors are much more diverse than the small ensemble we use for particle tracking.
The future of solid-state detectors for tracking is not contained solely in the DRD3 activities.
  Other collaborations are developing solid-state detectors.
  Single groups not active in DRD3 are doing excellent R&D.
Nicolò Cartiglia
INFN, Torino.
In this presentation, I will summarize the draft plan proposed as the starting point of the soon-to-be DRD3 collaboration.
The real plan will be decided by the DRD3 collaboration

## Slide 2: The definition of future
Future
What is needed by future experiments
What technologies will be used
What people want to do
What blue-sky R&D will make possible

## Slide 3: What is needed by future experiments
Lepton colliders:
4D tracking
Very low mass
  Low power
  Air cooling
Hadron colliders:
4D tracking
High occupancy
High radiation environment
Large area coverage
Broadly speaking, there are two large families of experiments that cover the needs of all other applications:

## Slide 4: Future experiments needs - I
This table details the need of the experiments in terms of
Spatial precision
Low mass
Low power
Large area
Temporal precision
Radiation levels
considering the division among detectors:
Vertex
Tracker
Calorimeter
Time-of-Flight

## Slide 5: Future experiments needs - II
The needs have been summarized into 4 large groups in the ECFA road-map
with a finer-grain definition in the DRD3 proposal

## Slide 6: Future experiments needs - examples
Example 1)
5-10 micron position resolution
10-20 ps temporal resolution
50 microns of silicon equivalent material budget
<1 W/cm2 power consumption (upper limit for air cooling)
Example 2)
~ 10 17 neq/cm2 radiation levels
Example 3)
12” wafer capability
1000 m2 detector

## Slide 7: What technologies will be used
No gain
Low-gain (LGADs)
No gain
Low-gain (LGADs)
BiCMOS
(SiGe)
3D
Si/Diamond
Resistive read-out
BiCMOS
(SiGe)
Standard read-out
CMOS
Planar
CMOS
Hybrid
Monolithic
Sensor
ASIC
Sensor
ASIC

## Slide 8: Technologies - I
This very nice and very difficult-to-read table links together the previous pieces:
The needs of the experiments
Applications,
Technologies
DRDT
and provide quantitative targets for the R&D.

## Slide 9: Technologies – Example
4D tracking: Interplay of power, pixel size, and electronics
The sensor design, based on the LGAD concept, is well-developed
The electronic design of accurate amplifiers for timing is well-known
Power will determine:
  The architecture of 4D tracking detectors
    how many layers will be 4D and how many will be 3D
  The pixel size and the temporal precisions.
Power
However: the power requirement for a large system with very good position resolution is presently too high.

## Slide 10: What people want to do – DRD3 composition
Presently, the DRD3 proto-collaboration comprises 119 groups from 28 countries, for about 900 interested people.
The more, the merrier…

## Slide 11: What people want to do – DRD3 working groups
The DRD3 activity is divided in 8 working groups.
WG 1
Monolithic
CMOS sensors
WG 2
Sensors for tracking
and Calorimetry with
space/time and/or
energy resolution
WG 5
Techniques,
Infrastructures, and
facilities for sensors
characterization
WG 3 Radiation damage
and extreme
fluence
operation
WG 4
Simulations
WG 6
Wide bandgap and
Innovative sensor
material
WG 8
Dissemination
and
outreach
WG 7
Sensor
Interconnection
techniques

## Slide 12: What people want to do - I
Chart: 
| WG1 Monolithic CMOS Sensors | WG2 Sensors for Tracking and Calorimetry | WG3 Radiation damage and extreme fluences | WG4 Simulation | WG5 Characterization techniques, facilities | WG6 Wide bandgap and innovative sensor materials | WG7 Interconnect and device fabrication | WG8 Dissemination and outreach
 | 82 | 84 | 84 | 64 | 76 | 53 | 46 | 63
Number of institutes interested in each working group
Interestingly, the number of institutes is evenly distributed among the working groups

## Slide 13: What people want to do – finer grain
Chart: Institutes interested in each DRD3 work package
| WP1: DMAPS Spatial resolution | WP2: DMAPS Timing resolution | WP3: DMAPS Readout architectures | WP4: DMAPS Radiation tolerance | WP5: 4D tracking with 3D sensors | WP6: 4D tracking with LGAD sensors | WP7: Extreme fluence - wide band-gap materials (SiC, GaN) | WP8: Extreme fluence - Diamond detectors | WP9: Extreme fluence - Silicon detectors | WP10: 3D integration - Fast and maskless interconnect | WP11: 3D Integration - in house post-processing for hybridization | WP12: Advanced interconnection techniques for detectors | WP13: 3D Integration - Mechanics and cooling | Common Projects
 | 60 | 53 | 53 | 59 | 56 | 70 | 46 | 33 | 71 | 26 | 26 | 41 | 39 | 60

## Slide 14: What blue-sky R&D will make possible
R&D aimed at increasing our understanding of solid-state detectors is a key ingredient of DRD3
Blue-sky R&D will be financed by the “blue-sky fund”, created by asking for an annual fee to each institute (about 2k CHF)
The blue-sky fund will finance projects proposed by DRD3 members (typically contributing about 50% of the total cost while the other 50% is shared among the proponents).

## Slide 15: Putting everything together: the DRD3 structure
DRD3 approval
CP1
…
CPn
Blue Sky R&D
DRDT 3.1
WP1
Deliverable #1
Deliverable #2
……
DRDT 3.2
DRDT 3.3
DRDT 3.3
…..
Strategic R&D
WP2
Deliverable #1
Deliverable #2
…..
WPn
Deliverable #1
Deliverable #2
…..
WG1
RG #1
RG #2
….
WG2
RG #1
RG #2
….
….
WG8
RG #1
RG #2
….
WG: Working group RG: Research goal WP: Work package CP: Common project

## Slide 16: The path to the DRD3 collaboration
The representatives from each of the intestested institutes (119 so far) form the collaboration board.
The DRDC gives the green light to form the DRD3 collaboration.
The collaboration board elects the chair.
The first DRD3 collaboration meeting is organized (Q1/2024).
The spokespersons are elected
The mandate of the DRD3 “facilitators” ends
The DRD3 MoU is signed

## Slide 17: Outlook
If your dreams do not scare you, they are not big enough
In the past 30 years, solid-state sensors have consistently exceeded expectations in terms of performance.
DRD3 is a new collaboration that aims to continue this tradition.
If you have not done it yet, please consider joining DRD3. We are now entering an important organizational phase that needs the broadest possible inputs.