## Slide 1: Pixel detector with built-in signal processing and bandwidth-efficient data transmission
June 12 -16 , 2022, Turin , Italy
XII Front-End Electronic Workshop
G.Pinaroli1 , G.W.Deptuch1, G.A.Carini1, D.S.Górni1, S.Mandal1, P.Maj1 ,N.St.John1
Instrumentation Division, Brookhaven National Laboratory, Upton NY 11973, USA

## Slide 2
Pixel detector with built-in signal processing and bandwidth-efficient data transmission
Talk: “Event-driven arbitrated protocols
implemented in integrated readout circuits
for segmented detectors” by D. Gorni,
Today (06/12) at 12:30 PM
Hybrid pixel detector with precision spectroscopy performances:
Low Equivalent Input Noise (ENC)
Output Voltage proportional to the impinging particle Energy
Continuous operation
Pixel size of ~100-150 um
We can define these developments as color camera detector
Platform for different applications using a matched sensor:
Full Field Fluorescence Imaging
Hard X-ray spectroscopy
Others…
 | Si | Ge | GaAs | Diamond | CdTe | CZT | TIBr | a-Se
Eg [eV] | 1.12 | 0.67 | 1.43 | 5.5 | 1.44 | 1.57 | 2.68 | 1.90
W [eV] | 3.6 | 2.96 | 4.20 | 13.00 | 4.43 | 4.64 | 6.50 | 6.00
ε | 11.7 | 16.0 | 12.8 | 5.7 | 10.9 | 10 | 30 | 12
μe [cm2/ (V⋅s)] | 1650 | 3900 | 8000 | 1800 | 1100 | 1000 | 30 | 1-4
μe [cm2/ (V⋅s)] | 450 | 1900 | 400 | 1200 | 100 | 120 | 4 | 0.05
ρ [g/cm3] | 2.33 | 5.33 | 5.32 | 3.52 | 5.85 | 5.78 | 7.56 | 2.30

## Slide 3: Generic readout chain for spectroscopic pixel detector
Low noise FE
Signal Gain
Continuous operation
I -> V converter
Voutmax proportional to Q
Storage of the max amplitude value
Readout architecture of pixel/matrix
Extraction of max value
Is there enough room to fit all of it in a 100-150 um pixel?
Power consumption? Readout? ….

## Slide 4: As example: HEXID ASIC
Sensor material | CZT, W = 4.6 eV/pair
Sensor thickness | ~1 mm
Ileak | ~10 pA
Pixel capacitance | ~ <150 fF
Collected Carriers | Electrons
Energy Range | ~2keV to ~160 keV
ENC | < 20 e
Pixel Pitch | 150 um , hexagonal
Detection Area | Target: ~ 12 mm x 10mm (64x80 pixels), Demonstrator: ~1.2mm x 1.2mm (8x8 pixels)
Technology node | 65 nm
Sensor material | CZT, W = 4.6 eV/pair
Sensor thickness | ~1 mm
Ileak | ~10 pA
Pixel capacitance | ~ <150 fF
Collected Carriers | Electrons
Energy Range | ~2keV to ~160 keV
ENC | 
Pixel Pitch | 150 um , hexagonal
Detection Area | Target: ~ 12 mm x 10mm (64x80 pixels), Demonstrator: ~1.2mm x 1.2mm (8x8 pixels)
Technology node | 65 nm
Figures from “Two-Dimensional Integrated Circuits for Hybrid Solid-State Pixel Detector”,
DOI: 10.1109/NSSMIC.2006.356182
The Hyperspectral Energy-resolving X-ray Imaging Detector will be
an attractive detector solution for the next generation of space-borne
Hard X-ray Telescopes [*].
[*] J. Tang, F. Kislat, H. Krawczynski,: Cadmium Zinc Telluride detectors for a next-generation hard X-ray telescope, https://doi.org/10.1016/j.astropartphys.2021.102563.

## Slide 5: HEXID ASIC:
A pixelated chip for finely segmented CZT Sensors suitable for Amplitude Spectroscopy in the hard X-ray regime

## Slide 6: HEXID Architecture
In-Pixel signal processing:
Implementation of two processing paths, i.e., High Sensitivity Path (HSP) and Low Sensitivity Path (LSP), operating simultaneously, is achieved thanks to forking of p-z cancellation paths;
Triggering on the HSP for amplitude recording (S/H) for both readout chain
Sequenced readout of amplitude values of the pixel and its six neighbors
IEEE NSS-MIC 2022: Front-End Processing Chain for Finely Pixelated CZT Sensors Suitable for
Amplitude Spectroscopy, G.W., Deptuch et all.
The advantage of using hexagonal over square pixels is that all the nearest neighbors of any given pixel are equivalent.

## Slide 7: CSA: Charge Sensitive Amplifier
BSA proprietary

## Slide 8: CSA criteria of choice
For these developments, a suitable CSA architecture must fulfil very aggressive requirements:
Connectable in p-z cancellation configuration (high gain with cascaded stages, continuous operation)
FB network capable to handle leakage current and minimizing additional noise contribution and deliver very low ENC (< 20 e-)
Power consumption compatible with pixel integration
Silicon real-estate compatible with pixel size
[1] F. Krummenacher, "Pixel detectors with local intelligence: An IC designer point of view", Nucl. Instrum. Methods Phys. Res., vol. A305, pp. 527-532, 1991, P.F. Manfredi, et al, “The analog front-end section of the BaBar silicon vertex tracker readout IC”, Nuclear Physics B - Proceedings Supplements, Vol. 61, Is. 3, February 1998, 532-538
[2] Y. Hu, et al, "A low-noise, low-power CMOS SOI readout front-end for silicon detector leakage current compensation with capability," in IEEE TCAS I, vol. 48, no. 8, pp. 1022-1030, Aug. 2001
[3] G. De Geronimo et al., “A CMOS detector leakage current self-adaptable continuous reset system: theoretical analysis”, Nucl. Instr. Meth. A 421 (1999) 322-333
[4] G. De Geronimo et al., “Front-End ASIC for a GEM Based Time Projection Chamber”, IEEE Trans. Nucl. Sci Vol. 51, No. 4, August 2004 1313-1317
Krummenacher’s / Manfredi’s [1]
Common Source Feedback (CSF) [4]
Common Gate
Feedback (CGF) [3]
feedback resistance µ current source,
IKRUM must exceed ILEAK, Þ parallel noise,
too large ILEAK Þ loss of stability [2],
requires large (~pF) Cint,
not connectable in p-z cancellation.
operates in p-z cancellation,
one-fit-all VRFB is needed,
Reset Quiescent Current (RQI) is optional; if used, multiplied RQI to next stages Þ shift of baseline.
operates in p-z cancellation,
RQI (typ. at some pAs) is required, but difficult to control and match,
larger ILEAK+RQIs Þ loss of stability,
multiplied both RQI and sensor ILEAK to next stages Þ shift of baseline.

## Slide 9
[5] G. W. Deptuch, P. Otfinowski, “Charge Sensitive Amplifier with Pole-Zero Cancellation”, provisional patent application USPTO Serial No. 63/379,887
CSA with Self-Cascoded Field-Effect Transistor (SCFET) feedback network in configuration for integration of input charge signals [5];
Í
CSA with (SCFET) configured in pole-zero cancellation scheme [5], realizing multiplication (gain) of input charge signal ´ n;
Ë
Assuming:
no body effect in transistors,
negligible sensor leakage current,
very high open-loop gain of amplifier (OpAmp or OTA)
… in real conditions, VDS1 is only close to “0”, nevertheless transistor M1 act as diode-connected, providing minimal voltage drop across and external voltage bias on its gate is not required
all shown for holes
New CSA concept
Solution with SCFET which enables: 1) ILEAK compensation, 3) Easy handling bias FB network, 3) p-z configuration

## Slide 10
Inverter-type OTA amplifier with bias current reuse and active cascode gain boosting
90 dB open loop DC gain from a single stage amplifier,
intrinsically stable as it is single stage amplifier,
M1 and M2 = thick gate oxide devices, low gate leakage currents,
other transistors are selected to optimize swing and open loop gain,
local bias generated for cascode stages and inverter-type stage has its bias current defined by power supply to reduced interferences.
Dual amplification path and dual polarities
either electrons or holes programmed or switched

## Slide 11: CSA in simulation
HSP two stage CSA Þ charge multiplication IOUT=18×14×IIN, with Cf1=4 fF, Cc1=18×4 fF, Cf2=40 fF and Cc2=14×40 fF
LSP one stage CSA Þ charge multiplication IOUT=20×IIN, with Cf1=4 fF, Cc1=20×4 fF,
left axis: orange 14keV and 7 keV
injections,
right axis: magenta Qout HSP
cyan Qout LSP
a_out
c_out
input

## Slide 12: Shaping Filter with Baseline Adjustment

## Slide 13
Cc is coupling capacitance for the last stage of the CSA
3rd order, 1-real + 2-complex conjugate poles [*], shaping filter (tp=300 ns) with baseline adjustment using current-mode DAC (7.5 bit equiv. +1 bit for polarity setting DAC – k=8)
Rpr = 571.6 kW, Cpr = 304.0 fF
Rpc11 = 183.2 kW /7 = 26.17 kW, Cpc11 = 4.52 pF
Rpc12 = 183.2 kW, Cpc12 = 304.0 fF / 2 =152.0 fF, Rpc13 = 183.2 kW
I current DAC = ±250 nA (baseline) + 1 mA (polarity)
DAC current is injected into node ‘d’ for noise performance
IR drop across Rpc12 Þ shifts of baseline.
Avoid AC coupling with voltage trim
[*] G. De Geronimo and S. Li, "Shaper Design in CMOS for High Dynamic Range," in IEEE Transactions on Nuclear Science, vol. 58, no. 5, pp. 2382-2390, Oct. 2011
Shaping filter with baseline adjustment

## Slide 14
Transient simulations
Linearity of HSP and LSP responses
Both paths work simultaneously;
HSP is non-saturated up to 18 keV;
LSP continues to operate up to one order of magnitude of input charge signal more;
Saturated HSP returns to baseline without visible perturbations;
Excess charge is dissipated by the reset network;
Both paths offer about ~1 V signal swings;
HSP
LSP

## Slide 15
Both Polarity are accepted
Both paths work simultaneously;
HSP is non-saturated up to 18 keV;
LSP continues to operate up to one order of magnitude of input charge signal more;
Saturated HSP returns to baseline without visible perturbations;
Excess charge is dissipated by the reset network;
Both paths offer about 1 V signal swings;
HSP and LSP simultaneous responses (both polarities)
e-
h+

## Slide 16: Correct ENC reporting
CSA uses passive, i.e., capacitors, and active, i.e., transistors, components in feedback path of high open-loop gain amplifier.
FE circuit transfer function is non-nonstationary Þ the noise (variance at specific points of time series data) needs to be calculated using transient noise simulation,
Simulation test setup for estimation of noise (SNR and DE/E)
1.5 ms long simulations with injections every 5 ms
(max noise frequency 250 MHz)
results presented in ‘eyeDiagram’ mode with period of 5 ms
Often SNR is incorrectly reported as
As ratio of pulse amplitude (transient sim.) to rms at not signal (AC noise sim.)

## Slide 17
AC “noise” SIMS estimates noise with no signal
RQI is the quiescent
current of the RESET.
It contributes to the parallel noise.
Programmable per Pixel with control bits.
Noise simulations

## Slide 18: S/H and readout sequencing

## Slide 19: Common Source S/H and Readout Interface
source follower = variable, typically <1, unless complicated architectures [US Patent No 11,108,981 B2]
CS with the S/H capacitor in feedback path is used
S/H for each adjacent pixel (HSP & LSP)
S/H in tracking mode
Discriminator detects SHAPER crossing of threshold (adjustable)
S/H exits tracking mode when SHAPER peak value is reached hence enter in read mode
Adjacent pixel max value are stored in in-pixel S/H cells
Pixel S/H is “blind” during readout sequence (high rate configuration available)
Pixel address is sent simultaneously on digital lines

## Slide 20: S/H readout sequence
Simulating an event @ 16keV with corresponding
charge sharing among adjacent pixels.
Output values must be referred to the corresponding baseline.
HSP
LSP

## Slide 21: S/H readout sequence
Simulating an event @ 160keV with corresponding
charge sharing among adjacent pixels.
Output values must be referred to the corresponding baseline.
HSP
LSP

## Slide 22: S/H readout sequence
Simulating an event @ 16keV. Only principal pixel (high-rate condition).
Output values must be referred to the corresponding baseline.
HSP
LSP

## Slide 23: Sparsified readout
More details in: “Event-driven arbitrated protocols implemented in integrated readout circuits
for segmented detectors” by D. Gorni

## Slide 24: EDWARD: Event Driven with Access and Reset Decoder
The high number of pixels requires robust, reliable, and preferably compact readout system on the chip to collect data from each structure and then transmit it out of the chip to communicate with acquisition systems.
Spectroscopy imaging is not Imaging -> Asynchronous and sparsed sources;
Optimal usage of available bandwidth (minimize dead time) -> Event driven readout instead frame readout;
Efficient transmission of data/configuration from/to multiple pixels;
Hierarchical design with arbitration tree -> No data collision;
General structure of the EDWARD architecture with highlighted functional blocks.
EDWARD readout:
Fully Scalable with the number of pixels
In-pixel logic with Arbitration tree to provide access to each pixel
Analog data bus and digital data bus
Design defined by geometry constraint
Physical design with automatic P&R tools (ensure timing requirements
Ideal for In-pixel ADC (future developments)
[ᙂ]Event driven readout architecture with
non-priority arbitration for radiation detectors,
D.S. Gorni et al 2022 JINST 17 C04027
First Physical implementation (1k pixel) submitted March 2023

## Slide 25: HEXID demonstrator 8x8 pixels

## Slide 26
HEXID test chip
5mm
3mm
Test struc. A
Test struc. B
Periphery
Pixel area 8x8
Expected submission: Aug 2023, MPW run, TSMS 65nm
BGR, DACs
OUTPUT BUFF,
CLK Receiver,
Global Logic, I2C

## Slide 27
HEXID pixel
CSA
SHAPER HSP
SHAPER LSP
S/H
EXT and Timing
Detector
~1200 Mosfet/Pixel
Custom Layout, MOMs above Mosfets
Power consumption: 0.5 mW/pixel
120um
130um

## Slide 28
HEXID pixel
Edward implementation:
Design defined by geometry constraint
Physical design with automatic P&R tools
(ensure timing requirements)

## Slide 29: Summary

## Slide 30
Objectives and Key Challenges:
A pixelated chip for finely segmented CZT Sensors suitable for Amplitude Spectroscopy in the hard X-ray regime
Handling two order of magnitude high DR with
a dual and built-in signal processing path
Optimize readout to cope with the nature of science
Development approach:
Pixel Front-End architecture with spectroscopic capabilities:
  Low noise;
  Adaptive reset mechanism;
  High Dynamic Range (up to 180 keV);
Event Driven Readout Mode:
  Asynchronous and Sparsed sources;
  Associated neighbors pixel readout scheme;
  In-pixel configuration (calibration)
  Future development with in-Pixel ADC
STATUS:
Front End architecture has been identified: Two path simultaneously
working covering wide energy range (2keV to 180keV)
Layout of several parts is present and verified (Silicon underway);
EDWARD Readout architecture has been developed.
  Sparsified readout platform;
  Analog Signal amplitude readout (In-pixel ADC in the future);
  Individual Pixel access and configuration;
NEXT STEPS:
Assembly of the entire test structure (85% done);
Submission of HEXID test structure (8x8 pixels)
  Validate chosen architecture with CZT sensor
  before large scale device;
  Expected submission Aug 2023
Pixel detector with built-in signal processing and bandwidth-efficient data transmission

## Slide 31: Thanks for your attention
Questions?

## Slide 32: BACK-UP

## Slide 33: Commonly used CSA concepts with ILEAK compensation and with p-z cancellation
Krummenacher’s / Manfredi’s [1]
Common Source Feedback (CSF) [4]
Common Gate
Feedback (CGF) [3]
Ð
Í
Í
feedback resistance µ current source,
IKRUM must exceed ILEAK, Þ parallel noise,
too large ILEAK Þ loss of stability [2],
requires large (~pF) Cint,
not connectable in p-z cancellation.
operates in p-z cancellation,
one-fit-all VRFB is needed,
Reset Quiescent Current (RQI) is optional; if used, multiplied RQI to next stages Þ shift of baseline.
operates in p-z cancellation,
RQI (typ. at some pAs) is required, but difficult to control and match,
larger ILEAK+RQIs Þ loss of stability,
multiplied both RQI and sensor ILEAK to next stages Þ shift of baseline.
input charge signal multiplication
L
L
L
[1] F. Krummenacher, "Pixel detectors with local intelligence: An IC designer point of view", Nucl. Instrum. Methods Phys. Res., vol. A305, pp. 527-532, 1991, P.F. Manfredi, et al, “The analog front-end section of the BaBar silicon vertex tracker readout IC”, Nuclear Physics B - Proceedings Supplements, Vol. 61, Is. 3, February 1998, 532-538
[2] Y. Hu, et al, "A low-noise, low-power CMOS SOI readout front-end for silicon detector leakage current compensation with capability," in IEEE TCAS I, vol. 48, no. 8, pp. 1022-1030, Aug. 2001
[3] G. De Geronimo et al., “A CMOS detector leakage current self-adaptable continuous reset system: theoretical analysis”, Nucl. Instr. Meth. A 421 (1999) 322-333
[4] G. De Geronimo et al., “Front-End ASIC for a GEM Based Time Projection Chamber”, IEEE Trans. Nucl. Sci Vol. 51, No. 4, August 2004 1313-1317
all shown for holes

## Slide 34: New CSA concept with ILEAK compensation and with p-z cancellation
[5] G. W. Deptuch, P. Otfinowski, “Charge Sensitive Amplifier with Pole-Zero Cancellation”, provisional patent application USPTO Serial No. 63/379,887
CSA with Self-Cascoded Field-Effect Transistor (SCFET) feedback network in configuration for integration of input charge signals [5];
Í
CSA with (SCFET) configured in pole-zero cancellation scheme [5], realizing multiplication (gain) of input charge signal ´ n;
Ë
assuming:
no body effect in transistors,
negligible sensor leakage current,
very high open-loop gain of amplifier (OpAmp or OTA)
… in real conditions, VDS1 is only close to “0”, nevertheless transistor M1 act as diode-connected, providing minimal voltage drop across and external voltage bias on its gate is not required
all shown for holes
J
J
L

## Slide 35: Charge gain maximization through cascading
1st charge gain stage ‘×n’
2nd charge gain stage ‘×m’

## Slide 36
ASIC Floorplan
HEXID_65nm chip (Final chip after test structure):
  Rotation help structuring vertical routing:
    less square chip: 64 × 80 pixels 12,340.50 × 10,020.00 mm2 active area
  10 × 8 - pixel groups combined into 5 blocks:
    64 × 80 pixels
    each block read out separately (5 outputs)
  sensor larger by 50 mm with respect to the lowest row of pixels
  distance from edge of sensors to wire-bonding pad not less than 400 mm (to allow tool access)
  75 wire bonding pads along one side (15 pads per group) @ pitch 120 mm
Approximated outside ASIC dimensions:
  12,550.00 × 10,750.00 mm2
Test structure:
  8x8 pixel to asset pixel circuitry and readout architecture
Edge circuitry, common blocks, I/O buffers
8x8
pixels

## Slide 37: SENSOR & ASIC FLOORPLAN

## Slide 38
Uncontacted gap between pixels: 15 µm
Bare CZT Area
Area for one CZT contact
150 µm
Sensor PADs Floorplan
Hexagonal pad with pitch 150um
Metal mask for
sensor fabrication
Sensor pads layout scheme.

## Slide 39
12,840.5 µm
10,520 µm
CZT Sensor:
  1 mm to 2 mm thick,
  ~1.3 x ~1 cm2
  64 x 80 pixels matrix
Full Sensor Floorplan
Mask alignment
point
8x8 test structure
Test structure:
  1 group = 8x8 pixel

## Slide 40
ToT simulations

## Slide 41
Threshold
Single Energy
If multiple
energies