## Slide 1: Event-Driven, Arbitrated Protocols Implemented in Integrated Readout Circuits for Segmented Sensors
Jun 12 – 16, 2023
Torino
XII Front-End Electronics Workshop
Dominik Górni, Gabriella Carini, Grzegorz Deptuch, Anthony Kuczewski, Soumyajit Mandal, Giovanni Pinaroli, Abdul Rumaiz, Peter Siddons, Nicholas St. John

## Slide 2: Motivation

## Slide 3: Readout from segmented sensors
How to read out data from segmented sensors to ensure data integrity and the least possible resource overhead, while providing the required speed and minimizing power consumption?
Maia X-ray Microprobe Detector Array System
D. P. Siddons et al., “Maia X-ray Microprobe Detector Array System,” vol. 499, pp. 012001–012001, Apr. 2014, doi: https://doi.org/10.1088/1742-6596/499/1/012001.

## Slide 4: Frame vs Event driven readout
Frame readout
Event-driven readout
Fully sequential
All data are read out which requires additional processing and compression
Asynchronous sequence is started in response to an external event e.g., particle hit
Only relevant data are read out -> low throughput
Sparse readout
External event sets a flag which is then checked by the readout circuitry

## Slide 5: Readout Circuits

## Slide 6: Priority arbitration scheme
HIT – logic sum of all inputs inXX.
Back signal propagated through the multiple stages of gating logic to activate the channel with the highest priority.
Risk of toggling the active pixel during readout if pixel with higher priority generates event.
To avoid jumping to higher priority pixel, an image of the matrix needs to be snapshotted.
G.W. Deptuch et al., "Design and Tests of the Vertically Integrated Photon Imaging Chip," in IEEE Transactions on Nuclear Science, vol. 61, no. 1, pp. 663-674, Feb. 2014

## Slide 7: How to avoid toggling
By using global strobe signal which freeze the state of the pixels
By using memory elements
x1 | x2 | ynext
0 | 0 | 0
0 | 1 | y
1 | 0 | y
1 | 1 | 1
https://en.wikipedia.org/wiki/C-element
C-element
req0 | req1 | gnt0next | gnt1next
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | gnt0 | gnt1
Arbiter based on Seitz arbiter
C. L. Seitz, “Ideas about arbiters”, Lambda, no 1, pp. 10–14, 1980.

## Slide 8: Arbitration cell with C-elements
A. J. Martin and M. Nystrom, "Asynchronous Techniques for System-on-Chip Design," in Proceedings of the IEEE, vol. 94, no. 6, pp. 1089-1120, June 2006, doi: 10.1109/JPROC.2006.875789.
Request is cleared once acknowledge signal reached the arbitration cell and acknowledge path is detached after acknowledge signals changes to inactive

## Slide 9: EDWARD readout architecture
D. S. Gorni et al., “Event driven readout architecture with non-priority arbitration for radiation detectors,” Journal of Instrumentation, vol. 17, no. 04, p. C04027, Apr. 2022, doi: https://doi.org/10.1088/1748-0221/17/04/c04027.
EDWARD – Event Driven with Access and Reset Decoder

## Slide 10: EDWARD arbitration cell
Acknowledge path is not detached until request is cleared in the pixel – it allows multiple “acknowledge tokens” to be sent without interruption from another requests.

## Slide 11: EDWARD arbitration cell – unfair version

## Slide 12: EDWARD arbitration tree
WO/2022/221068 - EVENT-DRIVEN READOUT SYSTEM WITH NON-PRIORITY ARBITRATION FOR MULTICHANNEL DATA SOURCES

## Slide 13: EDWARD in-pixel logic

## Slide 14: Requests rate dependence

## Slide 15: 3FI65P1 chip
The 3FI65P1 contains a matrix consisting of 1024 pixels. The matrix is made up of 16 groups (4x4), which contains 64 pixels (8x8).
The EDWARD65P1 chip has an identical architecture, but in place of the AFE has been placed a signal generator with an exponential distribution.

## Slide 16: Poisson process signal generator
Alejandro Luis Veiga and Enrique Mario Spinelli, “A pulse generator with poisson-exponential distribution for emulation of radioactive decay events,” Latin American Symposium on Circuits and Systems, Apr. 2016, doi: https://doi.org/10.1109/lascas.2016.7451002.

## Slide 17: Poisson process signal generator

## Slide 18: Only one pixel active
In this scenario only one pixel (with address ‘1’) is active.
Theoretical span of the readout delay:

## Slide 19: Only one pixel active
In this scenario only one pixel (with address ‘1’) is active.
Measured span of the readout delay:

## Slide 20: Low requests rate
[1]

## Slide 21: Low requests rate – readout delay
[1]
Max readout delay [ns]: 196.22
Min readout delay [ns] : 33.42
Max readout delay [ns]: 206.29
Min readout delay [ns] : 32.09

## Slide 22: Low requests rate – pileup rate
Minimum pileup count value: 0 (0)
Maximum pileup count value: 2 (18)
Minimum pileup rate value: 0.0% (0)
Maximum pileup rate value: 0.10% (503)

## Slide 23: Low requests rate – error bar plot
 | μ [ns] | σ [ns]
min | 59.5 (265) | 16.9 (277)
max | 70.0 (760) | 19.3 (469)
cum* | 64.2 | 18.2
*the cumulative value for all pixels together
μ
σ
-σ
pixel address

## Slide 24: Low requests rate – error bar plot
 | μ [ns] | σ [ns]
min | 59.5 (265) | 16.9 (277)
max | 70.0 (760) | 19.3 (469)
cum* | 64.2 | 18.2
*the cumulative value for all pixels together

## Slide 25: Medium requests rate
[1]

## Slide 26: Medium requests rate – readout delay
[1]
Max readout delay [ns]: 4,368.29
Min readout delay [ns] : 32.09
Max readout delay [ns]: 5,177.62
Min readout delay [ns] : 33.42

## Slide 27: Medium requests rate – pileup rate
Minimum pileup count value: 32 (418)
Maximum pileup count value: 81 (762)
Minimum pileup rate value: 0.18% (418)
Maximum pileup rate value: 0.44% (762)

## Slide 28: Medium requests rate – error bar plot
 | μ [ns] | σ [ns]
min | 223.0 (293) | 253.3 (1000)
max | 243.6 (766) | 304.0 (565)
cum | 232.6 | 272.9

## Slide 29: High requests rate
[1]

## Slide 30: High requests rate – readout delay
[1]
Max readout delay [ns]: 57,334.29
Min readout delay [ns] : 6,477.49
Max readout delay [ns]: 57,332.82
Min readout delay [ns] : 21,534.22

## Slide 31: High requests rate – pileup rate
Minimum pileup count value: 111539 (902)
Maximum pileup count value: 113923 (813)
Minimum pileup rate value: 92.66 (902)
Maximum pileup rate value: 92.80 (813)

## Slide 32: High requests rate – error bar plot
 | μ [ns] | σ [ns]
min | 53,056 (284) | 3,939 (171)
max | 53,332 (643) | 4,320 (95)
cum | 53,207 | 4,121

## Slide 33: Readout delay comparison
Rate: Low Medium High

## Slide 34: Comparison for readout using shift register (frame readout)
Rate | μ [ns]
Low | 64.2
Medium | 232.6
High | 53,200
To match EDWARD parallel readout speed from the pixel

## Slide 35: Summary

## Slide 36: Summary
Readout circuits for segmented sensors based on event triggering has been shown.
The dependence of the readout delay in relation to the requests rate was investigated.
In order to carry out this study, a circuit was designed to generate a signal to match the Poisson process (exponential distribution).
Based on this investigation, it was found that none of the pixels suffer from starvation regardless of the requests rate.
Hence the conclusion that there is no priority in readout between pixels.

## Slide 37: Thank you for your attention!
Questions?