## Slide 1: ASTRA: a high dynamic range front end embedded with HV monolithic silicon micro-strip sensors
Fabio Cossio (INFN Torino)
on behalf of the ASTRA group
XII Front-end Electronics Workshop
Torino - 14.06.2023

## Slide 2: Outline
ASTRA versions overview and motivation
ASTRA monolithic implementation
ASTRA readout architecture
Results from first measurements
Summary and outlook

## Slide 3: ASTRA: Adaptable Space sTrip Readout ASIC
Family of ASICs for the readout of silicon strip sensors (100 µm strip pitch readout). Two versions:
32-channel monolithic
64-channel with only electronics for commercial µstrips
Two versions share the same electronics with configurable Gain, Peaking Time, Readout mode (analog or digital)
ASTRA32
STRIPS
1.3 cm
3 mm
monolithic
ASTRA64
standalone
3.1 mm
8.0624 mm

## Slide 4: ASTRA requirements for space strip sensor
Target applications
Silicon Charge Detector (SCD) of the High Energy cosmic-Radiation Detection (HERD) facility on board of future China’s Space Station
  SCD design carried out by INFN Perugia: silicon strip detector for cosmic Rays tracking and complementary charge measurement
  Readout electronics current version based on IDEAS IDE1140 commercial ASIC
  32/64 channels (pre-Amp + Shaper + Sample&Hold) for 100μm strip pitch readout
  Low power consumption: < 1 mW/channel
  High dynamic range for high Z identification: 10k to 1000k electrons  1.6-160 fC
  Low noise: SNR > 10  ENC < 1000 electrons at Cin = 100 pF
  Adjustable shaping time: τ = 1-10 μs
Fully depleted monolithic active CMOS microstrip sensor using the same readout electronics architecture within the INFN Project ARCADIA (see Lucio Pancheri slides from yesterday)

## Slide 5: ARCADIA FD-MAPS
Advanced Readout CMOS Architectures with Depleted Integrated sensor Arrays
110 nm CMOS process (LFoundry)
n-type high resistivity active region
Fully depleted substrate: depletion grows from back to top
Electronics buried in deep p-well
Sensing electrodes biased at low voltage (< 1V)
CMOS circuitry can be implemented, but no triple well process for deep n-well NMOS isolation
Only HVT transistors (1.2 V) available

## Slide 6: ASTRA monolithic implementation

## Slide 7: ASTRA-32 with monolithic Si-Strips
Fully depleted monolithic pixelated strips based on ARCADIA sensor design
32 columns of 2 x 256 pixels connected in parallel
50 x 50 μm2 pixels
Total strip capacitance between 5 and 10 pF
The 32 columns are read by an array of 32 readout channels
Modular layout allows to characterize the electronics independently of the microstrips
Future versions with the electronics fully included in the deep p-wells in the microstrips and larger active area

## Slide 8: Electronics enclosure
1.3 cm
3 mm
Electronics enclosed in a large deep p-well
Protected by n-well guard rings
Guard rings are biased at 1.2 V
They collect stray electrons generated in the substrate directly below the electronics

## Slide 9: Strips – electronics interface
1.3 cm
3 mm
Two pixel-columns connected to channel FE input using top metal (ME6)
GND connection to the deep p-wells surrounding the pixels active region
n-well guard ring also around the microstrips to collect stray electrons generated in the depleted substrate outside the active sensor volume
n-well guard ring

## Slide 10: Top-side back-biasing
1.3 cm
3 mm
Substrate bias can be applied also from the top via dedicated pads
n-well 1.2V guard ring
top-side back biasing p-well structure

## Slide 11: ASTRA architecture

## Slide 12: ASTRA channel architecture
preAmp: CSA + TP injection circuit
Slow Shaper branch for charge measurement with externally controlled S&H circuit
Analogue readout: MUX-differential output buffer
Digital readout: Wilkinson ADC and serializer
Trigger output: Fast Shaper branch providing a fast-OR output

## Slide 13: Preamplifier stage
Cf
CSA
Cz
Feedback n
Feedback p
Inv stage
pol 0
pol 1
pol 1
pol 0
CSA suitable for both input signal polarities and with 2 programmable gain configurations
Gm feedback implemented with current mirrors, also providing output charge amplification with pole-zero cancelation
Inverting stage to feed the shaper with the correct signal polarity
1
2
3
2
to shaper stage
IN
TP inj

## Slide 14: CSA – core amplifier
Telescopic cascode amplifier with PMOS input transistor and split bias current with source degeneration
Programmable gain (Cf = 200-400 fF) to make it suitable for different sensors topologies
Output stage implemented with voltage-buffer OpAmp to reduce voltage headroom loss introduced by HVT transistors
Test-pulse injection circuit to test and calibrate the FE
Cf
Thick oxide input transistor for commercial μstrip version to reduce gate leakage current
(Vin > 0.8 V for monolithic ASTRA)

## Slide 15: CSA – feedback and output network
Gm feedback implemented with current mirrors, also providing output charge amplification with pole-zero cancelation
Programmable switches for Gain and Polarity select
pol 0
1 : 50

## Slide 16: Inverting stage
Inverting stage to feed the shaper with the correct signal polarity
Programmable switches to turn ON/OFF this stage according to the selected polarity
Current mirror with gm boosting and source follower buffer
IN
OUT

## Slide 17: Shaper stage
CR-RC Shaper with 4 programmable peaking time settings between 1.5 and 9 μs
Shaper core amplifiers employ same architecture of CSA core amplifier but with scaled-down bias current and transistors size
Baseline holder (BLH) circuit to control Shaper DC output voltage (nominal VBLH = 870 mV)
BLH
VBLH
Fast Shaper

## Slide 18: Slow shaper – simulation (1-200 fC)
Standard gain, pol=0, Tp = 9 μs
Standard gain, pol=1, Tp = 9 μs

## Slide 19: Slow shaper – simulation (1-200 fC)
Standard gain, pol=1, Tp = 7 μs
Standard gain, pol=0, Tp = 7 μs

## Slide 20: Slow shaper – simulation (1-200 fC)
Standard gain, Tp = 7 μs
Standard gain, Tp = 6.5 us
High gain, Tp = 7 μs

## Slide 21: Analogue readout
External HOLD signal to store the shaper output peak voltage for each channel
MUX to send off-chip the sampled signals of the channels (5 MHz readout clock frequency)
Unity-gain single ended to differential folded cascode amplifier
Class-AB output buffers can drive 50 Ω resistor and 20 pF capacitor
external ADC
trigger

## Slide 22: Digital readout
Analogue MUX is kept disabled, signal stored in the S&H capacitor is digitized by on-channel Wilkinson ADC with programmable recharge current
12-bit Gray counter
Serializer + SLVS Tx link
IADC [nA] | MAX recharge time [μs] | # BITs
70 | 2.7 | 8
35 | 5.4 | 9
17 | 11.1 | 10
9 | 20.9 | 11
4.5 | 41.9 | 12
100 MHz clock

## Slide 23: Fast branch – trigger output
Fast shaper: ~800 ns peaking time, ~25 mV/fC
LE discriminator with hysteresis (Vth generated off-chip and common to all 32 channels)
Fast OR logic to generate trigger output: each channel can be masked to remove noisy channels
-
Vth
LE discriminator
Fast Shaper
32-channel Fast OR
FAST OR
mask
SLVS Tx
Vb
12 C
C

## Slide 24: ASTRA layout
3 mm
4.4 mm

## Slide 25: ASTRA specifications
Technology | 110 nm CMOS Image Sensor
Power supply | 1.2 V
Number of channels | 32/64
Input polarity | Positive and negative
Sensor capacitance | Up to 100 pF
Input dynamic range | 1.6 - 160 fC
Peaking time | 1.5 µs to 10 μs
ENC | < 1000 e-
Outputs | Multiplexed pulse height, Digitized pulse height, Channels FastOR
Test and calibration | Internal injection circuit
Power consumption | <1 mW / channel

## Slide 26: ASTRA first measurements

## Slide 27: ASTRA testboard and DAQ (INFN Perugia)
Testboard
Can accommodate both ASTRA-32 (monolithic version) and ASTRA-64
Trimmer resistors for external bias (optional)
ADCs for analogue MUX readout digitization
3.3V/1.2V level shifters and CMOS/LVDS buffers for digital signals transmission
LDOs for ASTRA 1.2V AVDD and DVDD power supplies, and for 3.3V discrete components
Sensor HV bias (from top and bottom)
DAQ
Based on Terasic DE10-Standard development board with Intel Cyclone V FPGA
Handles ASTRA configuration, readout operations and data acquisition

## Slide 28: ASTRA-32 with monolithic Si-Strips

## Slide 29: IV curve
Backside voltage applied from top (HV = 30 V)

## Slide 30: Front-end response
Test-pulse injection: ~7.5 fC
Slow shaper response for different gain and shaping time settings
Waveforms measured from debug output

## Slide 31: Front-end linearity
Slow Shaper peak voltage from debug output
Shaping time settings: 7 μs
Higher gain compared to simulations:
  4.3 mV/fC (GAIN = 0)
  8.1 mV/fC (GAIN = 1)
PT = 01

## Slide 32: Analogue readout with 90Sr
ASTRA FastOR signal provides trigger to the FPGA
FPGA sends HOLD signal and then start readout of analogue MUX
Noisy channel excluded from FastOR

## Slide 33: ASTRA-64
Developed for readout of silicon strip sensors (INFN Perugia)
Made of 2 independent ASTRA-32 blocks
3.1 mm
8.0624 mm

## Slide 34: ASTRA-64 v2
3.1 mm
6.674 mm
Removed side pads to be 2-side abuttable
Already available from ARCADIA RUN2
Design of PCB hosting ~4 ASTRA-64 v2 ASICs starting soon

## Slide 35: Summary and outlook
The ASTRA ASICs family includes
  A 32-channel fully depleted monolithic active microstrip sensor with embedded electronics built on the top side and compatible with a standard CMOS process fabrication flow
  A 64-channel ASIC with only the readout electronics for commercial µstrips with two different layout flavors
Each ASTRA channel performs signal amplification and charge measurement, and the configurability of the chip makes it suitable for the readout of different topologies of Si-strip sensors
  Positive and negative input signal polarities readout capability
  2 gain settings providing input dynamic range up to 80 or 160 fC, suited for different thickness sensors
  4 peaking time configurations: 1.5-10 μs
  Dual-readout mode: analogue and digital + FastOR trigger output
ASTRA electrical characterization just started this month
Future version of monolithic ASTRA envisions the electronics fully included in the deep p-wells in the microstrips allowing for wafer-level detector stitching

## Slide 36
fcossio@to.infn.it
ASTRA Design and Test Group
G. Ambrosi, M. Barbanera, E. Bianco, F. Cossio, M. D. Da Rocha Rolo, M. Duranti, R. A. Giampaolo, A. Rivetti

## Slide 37: Backup slides

## Slide 38: IDE1140 ASIC
Previously VA140
64 channel
High dynamic range charge sensitive preamplifier-shaper circuit
Large integration time
Simultaneous sample and hold with multiplexed analogue readout
Calibration facilities
Internally generated biases

## Slide 39: Edge and back structures
1.3 cm
3 mm

## Slide 40: Shaper – response (1-200 fC)
Standard gain, pol=1, Tp = 4 μs
Standard gain, pol=0, Tp = 4 μs

## Slide 41: ENC vs Cin
Standard gain, Tp = 7 μs
Standard gain, Tp = 4 μs

## Slide 42: Noise – Peaking Time optimum
Cin = 10 pF
Cin = 100 pF

## Slide 43: Test pulse injection circuit
Cinj = test-pulse injection capacitance connected in series at the input of each channel (shorted to GND or VDD when test-pulse is disabled)
External reference voltage (TPinj) used to generate a voltage step (from VDD or GND to TPinj) across Cinj thus injecting a current at the input of the preamplifier

## Slide 44: Baseline Holder circuit
Differential stage + current starved SF

## Slide 45: Hysteresis discriminator

## Slide 46: Test pulse simulation
Cinj = 242 fF
TPinj = 10mV – 600mV
Qin = 2.5 fC – 145 fC

## Slide 47: Analogue readout
External HOLD signal opens the switch and store the shaper output peak voltage for each channel
MUX allows to send off-chip the sampled signals of the channels one by one (5-10 MHz readout clock frequency)
ch0
ch1
ch2
ch30
ch31
output buffer
MUX
outp
outn
0
0
1
0
0
ch0
ch1
ch2
ch30
ch31
read_clk
read_en
MUX
bit_out
external ADC
Slow shaper output
HOLD

## Slide 48: ASTRA-64 architecture
2 independent 32-channel blocks

## Slide 49: ASTRA-64
8.0624 mm
3.1 mm