## Slide 1: mechanical DESIGN OF fcc ir
Thanks to Manuela Boscolo, Stefano Lauciani, Luigi Pellegrino, Fabrizio Palla, Filippo Bosi
This project has received funding from the European Union's Horizon 2020 research and innovation programme under the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754

## Slide 2: FCC IR region
Support tube
LumiCal
Trapezoidal chamber
Central chamber
Cooling
Cryomagnet
This design is based on the IDEA detector concept, in fact we are working in close contact with INFN-Pisa integrating their Vertex and Tracker detector design.
IDEA detector
Bellows

## Slide 3
Central chamber
Trapezoidal chamber
Three layers from 0-90 mm from IP
0.35 mm of AlBeMet162 (62% Be, 38% Al)
1 mm gap for Paraffin
0.35 mm of AlBeMet162
Inlet/outlet for paraffin cooling (copper)
Starting from 90 mm to 1190 mm from IP
AlBeMet162 as main material
Chamber in two halves and assembled using electron beam welding (EBW )
Copper cooling system

## Slide 4
1st Bellows (Single bellows)
2nd Bellows (Double bellows)
Anchoring flange to support tube
IP SIDE
CRYOSTAT SIDE
Linear bearing system
Few convolutions inside support tube for thermal expansion
Convolutions to compensate
Cryostat expansion and assembly
CRYOSTAT SIDE
IP SIDE

## Slide 5
Support tube
Aluminium endcaps
Aluminium ribs to support:
Outer and medium tracker
Disk 1, 2 and 3
The structure is made with a multiple layer structure:
1mm CF + 4mm HC + 1mm CF
To allow the support of the disks are necessary 6 reinforcement ribs.
The cylinder is split in two halves to simplify the assembly procedure
The Aluminium endcaps support the LumiCal and the beampipe
The support tube aims to :
Provide a cantilevered support for the pipe
Avoid loads on thin-walled central chamber during assembly or due to its own weight
Support LumiCal
Support the outer and disk tracker

## Slide 6
Update of the vertex detector, disks and barrels integration
Update of the diameters of disks and outer barrel.
Change of the disks’ position according to the last layout version from INFN-Pisa group.
Change of the reinforcing ribs position.
Update of the Support Tube structural analysis.

## Slide 7: Structural optimization of Support Tube flanges
At the moment, the SIMP algorithm has been used, based on the concept of penalty, and the Generative Design method, capable of creating a structure from an initial shape and from imposed spatial constraints.

## Slide 8
Constraints in term of stress and displacement
Minimizing of the mass
No design zone where the constraint and loads are applied and in functional area

## Slide 9: Crotch chamber
-1175 mm
Solution A:
Standard flanges
More space available for the crotch
Flanges in Helium
Solution B:
Flanges not in contact with Helium
Shorter chamber than solution A
No standard flanges
Chart: 
| -5560 | -2500 | -90 | 0
X4 | 106.4627 | 52.5 | 10 | 10
X3 | -98.4 | -52.5 | -46.8 | -38.5 | -38.2 | -45.9 | -10 | -10
X2 | 71.1818 | 22.5 | 5 | 1 | 0.5 | 0
X1 | -71.1818 | -22.5 | -5 | -1 | -0.5 | 0
Xc | -84.7909 | -37.5 | 0
Solution A
Solution B
Work in progress
Remote vacuum connection

## Slide 10: Accelerator division internal notes
Calculation of the paraffin flow parameters needed to remove the heat load
Published17-04-2023
https://da.lnf.infn.it/documentation/accelerator-division-technical-notes/accelerator-division-technical-notes/
Case | A | B
Velocity | V=0.3 m/s | V=0.5 m/s
[°C] | 18.5 | 18.3
[°C] | 18.3 | 18.2
[°C] | 23.4 | 23.0
Case | A | B
Velocity | V=0.3 m/s | V=0.5 m/s
 | 18.5 | 18.3
 | 18.3 | 18.2
 | 23.4 | 23.0

## Slide 11: IFAE 2023
IPAC 2023

## Slide 12: INFN note
Published on 28-03-2023
http://www.lnf.infn.it/sis/preprint/search.php
Main themes:
Mechanical Model of the Beam Pipe and structural analysis
Mechanical Model of the IR Bellows
IR Carbon-fibre Support tube
Assembly sequence and alignment
Future plans

## Slide 15: Chamber design – central chamber
The central has the following characteristics:
AlBeMet 162 as main material
Three layers from 0-90 mm from IP
0.35 mm of AlBeMet162 (62% Be, 38% Al)
1 mm gap for Paraffin
0.35 mm of AlBeMet162
Paraffin as coolant
Geometry studied to integrate the central chamber with the vertex detector
Inlet/outlet for paraffin cooling (copper)

## Slide 16: Chamber design – trapezoidal chamber
Two halves AlBeMet pipe
Transition
Bellows
EBW
Thick copper deposition
90 mm
1190 mm
Main characteristics:
Starting from 90 mm to 1190 mm from IP
AlBeMet162 as main material
Chamber in two halves and assembled using electron beam welding (EBW )
Copper cooling system
IP

## Slide 17: Structural analysis – central chamber
Loads, constraints, characteristic parameters, design
FEA (Ansys)
Temperature distribution, stress and displacement along the pipe
Paraffin flow (central chamber)
Flow rate: 0,015 kg/s
Section:68,17 mm2
Velocity: 0,3 m/s
Inlet temperature: 18°C
Convective coefficient: 900 W/m2K
Water flow (trapezoidal chamber)
Flow rate: 0,0019 kg/s
Section: 9,62 mm2 (20 different channel)
Velocity: 0,2 m/s
Inlet temperature: 18°C
Convective coefficient: 1200 W/m2K
Heat load
54 W central
130 W AlBeMet162 for each part
From CST calculations (Alexander Novokhatski (SLAC))
Chamber design
Weight
chamber
Vertex detector first layer
Constraint
Cantilevered, simply supported configuration
RESULTS
Hypothesis:
Perfect thermal contact between the materials

## Slide 18
 | Trapezoidal chamber | Central chamber
Coolant | Water | Paraffin
Maximum chamber temperature [°C] | 47,6 | 33,1
T_out coolant [°C] | 20,5 | 20,1
Von Mises stress [MPa] |  |  |  |  | 
 |  | Trapezoidal SX | Trapezoidal DX | Central IN | Central EX
BEAM | Fixed ends | 22,07 | 21,86 | 46,8 | 38,9
 | Fixed+displ | 14,65 | 10,63 | 9,69 | 17
Maximum displacement [mm] |  |  | 
 |  | X | Y
BEAM | Fixed ends | 0,031 | 0,07
 | Fixed+displ | 0,1 | 0,29
Structural analysis – central chamber- results

## Slide 19: Support tube – Structural analysis
The aim of this analysis is to calculate the stress and displacement in each part of the cylinder (Al reinforcement, carbon fiber, honeycomb).
It is necessary to set:
Constraint configuration  double fixed ends
Loads configuration
Chamber | 50 kg
LumiCal | 70 kg + 70 kg
Disk tracker | 6*10 kg
Outer tracker | 15
Medium tracker | 7
First guess loads (overestimated) | 
Loads applied to remote point to distribute
Carbon fiber/ honeycomb creation  layered section

## Slide 20: Support tube – Structural analysis – results
 | Maximum stress [MPa]
Aluminium flanges | 2.08
Aluminium ribs | 0.20
Honeycomb | 0.02
Carbon fiber | 0.60
 | Maximum displacement X [mm]
Aluminium flanges | 1.34 e-2
Aluminium ribs | 2.62 e-2
Composite | 2.80 e-2

## Slide 21: Support tube – Rail
The support tube needs to be inserted into the main detector; the idea is to use a rail, starting from the outside of the detector to allow the sliding of the cylinder.
To assure a good precision and appropriate support it is necessary to use the linear bearings; different types are available, the choice has to be made considering:
Required positioning precision
Weight of the whole structure
Necessary degrees of freedom
SECTION

## Slide 22: Assembly procedure
1) Outer tracker, Medium tracker and disks 1 are installed as a rigid structure inside the support tube
2) Disks 2 and 3 are installed inside the support tube

## Slide 23: Assembly procedure
3) LumiCal is installed in centered position, then beam pipe with vertex detector is inserted with a dedicated tool inside disks and outer tracker, then fixed to both endcaps
4) LumiCal can be aligned in the correct position on the outgoing beams
5) Support tube can be closed

## Slide 24: 1st Bellows (Single bellows)
Anchoring flange to support tube
IP SIDE
CRYOSTAT SIDE

## Slide 25: 2nd Bellows (Double bellows)
Anchoring flange to support tube
IP SIDE
CRYOSTAT SIDE
Linear bearing system
Few convolutions inside support tube for thermal expansion
Convolutions to compensate
Cryostat expansion and assembly

## Slide 26
Bellows – constraint configuration
The use of support tube is designed to avoid overloads on central chamber during assembly and operation (thermal expansion). This solution has been obtained using different kind of bellows for the two side of the support tube.
To understand the constraint configuration, it is useful to create a simplified schema with bellows, support tube and chamber.
In short, in this way we can:
Protect the central chamber during the assembly procedure
Support properly the chamber bellows-to-bellows, containing the deformation
Allow the thermal deformation without compromising the chamber
1st Bellows
(named single bellows)
2nd Bellows
(named double bellows)
Chamber
Support tube
End cap
End cap
IP