## Slide 1: The LNL computing and network infrastructure
LNL User Community Meeting – 16 November, 2023
Michele Gulmini
INFN-LNL
Divisione Ricerca – Servizio Tecnologie Informatiche

## Slide 2
LNL Computing Infrastructure
  New VAX Computing Room
  New Data Center
LNL Network Infrastructure
  Fiber Installations
  Network gateway and VPN for experiments
  Wi-Fi support
Outline
M.Gulmini, LNL User Meeting, 16 November, 2023

## Slide 3
LNL Computing Infrastructure – Data Centers
The support for AGATA@LNL 2p was an opportunity for the LNL to renew and upgrade the computing infrastructures
  VAX Computing Room renovation
  New Data Center
New Data Center
GRID Data Center
VAX Room
New VAX Room
Support for AGATA DAQ, up to 20kW IT power, V1 electronics, ancillaries
Support for AGATA DAQ up to 2p configuration, V2 electronics, ancillaries

## Slide 4
New VAX Computing Room (Feb 2022)
AGATA fibers
REI120 walls
Cooling
New racks
Power distribution: electric panels
Fire estinguishing system

## Slide 5
New VAX Computing Room
AGATA DAQ (March/May 2022)

## Slide 6
New VAX Computing Room
Summer 2023
Fiber reorganization and Upgrade of the air conditioning

## Slide 7
New VAX Computing Room
Today
Up to 20 kW IT power
5 AGATA DAQ racks
2 Network racks
2 LNL IT racks
Coming: GARR-T POP
  1 rack
  2 x 100 Gb internet link
  Terabit ready

## Slide 8
LNL Computing Infrastructure:
New Data Center
New Data Center
GRID Data Center
The New Data Center will replace the Grid Computing Room
  AGATA@LNL DAQ + ancillaries, local experiments, local IT network services
  INFN Business Continuity and Disaster Recovery center (LNL, CNAF, LNF)
  LHC-Grid Tier2 Data Analysis Center: CMS and Alice experiments
  PNRR: ICSC (Italian Center for Supercomputing) and Terabit (Terabit Network for Research and Academic Big Data in Italy) projects
  INFN Cloud and CloudVeneto (INFN-LNL, INFN-PD, UniPD) Data Center
  Regione Veneto supercomputing HPC infrastructure - Application
          UniPD, UniVE, UniVR, INFN-LNL, INFN-PD

## Slide 9
NEW DATA CENTER
SPES
AGATA
GRID
VAX
LNL
Entrance
LNL New Data Center
M.Gulmini, LNL User Meeting, 16 November, 2023
Project phases:
Phase 0: Building
Phase 1: AGATA DAQ support
Phase 2: Scientific Computing (Grid Data Center replacement)
Phase 3: Upgrade for New Applications

## Slide 10
New Data Center
Nov 2023 – Building
M.Gulmini, LNL User Meeting, 16 November, 2023
15/11/2023
Ready Feb 2024

## Slide 11
New Data Center: layout
Phase 1 and 2 Funded (INFN + PNRR):
  40 computing racks
  6 network racks
  390 kW IT power
Racks
Technical Rooms
Entrance/Temporary Storage Area
M.Gulmini, LNL User Meeting, 16 November, 2023
Phase 3: application to Regional Research HPC Center
  Up to 66 computing racks
  Up to 1 MW IT power
Energy Efficiency: Annual PUE ~1.2
High Availability: Tier3 “Uptime Institute” classification
Tender DONE (waiting for contract signature)
Ready: end 2024
HW installation and operation: 2025

## Slide 12
M.Gulmini, LNL User Meeting, 16 November, 2023
Network Infrastructure: fibers
  2022-2023
  AGATA Control Room: New rack, OM4 fibers to VAX: 2x10Gb link
  Hall 1 – AGATA: 24 OM4 fibers to VAX
  Hall 1 – PRISMA: 12 OM4 fibers to VAX: 2x10Gb link
  SPES Building: full backbone (16 new network racks, OM4 and SM fibers)
  2024
  New Data Center: OM4 and SM fibers
  LNL Buildings (LAE, Auriga)
  Guest Houses

## Slide 13
M.Gulmini, LNL User Meeting, 16 November, 2023
Network Infrastructure for experiments
AGATA (+ancillaries), NUCLEX, GARFIELD: dedicated VPN network
  OpenVPN access: personal certificates delivered on demand
    Easier access to for external users and experts
    Requires “LNL User” Registration, INFN-AAI account, security course…)
  Configurable gateway in terms of services (ntp, dns, dhcp, …)
  Dedicated network subnet/VLAN
  Easily extendable to the different parts of the lab through the laboratory switch VLAN configuration
Small DAQ setups provided by users
  Private network for the devices, dedicated gateway
  Contact well in advance the Information Technologies – Network Service
User personal devices: normal registration on general LNL network
  email to calcolo@lnl.infn.it

## Slide 14
M.Gulmini, LNL User Meeting, 16 November, 2023
Wi-Fi Network
Wi-Fi is available in the LNL working areas
  eduroam, INFN-dot1x
Ongoing: gradual replacement of older devices with new access points
Tandem Building
  Improved signal quality in the meeting room
  Some issues during VAX Computing Room works are now fixed
Guest Houses
  Guest Houses C and B miss fiber network infrastructure (no cabling at all)
    Very weak signal from other buildings
    Fibers installation scheduled in 2024
  Temporary solution for Guest House C in Advanced Test Phase
    Mesh Technology
    Available by end 2023

## Slide 15
Thanks
Q&A
M.Gulmini, LNL User Meeting, 16 November, 2023

## Slide 16: SPARE
M.Gulmini, LNL User Meeting, 16 November, 2023