## Slide 2
SCIENCE SCOPE
THE NUSES SPACE MISSION
1
NeUtrino and Seismic Electromagnetic Signals
N
U
S
S
E
3 years mission
mid-2026
Low Earth orbit 535km
Sun-sunchronous
to limb
ZIRÈ
TERZINA
TERZINA
First observation of Cherenkov light emitted by atmospheric showers from space!
S Davarpanah
Technology pathfinder for New processing, Low power,
High speed electronics of novel silicon photosensors and radiation hardness
(not in scale)

## Slide 3
Radiation Background at the NUSES Orbit
2
No atmospheric shield
S. Davarpanah
Background radiation
e
p
Energy loss
Absorption
Multiple Scattering
Radiation damage
Sensor noise
Image quality
Energy threshold
Flux from SPENVIS
trapped electrons, trapped protons, solar protons

## Slide 4
3
Measurements and results
S. Davarpanah
IV measurement during irradiation:
Proton irradiation: 50MeV proton beam
Electron irradiation: β-source strontium-90, up to 2.2MeV
Realistic simulation with Geant4 gives us Non-ionizing dose
Dark Count Rate
SiPM response to the irradiation
+
non-ionizing dose
+
SiPM specification
Annealing
by placing the devices in a climatic chamber
@ fixed temperature for a set period of time
at T > 50°C, annealing cycle ~ 84 hours
recovery up to 40%
FBK NUV-HD_MT ( 3x3 mm2, 30um cell size )

## Slide 5
Thank you for your attention!
S. Davarpanah