## Slide 1
INFN-Milano beam dynamics activities in the frame of FCC study
A. Bacci, F. Broggi, Illya Drebot, M. Rossetti Conti

## Slide 2
Diagnostics and bunch intensity control via Compton scattering
Before collision
After collision
In the future circular electron-positron collider “FCC-ee”, the intensity of colliding bunches must be tightly controlled, with a maximum charge imbalance between collision partner bunches of less than 3–5%. Laser Compton back scattering could be used to adjust and fine-tune the bunch intensity.
Sketch of the Compton collision inside a single 10 m long dipole.
To-Do: Find better position for Compton IP and optimise focusing parameters to increase efficiency of collision
Next step start simulation with polarisation for beam diagnostic
I. Drebot, S. Cialdi2, INFN-Milano, [20133] Milano 2also at Universitá degli Studi, [20133], Milano, Italy A. Abramov, M. Hofer, F. Zimmermann, CERN, [1211] Geneva, Switzerland

## Slide 3
Layout of the collimation section under study for the FCC-ee at the Z operation mode. The location of the laser interaction is indicated by black bars, together with the optics functions.
Single-bunch loss map after 500 turns with laser interaction for the Z operation mode and a laser spot size of 100 μm. Aperture losses in normal conducting magnets are shown in red, and losses on superconducting magnets are shown in blue.
Emittance evolution of the particle bunch for different laser spot size and for the Z operation mode.
Result was presented at
IPAC23
Defined optimal place for IP
Improved tracking code to simulate CBS during injection in the FCC ring
Surviving fraction of the initial particle bunch of 106 particles for different laser spot size. The dashed line indicates the results for the 𝑍 operation mode, whereas the solid line is for tracking with 𝑡 parameters.
https://www.ipac23.org/
preproc/pdf/MOPA074.pdf
List ToDo:
Improve IP inside bending magnet
Find optimum between reducing bunch charge to exclude flip-flop instability and emittance growing
Study possibility to optimise energy distribution e- e+ using dispersion inside bending magnet
Study possibility to reduce beam halo using Donuts-shaped laser beam
Study polarization of scattered photons for diagnostic
Find application and users for 25 and 150 GeV photon beam 🖖

## Slide 4
FCC Week 2023 – London
Iryna Iryna Chaikovska courtesy

## Slide 5
FCC Week 2023 – London
Iryna Iryna Chaikovska courtesy

## Slide 6
FCC Week 2023 – London
Iryna Iryna Chaikovska courtesy

## Slide 7
FCC-ee Pre-Injector: CHART Collaboration Meeting, 21 April 2023, LNF, Italy
Marcello Rossetti Conti Talk

## Slide 8
Bz [T]
Z [m]
All beam dynamic optics regenerated by us to maximize optimization knobs
Flux concentrator
Acc. cavities solenoids
Bridge Solenoids

## Slide 9
FCC-ee Pre-Injector: CHART Collaboration Meeting, 21 April 2023, LNF, Italy
Marcello Rossetti Conti Talk

## Slide 10
Genetic Interface for OpTimizing Tracking with Optics
One of first AI codes for beam line design & optimization born @ INFN-Milano. Solves complex multi-objective problems (space-charge BD) & statistical analysis (BD jitters studies).
Successfully used in important projects, as:
Publication on major journals: PRAB 22 (2019) - NIM A 909 (2019) - JAP 133 (2013) New study Submitted @ PRAB in January (2023)
40.7% of extracted e+ in 1st RF bucket E = 45 MeV (64% ΔE/E)
Starting Point
GIOTTO Optimized Point
59.4% of extracted e+ in 1st RF bucket E = 100 MeV (24% ΔE/E)
@ FCC-ee: first application in e+ capture line presented by M. Rossetti Conti in Lyon FCC-workshop 21-nov-22
Disponibilità di GIOTTO + la nostra compentenza nella fisica dei fasci.

## Slide 11
Few weeks ago update
Capability to optimize into a rf bucket

## Slide 12
59.4%

## Slide 13
Contribute recap beam dynamics Milano group
Lione: Marcello Rossetti Conti talk Illya Drebot talk
Orsay: Iryna talk
Frascati: Marcello Rossetti Conti talk
IPAC 2023:
2 Posters & proceedings
London: Iryna Chaikovska talk

## Slide 14
1 missione Illya Orsay ~800 € altri fondi + 1 Marcello su Milano 1000 €
Io escluso per infortunino
1 missione Illya IPAC ~2000 € Pisa 1 missione Marcello IPAC ~2000 € altri fondi
1missione 2 persone Frascati ~500 € Milano
Milano (Romualdo): 1.5k€ Pisa:2.5k€
Altri fondi:2.8k€
A disposizione circa 20k€ di workstation
Totale Missioni 2023: 6.8k€ (nessuno è andato alla FCC week)
Richieste solo missioni 2024: 7 k€ (deve si possono allocare?) Non sempre straight forward l’utilizzo dei fondi missione
FTE Marcello (5 -> 15), Illya (5 -> 15), Alberto (5 -> 15), Francesco (10)