## Slide 1: XRO X-Ray Observatories
Irina Rashevskaya
29 giugno 2023 CSN2

## Slide 2: XRO eXTP science
Study of matter under extreme conditions of gravity, density and magnetism. For the first time: simultaneous, high-throughput spectral, timing and polarimetry observations.
Constrain the Equation of state of the supra-nuclear density matter in the interior of neutron stars.
Accretion physics in the strong-field regime of gravity and tests of General Relativity in neutron stars and black holes over the mass scale.
Physics of light and matter in the presence of ultra-strong magnetic fields in magnetars and X-ray pulsars.
Multi-purpose observatory and wide-field monitoring for transients (and e.m. counterparts of GWs). Rapid follow-up.

## Slide 3: XRO
Sigla CSN2 da 2021
IXPE Imaging X-Ray Polarimetry Explorer
L. Baldini (PI)
eXTP enhanced X-ray Timing and Polarimetry
V. Bonvicini (TS)
Strutture partecipanti:
TS, PI, TO, MI, PV, BO, TIFPA, PG, RM2
~ 30 FTE complessivi
Attivita’ di TIFPA focalizzata su eXTP
Silicon Drift Detector per LAD e WFM

## Slide 4
Linear Silicon Drift Detector
Large Area Silicon Drift Detectors for X-ray spectroscopy, timing and imaging
designed by INFN,
produced by FBK
developed in collaboration REDSOX .
More than10 yrs R&D activity.

## Slide 5: eXTP LAD – Large Area Detector WFM-Wide Field Monitor
x4
Total effective area: 3.4 m2 @8 keV
Energy band: 2-30 keV
Energy resolution: <240 eV FWHM @6 keV
Based on the LOFT/LAD design
40 Modules on 2 deployable panels
640 large-area SDD detector
112 anods pitch 970um x2
Field of View: 4 steradian (at 20% response)
Imaging, <5 arcmin angular resolution,
Energy band: 2-50 keV
Energy resolution: 300 eV FWHM @6 keV
Effective area: 80 cm2 @6 keV
3 units (6 cameras)
24 large-area SDD detectors
384 anodes pitch 169um x2
WFM

## Slide 6
LOTTO WFM 211-
dicembre 2022
FBK
Misura I-V a tre punte 15 wafer
Scan Catodi 15 wafer
TIFPA
Misura I-V GelPack 6 sensors
Scan Anodi GIG 10 sensors

## Slide 7
eXTP WFM

## Slide 8
WFM 211 Montaggio GIG
HV
C 292
MV
C 291
BOND
P&N side - C0, C291, C292, ogni 30 Catodi
N side – Grid, GND
P side –W2, W1
Applicando
HV C0 -1100V Keithley 237
MV W2 -70V HP4141B
Viene misurato
V C291, V C292

## Slide 9
WFM 211 Probe Station

## Slide 10
WFM 211 SCAN

## Slide 11
WFM 211 SCAN Anodi
384 Anodi con passo 169 um
Lo scan automatico viene eseguito con la ProbeCard da 50 punte e gestito dai programmi LabView. Ci sono esatamente 8 posizioni della probecard. Nella prima posizione vengono misurati gli anodi 1- 48. Poi per 6 posizioni della probecard vengono misurati 48 anodi centrali con due punte esterne connesse a GND. Nell’ultima posizione vengono testati gli ultimi 48 anodi con due prime punte conesse a GND.
Gli scan vengono eseguiti per gli Down12 e UP34.

## Slide 12
WFM 211 W91 SCAN Anodi
THE BEST
Chart: Anodes

## Slide 13
WFM 211 SCAN Anodi DOWN12

## Slide 14
WFM 211 SCAN Anodi UP34
08-02-2023
Anodi 59-60
Anod 291-292

## Slide 15
WFM 211 SCAN Anodi

## Slide 16
WFM W18 C292
I C292 = 74uA
Non è questo.

## Slide 17
WFM montaggio NEWAYS
Montaggio
Meccanica
Bonding 17-200 um
Camere pulite
Altissima professionalita e capacita.
(MIPOT ???) 

## Slide 18
eXTP WFMino
04/07/2022
HV
MV
LV
-1100V
-40V
-70V
WFMino 64 Anodi con passo 169um
Lo scan automatico viene eseguito con tre punte.
La punta centrale misura la corrente dell’anodo e le punte 1 e 3 raccolgono corrente variabile dal resto del sensore e vengono misurate insiemi.

## Slide 19: XRO eXTP TIFPA contributo 2023
Test e la caratterizzazione eletrica di WFM (Lotto WFM211- dicembre 2022)
Ispezione ottica dei sensori LAD WFM LADino WFMino
Classificazione dei difetti e Studio di resa
Definizione dei parametri di processo e del materiale attraverso la caratterizzazione delle strutture di test
Partecipazione al design del nuovo anodo del LAD.
Test e la caratterizzazione eletrica LADino WFMino

## Slide 20: eXTP TIFPA Articoli 2023

## Slide 21: eXTP TIFPA Spese 2023
Richeste finanziarie 2023

## Slide 22: XRO eXTP TIFPA obiettivi 2024
Test e la caratterizzazione eletrica di WFM (Lotto WFM231 marzo – settembre (?) 2023)
Ispezione ottica dei sensori LAD WFM LADino WFMino
Classificazione dei difetti e Studio di resa
Definizione dei parametri di processo e del materiale attraverso la caratterizzazione delle strutture di test
Partecipazione al design
Test e la caratterizzazione eletrica LADino WFMino
Test e la caratterizzazione eletrica Lotto LAD senza gettering (settembre - dicembre 2023(?))

## Slide 23: eXTP TIFPA FTE 2024
Irina Rashevskaya Tecnologo TIFPA 70% RESP
Antonino Picciotto FBK 20%
Mateo Centis Vignali FBK 20%
Francesco Ficorella FBK 20%
Nicola Zorzi FBK 20%
TOTALE 1.5 FTE
Richeste finanziarie 2024
Missioni:
1. Riunione del TEAM a Roma 2gg. 2.00 kE
2. Test di sensori in lab a Trieste. Solo viaggio. 4.00 kE
Consumo: 4.00 kE

## Slide 24: Thank you

## Slide 25
LAB a TRIESTE
Messa in funzione seconda postazione di test con la Probe Station semiautomatica KarSuss e rack di strumenti.

## Slide 26
Parameter | Value
Orbit | 550 km, <2.5 inclination
Launcher | Long-March CZ-7 + upper stage, from Wenchang
Mass | 4500 kg
Power | 3.6 kW
Telemetry | 3.2 Tb/day (X-band)
Ground Stations | Sanya, Malindi
Pointing | 3-axis stabilized, < 0.01° (3-sigma)
Sky visibility | 50% (goal 75%)
Mission Duration | 5 years (goal 8 years)
Launch date | 2027

## Slide 27
Payload | Parameter | Specification
SFA | Energy range | 0.5-10 keV
 | Effective area | >7000 cm2 @1 keV, >5000 cm2 @6 keV
 | Energy resolution | <180 eV FWHM @6 keV
 | FoV/HPD | 12 arcmin / 1 arcmin
 | Focal plane detector | Pixelated SDD (19 pixels)
LAD | Energy range | 2-30 keV (extended: 30-80 keV for out-FoV)
 | Effective area | 34000 cm2
 | Energy resolution | <240 eV FWHM @6 keV
 | FoV | 1 (FWHM)
 | Detector | Large area SDD (640 units, 40 Modules)
PFA | Energy range | 2-10 keV
 | Effective area | >900 cm2 @2 keV (including QE)
 | Energy resolution | 1.2 keV FWHM @6 keV
 | FoV/HPD | 12 arcmin / 20 arcsec
 | Focal plane detector | GPD (4 units)
WFM | Energy range | 2-50 keV
 | Energy resolution | 300 eV FWHM @6keV
 | FoV | >4 sr (at 20% of peak response)
 | Angular resolution | <5 arcmin
 | Localization accuracy | <1 arcmin
 | Detector | Large area SDD
Soft Response
Large area
Polarization
Monitoring