## Slide 1: CHIRONE… 2021-2023 & 2024-2025… …as seen from MILANO Chiara Guazzoni
Milano, 5 Luglio 2023 – Consiglio di Sezione, INFN Sezione di Milano

## Slide 2: Outline
CHIRONE, who’s who?
The Collaboration: participating Sections and People @ INFN-MI
The CHIRONE main apparata:
  (CHIMERA and) FARCOS
  Novel detection system for in-flight tagging and tracking for exotic beams
  NARCOS Charged particle/neutron detection system
Main activities and results 2022 - 2023
Activities foreseen for 2024 – 2025

## Slide 3: CHIRONE, who’s who?
Gem of black glass paste engraved with the centaur Cheiron teaching Achilles to play the lyre.
Brithish Museum, 1923,0401.772
I-III century
https://www.britishmuseum.org/collection/object/G_1923-0401-772
CHIRONE (Chieron), Χείρων, held to be the superlative centaur amongst his brethren since he was called the "wisest and justest of all the centaurs“
CHIRONE was sired by the Titan Cronus when he had taken the form of a horse and impregnated the nymph Philyra
Apollo took him under his wing and taught him the art of music, lyre, archery, medicine and prophecy. Artemis trained him in archery and hunting. Chiron with his uniquely peaceful character, kindness and intelligence was a highly revered teacher and tutor
CHI  CHImera
R  R3B
O  hOdoscopes
N  Neutrons
E  Experiment

## Slide 4: CHIRONE (2021-2023+2024/25)
Sezione di Milano (RL: C.Guazzoni)
Sezione di Catania (RL: G. Politi)
LNS (RL: E.V.Pagano)
Resp. Nazionali: Sara Pirrone (INFN-CT) & Paolo Russotto (INFN-LNS)
Anagrafica Milano 2024
C. Guazzoni 0.8 FTE (0.2 Gr. V ASTAROTH)
A. Castoldi 0.8 FTE (0.2 Gr. V ASTAROTH)
+ PhD student in corso di associazione 0.5 FTE
Richieste Servizi Milano 2024
      = Servizio Elettronica:
      2 mesi/uomo (nella persona di Ciro Boiano, per conoscenza setup)
      = Uso CleanRoom e Bonding Machine ???
      = Servizio Officina Meccanica:
      1 mese/uomo
      - supporti bonding rivelatore
      piccole lavorazioni flange
      stampa particolari 3D
      consulenza struttura meccanica sistema di tagging
Richiesta Prolungamento 2024 - 2025
- Restrizioni COVID 19 (2020 - 2021- PARTE 2022)
- Chiusura attività sperimentali @LNS (da giugno 2020) per upgrade Ciclotrone HI e FRAISE
- Restrizioni assegnazione @GSI (2023-2024-2025) er upgrade FAIR
Assegnazione PRIN - ANCHISE (da giugno 2022 a 2025)
Partecipazione PNRR – SAMOTRACE @CT (da ottobre 2022 a 2025)
Anagrafica Nazionale
2024 - 17.8 FTE
22 persone ( 19 Ric. + 3 Tecno)
2023 - 16.1 FTE
20 persone ( 18 Ric. + 2 Tecnο)

## Slide 5: The CHIRONE main apparata… (existing…)
CHIMERA - Charge Heavy Ion Mass and Energy Resolving Array
FARCOS - Femtoscope Array for COrrelations and Spectroscopy
20 clusters

## Slide 6: Esperimento CHIFAR
0.76±(<0.01)
0.70±(<0.01)
0.38±0.01
0.13±0.01
0.73±(<0.01)
0.66±(<0.01)
0.37±0.01
0.10±0.01
4.6<AH/AL<10
2.6<AH/AL<4.6
1.6<AH/AL<2.6
1.0<AH/AL<1.6
124Sn+64Ni
Dyn %
124Sn+64Zn
TKE>2200 MeV
1900<TKE<2200 MeV
1675<TKE<1900 MeV
TKE<1675 MeV &&
θcm 1>25°
CHIMERA DATA
✅ Analysis of fusion-fission events in central collisions
✅ Selection of PLF splitting events
✅ Extraction dynamical component for various splitting mass asymmetries and energy dissipation
✅ Simulations by using HIPSE event generator filtered with a software replica of the detector
Extension of the analysis to 112Sn and 124 Xe beams in progress
Estensione a bassa energia degli studi sulla competizione delle componenti dinamica e statistica e sull’influenza dell’isospin nel break-up del proiettile.
124Sn+64Ni
112Sn+58Ni
124Xe+64Zn
at 20 AMeV

## Slide 7: Esperimento CHIFAR - FARCOS Data (NEW)
Estensione a bassa energia degli studi sulla competizione delle componenti dinamica e statistica e sull’influenza dell’isospin nel break-up del proiettile.
124Sn+64Ni
112Sn+58Ni
124Xe+64Zn
at 20 AMeV
Z=4
Z=6
Mass spectra: isotopic identification

## Slide 8: Esperimento CLIR
Studio di stati di clustering in nuclei leggeri (10Be – 16C)
In-Flight 18O + 9Be (1500 μm) 55 MeV/A - Cocktail beam (FRIBs@LNS) on (CH2)n
4 FARCOS telescopes + CHIMERA
Tagging calibration by simulations with LISE++
16C
17C
13B
12B
14B
15B
9Be
10Be
11Be
12Be
7Li
8Li
9Li
6He
FARCOS: calibrations through energy loss simulations of the three stages
Calibration of the CsI(Tl) stages through RNQM model (Parlog M., et al., NIM A 482 (2002) 693);
Calibration of the front and back strips of the 1500 μm stage;
Counts per 200 keV
10Be relative energy spectrum obtained for the 4He+6He break-up channel. Location of known peaks is shown, while possible evidence of the 13.5 MeV (6+) state is shown.
13.5? MeV
14.8? MeV
11.8 MeV
10.6 MeV
Preliminary – PHD thesis Risitano

## Slide 9: Analisi dei metodi di rivelazione del 8Be con CHIMERA e FARCOS
1. Si è confrontato la risoluzione del picco del 8Begs misurato a vari angoli con CHIMERA e FARCOS con cui otteniamo σ = 7 keV
2. Si è poi evidenziato come CHIMERA permetta di misurare il 8Be con la rivelazione delle 2 alfa in pile up nello stesso rivelatore evidenziando questi eventi nelle matrici TOF
Pulse shape silicio (mai osservata prima)…..
…..Ma anche pulse shape CsI(Tl) e ovviamente ΔE-E in silicio
G.Cardella, B.Gnoffo, …, C. Guazzoni, et al Eur. Phys. J. Plus (2023) 138:89

## Slide 10: Esperimento Hoyle-γ
Misura del branching ratio dello stato di Hoyle del 12C e studio del livello 9.64 MeV
LNS – CHIMERA & FARCOS
Luglio 2019
A.Raduta et al., PLB 705, 65 (2011)
G. Cardella et al., Nucl. Instr. and Meth. A 799, 64 (2015)

## Slide 11: Highlight 2023 CHIRONE - study of γ-decay of excited 12C states
The γ-decay of 12C levels above the particle emission threshold have a crucial role in the production of 12C in astrophysical environments, and the Hoyle state is fundamental for the synthesis of 12C. Despite of the numerous studies in this field, there is still a lot to understand.
With FARCOS, we will get a relevant improvement in measuring CM energy for 3-α coincidences (yellow 27 KeV) than with CHIMERA (cyan 200 keV)
We will use α beam at energy of 40 MeV on 12C
(Tandem @LNS) measuring both particles and γ rays with FARCOS telescopes
We take advantage by the improved γ-resolution with FARCOS (respect to CHIMERA) from 1 MeV to 150 KeV
CHIMERA
FARCOS
ECM
The CHIRONE collaboration performed 4 fold coincidence measurements with the results of enhancement both the 9.64 MeV level and the Hoyle state γ-decay yields. This last result can be explained by the excitation of an Efimov state
G. Cardella, A. et al., Nuclear Physics A 1020 (2022) 122395
EFIMOV
Each couple of α has a CM energy like a 8Be - Energy of the level results 180 keV - 200 keV smaller than the Hoyle state
New more precise measurements needed to confirm effects on 12C creation in the universe
Cardella G. et al., PRC 104, 064315 (2021)

## Slide 12: The CHIRONE main apparata… (new developments)
NArCoS (Neutron Array for Correlation Studies)
New CHIMERA RIBs tagging system
3x3 Matrix
2 Clusters
PRIN ANCHISE-2020 (period 3 years starting June 2022 cod. 2020H8YFRE)
Collaboration: INFN-Unict-UniMe-PoliMI.
Coordinator and spokes: A.Pagano (INFN) – G.Politi (Unict) - M.Trimarchi (UniME) - A.Castoldi (PoliMI).

## Slide 13: NArCoS (Neutron Array for Correlation Studies)
Prototypal readout electronic in preparation of the CROSSTEST exp at LNL (end of 2023)
(C. Boiano)
Each elementary cell of EJ276G (3x3x3 cm3) is equipped with a matrix of 25 SiPM (6x6 mm2) of 30 𝜇m of thickness (≈ 40k microcells). The SiPM matrix is coupled with the plastic having their PAC and bias/temperature compensation circuit
EJ276G
AmBe source: PSD test
400 ns
Fast respons < 4 ns
500 MHz sampling

## Slide 14: NArCoS (Neutron Array for Correlation Studies)
Attenuation shield tests in preparation of the CROSSTEST exp at LNL (end of 2023)
Material: Polyethylene
Neutron source: AmBe
Attenuator Thickness: 2.5 cm
≈1%
Attenuator of 30 cm ≈ 1%

## Slide 15
Several beam diagnostic/tagging devices provide beam info:
within the fragment separator in two points (degrarder & exit slits):
  need of a point-to-point measurement of cocktail intensity, relative composition, energy distribution, 2D profile, angular distribution during optimization;
  monitoring of beam properties, start time for event-by-event ToF/energy mesurement during data taking;
in the final set-up point (measurement chamber):
  need of event-by-event tagging of cocktail beam and trajectory measurements
15
courtesy of G. Cardella, P. Russotto, N. Martorana
FraIsE @ LNS
The FraISe fragment separator, presently being built at INFN-LNS, will produce particle rate ranging from 102 pps (very exotic isotopes, extremely far from stability valley) up to 107 pps (exotic isotopes near to stability valley).
beam exit
Improvement in intensity opens the way to more precise studies on nuclei close to stability and allows to extend investigations to nuclei far from stability
Nuclide of interest | Intensity* (kHz)
14Be | 1.4
16C | 6800
17F | 99700
20O | 190
Some examples (E/A≈40 MeV)
* in the cocktail beam
FraIsE

## Slide 16: State of the art tagging systems
FRIBS@LNS
Diagnostics:
  plastic scintilators: check yield at rate< 105 pps
  RF-DSSSD: check yield, composition (ΔE-ToF), 2D profile
At final user point of CHIMERA line:
  event-by-event tagging of cocktail beam, ΔE-ToF with a MCP-DSSSD system
ΔE (MeV)
ToF (ns)
18O(55 AMeV) + 9Be(1500 um)
Bρ=2.78Tm
6He
9Li
12Be
15B
18C
16C
8Li
MCP: up to 105 pps
Δt ≈ 200-300 ps
DSSSD: max rate 200 kHz, performance worsening ≈1 week with medium mass beam at 30 kHz;
overall Δt <≈1 ns
I. Lombardo et al., NIMB 215, 2011
LISE@GANIL
Diagnostics:
  CATS: multi-wire proportional detector for ToF and trajectory measurements
  MCP for ToF and X-Y position measurements
  Si at low beam intensity to check composition (ΔE-ToF)
Limited below 106 pps and significant damages at high rates.
Super-FRS@GSI
Diagnostics:
  Combination of GEM-TPC, Diamond detector, Scintillator detector
Other fast and rad-hard sensors are welcome
courtesy of G. Cardella & P. Russotto

## Slide 17: The tagging system: specs and design
network of rad-hard sensors, equipped with optimized fast frontend electronics, DAQ with Data Real-Time Management capabilities and a dedicated software layer implementing AI and ML techniques
The system needs to be compact, removable and easily interchangeable.
The system must sustain a beam intensity up to 107 pps for several experiments a year,
Housed in a DN160 spherical cross, the full detection system is based on a matrix of 100 mm thick 4H-SiC detectors with 30 mm x 60 mm active area segmented in small detection units (25mm2), large enough to cover the entire beam size with a maximum dead area of 15%.
RIB composition determined by joint measurement of energy loss DE and time of flight (ToF).
Required energy resolution below 100 - 200 keV, required time resolution below 100 ps rms.

## Slide 18
SPOKE 5 (INFN), WP4: Micro detectors for particle therapy, dosimetry e micro-dosimetry
TASK: Design study of a Silicon Carbide (SiC) particle detector for dose measurements in radiation dosimetry and real-time beam monitoring
Scopo
ottimizzare produzione di un fascio test di 11C per eseguire in contemporanea adroterapia e PET – attivo da 1 ottobre 2022 - finanziamento INFN WP 700k€ - finanziamento tematica beam monitor circa 250 k€ (costi produzione SiC tagging)
Stato
scelta configurazione finale rivelatori (slice da 15x15 mm2 con 9 pixel da 5x5 mm2)
In consegna substrati per la crescita epitassiale dei rivelatori – ordine in preparazione per la realizzazione dei rivelatori - Prevista consegna primi prototipi Luglio 2024
In corso
test con rivelatori simili realizzati in precedenti batch

## Slide 19: SiC vs. Silicon

## Slide 20: Simulation of induced signals in SiC & Si
11Be ion at 47 AMeV – as produced in the FraISe facility in the case of a primary beam of 13C at 55 AMeV – passing through a 100 μm thick detector in transmission mode
energy loss
deposited charge
induced current in SiC
induced charge in SiC/Si

## Slide 21: Simulation of induced signals in SiC & Si
11Be ion at 47 AMeV – as produced in the FraISe facility in the case of a primary beam of 13C at 55 AMeV – passing through a 100 μm thick detector in transmission mode
energy loss
deposited charge
impact of overbias on induced charge
5%, 10%, 20%, 50% overbias

## Slide 22: Prototype Detection System Components
100 mm thick SiC detectors
25 mm2 single unit
25 mm2 unit segmented in 4 subunits
1 cm2 single unit & 1 cm2 segmented in 4 subunits
5 mm
10 mm
5 mm
10 mm
1cm2 detector carrier with custom stackup or full transmission mode
4-channels preamplifier/shaper board with differential output drivers
35 mm
25 mm
U.FL-R-SMT-1(10)
HSEC8-113-01-S-DV-A-K
differential output line driver
preamplifier/shaper
0.50mm Pitch SlimStack Plug
Pico-Clasp PCB Header (bot)

## Slide 23: SiC detector 100 μm thick, 25 mm2: device qualification
Experimental apparatus for CV measurements, based on the Agilent E4980A, custom modified for high voltage operation

## Slide 24: Frontend electronics: Functional qualification
Integral Non Linearity
for every input signal amplitude: INL computed as maximum deviation from linear LSQ fit up to considered amplitude
INL < 0.2% up to 50 MeV input dynamics
Output waveforms
“rise” time
measured rise time includes 3.8ns input signal risetime (Agilent 33250A Function / Arbitrary Waveform Generator)

## Slide 25: Impact of reverse bias voltage on the output response
100 mm thick SiC detectors
At very low reverse bias (<100V), detector capacitance is too high for a stable response
Increasing reverse bias, output slope increases (beneficial for time resolution).
No degradation of the output response up to tested overbias (250 V).

## Slide 26: Preliminary system performance - in air
mixed nuclei α source
100 mm thick SiC detector – 25 mm2

## Slide 27: Coupling with custom ASIC for spectroscopy - preliminary
100 mm thick SiC detector – 25 mm2
68M
Telescopic cascode topology with external feedback network. Trade-off between the requirement of a low equivalent input series noise and low-power constraint (10 mW/channel).
AMS CMOS C35B4C3 technology
Custom CMOS preamplifier with a target dynamic range of 100 MeV (Si equivalent), over an output voltage range of 1.1 V.
in vacuum

## Slide 28: Financial requests

## Slide 29: CHIRONE Richieste Finanziarie Preliminari per 2024 @MI
MISSIONI: 7.2 k€ + 2.0 k€ SJ
  Spostamenti Responsabile Locale e riunioni di collaborazione 0.5 k€
  Partecipazione preparativi per esperimento GSI SJ 2.0k€
  Spostamento @INFN-CT per iniziative specifiche (SiC) (x 2 viaggi, x2 pp) 3.0 k€
  Spostamento @LNS per iniziative specifiche (SiC) (x 1 viaggi, x2 pp) 2.0 k€
  Spostamento @Labec per qualificazione rivelatori SiC con protoni (x 1 viaggio, x2 pp) 1.7k€
CONSUMO: 4.0 k€
  mat. specifico da laboratorio: filo bonding, colle, alcool isopropilico, thermal pads 1.0 k€
  cavi schermati linee differenziali per setup di test in aria e in vuoto 1.0 k€
  cavi distribuzione power per setup di test in aria e in vuoto 1.0 k€
  materiale consumo per montaggi e test 0.5 k€
  materiale stampante 3D 0.5 k€
COSTRUZIONE APPARATI: 29.7 k€
  run produzione ASIC elettronica frontend FARCOS 11.2 k€
  PCB custom for SiC MB + mounting & PCB final frontend SiC + mounting 3.0 k€ + 4.5 k€
  componenti attivi e passivi 8.0 k€
  meccanica SiC 3.0 k€
INVENTARIO: 7.2 k€
  AMETEK HV power supply XG 600-1.4MEBR 3.6 k€
  5 slots NIM crate 3.6 k€
TRASPORTO: 1 k€​
  Trasporti elettronica, flange/cavi da/per CT e LNS 1.0 k€ ​
Miss.@MI | Cons.@MI | Tras.@MI | App. @MI | Inv. @MI
7.2 + 2.0SJ | 4 | 1 | 29.7 | 7.2